## Slide 1: CoMeT Count-Min-Sketch-based Row Tracking to Mitigate RowHammer at Low Cost
1: DRAM Organization
DRAM Chip
DRAM Chip
Bank
Chip I/O
DRAM Bank
Subarray
. . .
DRAM Subarray
DRAM Cell
Wordline
…
…
…
…
Row Buffer
Bitline
…
…
DRAM Row
…
…
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
Row 1
Row 3
Row 0
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
DRAM Subarray
Repeatedly activating and precharging a DRAM row causes RowHammer bitflips in nearby cells
The minimum number of activations that causes a bitflip is called the RowHammer threshold
DRAM chips are more vulnerable to read disturbance today
Read disturbance bitflips occur at much lower activation counts (more than two orders of magnitude decrease in less than a decade):
Mitigation techniques against read disturbance attacks need to be effective and efficient for highly vulnerable systems
NRH = ∞
(all good)
NRH = 1
139K
[Kim+, ISCA’14]
9.6K
[Kim+, ISCA’20]
<1K
[Luo+, ISCA’23]
2: Read Disturbance Vulnerabilities
CoMeT
ABACuS
3: Limitations of Existing Mitigations
VERY LOW
Performance & Energy Costs
VERY HIGH
Area Cost
One ACT counter per aggressor row
Processor Chip
Counter A
Counter B
Counter C
Tag A
Tag B
Tag C
One ACT counter
per DRAM row
Processor Chip
DRAM
Row A
Counter A
Row B
Row C
Counter B
Counter C
Counter D
Row D
HIGH
LOW
Processor Chip
<1 counter per DRAM row
Shared Counters
Counter A
Counter B
Tag A
Tag B
HIGH
LOW
Many DRAM rows
(e.g., 128K per bank)
# of aggressor rows
increases significantly
High DRAM bandwidth consumption
CAM-based implementation
No existing mitigation technique prevents RowHammer bitflips at low area, performance and energy costs
4: Goal
Prevent RowHammer bitflips with low area, performance, and energy overheads in highly RowHammer-vulnerable DRAM-based systems
(e.g., a RowHammer threshold of 125)
5: CoMeT’s Key Observation and Key Idea
Tag-based counters are highly accurate:
Each one tracks one row's activation count
HIGH ACCURACY
Row 0
…
Row 0
Tag
Counter
Mapping without tags
1
H0(ID) = ID % 4
Hash Function
(Example)
DRAM
Row 0
Row 1
Row 2
Row 3
Row 4
Fixed number of counters
2
0
1
2
3
Counters
Hash-based counters are low-cost:
can be implemented with low-cost structures and
can aggregate many rows' activation counts together
Row 0
Row 4
1
Track most DRAM rows’ activations with low area cost
2
Track a small set of hot rows accurately
Key Idea
Key Observation
Counter Table (CT):
Maps each DRAM row to a group of low-cost hash-based counters by employing the Count-Min Sketch technique
Triggers a preventive refreshes when the aggressor's counter group reaches an activation threshold
Recent Aggressor Table (RAT):
Allocates highly accurate per-DRAM-row counters for only a small set of DRAM rows that are activated many times
Tracks DRAM row activations at low area cost
Reduces performance penalties by increasing tracking accuracy
Chart: RowHammer Threshold
| 1000 | 500 | 250 | 125
Normalized IPC | 0.9981 | 0.99136 | 0.98131 | 0.95986
Chart: RowHammer Threshold
| 1000 | 500 | 250 | 125
Normalized DRAM Energy | 1.0009 | 1.0039 | 1.0089 | 1.0207
4.01%
2.07%
Performance and DRAM Energy Analysis across single-core applications
Scalable and Low Overhead DRAM Read Disturbance Mitigation
Nisa Bostanci Ataberk Olgun Giray Yaglikci Geraldo de Oliveira Yahya Tugrul
Haocong Luo Ismail Yuksel Konstantinos Kanellopoulos Mohammad Sadrosadati Onur Mutlu
Key Mechanism: ABACuS Track the maximum (worst) activation count of sibling rows using one counter
7: ABACuS’s Key Observation and Key Idea
1
Address mappings distribute consecutive cache blocks to different banks (but to the same row ID)
2
Workloads tend to access cache blocks in close proximity at around the same time
Many workloads access the same row ID in different banks at around the same time
Sibling rows: Rows with the same ID across all banks
Key Idea: Sibling rows can share one hardware counter
Reduce the number of counters by a factor of the number of banks in the chip
Lower overhead than all evaluated state-of-the-art mechanisms
8: ABACuS’s Evaluation and Conclusion
Cycle-level simulations using Ramulator
Workloads:
62 1- & 8-core workloads
Four different very low nRH values: 1000, 500, 250, 125
Four state-of-the-art mitigation mechanisms
Graphene, Hydra, PARA, REGA
Open-sourced: https://github.com/CMU-SAFARI/ABACuS
6: CoMeT’s Evaluation and Conclusion
Chart: RowHammer Threshold
| 1K | 125
CoMeT | 0.09 | 0.07
Graphene | 0.49 | 4.89
Hydra | 0.08 | 0.07
4.89
0.89
74.2×
5.4×
CoMeT achieves a good trade-off between area, performance and energy costs - incurs significantly less area overhead (74.2×)
- outperforms the state-of-the-art (by up to 39.1%)
Cycle-level simulations using Ramulator
Workloads:
62 1- & 8-core workloads
Four different very low nRH values: 1000, 500, 250, 125
Four state-of-the-art mitigation mechanisms
Graphene, Hydra, PARA, REGA
Artifact available, functional, and reproduced
Open-sourced: https://github.com/CMU-SAFARI/CoMeT
Bostanci et al., "CoMeT: Count-Min-Sketch-based Row Tracking to Mitigate RowHammer at Low Cost,” in HPCA, 2024
Olgun et al., “ABACuS: All-Bank Activation Counters for Scalable and Low Overhead RowHammer Mitigation,” in USENIX Security, 2024