## Slide 1: Scalable and Low Overhead DRAM Read Disturbance Mitigation
Abdullah Giray Yağlıkçı
(on behalf of Ataberk Olgun)
The Future of Memory and Storage
August 6, 2024
Notes: Hello everyone, welcome to my doctoral examination. Today, I will give a high-level overview of the work that I have done throughout my Ph.D.

## Slide 2: Brief Self Introduction
Abdullah Giray Yaglikci
  Researcher @ SAFARI Research Group since August 2016
    ETH Zurich (Feb 2018 – ongoing)
    Intel Labs (Aug 2017 – Feb 2018)
    Carnegie Mellon University (Aug 2016 – Aug 2017)
  Defended my PhD thesis, advised by Onur Mutlu, in April 2024
  https://agyaglikci.github.io/
  agirayyaglikci@gmail.com (Best way to reach me)
  https://safari.ethz.ch
Research interests:
  Computer architecture, hardware security
  Memory and storage systems
  Hardware security, safety, reliability, performance, availability, fairness, energy efficiency
  Hardware/software cooperation
  …

## Slide 3: Papers in This Talk
Ataberk Olgun, Yahya Can Tugrul, Nisa Bostanci, Ismail Emir Yuksel, Haocong Luo, Steve Rhyner, Abdullah Giray Yaglikci, Geraldo F. Oliveira, and Onur Mutlu, "ABACuS: All-Bank Activation Counters for Scalable and Low Overhead RowHammer Mitigation” Proceedings of the 33rd USENIX Security Symposium (USENIX Security), Philadelphia, PA, USA, August 2024. [arXiv version] [ABACuS Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, functional, and reproduced.
F. Nisa Bostanci, Ismail Emir Yuksel, Ataberk Olgun, Konstantinos Kanellopoulos, Yahya Can Tugrul, A. Giray Yaglikci, Mohammad Sadrosadati, and Onur Mutlu, "CoMeT: Count-Min-Sketch-based Row Tracking to Mitigate RowHammer at Low Cost” Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), April 2024. [Slides (pptx) (pdf)] [arXiv version] [CoMeT Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reviewed and reproducible.

## Slide 4: Memory & Generative AI (I)
Image Source: https://www.cerebras.net/blog/cerebras-architecture-deep-dive-first-look-inside-the-hw/sw-co-design-for-deep-learning

## Slide 5: Memory & Generative AI (II)
Gholami A, Yao Z, Kim S, Mahoney MW, Keutzer K. AI and Memory Wall. RiseLab Medium Blog Post, University of Califonia Berkeley, 2021, March 29.
Increasing gap

## Slide 6: Memory Isolation
A memory access should not have unintended side effects on data stored in other addresses
A fundamental property for robustness (safety, security, and reliability)
Memory
access
1  0
Leak private information
Take over a computer
Data loss or corruption
Compromise application correctness
Memory isolation is difficult in modern memory chips
Notes: Let’s start with the concept of memory isolation, a fundamental primitive for system security and privacy [CLICK]
Imagine that you access a memory location, and a bitflip occurs in some other location [CLICK]
We would not want this to happen because it can lead to data loss or corruption [CLICK]
Compromise application correctness [CLICK]
It can be used to leak private information [CLICK]
Or even to take over a computer [CLICK]
Therefore, we have this principle called memory isolation dictating that a memory access should not have unintended side effects on data stored in other addresses. This is important for memory integrity [CLICK]
Unfortunately, it is difficult in modern memory chips and here is why [CLICK]

## Slide 7: Read Disturbance in Modern Memory Chips
Prevalent memory technology: Dynamic Random Access Memory (DRAM)
DRAM stores data in the form of electrical charge on a capacitor
DRAM leaks charge over time and needs periodic refresh
DRAM Read Disturbance: Accessing a DRAM cell disturbs other physically nearby cells and exacerbates their charge leakage
Wordline
Bitline
Charge
leakage
paths
Notes: Dynamic random access memory (DRAM) is the prevalent memory technology today. [CLICK]
DRAM stores a bit of data in the form of electrical charge on a capacitor [CLICK]
To access we assert a wire called wordline [CLICK]
Which enables a transistor, conducting the capacitor to another wire called bitline [CLICK]
DRAM is a volatile memory technology as it leaks charge over time and needs to be periodically refreshed [CLICK]
Accessing a DRAM cell disturbs other physically nearby cells and exacerbates their charge leakage. This is called DRAM read disturbance [CLICK]

## Slide 8: High-Level DRAM Organization
DRAM
Channel
DRAM Module
DRAM chips

## Slide 9: DRAM Chip Internals
Bitline
S
S
S
S
Sense amplifiers
(row buffer)
Wordline
DRAM Cell
Bank
DRAM Array

## Slide 10: RowHammer: An Example of DRAM Read Disturbance
Row 0
Row 1
Row 2
Row 3
Row 4
Repeatedly opening (activating) and closing (precharging)
a DRAM row causes RowHammer bitflips in nearby cells
and breaks memory isolation
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 2
closed
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
closed
Aggressor Row
DRAM Subarray
Notes: A prime example of DRAM read disturbance is RowHammer, which I will show in this slide.
DRAM cells are organized in 2 dimensional arrays as rows and columns and internally accessed in a DRAM row granularity. For example, to access a data stored in Row 2, [CLICK]
We first need to open Row 2, and then perform accesses. Once we need to access another row, we need to close Row 2 and open the other row [CLICK]
[BACK& FORTH] If we keep opening and closing this row many times, called hammering a row, [CLICK]
We observe bitflips in physically nearby DRAM rows [CLICK]
This phenomenon is called RowHammer. We refer to the hammered row as the aggressor row and the rows that are affected as victim rows. [CLICK]

## Slide 11: One Can Take Over an Otherwise-Secure System
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn, 2015)
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
Induce bit flips in page table entries (PTEs).
Gain write access to its own page table, and hence gain read-write access to all of physical memory.

## Slide 12: More Security Implications (I)
Source: https://lab.dsst.io/32c3-slides/7197.html
Rowhammer.js: A Remote Software-Induced Fault Attack in JavaScript (DIMVA’16)
“We can gain unrestricted access to systems of website visitors.”

## Slide 13: More Security Implications (II)
Source: https://fossbytes.com/drammer-rowhammer-attack-android-root-devices/
Drammer: Deterministic Rowhammer Attacks on Mobile Platforms, CCS’16
  “Can gain control of a smart phone deterministically”

## Slide 14: More Security Implications (III)
Using an integrated GPU in a mobile system to remotely escalate privilege via the WebGL interface. IEEE S&P 2018

## Slide 15: More Security Implications (IV)
Rowhammer over RDMA (I)
[Tatar+ USENIX ATC, 2018]

## Slide 16: More Security Implications (V)
Rowhammer over RDMA (II)
[Lipp+ EuroS&PW, 2020]

## Slide 17: More Security Implications (VI)
An FPGA-based RowHammer attack recovering private keys twice as fast compared to CPU-based attacks
[Weissman+ CHES 2020]

## Slide 18: More Security Implications (VII)
[Kwong+ IEEE S&P 2020]

## Slide 19: More Security Implications (VIII)
[Hong+ USENIX Security 2019]

## Slide 20: More Security Implications (IX)
[Yao+ USENIX Security 2020]

## Slide 21: More Security Implications (X)
HammerScope is a software-based power analysis method using RowHammer as a side channel
[Cohen+ CCS 2022]

## Slide 22: More Security Implications (XI)
Exploiting Correcting Codes: On the Effectiveness of ECC Memory Against Rowhammer Attacks. Cojocar, L. .; Razavi, K.; Giuffrida, C.; and Bos, H. In S&P, May 2019 Best Practical Paper Award, Pwnie Award Nomination for Most Innovative Research [Paper] [Slides]
Thus, many believed that Rowhammer on ECC memory, even if plausible in theory, is simply impractical. This paper shows this to be false: while harder, Rowhammer attacks are still a realistic threat even to modern ECC-equipped systems.

## Slide 23: More Security Implications (XII)
15x Vendor A DDR4 modules
U-TRR
New RowHammer access patterns
15x Vendor B DDR4 modules
15x Vendor C DDR4 modules
All 45 modules we test are vulnerable
99.9% of rows in a DRAM bank experience at least one RowHammer bit flip
Up to 7 RowHammer bitflips in an 8-byte dataword, making ECC ineffective
TRR does not provide security against RowHammer
U-TRR can facilitate the development of new RowHammer attacks and more secure RowHammer protection mechanisms
Hasan Hassan, Yahya Can Tugrul, Jeremie S. Kim, Victor van der Veen, Kaveh Razavi, and Onur Mutlu, "Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications,” MICRO, 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Full Talk (25 mins)] [Lightning Talk (1.5 mins)]
Notes: [CLICK] The RowHammer vulnerability of modern DRAM is a critical reliability and security threat.
[CLICK] The security guarantees of TRR, which is the commonly used RowHammer protection mechanism, cannot be easily studied as TRR is obscure, undocumented, and proprietary.
[CLICK] In this work, our main goal is to answer the following questions. Is TRR fully secure? How can we validate the security guarantees of different TRR mechanisms?
[CLICK] To this end, we propose U-TRR, a new methodology that leverages data retention failures in DRAM to uncover the inner workings of TRR and study its security.
[CLICK] Using U-TRR, we analyze 15 DDR4 DRAM modules from each of the three major DRAM vendors.
[CLICK] Through these analyses, we make several observations regarding the TRR mechanisms implemented in these modules and craft new custom RowHammer access patterns that cause RowHammer bit flips in TRR-protected DRAM modules.
[CLICK] Our results show that: First, all 45 modules that we test across three vendors are vulnerable to our new RowHammer access patterns.
[CLICK] Second, our access pattern cause at least one bit flip in almost all DRAM rows in many modules. This makes system-level RowHammer attacks easier to mount as the attacker would have the ability to cause bit flips in almost any DRAM row [CLICK] Third, we observe that our access patterns cause up to 7 RowHammer bit flips in an 8-byte dataword, making ECC ineffective and systems equipped with ECC also susceptible to RowHammer attacks
[CLICK] We conclude that TRR does not provide security against RowHammer and can be easily circumvented using the new understanding provided by U-TRR.
[CLICK] We believe and hope that U-TRR will facilitate future research by enabling rigorous and open analysis of RowHammer mitigation mechanisms, leading to the development of both new RowHammer attacks and more secure RowHammer protection mechanisms.

## Slide 24: A RowHammer Survey:
Onur Mutlu, Ataberk Olgun, and A. Giray Yaglikci, "Fundamentally Understanding and Solving RowHammer” Invited Special Session Paper at the 28th Asia and South Pacific Design Automation Conference (ASP-DAC), Tokyo, Japan, January 2023. [arXiv version] [Slides (pptx) (pdf)] [Talk Video (26 minutes)]
https://arxiv.org/pdf/2211.07613.pdf

## Slide 25: Breaking Samsung’s Best Practice
Salman Qazi and Daniel Moghimi, “SoothSayer: Bypassing DSAC Mitigation by Predicting Counter Replacement,” DRAMSec, 2024

## Slide 26: RowHammer in DDR5
Patrick Jattke; Max Wipfli; Flavien Solt; Michele Marazzi; Matej Bölcskei; and Kaveh Razavi, “ZenHammer: Rowhammer Attacks on AMD Zen-based Platforms,” in USENIX Security, 2024. [Paper] [URL]
We found bit flips on only 1 of 10 tested devices (S1), suggesting that the changes in DDR5 such as improved Rowhammer mitigations, on-die error correction code (ECC), and a higher refresh rate (32 ms) make it harder to trigger bit flips.

## Slide 27: DRAM Read Disturbance: A Critical Challenge
DRAM cells become increasingly more vulnerable to read disturbance
Technology node scaling
Chart: 
| The Min. ACT Count to Observe Bit Flips
2023 | 1
2020 | 9.6
2014 | 139.2
[Luo+, ISCA’23]
[Kim+, ISCA’20]
[Kim+, ISCA’14]
Notes: With technology node scaling, DRAM cells get smaller in size and closer to each other[CLICK]
Such that we observe significant reductions in the minimum hammer count to induce the first bitflip in the last decade [CLICK]
Thus DRAM cells become increasingly more vulnerable to read disturbance [CLICK]

## Slide 28: Existing RowHammer Mitigations (I)
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 0
Row 1
Row 3
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
DRAM Subarray
Refreshing potential victim rows mitigates read disturbance bitflips
Aggressor Row

## Slide 29: Existing RowHammer Mitigations (II)
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 0
Row 1
Row 3
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
DRAM Subarray
Mitigation techniques track DRAM row activation counts (of aggressor rows) to preventively refresh potential victim rows
Aggressor Row

## Slide 30: Existing RowHammer Mitigations (III) Overview of Preventive Refresh-Based Mitigation Techniques
VERY LOW
Performance & Energy Costs
VERY HIGH
Area Cost
One ACT counter per aggressor row
Processor Chip
Counter A
Counter B
Counter C
Tag A
Tag B
Tag C
One ACT counter
per DRAM row
Processor Chip
DRAM
Row A
Counter A
Row B
Row C
Counter B
Counter C
Counter D
Row D
HIGH
LOW
Processor Chip
<1 counter per DRAM row
Shared Counters
Counter A
Counter B
Tag A
Tag B
HIGH
LOW
Many DRAM rows
(e.g., 128K per bank)
# of aggressor rows
increases significantly
High DRAM bandwidth consumption
CAM-based implementation

## Slide 31: Existing RowHammer Mitigations (IV) Overhead Trade-Off of State-of-the-Art Mitigation Techniques
Notes: Ideally, we would like to achieve low energy, processor chip and DRAM area and performance overheads
[CLICK]
As you can see from this radar chart

## Slide 32: Existing RowHammer Mitigations (IV) Overhead Trade-Off of State-of-the-Art Mitigation Techniques
No existing mitigation technique prevents RowHammer bitflips at low area, performance and energy costs
Notes: None of the existing mitigation techniques prevents RowHammer at low area performance and energy costs

## Slide 33: Our Goal
Prevent RowHammer bitflips with low area, performance, and energy overheads in highly vulnerable DRAM-based systems
(e.g., a RowHammer threshold of 125)

## Slide 34: ABACuS: All-Bank Activation Counters
Ataberk Olgun, Yahya Can Tugrul, Nisa Bostanci, Ismail Emir Yuksel, Haocong Luo, Steve Rhyner, Abdullah Giray Yaglikci, Geraldo F. Oliveira, and Onur Mutlu, "ABACuS: All-Bank Activation Counters for Scalable and Low Overhead RowHammer Mitigation” To appear in Proceedings of the 33rd USENIX Security Symposium (USENIX Security), Philadelphia, PA, USA, August 2024. [arXiv version] [ABACuS Source Code]

## Slide 35: ABACuS All-Bank Activation Counters for Scalable and Low Overhead RowHammer Mitigation
Ataberk Olgun
Yahya Can Tuğrul
F. Nisa Bostancı
İsmail Emir Yüksel
Haocong Luo
Steve Rhyner
A. Giray Yağlıkçı
Geraldo F. Oliveira
Onur Mutlu
will be presented next week in USENIX Security 2024
35

## Slide 36: Key Observation
Many workloads access the same row address in different banks at around the same time
Bank 0
Bank 1
Bank 2
Bank 3
Row X
Row X
Row X
Row X
CPU
Load request targeting bank 0 row X
LD (0,X)
Time
LD (1,X)
LD (3,Y)
LD (3,X)
LD (2,X)
LD (2,X)
LD (3,X)
LD (3,Y)
LD (1,X)
LD (0,X)
Sibling rows
36
Notes: Many workloads access the same row address in different banks at around the same time. We will show what we observe over an example.

## Slide 37: Explanation for the Key Observation
2
Address mappings distribute consecutive cache blocks to different banks to leverage bank-level parallelism (using the same row ID)
1
Programs exhibit spatial locality: access cache blocks around each other at around the same time
37
Notes: 32-bank system
Window of 128 row activations
Shows the numbe rof different banks accessed in each window

## Slide 38: Motivational Analysis
Workloads access the same row address in different DRAM banks at around the same time
38
Gathered from 128 row activation windows in a 32-bank system
Notes: 32-bank system
Window of 128 row activations
Shows the numbe rof different banks accessed in each window

## Slide 39: Problem
No mitigation mechanism leverages
the spatial locality across banks
Area overhead linearly increases
with the number of banks

## Slide 40: Key Idea
Sibling rows: Rows with the same ID across all banks
Sibling rows can share one activation counter
to reduce the number of counters
by a factor of the bank count
Bank 0
Counter X
Bank 1
Counter X
Bank 15
Counter X
…
…
…
Bank 0-15
Counter X
Existing Row Activation Tracker
ABACuS-Based Tracker
16x reduction in number of counters

## Slide 41: ABACuS: High-level Overview
Key Mechanism: Track the maximum (worst) activation count of sibling rows using one counter
41

## Slide 42: ABACuS’s Integration with Misra-Gries Algorithm (I)
42
Notes: Need to describe misra gries as something secondary and not very fundamental

## Slide 43: ABACuS’s Integration with Misra-Gries Algorithm (II)
43
ABACuS does not underestimate but can overestimate
a DRAM row’s activation count
potential
performance
overhead
secure

## Slide 44: Evaluation
System Configuration
Workloads: 62 1- & 8-core workloads
Four different very low nRH values: 1000, 500, 250, 125
Four state-of-the-art mitigation mechanisms
44

## Slide 45: Performance Comparison
Lower overhead than all evaluated state-of-the-art mechanisms (except Graphene)
45

## Slide 46: More in the Paper
More motivational analysis
Multi-core performance & energy results
Performance under adversarial workloads
  Alternative ABACuS design
Performance & energy sensitivity to:
  Blast radius
  Number of ABACuS counters
  Number of banks
Circuit area, latency, energy, and power
Security proof
46

## Slide 47: ABACuS Summary
Goal: Prevent RowHammer bitflips at low performance, energy, and area cost especially at very low RowHammer thresholds (e.g., 125 aggressor row activations induce a bitflip)
Key Observation: Many workloads access the same row address in different DRAM banks at around the same time
Key Idea: Use one counter to track the activation count of many rows with the same address across all DRAM banks
Key Results: At very low RowHammer thresholds, ABACuS:
Induces small system performance and DRAM energy overhead
Outperforms the state-of-the-art mitigation (Hydra)
Takes up 22.7X smaller chip area than state-of-the-art (Graphene)
https://github.com/CMU-SAFARI/ABACuS
47

## Slide 48: Extended Version on arXiv
https://arxiv.org/pdf/2310.09977.pdf
48

## Slide 49: ABACuS is Open Source
https://github.com/CMU-SAFARI/ABACuS
49

## Slide 50: CoMeT: Count-Min-Sketch-based Row Tracking
F. Nisa Bostanci, Ismail Emir Yuksel, Ataberk Olgun, Konstantinos Kanellopoulos, Yahya Can Tugrul, A. Giray Yaglikci, Mohammad Sadrosadati, and Onur Mutlu, "CoMeT: Count-Min-Sketch-based Row Tracking to Mitigate RowHammer at Low Cost” Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), April 2024. [Slides (pptx) (pdf)] [arXiv version] [CoMeT Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reviewed and reproducible.

## Slide 51: CoMeT Count-Min-Sketch-based Row Tracking to Mitigate RowHammer at Low Cost
F. Nisa Bostancı
I. E. Yüksel A. Olgun K. Kanellopoulos Y. C. Tuğrul
A. G. Yağlıkçı M. Sadrosadati O. Mutlu
https://github.com/CMU-SAFARI/CoMeT
HPCA 2024

## Slide 52: Key Observation
Tag-based counters are highly accurate:
Each one tracks one row's activation count
HIGH ACCURACY
Row 0
…
Row 0
Tag
Counter
Mapping without tags
1
H(ID) = ID % 4
Hash Function
(Example)
DRAM
Row 0
Row 1
Row 2
Row 3
Row 4
Fixed number of counters
2
0
1
2
3
Counters
Hash-based counters are low-cost:
can be implemented with low-cost structures and
can aggregate many rows' activation counts together
Row 0
Row 4
LOW COST
Notes: We observe that there are two types of counters
[CLICK]Hash based counters are low cost
[CLICK]And tag based counters are highly accurate
We want to get the best of both worlds
Now let me explain how these work

## Slide 53: Key Idea
1
Use low-cost and scalable hash-based counters to track most DRAM rows' activations with low area overhead
2
Use highly accurate tag-based counters to track only a small set of DRAM rows to achieve low performance overhead

## Slide 54: CoMeT Overview
Counter Table (CT):
Maps each DRAM row to a group of low-cost hash-based counters as uniquely as possible by employing the Count-Min Sketch technique
Triggers a preventive refresh to an aggressor row's victim rows when the aggressor's counter group reaches an activation threshold
Recent Aggressor Table (RAT):
Allocates highly accurate per-DRAM-row counters for only a small set of DRAM rows that are activated many times
Tracks DRAM row activations at low area cost
Reduces performance penalties by increasing tracking accuracy

## Slide 55: More Operational Details for CoMeT
CoMeT
Counter Table
Hash-based Counters
Recent Aggressor Table
ACT A
Counter Table-Based Estimation
Recent Aggressor Table-Based
Estimation
1
2
used when there is a row ID match
ACT_Count(A) == NPR
ESTIMATION
Preventively Refresh
A's victim rows
preventive refresh threshold
3
Tag-based Counters
https://arxiv.org/abs/2402.18769
https://github.com/CMU-SAFARI/CoMeT

## Slide 56: Hardware Complexity
Storage and area overhead analysis: CACTI
Dual-rank area overhead comparison:
Chart: RowHammer Threshold
| 1K | 125
CoMeT | 0.09 | 0.07
Graphene | 0.49 | 4.89
Hydra | 0.08 | 0.07
4.89
0.89
CoMeT stores fewer bits as the RowHammer threshold decreases
74.2×
5.4×
CoMeT incurs a significantly less area overhead than Graphene and a similar area overhead to Hydra
Similar area overheads
Significantly less area overhead

## Slide 57: Evaluation Methodology
Performance and energy consumption evaluation: cycle-level simulations using Ramulator [Kim+, CAL 2015] and DRAMPower [Chandrasekar+, DATE 2013]
System Configuration:
  Processor 1 or 8 cores, 3.6GHz clock frequency,
  4-wide issue, 128-entry instruction window
  DRAM DDR4, 1 channel, 2 rank/channel, 4 bank groups,
  4 banks/bank group, 128K rows/bank
  Memory Ctrl. 64-entry read and write requests queues,
  Scheduling policy: FR-FCFS with a column cap of 16 Last-Level Cache 8 MiB (single-core), 16 MiB (8-core)
  CoMeT Counter Table: 4 hash functions 512 counters per hash Recent Aggressor Table: 128 entries
Comparison Points: 4 state-of-the-art RowHammer mitigations
  Graphene (best performing), Hydra (area-optimized best performing), Low Processor Chip Area Cost: REGA, PARA
Workloads: 61 single-core applications and 56 8-core workload mixes
  SPEC CPU2006, SPEC CPU2017, TPC, MediaBench, YCSB
https://github.com/CMU-SAFARI/CoMeT

## Slide 58: Performance and DRAM Energy
Chart: RowHammer Threshold
| 1000 | 500 | 250 | 125
Normalized IPC | 0.9981 | 0.99136 | 0.98131 | 0.95986
Chart: RowHammer Threshold
| 1000 | 500 | 250 | 125
Normalized DRAM Energy | 1.0009 | 1.0039 | 1.0089 | 1.0207
4.01%
2.07%
CoMeT prevents bitflips with very small average performance and DRAM energy overheads compared to a baseline system with no RowHammer mitigation
Average performance and DRAM energy overheads of CoMeT across single-core applications
Notes: We evaluate the average performance and DRAM energy overheads of CoMeT across single core applications
[CLICK] This is CoMeT's performance normalized to a system with no RH mitigation across different RH thresholds [CLICK]
As RH threshold decreases CoMeT has a small performance overhead due to preventive refreshes as opposed to the baseline that does not do preventive refresh
[CLICK] This is CoMeT's DRAM energy consumption normalized to the same baseline [CLICK] and it shows a similar result
[CLICK] We conclude that CoMeT prevents bitflips with very small average performance ….

## Slide 59: Performance Comparison: Single-Core Applications
1.75%
1.75%
(average)
CoMeT outperforms all low-area-cost mitigations starting from the RowHammer threshold of 500
CoMeT incurs a small performance overhead (≤ 1.75%) over Graphene and outperforms Hydra (by up to 39.1%) at all RowHammer thresholds

## Slide 60: Performance Comparison: 8-Core Workloads
Trends are similar to single-core application evaluation trends

## Slide 61: DRAM Energy Comparison: Single-Core Applications
0.96%
0.04%
CoMeT incurs a small DRAM energy overhead (<1%) over Graphene and consumes less DRAM energy than Hydra
CoMeT consumes less DRAM energy than all low-area-cost mitigations for all RowHammer thresholds
1.88%
0.39%

## Slide 62: DRAM Energy Comparison: 8-Core Workloads
Multicore energy trends are similar to single core energy trends

## Slide 63: More in the Paper
Security Analysis of CoMeT
Sensitivity Analysis
  Counter Table Configurations
  Recent Aggressor Table Configurations
  Counter Reset Period and Preventive Refresh Threshold Values
CoMeT's Performance under Adversarial Workloads
Comparison against Throttling-Based Mitigation Techniques
CoMeT's Performance at High RowHammer Thresholds

## Slide 64: More in the Paper
Security Analysis of CoMeT
Sensitivity Analysis
  Counter Table Configurations
  Recent Aggressor Table Configurations
  Counter Reset Period and Preventive Refresh Threshold values
Performance Evaluation under Adversarial Workloads
Performance Evaluation Comparison against Throttling-Based Mitigation Techniques
Performance Evaluation at High RowHammer Thresholds
https://arxiv.org/abs/2402.18769

## Slide 65: Conclusion
https://github.com/CMU-SAFARI/CoMeT
Evaluation: CoMeT achieves a good trade-off between area, performance and energy costs
incurs significantly less area overhead (74.2×) compared to the state-of-the-art technique
outperforms the state-of-the-art technique (by up to 39.1%)
CoMeT:
tracks most DRAM rows with scalable hash-based counters by employing the Count-Min-Sketch technique to achieve a low area cost
tracks only a small set of DRAM rows that are activated many times with highly accurate per-DRAM-row activation counters to reduce performance penalties
Key Idea: Use low-cost and scalable hash-based counters to accurately track DRAM rows
Goal: Prevent RowHammer bitflips with low area, performance, and energy overheads in highly RowHammer-vulnerable DRAM-based systems

## Slide 66: CoMeT is Open Source and Artifact Evaluated
https://github.com/CMU-SAFARI/CoMeT

## Slide 67: Scalable and Low Overhead DRAM Read Disturbance Mitigation
Abdullah Giray Yağlıkçı
(on behalf of Ataberk Olgun)
The Future of Memory and Storage
August 6, 2024
Notes: Hello everyone, welcome to my doctoral examination. Today, I will give a high-level overview of the work that I have done throughout my Ph.D.

## Slide 68: Scalable and Low Overhead DRAM Read Disturbance Mitigation
Abdullah Giray Yağlıkçı
(on behalf of Ataberk Olgun)
The Future of Memory and Storage
August 6, 2024
Backup Slides
Notes: Hello everyone, welcome to my doctoral examination. Today, I will give a high-level overview of the work that I have done throughout my Ph.D.

## Slide 69: ABACuS All-Bank Activation Counters for Scalable and Low Overhead RowHammer Mitigation
Ataberk Olgun
Yahya Can Tuğrul
F. Nisa Bostancı
İsmail Emir Yüksel
Haocong Luo
Steve Rhyner
A. Giray Yağlıkçı
Geraldo F. Oliveira
Onur Mutlu

## Slide 70: ABACuS Summary
Problem: As DRAM becomes more vulnerable to read disturbance, existing RowHammer mitigation techniques either prevent bitflips
at high area overheads or
with prohibitively large performance and energy overheads
Goal: Prevent RowHammer bitflips at low performance, energy, and area cost especially at very low RowHammer thresholds (e.g., 125 aggressor row activations induce a bitflip)
Key Observation: Many workloads access the same row address in different DRAM banks at around the same time
Key Idea: Use one counter to track the activation count of many rows with the same address across all DRAM banks
Key Results: At very low RowHammer thresholds, ABACuS:
Induces small system performance and DRAM energy overhead
Outperforms the state-of-the-art mitigation (Hydra)
Takes up 22.7X smaller chip area than state-of-the-art (Graphene)
https://github.com/CMU-SAFARI/ABACuS

## Slide 71: Outline
1. Background & Motivation
3. Evaluation
4. Conclusion
2. ABACuS: Key Idea and Mechanism

## Slide 72: Outline
1. Background & Motivation
3. Evaluation
4. Conclusion
2. ABACuS: Key Idea and Mechanism

## Slide 73: DRAM Read Disturbance (I)
CPU
DRAM Module
DRAM Chip
Notes: This is a typical DRAM-based computing system with a CPU and a DRAM module
[CLICK] We will look at a simplified depiction of this DRAM chip to better understand the read disturbance vulnerability

## Slide 74: DRAM Read Disturbance (II)
Read disturbance in DRAM breaks memory isolation
Prominent example: RowHammer
Row 1
Row 2
Row 3
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 2
open
Row 2
closed
DRAM Chip
Victim Row
Victim Row
Aggressor Row
Repeatedly opening (activating) and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
[Kim+, ISCA’14]
Notes: Read disturbance has significant system-level implications because it breaks memory isolation.
[CLICK] A prominent example of read disturbance is RowHammer.
[CLICK] [CLICKx8] Repeatedly activating and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
We call the repeatedly activated row the aggressor row and the rows that have bitflips victim rows

## Slide 75: Read Disturbance Worsens
Read disturbance bitflips occur at much smaller activation counts
  More than 100x decrease in less than a decade
139K
[Kim+, ISCA’14]
9.6K
[Kim+, ISCA’20]
<1K
[Luo+, ISCA’23]
Mitigation techniques against read disturbance attacks need to be effective and efficient for highly vulnerable systems
[Bostanci+, HPCA’24]

## Slide 76: Read Disturbance Mitigation Approaches
There are many ways to mitigate RowHammer bitflips
More robust DRAM chips and/or error-correcting codes
Increased refresh rate
Physical isolation
Preventive refresh
Proactive throttling
Notes: [CLICKx5] There are multiple ways to mitigate RowHammer bitflips each offering a different system
design point in the performance, energy, area tradeoff space
[CLICK] Preventive refresh-based ones are promising because of X and Y

## Slide 77: Preventive Refresh
Row 1
Row 2
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 2
open
Row 1
Row 3
Row 0
Row 2
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 1
DRAM Chip
Refreshing potential victim rows mitigates read disturbance bitflips
Aggressor Row
[Kim+, ISCA’20]
Requires aggressor row activation count estimation or tracking
Notes: [CLICKx5] There are multiple ways to mitigate RowHammer bitflips each offering a different system
design point in the performance, energy, area tradeoff space
[CLICK] Preventive refresh-based ones are promising because of X and Y

## Slide 78: Preventive-Refresh-Based Mitigations
VERY LOW
Performance & Energy Costs
VERY HIGH
Area Cost
One ACT counter per aggressor row
Processor Chip
Counter A
Counter B
Counter C
Tag A
Tag B
Tag C
One ACT counter
per DRAM row
Processor Chip
DRAM
Row A
Counter A
Row B
Row C
Counter B
Counter C
Counter D
Row D
HIGH
LOW
Processor Chip
<1 counter per DRAM row
Shared Counters
Counter A
Counter B
Tag A
Tag B
HIGH
LOW
Many DRAM rows
(e.g., >1M)
# of aggressor rows
increases significantly
High DRAM bandwidth consumption
CAM-based implementation
[Bostanci+, HPCA’24]
Notes: If we look at how prior works estimate or track the activation count of DRAM rows, we see three main design choices

## Slide 79: Problem & Goal
Prevent RowHammer bitflips at low performance, energy, and area cost especially at very low RowHammer thresholds (e.g., 125 aggressor row activations induce a bitflip)
No existing mitigation technique prevents RowHammer bitflips at low area, performance and energy costs
Problem
Goal

## Slide 80: Outline
1. Background & Motivation
3. Evaluation
4. Conclusion
2. ABACuS: Key Idea and Mechanism

## Slide 81: Key Observation
Many workloads access the same row address in different banks at around the same time
Bank 0
Bank 1
Bank 2
Bank 3
Row X
Row X
Row X
Row X
CPU
Load request targeting bank 0 row X
LD (0,X)
Time
LD (1,X)
LD (3,Y)
LD (3,X)
LD (2,X)
LD (2,X)
LD (3,X)
LD (3,Y)
LD (1,X)
LD (0,X)
Sibling rows
Notes: Many workloads access the same row address in different banks at around the same time. We will show what we observe over an example.

## Slide 82: Explanation for the Key Observation
1
A program tends to access neighboring cache blocks at around the same time
e.g., a streaming access to an array
2
Spatial locality in memory accesses
Modern physical  DRAM address mappings
Place neighboring cache blocks into different banks, but into the same row
Leverage DRAM bank-level parallelism for higher-throughput DRAM access

## Slide 83: Sibling Row Activation Count
If a row is activated RowHammer threshold (NRH) times its siblings are likely activated more than NRH/2 times
Sibling Row Activation Count
Workloads
Notes: This plot pictorially depicts our key observation across many tested [CLICK] workloads. I will not explain this in detail in the interest of time.
When a row gets activated RowHammer threshold times, which is 500 for this figure, we record the activation counts of that DRAM row’s siblings.
Each box in this plot shows the distribution of sibling rows’ activation counts for a tested workload.
[CLICK] Above the horizontal green line in the figure shows that [CLICK] if a row is activated RowHammer threshold times, its siblings are activated more than half the RowHammer threshold times.

## Slide 84: Key Idea
There are many (e.g., 16) banks in a DRAM chip
  Newer DRAM standards (DDR5) have more (32) banks
  # of activation counters linearly increases with # of banks
Sibling rows have similar activation counts
Have one counter for all siblings
  Reduce the number of counters by a factor of the number of banks
Bank 0
Counter X
Bank 1
Counter X
Bank 15
Counter X
…
…
…
Bank 0-15
Counter X
Existing Row Activation Tracker
ABACuS-Based Tracker
16x reduction in number of counters

## Slide 85: ABACuS: Overview
Track the maximum (worst) activation count across all sibling rows using one counter
Notes: ABACuS’s objective is to track the maximum activation count across all sibling rows using one counter

## Slide 86: Key Components
Adopt a frequent item counting algorithm
  Area-efficient, fewer counters to track more DRAM rows
  ABACuS is compatible with other counting methods
ABACuS Counter Table
ABACuS Counter
Row Activation Counter (RAC)
Sibling Activation Vector (SAV)
ABACuS Counter
ABACuS Counter
…
…
…
…
…
Spillover Counter
RowID
RowID
RowID
…
…
Nentries

## Slide 87: Operation
The RAC always stores the maximum activation count
  Store small additional information in SAV
ABACuS Counter
Row Activation Counter (RAC)
Sibling Activation Vector (SAV)
“Which siblings were activated since RAC was last incremented?” One bit per bank
Increment only when a sibling is activated “again” (i.e., activate targets a set SAV bit)
Notes: Recall that we want to keep track of the maximum activation count…
I will briefly explain the intuition
We have a proof in the paper.

## Slide 88: Outline
1. Background & Motivation
3. Evaluation
4. Conclusion
2. ABACuS: Key Idea and Mechanism

## Slide 89: Evaluation Methodology
Performance and energy consumption evaluation: Cycle-level simulations using Ramulator [Kim+, CAL 2015] and DRAMPower [Chandrasekar+, DATE 2013]
System Configuration:
  Processor 1 or 8 cores, 3.6GHz clock frequency,
  4-wide issue, 128-entry instruction window
  DRAM DDR4, 1 channel, 2 rank/channel, 4 bank groups,
  4 banks/bank group, 128K rows/bank, 3200 MT/s
  Memory Ctrl. 64-entry read and write requests queues,
  Scheduling policy: FR-FCFS with a column cap of 16 Last-Level Cache 2 MiB (single-core), 16 MiB (8-core)
Comparison Points: 4 state-of-the-art RowHammer mitigations
  Graphene (best performing), Hydra (area-optimized best performing), Low Processor Chip Area Cost: REGA, PARA
Workloads: 62 1- & 8-core workloads
  SPEC CPU2006, SPEC CPU2017, TPC, MediaBench, YCSB

## Slide 90: Single-Core Performance and Energy
Small 0.6% average performance overhead at nRH = 1000 1.5% at nRH = 125
ENERGY

## Slide 91: Multi-Core Performance

## Slide 92: Storage and Area Overhead
ABACuS takes up 18.93 KiB at 1K and 151.41 KiB at 125 RowHammer threshold
Area overhead analysis: CACTI
Chart: RowHammer Threshold
| 1K | 125
ABACuS | 0.04 | 0.25
Graphene | 0.81 | 5.68
Hydra | 0.1 | 0.07
Area overhead for a dual-rank system

## Slide 93: More in the Paper
More motivational analysis
Multi-core performance & energy results
Performance under adversarial workloads
  Alternative ABACuS design
Performance & energy sensitivity to:
  Blast radius
  Number of ABACuS counters
  Number of banks
Circuit area, latency, energy, and power
Security proof

## Slide 94: Outline
1. Background & Motivation
3. Evaluation
4. Conclusion
2. ABACuS: Key Idea and Mechanism

## Slide 95: ABACuS Summary
Goal: Prevent RowHammer bitflips at low performance, energy, and area cost especially at very low RowHammer thresholds (e.g., 125 aggressor row activations induce a bitflip)
Key Observation: Many workloads access the same row address in different DRAM banks at around the same time
Key Idea: Use one counter to track the activation count of many rows with the same address across all DRAM banks
Key Results: At very low RowHammer thresholds, ABACuS:
Induces small system performance and DRAM energy overhead
Outperforms the state-of-the-art mitigation (Hydra)
Takes up 22.7X smaller chip area than state-of-the-art (Graphene)
https://github.com/CMU-SAFARI/ABACuS

## Slide 96: Extended Version on arXiv
https://arxiv.org/pdf/2310.09977.pdf

## Slide 97: ABACuS is Open Source
https://github.com/CMU-SAFARI/ABACuS

## Slide 98: ABACuS All-Bank Activation Counters for Scalable and Low Overhead RowHammer Mitigation
Ataberk Olgun
Yahya Can Tuğrul
F. Nisa Bostancı
İsmail Emir Yüksel
Haocong Luo
Steve Rhyner
A. Giray Yağlıkçı
Geraldo F. Oliveira
Onur Mutlu

## Slide 99: CoMeT Count-Min-Sketch-based Row Tracking to Mitigate RowHammer at Low Cost
F. Nisa Bostancı
I. E. Yüksel A. Olgun K. Kanellopoulos Y. C. Tuğrul
A. G. Yağlıkçı M. Sadrosadati O. Mutlu
https://github.com/CMU-SAFARI/CoMeT

## Slide 100: Executive Summary
Evaluation: CoMeT achieves a good trade-off between area, performance and energy costs
incurs significantly less area overhead (74.2×) compared to the state-of-the-art technique
outperforms the state-of-the-art technique (by up to 39.1%)
CoMeT:
tracks most DRAM rows with scalable hash-based counters by employing the Count-Min-Sketch technique to achieve a low area cost
tracks only a small set of DRAM rows that are activated many times with highly accurate per-DRAM-row activation counters to reduce performance penalties
Key Idea: Use low-cost and scalable hash-based counters to accurately track DRAM rows
Goal: Prevent RowHammer bitflips with low area, performance, and energy overheads in highly RowHammer-vulnerable DRAM-based systems
Problem: As DRAM becomes more vulnerable to read disturbance, existing RowHammer mitigation techniques either prevent bitflips
at low performance cost but with high area overheads or
at low area cost but with prohibitively large performance and energy overheads
https://github.com/CMU-SAFARI/CoMeT

## Slide 101: Outline
Background and Problem
Goal and Key Idea
Conclusion
CoMeT: Count-Min-Sketch-based Row Tracking
Evaluation

## Slide 102: Read Disturbance Vulnerabilities (I)
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
closed
DRAM Subarray
Repeatedly opening (activating) and closing (precharging)
a DRAM row causes RowHammer bitflips in nearby cells
Notes: Todays DRAM chips are vulnerable to read disturbance
Where repeatedly opening and closing or activating and precharging the same DRAM row results in bitflips in nearby DRAM cells which we call the RowHammer bitflips

## Slide 103: Read Disturbance Vulnerabilities (I)
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
DRAM Subarray
The minimum number of activations that causes a bitflip is called the RowHammer threshold

## Slide 104: Read Disturbance Vulnerabilities (II)
DRAM chips are more vulnerable to read disturbance today
Read disturbance bitflips occur at much lower activation counts
(more than two orders of magnitude decrease in less than a decade):
Mitigation techniques against read disturbance attacks need to be effective and efficient for highly vulnerable systems
139K
[Kim+, ISCA’14]
9.6K
[Kim+, ISCA’20]
<1K
[Luo+, ISCA’23]

## Slide 105: Existing RowHammer Mitigations (I): Preventive Refresh
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 0
Row 1
Row 3
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
DRAM Subarray
Refreshing potential victim rows mitigates read disturbance bitflips
Aggressor Row

## Slide 106: Existing RowHammer Mitigations (II): DRAM Row Activation Tracking
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 0
Row 1
Row 3
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
DRAM Subarray
Mitigation techniques track DRAM row activation counts (of aggressor rows) to preventively refresh potential victim rows
Aggressor Row

## Slide 107: Existing RowHammer Mitigations (III): Overview of Preventive Refresh-Based Mitigation Techniques
VERY LOW
Performance & Energy Costs
VERY HIGH
Area Cost
One ACT counter per aggressor row
Processor Chip
Counter A
Counter B
Counter C
Tag A
Tag B
Tag C
One ACT counter
per DRAM row
Processor Chip
DRAM
Row A
Counter A
Row B
Row C
Counter B
Counter C
Counter D
Row D
HIGH
LOW
Processor Chip
<1 counter per DRAM row
Shared Counters
Counter A
Counter B
Tag A
Tag B
HIGH
LOW
Many DRAM rows
(e.g., 128K per bank)
# of aggressor rows
increases significantly
High DRAM bandwidth consumption
CAM-based implementation

## Slide 108: Existing RowHammer Mitigations (IV): Overhead Trade-Off of State-of-the-Art Mitigation Techniques
Notes: Ideally, we would like to achieve low energy, processor chip and DRAM area and performance overheads
[CLICK]
As you can see from this radar chart

## Slide 109: Existing RowHammer Mitigations (IV): Overhead Trade-Off of State-of-the-Art Mitigation Techniques
No existing mitigation technique prevents RowHammer bitflips at low area, performance and energy costs
Notes: None of the existing mitigation techniques prevents RowHammer at low area performance and energy costs

## Slide 110: Outline
Background and Problem
Goal and Key Idea
Conclusion
CoMeT: Count-Min-Sketch-based Row Tracking
Evaluation

## Slide 111: Our Goal
Prevent RowHammer bitflips with low area, performance, and energy overheads in highly RowHammer-vulnerable DRAM-based systems
(e.g., a RowHammer threshold of 125)

## Slide 112: Key Observation
Tag-based counters are highly accurate:
Each one tracks one row's activation count
HIGH ACCURACY
Row 0
…
Row 0
Tag
Counter
Mapping without tags
1
H(ID) = ID % 4
Hash Function
(Example)
DRAM
Row 0
Row 1
Row 2
Row 3
Row 4
Fixed number of counters
2
0
1
2
3
Counters
Hash-based counters are low-cost:
can be implemented with low-cost structures and
can aggregate many rows' activation counts together
Row 0
Row 4
LOW COST
Notes: We observe that there are two types of counters
[CLICK]Hash based counters are low cost
[CLICK]And tag based counters are highly accurate
We want to get the best of both worlds
Now let me explain how these work

## Slide 113: Key Idea
1
Use low-cost and scalable hash-based counters to track most DRAM rows' activations with low area overhead
2
Use highly accurate tag-based counters to track only a small set of DRAM rows to achieve low performance overhead

## Slide 114: Outline
Background and Problem
Goal and Key Idea
Conclusion
CoMeT: Count-Min-Sketch-based Row Tracking
Evaluation

## Slide 115: CoMeT Overview
Counter Table (CT):
Maps each DRAM row to a group of low-cost hash-based counters as uniquely as possible by employing the Count-Min Sketch technique
Triggers a preventive refresh to an aggressor row's victim rows when the aggressor's counter group reaches an activation threshold
Recent Aggressor Table (RAT):
Allocates highly accurate per-DRAM-row counters for only a small set of DRAM rows that are activated many times
Tracks DRAM row activations at low area cost
Reduces performance penalties by increasing tracking accuracy

## Slide 116: Operation of CoMeT
CoMeT
Counter Table
Hash-based Counters
Recent Aggressor Table
ACT A
Counter Table-Based Estimation
Recent Aggressor Table-Based
Estimation
1
2
used when there is a tag match
Row A's ACT Count to NPR
COMPARE
Preventively Refresh
A's victim rows
preventive refresh threshold
3
Tag-based Counters
Notes: Lets look at a high level summary of how CoMeT operates
[CLICK] When there is an activation to row A, CoMeT first checks the counter table that implements hash-based counters
And gets [CLICK] an estimation based on the counter table
At the same time [CLICK] it checks the recent aggressor table that has tag-based counters
[CLICK] And gets another estimation from the recent aggressor table.
[CLICK] CoMeT uses the recent aggressor table based estimation when there is a tag match because the tag-based counters are more accurate
[CLICK] CoMeT compares the activation count estimation to a preventive refresh threshold
[CLICK]And preventively refreshes row A's victim rows if the estimation reaches the threshold value

## Slide 117: Counter Table (CT): Count-Min-Sketch-based Row Tracking
Count-Min Sketch: A hash-based frequent item counting technique
Counter Table
Hash Functions
0 | 0 | 0 | 0 | 0
0
1
2
3
4
ACT A
Counters
H1
H1(A) → 0
H1(B) → 4
H1(C) → 0
1
ACT A
2
ACT B
1
ACT C
3
Action Timeline
  COUNTER COLLISION
causes overestimation
ACT_Count(A) = 3
ESTIMATION
Actual ACT_Count(A) = 2
Notes: Lets look into the Counter table in more detail
The counter table employs the count min sketch technique which is a hash based frequent item counting technique
That uses hash functions and a counter array per hash function
[CLICK] When we have an activation to Row A, Counter table first gets the output of the hash function using the row id as an input.
This output is used as an index for the counter array mapping the DRAM row to a counter.
[CLICK] And the counter table increments the indexed counter.
[CLICK] when we receive another activation to the same row, the hash outputs the same index and counter table increments the same counter
[CLICK] When we receive an activation to another row, ideally the output of the hash function maps th row to another counter
[CLICK] counter table increments that counter

## Slide 118: Counter Table (CT): Count-Min-Sketch-based Row Tracking
To avoid overestimations, Counter Table implements multiple hash functions
Counter Table
Hash Functions
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
2
2
1
1
1
1
0
1
2
3
4
ACT A
Counters
H1
H1(A) → 0
H1(B) → 4
H1(C) → 0
ACT A
ACT B
1
ACT C
3
H2
H3
CounterGroupA
Action Timeline
ACT_Count(A) = MIN(CounterGroupA)
ESTIMATION
ACT_Count(A) = 3
ESTIMATION
Actual ACT_Count(A) = 2
The minimum counter value is an upper bound for the actual activation count
ACT_Count(A) = 2
ESTIMATION
CounterGroupC
CounterGroupB
Notes: Counter Table implements multiple hash functions that map DRAM rows to different counters
[CLICK] As a result, each DRAM row is mapped to a counter group [CLICK] as unique as possible [CLICK]
When there is an activation to a row, all counters in its counter group are incremented
[CLICK] therefore the minimum counter value is an upper bound of the actual activation count
[CLICK] so counter table estimates the activation count as the minimum counter value.
[CLICK] In this example, this estimation leads to estimating the act count of A as 2, which is the actual activation count

## Slide 119: Counter Table (CT): Identifying Aggressor Rows
CoMeT sets a preventive refresh threshold (NPR ) to timely refresh an aggressor row's victim rows to prevent bitflips
Counter Table
Hash
0
1
2
3
4
Counters
H1
H2
H3
Functions
ACT A
Action Timeline
* NPR: Preventive Refresh Threshold
NPR
NPR
NPR
ACT_Count(A) = NPR
ESTIMATION
Identify A as an aggressor row
1
Preventively refresh
A's victim rows
2
NPR
NPR
0
ACT_Count(C) = 0
ESTIMATION
Reset counters?
0
0
CounterGroupA
:
CounterGroupC

## Slide 120: Counter Table (CT): Counter Saturation
CoMeT does not reset any counter in CT after preventive refresh
  CT counters saturate at NPR
Counter Table
Hash
0
1
2
3
4
Counters
H0
H1
H2
Functions
ACT A
Action Timeline
* NPR: Preventive Refresh Threshold
NPR
NPR
NPR
CounterGroupA
:
Preventively refresh
A's victim rows
Actual ACT_Count(A) after preventive refresh is 0
ACT A
ACT_Count(A) = NPR
ESTIMATION
Preventively refresh
A's victim rows
can potentially incur performance and energy overheads

## Slide 121: Recent Aggressor Table
Allocates per-DRAM-row counters for aggressor rows to accurately estimate their activation counts after preventive refreshes
  Implemented for only a small set of DRAM rows to maintain a low area cost
Counter Table
Hash
0
1
2
3
4
Counters
H1
H2
H3
Functions
* NPR: Preventive Refresh Threshold
NPR
NPR
NPR
Identify A as an aggressor row
1
Preventively refresh
A's victim rows
2
Allocate a Recent Aggressor Table entry
3
CounterGroupA
:
Recent Aggressor Table
Row Tag
Counter
A
0
TAG MATCH
If a DRAM row has a Recent Aggressor Table entry, CoMeT estimates its activation count 100% accurately
ACT_Count(A) = 0
ESTIMATION

## Slide 122: Operation of CoMeT
CoMeT
Counter Table
Hash-based Counters
Recent Aggressor Table
ACT A
Counter Table-Based Estimation
Recent Aggressor Table-Based
Estimation
1
2
used when there is a tag match
Tag-based Counters
Row A's ACT Count to NPR
COMPARE
preventive refresh threshold
3
Preventively Refresh
A's victim rows

## Slide 123: More Operational Details for CoMeT
Counter update policy
Periodic counter reset mechanism
Recent Aggressor Table eviction policy
Early preventive refresh at coarse granularity
Determining the preventive refresh threshold

## Slide 124: More Operational Details for CoMeT
CoMeT
Counter Table
Hash-based Counters
Recent Aggressor Table
ACT A
Counter Table-Based Estimation
Recent Aggressor Table-Based
Estimation
1
2
used when there is a row ID match
ACT_Count(A) == NPR
ESTIMATION
Preventively Refresh
A's victim rows
preventive refresh threshold
3
Tag-based Counters
https://arxiv.org/abs/2402.18769
https://github.com/CMU-SAFARI/CoMeT

## Slide 125: Outline
Background and Problem
Goal and Key Idea
Conclusion
CoMeT: Count-Min-Sketch-based Row Tracking
Evaluation

## Slide 126: Evaluation Methodology
Performance and energy consumption evaluation: cycle-level simulations using Ramulator [Kim+, CAL 2015] and DRAMPower [Chandrasekar+, DATE 2013]
System Configuration:
  Processor 1 or 8 cores, 3.6GHz clock frequency,
  4-wide issue, 128-entry instruction window
  DRAM DDR4, 1 channel, 2 rank/channel, 4 bank groups,
  4 banks/bank group, 128K rows/bank
  Memory Ctrl. 64-entry read and write requests queues,
  Scheduling policy: FR-FCFS with a column cap of 16 Last-Level Cache 8 MiB (single-core), 16 MiB (8-core)
  CoMeT Counter Table: 4 hash functions 512 counters per hash Recent Aggressor Table: 128 entries
Comparison Points: 4 state-of-the-art RowHammer mitigations
  Graphene (best performing), Hydra (area-optimized best performing), Low Processor Chip Area Cost: REGA, PARA
Workloads: 61 single-core applications and 56 8-core workload mixes
  SPEC CPU2006, SPEC CPU2017, TPC, MediaBench, YCSB
https://github.com/CMU-SAFARI/CoMeT

## Slide 127: Hardware Implementation
Storage and area overhead analysis: CACTI
Dual-rank area overhead comparison:
Chart: RowHammer Threshold
| 1K | 125
CoMeT | 0.09 | 0.07
Graphene | 0.49 | 4.89
Hydra | 0.08 | 0.07
4.89
0.89
CoMeT stores fewer bits as the RowHammer threshold decreases
74.2×
5.4×
CoMeT incurs a significantly less area overhead than Graphene and a similar area overhead to Hydra
Similar area overheads
Significantly less area overhead

## Slide 128: Performance and DRAM Energy
Chart: RowHammer Threshold
| 1000 | 500 | 250 | 125
Normalized IPC | 0.9981 | 0.99136 | 0.98131 | 0.95986
Chart: RowHammer Threshold
| 1000 | 500 | 250 | 125
Normalized DRAM Energy | 1.0009 | 1.0039 | 1.0089 | 1.0207
4.01%
2.07%
CoMeT prevents bitflips with very small average performance and DRAM energy overheads compared to a baseline system with no RowHammer mitigation
Average performance and DRAM energy overheads of CoMeT across single-core applications
Notes: We evaluate the average performance and DRAM energy overheads of CoMeT across single core applications
[CLICK] This is CoMeT's performance normalized to a system with no RH mitigation across different RH thresholds [CLICK]
As RH threshold decreases CoMeT has a small performance overhead due to preventive refreshes as opposed to the baseline that does not do preventive refresh
[CLICK] This is CoMeT's DRAM energy consumption normalized to the same baseline [CLICK] and it shows a similar result
[CLICK] We conclude that CoMeT prevents bitflips with very small average performance ….

## Slide 129: Performance Comparison: Single-Core Applications
1.75%
1.75%
(average)
CoMeT outperforms all low-area-cost mitigations starting from the RowHammer threshold of 500
CoMeT incurs a small performance overhead (≤ 1.75%) over Graphene and outperforms Hydra (by up to 39.1%) at all RowHammer thresholds

## Slide 130: Performance Comparison: 8-Core Workloads
Trends are similar to single-core application evaluation trends

## Slide 131: DRAM Energy Comparison: Single-Core Applications
0.96%
0.04%
CoMeT incurs a small DRAM energy overhead (<1%) over Graphene and consumes less DRAM energy than Hydra
CoMeT consumes less DRAM energy than all low-area-cost mitigations for all RowHammer thresholds
1.88%
0.39%

## Slide 132: DRAM Energy Comparison: 8-Core Workloads
Multicore energy trends are similar to single core energy trends

## Slide 133: More in the Paper
Security Analysis of CoMeT
Sensitivity Analysis
  Counter Table Configurations
  Recent Aggressor Table Configurations
  Counter Reset Period and Preventive Refresh Threshold Values
CoMeT's Performance under Adversarial Workloads
Comparison against Throttling-Based Mitigation Techniques
CoMeT's Performance at High RowHammer Thresholds

## Slide 134: More in the Paper
Security Analysis of CoMeT
Sensitivity Analysis
  Counter Table Configurations
  Recent Aggressor Table Configurations
  Counter Reset Period and Preventive Refresh Threshold values
Performance Evaluation under Adversarial Workloads
Performance Evaluation Comparison against Throttling-Based Mitigation Techniques
Performance Evaluation at High RowHammer Thresholds
https://arxiv.org/abs/2402.18769

## Slide 135: CoMeT is Open Source and Artifact Evaluated
https://github.com/CMU-SAFARI/CoMeT

## Slide 136: Outline
Background and Problem
Goal and Key Idea
Conclusion
CoMeT: Count-Min-Sketch-based Row Tracking
Evaluation

## Slide 137: Conclusion
https://github.com/CMU-SAFARI/CoMeT
Evaluation: CoMeT achieves a good trade-off between area, performance and energy costs
incurs significantly less area overhead (74.2×) compared to the state-of-the-art technique
outperforms the state-of-the-art technique (by up to 39.1%)
CoMeT:
tracks most DRAM rows with scalable hash-based counters by employing the Count-Min-Sketch technique to achieve a low area cost
tracks only a small set of DRAM rows that are activated many times with highly accurate per-DRAM-row activation counters to reduce performance penalties
Key Idea: Use low-cost and scalable hash-based counters to accurately track DRAM rows
Goal: Prevent RowHammer bitflips with low area, performance, and energy overheads in highly RowHammer-vulnerable DRAM-based systems

## Slide 138: CoMeT Count-Min-Sketch-based Row Tracking to Mitigate RowHammer at Low Cost
F. Nisa Bostancı
I. E. Yüksel A. Olgun K. Kanellopoulos Y. C. Tuğrul
A. G. Yağlıkçı M. Sadrosadati O. Mutlu
Paper Link
GitHub Repo

## Slide 139: CoMeT Count-Min-Sketch-based Row Tracking to Mitigate RowHammer at Low Cost
F. Nisa Bostancı
I. E. Yüksel A. Olgun K. Kanellopoulos Y. C. Tuğrul
A. G. Yağlıkçı M. Sadrosadati O. Mutlu
Paper Link
GitHub Repo
BACKUP SLIDES

## Slide 140: DRAM Organization
DRAM Chip
DRAM Chip
Bank
Chip I/O
DRAM Bank
Subarray
. . .
DRAM Subarray
DRAM Cell
Wordline
…
…
…
…
Row Buffer
Bitline
…
…
DRAM Row
…
…

## Slide 141: Read Disturbance Vulnerabilities
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
closed
DRAM Subarray
Repeatedly opening (activating) and closing (precharging)
a DRAM row causes RowHammer bitflips in nearby cells
The minimum number of row activations needed to cause a bitflip (i.e., RowHammer threshold (NRH )) has reduced by more than an order of magnitude in less than a decade
[Kim+ ISCA'20]
RowPress is shown to lead to bitflips with one to two orders of magnitude fewer activations (than RowHammer) under realistic conditions
[Luo+ ISCA'23]

## Slide 142: Existing RowHammer Mitigations (II): Performance Optimized Mitigations
Accurately tracking DRAM row activations can be done by allocating per-row counters to potential aggressor rows
TAG | Counter
TAG | Counter
the number of potential aggressor rows
total number of DRAM rows
As DRAM becomes more vulnerable to read disturbance, tracking all potential aggressor rows with tag-based counters results in a high area overhead
the number of potential aggressor rows increases significantly
A tag-based counter has a high area cost
Accurate tracking enables low performance overhead by reducing unnecessary preventive refreshes
At low NRH
DRAM rows

## Slide 143: Existing RowHammer Mitigations (III): Area Optimized Mitigations: Hydra
Memory Controller
DRAM
As DRAM becomes more vulnerable to read disturbance, increased off-chip communication results in high performance and energy overheads
Low chip area overhead
TAG | Counter
Per-DRAM-row counters
DRAM rows
Incurs DRAM storage overhead
Group Counters and Filtering Mechanism
Increased off-chip communication

## Slide 144: Limitations of Existing Mitigations
No existing mitigation technique prevents RowHammer bitflips at low area, performance and energy costs
High area cost
due to many and expensive per-DRAM-row activation counters
High performance and energy costs
due to occupying the memory bandwidth with additional requests

## Slide 145: Operation of CoMeT
CoMeT
Counter Table
Hash
0
1
2
3
4
Counters
H0
H1
H2
Functions
Recent Aggressor Table
TAG MATCH
Row Tag
Counter
ACT A
CounterGroupA
ACT_Count(A) = MIN(CounterGroupA)
CT ESTIMATION
ACT_Count(A) = RAT_Counter(A)
RAT ESTIMATION
1
2
used when there is a tag match
ACT_Count(A) == NPR
ESTIMATION
Preventively Refresh
A's victim rows
preventive refresh threshold
3

## Slide 146: CoMeT Overview
DRAM Row Tag | Counter
Tag Match
C00 |  |  |  |  | 
 |  | C12 |  |  | 
H0
H1
…
Hk-1
…
…
…
…
0
1
2
m-1
Counter Table
Comparator
Min_Ctr
NPR
RAT_Ctr
Recent Aggressor Table
Num_ACT
Memory Request Scheduler
≥
Y: Preventive Refresh
SELECT
CoMeT
2
6
1
ACT Row X
NRAT_Entries
CG(X):
H0(X)=0 → C00,
H1(X)=2 → C12,
…
3
4
Row ID X
5
7

## Slide 147: Configuring CoMeT – Sensitivity Analysis: Counter Table and Recent Aggressor Table
Configuring RAT
Configuring Counter Table

## Slide 148: Configuring CoMeT – Sensitivity Analysis: Counter Table and Recent Aggressor Table
Configuring RAT
Configuring Counter Table
CoMeT configuration that achieves both performance and area efficiency:
Counter Table with 4 hash functions and 512 counters per hash function
Recent Aggressor Table with 128 entry
(more analyses in the paper)

## Slide 149: Configuring CoMeT – Sensitivity Analysis: Counter Reset Period and NPR
(1)
(2)

## Slide 150: The effect of EPRT and RAT Miss History Length on Performance and DRAM energy consumption

## Slide 151: Hardware Implementation
Storage and area overhead analysis: CACTI
  Logic circuitry overhead: Verilog HDL implementation and Synopsys DC
Dual-rank area overhead comparison:
As NRH decreases, CoMeT's area and storage overheads decrease due to storing fewer bits for its counters

## Slide 152: Hardware Implementation
Storage and area overhead analysis: CACTI
  Logic circuitry overhead: Verilog HDL implementation and Synopsys DC
Dual-rank area overhead comparison:
Compared to the best performing state-of-the-art mitigation, CoMeT induces significantly less area overhead

## Slide 153: Hardware Implementation
Storage and area overhead analysis: CACTI
  Logic circuitry overhead: Verilog HDL implementation and Synopsys DC
Dual-rank area overhead comparison:
Compared to the best performing low-area-cost mitigation, CoMeT induces similar area overhead

## Slide 154: Single-Core Performance Workload Breakdown (Medium and High Intensity)

## Slide 155: Single-Core DRAM Energy Workload Breakdown (Medium and High Intensity)

## Slide 156: Adversarial Access Patterns
CoMeT incurs negligible additional performance overhead on benign workloads when a traditional RowHammer attack is running at the same time
0.7%
(over the baseline)
42.1%

## Slide 157: Comparison Against BlockHammer (I) Tracker Comparison
CoMeT and BlockHammer employs different algorithms and this results in different DRAM-row-to-counter mappings
the average number of unique rows touched at least once by benign workloads
Average # of unique rows that are activated at least 125 times by benign workloads
When tracking at most 2,500 unique rows,
CoMeT’s tracker outperforms BlockHammer
Notes: We observe the total number of accesses in a refresh window is 10,000 on average across benign single-core workloads we evaluate

## Slide 158: Comparison Against BlockHammer (II) Single-Core Performance Comparison
9.5%
CoMeT outperforms BlockHammer due to BlockHammer's (i) high false positive rate and (ii) increased memory request latencies due to throttling

## Slide 159: Performance Comparison: 8-Core Workloads
CoMeT's performance overhead over Graphene is 0.9% and 14.9% at NRH = 1K and 125, respectively
0.9%
14.9%
CoMeT outperforms Hydra for all RowHammer thresholds (by up to 3.2× and 11.9% on average at NRH = 125)
CoMeT outperforms all low-cost RowHammer mitigations starting from NRH=250
11.9%

## Slide 160: Performance Comparison: 8-Core Workloads
0.9%
14.9%
CoMeT maintains a performance overhead between Graphene's and Hydra's performance overheads
11.9%
More preventive refreshes
CoMeT outperforms all low-area-cost mitigations starting from the RowHammer threshold of 250

## Slide 161: Single-Core Comparison – Radar Chart

## Slide 162: Multi-Core Comparison – Radar Chart

## Slide 163: Evaluated Workloads and Their Characteristics

## Slide 164: CoMeT's Performance at High RowHammer Thresholds

## Slide 165: Summary of the Results

## Slide 166: Storage Overhead of Graphene

## Slide 167: Performance Overhead of Hydra