## Slide 1: Enabling Efficient and Scalable DRAM Read Disturbance Mitigation via New Experimental Insights into Modern DRAM Chips
Abdullah Giray Yağlıkçı
Aug 12, 2024
Stanford University

## Slide 2: Brief Self Introduction
Abdullah Giray Yaglikci
  Researcher @ SAFARI Research Group since August 2016
    ETH Zurich (Feb 2018 – ongoing)
    Intel Labs (Aug 2017 – Feb 2018)
    Carnegie Mellon University (Aug 2016 – Aug 2017)
  Defended my PhD thesis, advised by Onur Mutlu, in April 2024
  https://agyaglikci.github.io/
  agirayyaglikci@gmail.com (Best way to reach me)
  https://safari.ethz.ch
Research interests:
  Computer architecture, hardware security
  Memory and storage systems
  Hardware security, safety, reliability, performance, availability, fairness, energy efficiency
  Hardware/software cooperation
  …

## Slide 3: Papers in This Talk
Lois Orosa, Abdullah Giray Yaglikci, Haocong Luo, Ataberk Olgun, Jisung Park, Hasan Hassan, Minesh Patel, Jeremie S. Kim, and Onur Mutlu, "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses” in MICRO, 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (21 mins)] [Lightning Talk]
A. Giray Yağlıkçı, Haocong Luo, Geraldo F. de Oliviera, Ataberk Olgun, Minesh Patel, Jisung Park, Hasan Hassan, Jeremie S. Kim, Lois Orosa, and Onur Mutlu, "Understanding RowHammer Under Reduced Wordline Voltage: An Experimental Study Using Real DRAM Devices” in DSN, 2022. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [arXiv version] [Talk Video (34 mins)] [Lightning Talk Video (2 mins)]
Abdullah Giray Yaglikci, Geraldo Francisco de Oliveira, Yahya Can Tugrul, Ismail Yuksel, Ataberk Olgun, Haocong Luo, and Onur Mutlu, "Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions” in HPCA, 2024. [Slides (pptx) (pdf)] [arXiv version]
A. Giray Yaglıkcı, Ataberk Olgun, Minesh Patel, Haocong Luo, Hasan Hassan, Lois Orosa, Oguz Ergin, and Onur Mutlu, "HiRA: Hidden Row Activation for Reducing Refresh Latency of Off-the-Shelf DRAM Chips” in MICRO, 2022. [Slides (pptx) (pdf)][Longer Lecture Slides (pptx) (pdf)] [Lecture Video (36 minutes)]
A. Giray Yaglikci, Minesh Patel, Jeremie S. Kim, Roknoddin Azizi, Ataberk Olgun, Lois Orosa, Hasan Hassan, Jisung Park, Konstantinos Kanellopoulos, Taha Shahroodi, Saugata Ghose, and Onur Mutlu, "BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows,” in HPCA, 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (22 minutes)] [Short Talk Video (7 minutes)] [Intel Hardware Security Academic Awards Short Talk Slides (pptx) (pdf)] [Intel Hardware Security Academic Awards Short Talk Video (2 minutes)] [BlockHammer Source Code] Intel Hardware Security Academic Award Finalist (one of 4 finalists out of 34 nominations)
Oğuzhan Canpolat, A. Giray Yağlıkçı, Geraldo F. Oliveira, Ataberk Olgun, Oğuz Ergin, and Onur Mutlu, "Understanding the Security Benefits and Overheads of Emerging Industry Solutions to DRAM Read Disturbance” DRAMSec, held with ISCA, 2024. [Slides (pptx) (pdf)] [arXiv version] [Source Code]
Oğuzhan Canpolat and A. Giray Yağlıkçı and Ataberk Olgun and İsmail Emir Yüksel and Yahya Can Tuğrul and Konstantinos Kanellopoulos and Oğuz Ergin and Onur Mutlu “Leveraging Adversarial Detection to Enable Scalable and Low Overhead RowHammer Mitigations,” arXiv [cs.CR 2404.13477], 2024.

## Slide 4: Memory & Generative AI (I)
Image Source: https://www.cerebras.net/blog/cerebras-architecture-deep-dive-first-look-inside-the-hw/sw-co-design-for-deep-learning

## Slide 5: Memory & Generative AI (II)
Gholami A, Yao Z, Kim S, Mahoney MW, Keutzer K. AI and Memory Wall. RiseLab Medium Blog Post, University of Califonia Berkeley, 2021, March 29.
Increasing gap

## Slide 6: Memory Isolation
A memory access should not have unintended side effects on data stored in other addresses
A fundamental property for robustness (safety, security, and reliability)
Memory
access
1  0
Leak private information
Take over a computer
Data loss or corruption
Compromise application correctness
Memory isolation is difficult in modern memory chips
Notes: Let’s start with the concept of memory isolation, a fundamental primitive for system security and privacy [CLICK]
Imagine that you access a memory location, and a bitflip occurs in some other location [CLICK]
We would not want this to happen because it can lead to data loss or corruption [CLICK]
Compromise application correctness [CLICK]
It can be used to leak private information [CLICK]
Or even to take over a computer [CLICK]
Therefore, we have this principle called memory isolation dictating that a memory access should not have unintended side effects on data stored in other addresses. This is important for memory integrity [CLICK]
Unfortunately, it is difficult in modern memory chips and here is why [CLICK]

## Slide 7: Read Disturbance in Modern Memory Chips
Prevalent memory technology: Dynamic Random Access Memory (DRAM)
DRAM stores data in the form of electrical charge on a capacitor
DRAM leaks charge over time and needs periodic refresh
DRAM Read Disturbance: Accessing a DRAM cell disturbs other physically nearby cells and exacerbates their charge leakage
Wordline
Bitline
Charge
leakage
paths
Notes: Dynamic random access memory (DRAM) is the prevalent memory technology today. [CLICK]
DRAM stores a bit of data in the form of electrical charge on a capacitor [CLICK]
To access we assert a wire called wordline [CLICK]
Which enables a transistor, conducting the capacitor to another wire called bitline [CLICK]
DRAM is a volatile memory technology as it leaks charge over time and needs to be periodically refreshed [CLICK]
Accessing a DRAM cell disturbs other physically nearby cells and exacerbates their charge leakage. This is called DRAM read disturbance [CLICK]

## Slide 8: RowHammer: An Example of DRAM Read Disturbance
Row 0
Row 1
Row 2
Row 3
Row 4
Repeatedly opening (activating) and closing (precharging)
a DRAM row causes RowHammer bitflips in nearby cells
and breaks memory isolation
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 2
closed
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
closed
Aggressor Row
DRAM Subarray
Notes: A prime example of DRAM read disturbance is RowHammer, which I will show in this slide.
DRAM cells are organized in 2 dimensional arrays as rows and columns and internally accessed in a DRAM row granularity. For example, to access a data stored in Row 2, [CLICK]
We first need to open Row 2, and then perform accesses. Once we need to access another row, we need to close Row 2 and open the other row [CLICK]
[BACK& FORTH] If we keep opening and closing this row many times, called hammering a row, [CLICK]
We observe bitflips in physically nearby DRAM rows [CLICK]
This phenomenon is called RowHammer. We refer to the hammered row as the aggressor row and the rows that are affected as victim rows. [CLICK]

## Slide 9: One Can Take Over an Otherwise-Secure System
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn, 2015)
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
Induce bit flips in page table entries (PTEs).
Gain write access to its own page table, and hence gain read-write access to all of physical memory.

## Slide 10: More Security Implications (I)
Source: https://lab.dsst.io/32c3-slides/7197.html
Rowhammer.js: A Remote Software-Induced Fault Attack in JavaScript (DIMVA’16)
“We can gain unrestricted access to systems of website visitors.”

## Slide 11: More Security Implications (II)
Source: https://fossbytes.com/drammer-rowhammer-attack-android-root-devices/
Drammer: Deterministic Rowhammer Attacks on Mobile Platforms, CCS’16
  “Can gain control of a smart phone deterministically”

## Slide 12: More Security Implications (III)
Using an integrated GPU in a mobile system to remotely escalate privilege via the WebGL interface. IEEE S&P 2018

## Slide 13: More Security Implications (IV)
Rowhammer over RDMA (I)
[Tatar+ USENIX ATC, 2018]

## Slide 14: More Security Implications (V)
Rowhammer over RDMA (II)
[Lipp+ EuroS&PW, 2020]

## Slide 15: More Security Implications (VI)
An FPGA-based RowHammer attack recovering private keys twice as fast compared to CPU-based attacks
[Weissman+ CHES 2020]

## Slide 16: More Security Implications (VII)
[Kwong+ IEEE S&P 2020]

## Slide 17: More Security Implications (VIII)
[Hong+ USENIX Security 2019]

## Slide 18: More Security Implications (IX)
[Yao+ USENIX Security 2020]

## Slide 19: More Security Implications (X)
HammerScope is a software-based power analysis method using RowHammer as a side channel
[Cohen+ CCS 2022]

## Slide 20: More Security Implications (XI)
Exploiting Correcting Codes: On the Effectiveness of ECC Memory Against Rowhammer Attacks. Cojocar, L. .; Razavi, K.; Giuffrida, C.; and Bos, H. In S&P, May 2019 Best Practical Paper Award, Pwnie Award Nomination for Most Innovative Research [Paper] [Slides]
Thus, many believed that Rowhammer on ECC memory, even if plausible in theory, is simply impractical. This paper shows this to be false: while harder, Rowhammer attacks are still a realistic threat even to modern ECC-equipped systems.

## Slide 21: More Security Implications (XII)
15x Vendor A DDR4 modules
U-TRR
New RowHammer access patterns
15x Vendor B DDR4 modules
15x Vendor C DDR4 modules
All 45 modules we test are vulnerable
99.9% of rows in a DRAM bank experience at least one RowHammer bit flip
Up to 7 RowHammer bitflips in an 8-byte dataword, making ECC ineffective
TRR does not provide security against RowHammer
U-TRR can facilitate the development of new RowHammer attacks and more secure RowHammer protection mechanisms
Hasan Hassan, Yahya Can Tugrul, Jeremie S. Kim, Victor van der Veen, Kaveh Razavi, and Onur Mutlu, "Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications,” MICRO, 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Full Talk (25 mins)] [Lightning Talk (1.5 mins)]
Notes: [CLICK] The RowHammer vulnerability of modern DRAM is a critical reliability and security threat.
[CLICK] The security guarantees of TRR, which is the commonly used RowHammer protection mechanism, cannot be easily studied as TRR is obscure, undocumented, and proprietary.
[CLICK] In this work, our main goal is to answer the following questions. Is TRR fully secure? How can we validate the security guarantees of different TRR mechanisms?
[CLICK] To this end, we propose U-TRR, a new methodology that leverages data retention failures in DRAM to uncover the inner workings of TRR and study its security.
[CLICK] Using U-TRR, we analyze 15 DDR4 DRAM modules from each of the three major DRAM vendors.
[CLICK] Through these analyses, we make several observations regarding the TRR mechanisms implemented in these modules and craft new custom RowHammer access patterns that cause RowHammer bit flips in TRR-protected DRAM modules.
[CLICK] Our results show that: First, all 45 modules that we test across three vendors are vulnerable to our new RowHammer access patterns.
[CLICK] Second, our access pattern cause at least one bit flip in almost all DRAM rows in many modules. This makes system-level RowHammer attacks easier to mount as the attacker would have the ability to cause bit flips in almost any DRAM row [CLICK] Third, we observe that our access patterns cause up to 7 RowHammer bit flips in an 8-byte dataword, making ECC ineffective and systems equipped with ECC also susceptible to RowHammer attacks
[CLICK] We conclude that TRR does not provide security against RowHammer and can be easily circumvented using the new understanding provided by U-TRR.
[CLICK] We believe and hope that U-TRR will facilitate future research by enabling rigorous and open analysis of RowHammer mitigation mechanisms, leading to the development of both new RowHammer attacks and more secure RowHammer protection mechanisms.

## Slide 22: A RowHammer Survey:
Onur Mutlu, Ataberk Olgun, and A. Giray Yaglikci, "Fundamentally Understanding and Solving RowHammer” Invited Special Session Paper at the 28th Asia and South Pacific Design Automation Conference (ASP-DAC), Tokyo, Japan, January 2023. [arXiv version] [Slides (pptx) (pdf)] [Talk Video (26 minutes)]
https://arxiv.org/pdf/2211.07613.pdf

## Slide 23: Breaking Samsung’s Best Practice in 2024
Salman Qazi and Daniel Moghimi, “SoothSayer: Bypassing DSAC Mitigation by Predicting Counter Replacement,” DRAMSec, 2024

## Slide 24: RowHammer in DDR5
Patrick Jattke; Max Wipfli; Flavien Solt; Michele Marazzi; Matej Bölcskei; and Kaveh Razavi, “ZenHammer: Rowhammer Attacks on AMD Zen-based Platforms,” in USENIX Security, 2024. [Paper] [URL]
We found bit flips on only 1 of 10 tested devices (S1), suggesting that the changes in DDR5 such as improved Rowhammer mitigations, on-die error correction code (ECC), and a higher refresh rate (32 ms) make it harder to trigger bit flips.

## Slide 25: DRAM Read Disturbance: A Critical Challenge
DRAM cells become increasingly more vulnerable to read disturbance
Technology node scaling
Chart: 
| The Min. ACT Count to Observe Bit Flips
2023 | 1
2020 | 9.6
2014 | 139.2
[Luo+, ISCA’23]
[Kim+, ISCA’20]
[Kim+, ISCA’14]
Notes: With technology node scaling, DRAM cells get smaller in size and closer to each other[CLICK]
Such that we observe significant reductions in the minimum hammer count to induce the first bitflip in the last decade [CLICK]
Thus DRAM cells become increasingly more vulnerable to read disturbance [CLICK]

## Slide 26: Existing RowHammer Mitigations (I)
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 0
Row 1
Row 3
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
DRAM Subarray
Refreshing potential victim rows mitigates read disturbance bitflips
Aggressor Row

## Slide 27: Existing RowHammer Mitigations (II)
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 0
Row 1
Row 3
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
DRAM Subarray
Mitigation techniques track DRAM row activation counts (of aggressor rows) to preventively refresh potential victim rows
Aggressor Row

## Slide 28: Scalability with Worsening RowHammer Vulnerability
DRAM cells become
increasingly more vulnerable
to read disturbance at device level
Existing solutions become prohibitively expensive or ineffective going forward [Kim+, ISCA’20] [Frigo+, IEEE S&P’20] [Hassan+, MICRO’21]
We need more efficient and scalable solutions to DRAM read disturbance
A more detailed understanding of DRAM read disturbance can help
Notes: My thesis identifies two problems about solving DRAM read disturbance [CLICK]
First, As DRAM cells become more vulnerable, [CLICK]
Existing solutions become prohibitively expensive or ineffective going forward [CLICK]
Thus, we need more efficient and scalable solutions [CLICK]
And we believe that a more detailed understanding of DRAM read disturbance can help us to achieve it[CLICK]

## Slide 29: Our Approach
We can mitigate DRAM read disturbance efficiently and scalably by
building a detailed understanding of DRAM read disturbance
leveraging insights into modern DRAM chips and memory controllers
throttling memory requests that lead to time-consuming preventive refreshes
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
Svärd: Leveraging heterogeneity
HiRA: Parallelizing preventive actions
1
2
3
MICRO’24
BreakHammer: Throttling malicious threads
BlockHammer: Selectively throttling unsafe accesses
Notes: To address these two problems, we conducted several studies encompassed in this thesis statement [CLICK]
We can mitigate DRAM read disturbance efficiently and scalably from three aspects [CLICK]
First, by building a detailed understanding of DRAM read disturbance [CLICK],
Which we explore for temperature [CLICK],
Memory access patterns [CLICK],
Victim cell’s physical location [CLICK],
And voltage [CLICK]
Second, by leveraging insights into modern DRAM chips and memory controllers [CLICK],
Where we leverage the heterogeneity in DRAM cells’ vulnerability levels [CLICK]
and parallelize preventive actions [CLICK]
Third, by devising novel solutions that do not require proprietary knowledge of DRAM chip internals[CLICK],
Which we achieve by selectively throttling unsafe accesses [CLICK]

## Slide 30: Core Contributions
building a detailed understanding of DRAM read disturbance
leveraging insights into modern DRAM chips and memory controllers
throttling memory requests that lead to time-consuming preventive refreshes
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
Svärd: Leveraging heterogeneity
HiRA: Parallelizing preventive actions
BlockHammer: Selectively throttling unsafe accesses
1
2
3
MICRO’24
Notes: Without further ado, let’s look into the detailed understanding we built [CLICK]

## Slide 31: A Deeper Look into RowHammer
Lois Orosa*, Abdullah Giray Yağlıkçı*, Haocong Luo, Ataberk Olgun, Jisung Park, Hasan Hassan, Minesh Patel, Jeremie S. Kim, and Onur Mutlu, "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Talk Video (21 minutes)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (1.5 minutes)] [arXiv version]
Notes: Our goal in this work is to Provide insights into three fundamental properties of RowHammer:
Temperature [CLICK]
Aggressor row active time [CLICK]
Victim DRAM cell's physical location [CLICK]
By doing so we aim enabling research to find effective and efficient attacks and defenses [CLICK]

## Slide 32: DRAM Testing Infrastructure
  DRAM Bender on a Xilinx Virtex UltraScale+ XCU200
Fine-grained control over DRAM commands,
timing parameters (±1.5ns), temperature (±0.5°C ),
and voltage (±1mV)
*Olgun et al., “DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips,” in TCAD, 2023. [GitHub: https://github.com/CMU-SAFARI/DRAM-Bender]
*
Notes: We use an FPGA-based experimental setup programmed with DRAM Bender, which is an open-sourced design available on github [CLICK]
We plug in a DRAM module to test on the FPGA board [CLICK]
The board communicates with the host machine to run the test routines [CLICK]
We control the chip temperature using a pair of heaters [CLICK] connected to a temperature controller [CLICK]
We also have an external power supply that we use to sweep voltage on a power rail [CLICK]
This infrastructure provides fine-grained control over DRAM commands, timing parameters, temperature, and wordline voltage [CLICK]
=======

## Slide 33: DRAM Testing Methodology
To characterize our DRAM chips at worst-case conditions:
Prevent sources of interference during core test loop
  No DRAM refresh: to avoid refreshing victim row
  No DRAM calibration events: to minimize variation in test timing
  No RowHammer mitigation mechanisms: to observe circuit-level effects
  Test for less than a refresh window (32ms) to avoid retention failures
Worst-case access sequence
We use worst-case access sequence based on prior works’ observations
For each row, repeatedly access the two physically-adjacent rows as fast as possible
Notes: To characterize our DRAM chips at worst-case conditions we take two measures:
[CLICK] First, we prevent external sources of interference such that our tests can run consistently as desired and without interruptions. To achieve this we disable:
[CLICK] DRAM refresh to avoid refreshing victim rows during a RowHammer test,
[CLICK] DRAM calibration events to minimize variation in test timings
[CLICK] and RowHammer mitigation mechanisms to ensure that we can directly observe circuit-level bit flips
[CLICK] we also ensure that our tests complete in less than a refresh window to prevent retention failures from interfering with our results
[CLICK] Second, we issue the worst-case access sequence for inducing RowHammer bit flips based on observations from prior work
[CLICK] Using these observations, we test each row’s worst-case vulnerability to RowHammer by repeatedly activating the two physically-adjacent rows as fast as possible
=========

## Slide 34: Tested DRAM Chips
Mfr. | DDR4 DIMMs | DDR3 SODIMMs | # Chips | Density | Die | Org.
A (Micron) | 9 | 1 | 144 (8) | 8Gb (4Gb) | B (P) | x4 (x8)
B (Samsung) | 4 | 1 | 32 (8) | 4Gb (4Gb) | F (Q) | x8 (x8)
C (SK Hynix) | 5 | 1 | 40 (8) | 4Gb (4Gb) | B (B) | x8 (x8)
D (Nanya) | 4 | - | 32 (-) | 8Gb (-) | C (-) | x8 (-)
272 DRAM Chips (24 DDR3 and 248 DDR4 DRAM Chips)
4 major manufacturers: Micron, Samsung, SK Hynix, and Nanya
272 DRAM chips
2 DRAM standards
4 major manufacturers
Notes: In our characterization, [CLICK]
we test 272 real DRAM chips [CLICK]
from four major manufacturers, [CLICK]
that implement DDR3 and DDR4 DRAM standards [CLICK]
and with different densities, die revisions, and chip organizations[CLICK]

## Slide 35: Key Finding 1: Temperature Range
DRAM read disturbance is more effective within a bounded vulnerable temperature range
Vulnerable temperature range varies across DRAM cells
Most cells are vulnerable in a continuous temperature range
Trap-Assisted Charge Leakage Model [Yang+, EDL 2019]
Hammering a wordline pulls and pushes electrons
Electrons get trapped and exacerbate charge leakage, leading to cause bitflips
More vulnerable to RowHammer at temperatures close to a temperature inflection point
50oC
90oC
Orosa, Yağlıkçı et al., "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" in MICRO, 2021.
Temperature
bitflips
no bitflips
Vulnerable Temperature Range
no bitflips
Lower
Bound
Upper
Bound
Micron | Samsung | SK Hynix | Nanya
99.1% | 98.9% | 98.0% | 99.2%
Vulnerable Temperature Range
Vulnerable Temperature Range
Vulnerable Temperature Range
Cell A
Cell B
Cell C
50oC
90oC
Temperature
Notes: Our first key finding is about the effect of temperature. [CLICK]
We sweep temperature from 50C to 90C on the x-axis[CLICK],
and show a DRAM cell's read disturbance vulnearbility on the y-axis [CLICK]
We observe that a DRAM cell becomes more vulnerable to read disturbance within a bounded temperature range [CLICK]
and this temperature range significantly varies across DRAM cells [CLICK]
One implication of this finding is for testing routines: To measure a cell's vulnerability to read disturbance, we need to test the cell at all possible operating temperatures [CLICK]
A follow up of this finding uses RowHammer’s temperature sensitivity as a side-channel to spy on a system’s temperature [CLICK]

## Slide 36: Key Finding 1: Temperature Range
DRAM read disturbance is more effective within a bounded vulnerable temperature range
Vulnerable temperature range varies across DRAM cells
Most cells are vulnerable in a continuous temperature range
Trap-Assisted Charge Leakage Model [Yang+, EDL 2019]
Hammering a wordline pulls and pushes electrons
Electrons get trapped and exacerbate charge leakage, leading to cause bitflips
More vulnerable to RowHammer at temperatures close to a temperature inflection point
50oC
90oC
Orosa, Yağlıkçı et al., "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" in MICRO, 2021.
Temperature
bitflips
no bitflips
Vulnerable Temperature Range
no bitflips
Lower
Bound
Upper
Bound
Micron | Samsung | SK Hynix | Nanya
99.1% | 98.9% | 98.0% | 99.2%
Vulnerable Temperature Range
Vulnerable Temperature Range
Vulnerable Temperature Range
Cell A
Cell B
Cell C
50oC
90oC
Temperature
This finding paved the way to SpyHammer,
a new attack that spies on temperature [Orosa+, 2022]
Follow-up
A DRAM cell should be tested
at each possible operating temperature
Implication on testing
A DRAM cell can be retired based on its vulnerable temperature range
Implication on defenses
Notes: Our first key finding is about the effect of temperature. [CLICK]
We sweep temperature from 50C to 90C on the x-axis[CLICK],
and show a DRAM cell's read disturbance vulnearbility on the y-axis [CLICK]
We observe that a DRAM cell becomes more vulnerable to read disturbance within a bounded temperature range [CLICK]
and this temperature range significantly varies across DRAM cells [CLICK]
One implication of this finding is for testing routines: To measure a cell's vulnerability to read disturbance, we need to test the cell at all possible operating temperatures [CLICK]
A follow up of this finding uses RowHammer’s temperature sensitivity as a side-channel to spy on a system’s temperature [CLICK]

## Slide 37: Key Finding 2: Aggressor Row On Time
Chart: 
| The Min. ACT Count to Observe Bit Flips
2014 | 6.4
2020 | 10
State-of-the-Art
Our Finding w/ 15 column accesses
Minimum hammer count to induce the first bitflip
36% reduction
A smaller hammer count is sufficient to induce bitflips
with increased aggressor row on time
Open
Close
Open
Close
Existing mitigations are ineffective without this insight
This finding paved the way to the discovery of RowPress [Luo+, ISCA’23]
Follow-up
Implication on defenses
Orosa, Yağlıkçı et al., "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" in MICRO, 2021.
on time
Notes: The second example is about the memory access patterns. [CLICK]
Previously known worst-case access pattern opens and closes an aggressor row as fast as possible [CLICK]
In contrast, in this study, we wait for some time after opening the aggressor row [CLICK]
We observe that doing this significantly reduces the necessary hammer count to induce the first bitflip [CLICK]
An implication is that an existing mitigation can be ineffective if it is not designed accounting for this effect [CLICK]
A follow-up of our work investigates this effect more rigorously and shows that this effect is an artifact of a new read disturbance phenomenon called RowPress [CLICK]

## Slide 38: Key Finding 3: Variation across DRAM Rows
All DRAM Rows in a DRAM Bank
RowHammer vulnerability
significantly varies across DRAM rows
Orosa, Yağlıkçı et al., "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" in MICRO, 2021.
90% of rows
Weakest
10% of rows
Say, bitflips occur at
N hammers in these rows
We need at least 2N hammers
to induce bitflips in these rows
Configuring a solution for the worst-case overprotects many rows and makes it expensive
Implication on defenses
This finding paved the way to the design of Svärd [Yaglikci+, HPCA’24] (will be covered)
Follow-up
Notes: The third key finding is about the variation of read disturbance across DRAM rows. Assume that this box represents all rows in a bank [CLICK]
If the weakest 10% of the rows experience bitflips after being hammered for N times, [CLICK]
We need at least 2N hammers to induce a bitflip in the remaining 90% [CLICK]
This shows that RowHammer vulnerability significantly varies across DRAM rows [CLICK]
And mitigation mechanisms that are configured for the worst row, overprotect many rows, leading to performance / energy / area overheads [CLICK]

## Slide 39: Core Contributions
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
Svärd: Leveraging heterogeneity
HiRA: Parallelizing preventive actions
BlockHammer: Selectively throttling unsafe accesses
1
2
3
Voltage
building a detailed understanding of DRAM read disturbance
leveraging insights into modern DRAM chips and memory controllers
throttling memory requests that lead to time-consuming preventive refreshes
Notes: Next, I will summarize our DSN22 paper on DRAM read disturbance under reduced wordline voltage

## Slide 40: RowHammer Under Reduced Voltage
A. Giray Yağlıkçı, Haocong Luo, Geraldo F. de Oliviera, Ataberk Olgun, Minesh Patel, Jisung Park, Hasan Hassan, Jeremie S. Kim, Lois Orosa, and Onur Mutlu, "Understanding RowHammer Under Reduced Wordline Voltage: An Experimental Study Using Real DRAM Devices" Proceedings of the 52nd Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Baltimore, MD, USA, June 2022. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [arXiv version] [Talk Video (34 minutes, including Q&A)] [Lightning Talk Video (2 minutes)]

## Slide 41: A Closer Look into RowHammer
Low Voltage
Victim Row
Bitline
Low Voltage
Victim Row
Aggressor Row
Disturbance
High Voltage
Aggressor Row
Low Voltage
Low Voltage
Victim Row
Victim Row
Low Voltage
time
Aggressor Row
Wordline Voltage
Repeatedly toggling
wordline voltage
leads to RowHammer bitflips
Yağlıkçı et al., ”Understanding RowHammer Under Reduced Wordline Voltage: An Experimental Study Using Real DRAM Devices," in DSN, 2022.
Notes: This cartoon provides a closer look into RowHammer. [CLICK]
Asserting high voltage to a row’s wordline for row activation disturbs nearby rows [CLICK]
Repeating this operation [CLICK] many times [CLICK] exacerbates the leakage in victim rows and leads to bit flips [CLICK]
So, repeatedly toggling wordline voltage leads to RowHammer bitflips [CLICK]

## Slide 42: Effect of Reducing Wordline Voltage
Reducing wordline voltage
can reduce RowHammer vulnerability
at the cost of weaker cells
time
Wordline
Voltage
Reduction in disturbance
Aggressor row
Victim row
Aggressor row
Victim row
Wordline
Bitline
Wordline
Bitline
Smaller charge
and
weaker channel
time
Wordline
Voltage
Yağlıkçı et al., ”Understanding RowHammer Under Reduced Wordline Voltage: An Experimental Study Using Real DRAM Devices," in DSN, 2022.
Notes: When we reduce wordline voltage, [CLICK]
we can reduce RowHammer vulnerability [CLICK]
At the potential cost of weakening DRAM cells by reducing their charge and weakening channels in their access transistors [END]

## Slide 43: Key Results of Voltage Scaling Study
Reducing wordline voltage can reduce RowHammer vulnerability
  15.2% (66.9% max) fewer bitflips occur
  7.4% (85.8% max) more activations needed to induce a bitflip
Row activation latency increases with reduced wordline voltage
  208 / 272 DRAM chips have no bitflips at nominal latency
  Changing timing constraint from 13.5ns to 24ns avoids bitflips
More DRAM cells tend to experience data retention bitflips when wordline voltage is reduced
  216 / 272 DRAM chips have no bitflips at nominal refresh rate
  SECDED ECC at nominal refresh rate avoids bitflips
  16% increase in refresh rate avoids bitflips
Yağlıkçı et al., ”Understanding RowHammer Under Reduced Wordline Voltage: An Experimental Study Using Real DRAM Devices," in DSN, 2022.
Notes: We begin with investigating wordline voltage's effect on row activation latency [CLICK]
This figure shows how [CLICK]
reducing wordline voltage [CLICK]
affects the row activation latency[CLICK]
We observe that the row activation latency increases with reduced wordline voltage [CLICK]
However, the nominal activation latency already has a significant guardband, [CLICK]
allowing most DRAM chips to complete row activation before the nominal activation latency [END]

## Slide 44: Core Contributions
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
BlockHammer: Selectively throttling unsafe accesses
1
2
3
Svärd: Leveraging heterogeneity
building a detailed understanding of DRAM read disturbance
leveraging insights into modern DRAM chips and memory controllers
throttling memory requests that lead to time-consuming preventive refreshes
MICRO’24
Notes: Next, I will summarize how we leverage the heterogeneity in read disturbance vulnerability across DRAM rows [CLICK]

## Slide 45: Spatial Variation-Aware Read Disturbance Defenses
A. Giray Yağlıkçı, Geraldo F. de Oliviera, Yahya Can Tuğrul, İsmail Emir Yüksel, Ataberk Olgun, Haocong Luo, and Onur Mutlu, “Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions,” Proceedings of the 30th Edition of The International Symposium on High-Performance Computer Architecture (HPCA), Edinburgh, Scotland, UK, March 2024. [Slides (pptx) (pdf)] [arXiv version]

## Slide 46: Tested DRAM Chips
144 DDR4 DRAM chips from SK Hynix, Micron, and Samsung
All rows in four different banks
Notes: We test 144 DRAM chips [CLICK]
That implement various densities-die revisions [CLICK]
And chip organizations [CLICK]

## Slide 47: Spatial Variation-Aware Mitigation
Significant and irregular variation in read disturbance vulnerability across DRAM rows
Read disturbance solutions:
  Configured for the worst row
  Overprotect many rows
  Incur large performance overheads
Key Idea: Dynamically tune the aggressiveness of existing solutions to the victim row’s read disturbance vulnerability
Svärd: Spatial Variation-Aware Read Disturbance Defenses
Fewer preventive actions (e.g., refresh) for stronger rows
*Svärd is the Swedish word for sword, a weapon with a long blade for cutting or thrusting [Merriam-Webster]
Yağlıkçı et al., "Spatial Variation-Aware Read Disturbance Defenses:
Experimental Analysis of Real DRAM Chips and Implications on Future Solutions,” in HPCA, 2024.
Notes: As I described earlier, there is a signficant variation in read disturbance vulnerability across DRAM rows [CLICK]
Existing solutions are configured for the worst row, [CLICK]
leading to overprotecting many rows and thus incurring large performance overheads [CLICK]
Our key idea is to dynamically tune the aggressiveness of existing solutions to the victim row’s read disturbance vulnerability [CLICK]
To this end, we propose a new mechanism called Svard, spatial variation-aware read disturbance defenses [CLICK]
Svard essentially performs fewer preventive actions for stronger rows [CLICK]

## Slide 48: Integrating Svärd with Existing Solutions
PARA: Probabilistic Row Activation [Kim+, ISCA’14]
Row
Activation
Random
Number
>
Threshold
Preventively
refresh the victim row
Yes
victim row
Svärd
>
Threshold
Svärd works with many other read disturbance solutions, including:
BlockHammer [Yaglikci+, HPCA’21]
Hydra [Qureshi+, ISCA’22]
RRS [Saileshwar+, ASPLOS’22]
AQUA [Saxena+, MICRO’22]
Less vulnerable
Higher threshold
More vulnerable
Lower threshold
 Fewer refresh
 More aggressive refresh
Yağlıkçı et al., "Spatial Variation-Aware Read Disturbance Defenses:
Experimental Analysis of Real DRAM Chips and Implications on Future Solutions,” in HPCA, 2024.

## Slide 49: Performance Evaluation
Cycle-level simulations using Ramulator 2.0 [Luo+, CAL 2023]
System Configuration:
Workloads: 120 different 8-core multiprogrammed workloads from SPEC CPU2006, SPEC CPU2017, TPC, MediaBench, and YCSB benchmark suites
Integrated with AQUA, BlockHammer, PARA, Hydra, and RRS
HCfirst: {4K, 2K, 1K, 512, 256, 128, 64} hammers The minimum hammer count needed to induce the first bitflip
Processor | 3.2 GHz, 8 core, 4-wide issue, 128-entry instr. window
Last-Level Cache | 64-byte cache line, 8-way set-associative, 8 MB
Memory Scheduler | FR-FCFS
Address Mapping | Minimalistic Open Pages
Main Memory | DDR4, 4 bank group, 4 banks per bank group (16 banks per rank)
Yağlıkçı et al., "Spatial Variation-Aware Read Disturbance Defenses:
Experimental Analysis of Real DRAM Chips and Implications on Future Solutions,” in HPCA, 2024.
Notes: We use Ramulator for cycle-level simulations in our performance evaluation [CLICK]
We simulate a realistic system with the shown parameters that I will not explain in detail [CLICK]
We simulate 125 different 8-core multiprogrammed workloads [CLICK]
We sweep DRAM chip capacity from 2Gb to 128Gb [CLICK]
And RowHammer threshold: the minimum number of activations needed to induce the first RowHammer bit flip from 1K to 64 [CLICK]

## Slide 50: Key Results
Svärd reduces the performance overhead of existing solutions and significantly improves system throughput
Svärd’s hardware complexity:
Yağlıkçı et al., "Spatial Variation-Aware Read Disturbance Defenses:
Experimental Analysis of Real DRAM Chips and Implications on Future Solutions,” in HPCA, 2024.
BlockHammer [Yaglikci+, HPCA’21]
4.9x
Hydra [Qureshi+, ISCA’22]
1.1x
RRS [Saileshwar+, ASPLOS’22]
4.8x
AQUA [Saxena+, MICRO’22]
1.6x
PARA [Kim+, ISCA’14]
2.0x
In-DRAM
Implementation
0.006%
In-Processor
Implementation
0.027%
No
Additional
Latency

## Slide 51: Core Contributions
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
BlockHammer: Selectively throttling unsafe accesses
1
2
3
HiRA: Parallelizing Preventive Actions
building a detailed understanding of DRAM read disturbance
leveraging insights into modern DRAM chips and memory controllers
throttling memory requests that lead to time-consuming preventive refreshes
MICRO’24
Notes: Without further ado, let’s look into the detailed understanding we built [CLICK]

## Slide 52: HiRA: Hidden Row Activation
Abdullah Giray Yağlıkçı, Ataberk Olgun, Minesh Patel, Haocong Luo, Hasan Hassan, Lois Orosa, Oguz Ergin, and Onur Mutlu, "HiRA: Hidden Row Activation for Reducing Refresh Latency of Off-the-Shelf DRAM Chips,” in MICRO 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (36 minutes)] [arXiv version]

## Slide 53: Subarray-Level Parallelism
Each subarray is mostly independent…
  except occasionally sharing global structures
Global I/O
Global Decoder
Bank
Local Row-Buf
Local Row-Buf
Subarray1
SubarrayN
···
Yoongu Kim, et al., "A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM,” in ISCA, 2012
Notes: Based on our observation, we propose two key ideas.
First, we realized that each subarray operates mostly independently of each other, except when occasionally sharing global structures, such as the global row-buffer. Additionally, each subarray has a row-decoder, which in turn is driven by the global row-decoder, another global structure.
Our first key idea is to reduce the sharing of global structures among subarrays to enable subarray-level parallelism.

## Slide 54: HiRA: Hidden Row Activation – Key Insight
Subarray X
Subarray Y
Concurrently activating two rows in different subarrays of the same bank can refresh one row while opening the other row
Row A
Row B
Refreshes RowA
concurrently with
opening RowB
ACT
ACT
DRAM Bank
Yağlıkçı et al., "HiRA: Hidden Row Activation for Reducing Refresh Latency
of Off-the-Shelf DRAM Chips,” in MICRO, 2022.
Notes: HiRA is based on the key insight that [CLICK]
activating two rows in quick succession [CLICK]
That are in different subarrays in the same bank[CLICK]
Can refresh one row [CLICK]
Concurrently with activating the other row [CLICK]

## Slide 55: HiRA: Hidden Row Activation
Refresh RowA concurrently with Activating RowB
HiRA
Saved time using HiRA
ACT
RowA
PRE
ACT
RowB
PRE
time
time
RowA’s
refresh
RowB’s activation
ACT
RowA
PRE
ACT
RowB
PRE
RowA’s
refresh
RowB’s activation
Reduction in the time spent for two refreshes
RD
RD
RD
RD
Without HiRA
With HiRA
Precharge
Yağlıkçı et al., "HiRA: Hidden Row Activation for Reducing Refresh Latency
of Off-the-Shelf DRAM Chips,” in MICRO, 2022.
Notes: Here is an example of how HiRA refreshes a RowA concurrently with activating a RowB [CLICK]
Without HiRA, only one row can be activated in a bank at a given time [CLICK]
Therefore, we activate RowA, wait until the row is refreshed [CLICK]
Precharge the bank [CLICK]
And activate RowB to read data from RowB [CLICK]
With HiRA, [CLICK]
We issue ACT-PRE-ACT command sequence [CLICK]
Which starts RowA’s refresh with the first ACT [CLICK]
And RowB’s activation with the second ACT [CLICK]
With this parallelization, we can perform the column access earlier [CLICK]

## Slide 56: HiRA in Off-the-Shelf DRAM Chips
HiRA works in 56 off-the-shelf DRAM chips from SK Hynix
51.4% reduction in the time spent for refresh operations
HiRA effectively reduces the time spent for refresh operations in off-the-shelf DRAM chips
Notes: And we observe that HiRA reduces time spent for refresh operations by 51.4% [CLICK]
Therefore, we conclude that HiRA effectively reduces the time spent for refresh operation in off-the-shelf DRAM chips [CLICK]

## Slide 57: HiRA-MC: HiRA Memory Controller
Generates each periodic refresh and RowHammer-preventive refresh with a deadline
Buffers each refresh request and performs the refresh request until the deadline
Finds if it can refresh a DRAM row concurrently with a DRAM access or another refresh
1
2
3
Notes: HiRA-MC contains the necessary components to timely generate each periodic and RowHammer-preventive refresh request with a deadline [CLICK]
To buffer each refresh request until its deadline [CLICK]
And to find if it can refresh a row concurrently with a DRAM access or another refresh request [CLICK]

## Slide 58: Performance Evaluation
Cycle-level simulations using Ramulator [Kim+, CAL 2015]
System Configuration:
Workloads: 125 different 8-core multiprogrammed workloads from the SPEC2006 benchmark suite
DRAM Chip Capacity: {2, 4, 8, 16, 32, 64, 128} Gb
RowHammer Threshold: {1024, 512, 256, 128, 64} activations The minimum hammer count needed to induce the first RowHammer bitflip
Processor | 3.2 GHz, 8 core, 4-wide issue, 128-entry instr. window
Last-Level Cache | 64-byte cache line, 8-way set-associative, 8 MB
Memory Scheduler | FR-FCFS
Address Mapping | Minimalistic Open Pages
Main Memory | DDR4, 4 bank group, 4 banks per bank group (16 banks per rank)
Timing Parameters | t1=t2=3ns, tRC= 46.25ns, tFAW=16ns
Notes: We use Ramulator for cycle-level simulations in our performance evaluation [CLICK]
We simulate a realistic system with the shown parameters that I will not explain in detail [CLICK]
We simulate 125 different 8-core multiprogrammed workloads [CLICK]
We sweep DRAM chip capacity from 2Gb to 128Gb [CLICK]
And RowHammer threshold: the minimum number of activations needed to induce the first RowHammer bit flip from 1K to 64 [CLICK]

## Slide 59: Key Results of HiRA
Performance Evaluation
  3.7x speedup by reducing time spent on RowHammer-preventive refreshes
  12.6% speedup by reducing time spent on periodic refreshes
Hardware Complexity Analysis
  Chip area cost of 0.0023% of a processor die
  No additional latency overhead
Yağlıkçı et al., "HiRA: Hidden Row Activation for Reducing Refresh Latency
of Off-the-Shelf DRAM Chips,” in MICRO, 2022.
Notes: And we observe that HiRA reduces time spent for refresh operations by 51.4% [CLICK]
Therefore, we conclude that HiRA effectively reduces the time spent for refresh operation in off-the-shelf DRAM chips [CLICK]

## Slide 60: Core Contributions
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
BlockHammer: Selectively throttling unsafe accesses
1
2
3
building a detailed understanding of DRAM read disturbance
leveraging insights into modern DRAM chips and memory controllers
throttling memory requests that lead to time-consuming preventive refreshes
MICRO’24
Notes: Without further ado, let’s look into the detailed understanding we built [CLICK]

## Slide 61: BlockHammer
A. Giray Yaglikci, Minesh Patel, Jeremie S. Kim, Roknoddin Azizi, Ataberk Olgun, Lois Orosa, Hasan Hassan, Jisung Park, Konstantinos Kanellopoulos, Taha Shahroodi, Saugata Ghose, and Onur Mutlu, "BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows" Proceedings of the 27th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, February-March 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Intel Hardware Security Academic Awards Short Talk Slides (pptx) (pdf)] [Talk Video (22 minutes)] [Short Talk Video (7 minutes)] [Intel Hardware Security Academic Awards Short Talk Video (2 minutes)] [BlockHammer Source Code] Intel Hardware Security Academic Award Finalist (one of 4 finalists out of 34 nominations)
Notes: We provide more analyses and implementation details available in the full paper.
[CLICK] First, the paper shares a security proof where we mathematically represent ALL POSSIBLE access patterns and show that NO ROW can be activated at a high-enough rate to induce bit-flips when BlockHammer is configured correctly.
[CLICK] Second, the paper explains how BlockHammer addresses many-sided attacks by tuning its thresholds.
[CLICK] Third, we evaluate all four high-level RowHammer mitigation approaches through analyzing 14 mechanisms from four aspects
[CLICK] comprehensive protection
[CLICK] compatibiltiy with commodity DRAM chips
[CLICK] scalability with worsening RowHammer vulnerability
[CLICK] and deterministic protection.
[CLICK] We show that BlockHammer is the only mechanism that satisfies all of them.
[END]

## Slide 62: BlockHammer: Key Idea
A RowHammer attack hammers Row A
BlockHammer detects hammered rows using area-efficient Bloom filters
Selectively throttles accesses targeting hammered rows
Row A
DRAM Bank
BlockHammer prevents read disturbance bitflips by selectively throttling the memory requests
that would otherwise cause
read disturbance bitflips and memory contention
Victim
Rows
Notes: The second problem is about compatibility with DRAM communication protocols [CLICK]
Let’s recap how we manage memory addresses. We use virtual addresses in the application level [CLICK]
The system software translates them to physical addresses [CLICK]
Which then parsed in the memory controller to identify DRAM bus addresses, such as banks and rows [CLICK]
All these translations are visible within the processor [CLICK]
However, yet another translation is performed within the DRAM chips from processor-visible addresses to physical row addresses [CLICK]
This translation is proprietary information of the DRAM vendors and obfuscated from the processor [CLICK]
When a RowHammer attack hammers a Row A [CLICK]
A defense implemented in the processor can detect this attack [CLICK]
And preventively refresh row addresses A+1 and A-1, which may not correspond to actual victim rows [CLICK]
As a result, bitflips still may occur [CLICK]
Unfortunately, many existing solutions rely on this proprietary information [CLICK]

## Slide 63: BlockHammer: Evaluation (1/2)
Qualitative comparison against 14 mechanisms
  Comprehensive protection
  Compatibility with commodity DRAM chips
  Scalability with worsening RowHammer vulnerability
  Deterministic protection
Quantitative comparison against 6 state-of-the-art mechanisms
  PARA [Kim+, ISCA’14]
  ProHIT [Son+, DAC’17]
  MRLoc [You+, DAC’19]
BlockHammer is the only mechanism that satisfies
all four properties
  CBT [Seyedzadeh+, ISCA’18]
  TWiCe [Lee+, ISCA’19]
  Graphene [Park+, MICRO’20]
BlockHammer is low cost and competitive

## Slide 64: BlockHammer: Evaluation (2/2)
Cycle-level simulations using Ramulator and DRAMPower
System Configuration:
Single-Core Benign Workloads:
  22 SPEC CPU 2006
  4 YCSB Disk I/O
  2 Network Accelerator Traces
  2 Bulk Data Copy with Non-Temporal Hint (movnti)
Randomly Chosen Multiprogrammed Workloads:
  125 workloads containing 8 benign applications
  125 workloads containing 7 benign applications and 1 RowHammer attack
Processor | 3.2 GHz, {1,8} core, 4-wide issue, 128-entry instr. window
LLC | 64-byte cache line, 8-way set-associative, {2,16} MB
Memory scheduler | FR-FCFS
Address mapping | Minimalistic Open Pages
DRAM | DDR4 1 channel, 1 rank, 4 bank group, 4 banks per bank group
RowHammer Threshold | 32K  1K
Notes: We conduct cycle-level simulations using RAMULATOR and DRAMPOWER to evaluate the performance and DRAM energy consumption.
[CLICK] We simulate a realistic system with a DDR4 DRAM module.
[CLICK] We use single-core workloads from four benchmarks in our simulations.
22 SPEC benchmarks, 4 disk I/O memory access traces from YCSB benchmark suite, 2 memory access traces collected from a network accelerator chip, and 2 synthetic traces that mimic bulk data copy with non-temporal hint.
[CLICK] We randomly combine these workloads to create two types of eight-core multiprogrammed workloads:
[CLICK] workloads that contain eight benign applications
[CLICK] and workloads that contain seven benign applications along with one thread performing RowHammer attack.

## Slide 65: BlockHammer: Evaluation (2/2)
Cycle-level simulations using Ramulator and DRAMPower
System Configuration:
Single-Core Benign Workloads:
  22 SPEC CPU 2006
  4 YCSB Disk I/O
  2 Network Accelerator Traces
  2 Bulk Data Copy with Non-Temporal Hint (movnti)
Randomly Chosen Multiprogrammed Workloads:
  125 workloads containing 8 benign applications
  125 workloads containing 7 benign applications and 1 RowHammer attack
Processor | 3.2 GHz, {1,8} core, 4-wide issue, 128-entry instr. window
LLC | 64-byte cacheline, 8-way set-associative, {2,16} MB
Memory scheduler | FR-FCFS
Address mapping | Minimalistic Open Pages
DRAM | DDR4 1 channel, 1 rank, 4 bank group, 4 banks per bank group
RowHammer Threshold | 32K
No RowHammer attack: Negligible (<0.6%) performance and energy overheads
RowHammer attack present: Significant improvement on system performance (71%) and energy consumption (32%)
Notes: We conduct cycle-level simulations using RAMULATOR and DRAMPOWER to evaluate the performance and DRAM energy consumption.
[CLICK] We simulate a realistic system with a DDR4 DRAM module.
[CLICK] We use single-core workloads from four benchmarks in our simulations.
22 SPEC benchmarks, 4 disk I/O memory access traces from YCSB benchmark suite, 2 memory access traces collected from a network accelerator chip, and 2 synthetic traces that mimic bulk data copy with non-temporal hint.
[CLICK] We randomly combine these workloads to create two types of eight-core multiprogrammed workloads:
[CLICK] workloads that contain eight benign applications
[CLICK] and workloads that contain seven benign applications along with one thread performing RowHammer attack.

## Slide 66: Core Contributions
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
BreakHammer: Throttling malicious threads
1
2
3
building a detailed understanding of DRAM read disturbance
leveraging insights into modern DRAM chips and memory controllers
throttling memory requests that lead to time-consuming preventive refreshes
MICRO’24
Notes: Without further ado, let’s look into the detailed understanding we built [CLICK]

## Slide 67: BreakHammer
Oğuzhan Canpolat, et al., "Leveraging Adversarial Detection to Enable Scalable and Low Overhead RowHammer Mitigations,” [cs.CR] 2404.13477, 2024.
available on arXiv and will appear in MICRO 2024
https://arxiv.org/abs/2404.13477
Notes: In summary,
[CLICK] The three major DRAM maintenance operations are refresh, RowHammer protection, and memory scrubbing.
[CLICK] We observe that implementing new and efficient maintenance mechanisms often requires difficult-to-realize changes in various system components, including the DRAM interface and the memory controller.
[CLICK] In this work, our goal is to first, ease the process of enabling new DRAM maintenance operations in DRAM and
[CLICK] enable more efficient in-DRAM maintenance operations
[CLICK] To this end, we propose Self-Managing DRAM (or SMD for short), which enables implementing new in-DRAM maintenance mechanisms with no further changes in the DRAM interface and the memory controller
[CLICK] According to our evaluations, SMD-based maintenance mechanisms achieve significant performance and energy efficiency benefits across many system configurations and workloads.
[CLICK] We release the source code of SMD on github.

## Slide 68: Motivation: Memory Performance Attacks
Attacker triggers many preventive actions
to block access to main memory
A new attack vector: Triggering preventive actions
to reduce availability of the main memory

## Slide 69: BreakHammer: Key Idea
Detect and slow down attackers
that trigger many preventive actions

## Slide 70: Evaluation
Performance and energy consumption evaluation: Ramulator 2.0 [Luo+, CAL 2023] and DRAMPower [Chandrasekar+, DATE 2013]
System Configuration:
  Processor 4 cores, 4.2GHz clock frequency, 4-wide issue, 128-entry instruction window
  DRAM DDR5, 1 channel, 2 rank/channel, 8 bank groups, 4 banks/bank group, 64K rows/bank
  Memory Ctrl. 64-entry read and write requests queues, Scheduling policy: FR-FCFS with a column cap of 4 LLC: 8 MiB (4-core)
Comparison Points: Integrated with 7 state-of-the-art RowHammer mitigation mechanisms
  PARA [Kim+ 2014]
  Graphene [Park+ 2020]
  AQUA [Saxena+ 2022]
  Hydra [Quershi+ 2022]
  TWiCe [Lee+ 2019]
  REGA [Marazzi+ 2023]
  RFM [JEDEC 2020]
Workloads: 4-core workload mixes from SPEC CPU2006/2017, TPC, MediaBench, and YCSB
  60 mixes all benign
  60 mixes with 3 benign and 1 attacker

## Slide 71: Evaluation
Performance and energy consumption evaluation: Ramulator 2.0 [Luo+, CAL 2023] and DRAMPower [Chandrasekar+, DATE 2013]
System Configuration:
  Processor 4 cores, 4.2GHz clock frequency, 4-wide issue, 128-entry instruction window
  DRAM DDR5, 1 channel, 2 rank/channel, 8 bank groups, 4 banks/bank group, 64K rows/bank
  Memory Ctrl. 64-entry read and write requests queues, Scheduling policy: FR-FCFS with a column cap of 4 LLC: 8 MiB (4-core)
Comparison Points: Integrated with 7 state-of-the-art RowHammer mitigation mechanisms
  PARA [Kim+ 2014]
  Graphene [Park+ 2020]
  AQUA [Saxena+ 2022]
  Hydra [Quershi+ 2022]
  TWiCe [Lee+ 2019]
  REGA [Marazzi+ 2023]
  RFM [JEDEC 2020]
Workloads: 4-core workload mixes from SPEC CPU2006/2017, TPC, MediaBench, and YCSB
  60 mixes all benign
  60 mixes with 3 benign and 1 attacker
BreakHammer does not degrade the average system performance
No attack
BreakHammer reduces preventive refresh count (by 67%)
Under attack
BreakHammer improves system performance (by 40%)
Under attack
BreakHammer reduces DRAM energy consumption (by 54%)
Under attack

## Slide 72: Conclusion
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
1
2
3
We can mitigate DRAM read disturbance efficiently and scalably by
building a detailed understanding of DRAM read disturbance
leveraging insights into modern DRAM chips and memory controllers
throttling memory requests that lead to time-consuming preventive refreshes
MICRO’24

## Slide 73: More Details and Discussion on YouTube
https://www.youtube.com/live/CRtm1es4n3o?si=8N5zB6e_RUc5Ejl8
https://www.youtube.com/live/YQwRYWpCsk0?si=jXPueMHb5wgs69-q

## Slide 74: Industry Solutions to RowHammer

## Slide 75: Per-Row Activation Counters in DRAM
Tanj Bennett, Stefan Saroiu, Alec Wolman, and Lucian Cojocar, “Panopticon: A Complete In-DRAM Rowhammer Mitigation,” DRAMSec Workshop (co-located with ISCA), 2021.
Accurate RowHammer detection using an activation counter per DRAM row
stored within the DRAM array leveraging high density  low cost

## Slide 76: RowHammer in 2023: SK Hynix

## Slide 77: RowHammer in 2023: Samsung
https://arxiv.org/pdf/2302.03591v1.pdf

## Slide 78: DDR5 Update in 2024
DRAM implements per-row activation counters
DRAM asserts a back-off signal when refresh is needed
Memory controller issues refresh upon back-off signal
JEDEC, “JESD79-5C_v1.30: DDR5 SDRAM Specification,” April, 2024.
similar to Panopticon and PRHT
similar to SMD, Mithril+, and Panopticon

## Slide 79: Understanding PRAC
PRAC is the latest update to DDR5 in April 2024
We show that
  PRAC is secure and has non-negligible performance, energy, and area overheads for benign workloads
  PRAC can be exploited by memory performance attacks (up to 79% reduction in DRAM chip’s throughput)
presented in DRAMSec 2024

## Slide 80: Industry Solutions to Read Disturbance: Per Row Activation Counting DRAM Timings
101010101010101010101010
0
101010101010101010101010
0
0
101010101010101010101010
0
101010101010101010101010
0
101010101010101010101010
Counters
DRAM Rows
Row counter updates are not completely parallelized
with DRAM access
PRAC increases row-close time (tRP) by ~140%
PRE
ACT
row-close time (tRP)

## Slide 81: Industry Solutions to Read Disturbance: Per Row Activation Counting DRAM Timings
tRP
tRAS
tRTP
tWR
: +21ns
: -16ns
: -2.5ns
: -20ns
tRC
: +5ns
(+140%)
(-50%)
(-33%)
(-66%)
(+10%)
Timing parameter changes for DDR5-3200AN speed bin
[JEDEC JESD79-5C, April 2024]

## Slide 82: Memory Performance Attacks
0
0
Many Back-Offs
Row Counters
Mathematically hogs up to 79% of DRAM throughput
of future DRAM chips
Degrades system performance by up to 65% (53% on average)
Access pattern to trigger most back-offs
with fewest activations possible by targeting a single row
Adversarial Access Pattern

## Slide 83: More in the Paper
https://arxiv.org/abs/2406.19094

## Slide 84: Open Sourced
https://github.com/CMU-SAFARI/ramulator2

## Slide 85: An Upcoming Paper: Self-Managing DRAM
Three example DRAM maintenance operations:
  Periodic refresh
  RowHammer-preventive refresh
  Memory scrubbing
Enables new in-DRAM maintenance mechanisms without modifications other than the ACT-NACK signal from the DRAM chip to the memory controller
Hasan Hassan, Ataberk Olgun, A. Giray Yaglikci, Haocong Luo, and Onur Mutlu, ``Self-Managing DRAM: A Low-Cost Framework for Enabling Autonomous and Efficient in-DRAM Operations,’’ cs.AR:2207.13358, 2022 (last update in 2024)
available on arXiv and will appear in MICRO 2024
Notes: In summary,
[CLICK] The three major DRAM maintenance operations are refresh, RowHammer protection, and memory scrubbing.
[CLICK] We observe that implementing new and efficient maintenance mechanisms often requires difficult-to-realize changes in various system components, including the DRAM interface and the memory controller.
[CLICK] In this work, our goal is to first, ease the process of enabling new DRAM maintenance operations in DRAM and
[CLICK] enable more efficient in-DRAM maintenance operations
[CLICK] To this end, we propose Self-Managing DRAM (or SMD for short), which enables implementing new in-DRAM maintenance mechanisms with no further changes in the DRAM interface and the memory controller
[CLICK] According to our evaluations, SMD-based maintenance mechanisms achieve significant performance and energy efficiency benefits across many system configurations and workloads.
[CLICK] We release the source code of SMD on github.

## Slide 86: Enabling Efficient and Scalable DRAM Read Disturbance Mitigation via New Experimental Insights into Modern DRAM Chips
Abdullah Giray Yağlıkçı
Aug 12, 2024
Stanford University
Notes: Hello everyone, welcome to my doctoral examination. Today, I will give a high-level overview of the work that I have done throughout my Ph.D.

## Slide 87: Enabling Efficient and Scalable DRAM Read Disturbance Mitigation via New Experimental Insights into Modern DRAM Chips
Abdullah Giray Yağlıkçı
Aug 12, 2024
Stanford University
Backup Slides
Notes: Hello everyone, welcome to my doctoral examination. Today, I will give a high-level overview of the work that I have done throughout my Ph.D.

## Slide 88: Understanding PRAC
PRAC is the latest update to DDR5 in April 2024
We show that
  PRAC is secure and has non-negligible performance, energy, and area overheads for benign workloads
  PRAC can be exploited by memory performance attacks (up to 79% reduction in DRAM chip’s throughput)
presented in DRAMSec 2024

## Slide 89: Industry Solutions to Read Disturbance: When To Refresh? (I)
DRAM
Channel
DRAM Module
Preventive refresh is a blocking operation
ACT
Memory controller cannot activate a row
while a preventive refresh blocks the bank

## Slide 90: Industry Solutions to Read Disturbance: When To Refresh? (II)
DRAM
Channel
DRAM Module
Earlier JEDEC DDR5 specifications introduce
Refresh Management (RFM) commands
RFM
Memory controller sends an RFM command
to allow time for preventive refreshes

## Slide 91: Industry Solutions to Read Disturbance
Periodic Refresh Management (PRFM)
Memory controller periodically issues RFM commands
Per Row Activation Counting and Back-Off (PRAC)
DRAM chip tracks row activations and requests RFMs by sending back-off signals
Periodic Refresh Management (PRFM)
Memory controller periodically issues RFM commands

## Slide 92: Industry Solutions to Read Disturbance: Periodic Refresh Management (PRFM)
0
0
0
0
0
1
2
3
0
Bank Activation Counters
ACT
ACT
ACT
RFM
DRAM Commands
RFM Threshold
ACT
RFM
PRFM tracks activations with low accuracy,
causing high number of preventive refreshes,
leading to large performance and energy overheads

## Slide 93: Industry Solutions to Read Disturbance
Periodic Refresh Management (PRFM)
Memory controller periodically issues RFM commands
Per Row Activation Counting and Back-Off (PRAC)
DRAM chip tracks row activations and requests RFMs by sending back-off
Per Row Activation Counting and Back-Off (PRAC)
DRAM chip tracks row activations and requests RFMs by sending back-off

## Slide 94: Industry Solutions to Read Disturbance: Per Row Activation Counting
0
101010101010101010101010
0
0
101010101010101010101010
0
0
1
2
3
4
0
101010101010101010101010
PRAC allows accurate tracking of aggressor row activations
Counters
DRAM Rows
Notes: The latest JEDEC DDR5 standard introduces the per row activation counting.
[CLICK] Where each row within DRAM is paired with a counter that tracks activations.
[CLICK] By doing so, the DRAM module perfectly tracks aggressors and their activations for preventive refreshes as we see in the animation.

## Slide 95: Industry Solutions to Read Disturbance: Per Row Activation Counting (PRAC)
0
1
2
3
4
0
Back-Off
0
Row Counters
0
ACT
ACT
RFM
ACT
ACT
RFM
DRAM Commands
Back-Off Threshold
ACT
normal traffic
(180 ns)
recovery
(N RFMs)
RFM
PRAC-N

## Slide 96: Performance Comparison: Industry Solutions
PRFM
Memory controller periodically issues RFM
PRAC-N
Memory controller issues N RFMs each with back-off
PRAC+PRFM
Memory controller issues RFM periodically and with back-offs
PRAC-Optimistic
PRAC-4 with no change in DRAM timing parameters
1
2
3
4

## Slide 97: Experimental Results: Performance Overhead and Its Scaling
Lower is worse
Higher is better

## Slide 98: Experimental Results: Performance Overhead and Its Scaling
PRAC has non-negligible performance overhead (10%)
due to increased access latency
10%

## Slide 99: Experimental Results: Performance Overhead and Its Scaling
Graphene and Hydra outperform PRAC
at relatively high NRH values

## Slide 100: Experimental Results: Performance Overhead and Its Scaling
PRAC-Optimistic outperforms all evaluated mitigation mechanisms
(above NRH of 32)

## Slide 101: Experimental Results: Performance Overhead and Its Scaling
PRFM’s system performance overheads
significantly increase (by 37x) as NRH decreases

## Slide 102: Experimental Results: DRAM Energy Overhead and Its Scaling
Above NRH of 32, PRAC overhead only slightly increases due to timely preventive refreshes
Below NRH of 32, PRAC overhead significantly increases
due to conservative thresholds against a wave attack

## Slide 103: How Large is 1000 Activations?
Bitflips occur at ~1000 activations
Mitigation mechanisms trigger preventive actions (e.g., preventive refresh) at ~500 activations
Is 500 a distinctive activation count?
Benign workloads activate hundreds of rows more than 500 times in a refresh window
Memory intensive workloads from SPEC’06, SPEC’17, TPC, YCSB, and MediaBench
Benign workloads might not be so benign

## Slide 104: Circuit-Level Justification Temperature Analysis
We hypothesize that our observations are caused by the non-monotonic behavior of charge trapping characteristics of DRAM cells
3D TCAD model [Yang+, EDL'19]
HCfirst decreases as temperature increases, until a temperature inflection point where HCfirst starts to increase as temperature increases
A cell is more vulnerable to RowHammer at temperatures close to its temperature inflection point
Notes: And third, [CLICK]
We observe thatThe HCfirst change tends to be larger as temperature change increases [CLICK]
The figure shows that, for all manufacturer, when increase the temperature change from 50-55C to 50-90C, the absolute changes values increase [CLICK]

## Slide 105: Deeper Understanding of Physics and Vulnerabilities
The effect of aging Preliminary data on aging via 68-day of continuous hammering
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
Aging can lead to read disturbance bitflips at smaller hammer counts
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
105

## Slide 106: Deeper Understanding of Physics and Vulnerabilities
The effect of aging Preliminary data on aging via 68-day of continuous hammering
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
Aging can lead to read disturbance bitflips at smaller hammer counts
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
106
Future work:
rigorous aging characterization
and online profiling of read disturbance vulnerability

## Slide 107: Deeper Understanding of Physics and Vulnerabilities
The effect of aging
Interactions across different error mechanisms
RowHammer
RowPress
Data retention time errors
Variable retention time
…

## Slide 108: Deeper Understanding of Physics and Vulnerabilities
The effect of aging
Interactions across different error mechanisms
What is the worst-case?
  Temperature
  Data pattern
  Memory access pattern
  Spatial variation
  Voltage
What is the worst-case considering all these sensitivities?
What is the minimum hammer count to induce a read disturbance bitflip?

## Slide 109: Deeper Understanding of Physics and Vulnerabilities
The effect of aging
Interactions across different error mechanisms
What is the worst-case?
How reliable are our DRAM chips?
How reliable will our DRAM chips be tomorrow?
We do not know! This is an open research problem

## Slide 110: Future Research for Better Memory Systems



Cross-Layer
Communication
Flexible and Intelligent Memory Chips, Interfaces, Controllers
Deeper Understanding of
Physics and Vulnerabilities
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 111: Flexible and Intelligent Chips, Interfaces, Controllers
In-field patching is necessary
DRAM read disturbance solution is here
DRAM chip is here
Configuration
Aging might change the chip’s characteristics
DRAM module can be replaced
Reconfiguration is needed
+ add more hardware counters
+ increase metadata cache capacity
Deployed solutions should be patchable in field

## Slide 112: Future Research for Better Memory Systems



Cross-Layer
Communication
Flexible and Intelligent Memory Chips, Interfaces, Controllers
Deeper Understanding of
Physics and Vulnerabilities
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 113: Cross-Layer Communication
Attacker is often an application
Bitflips occur in the circuit level
Hardware is good at
  Detecting an attack
  Performing counter-measures
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Memory allocations
Memory access patterns
Control flow patterns
Time / power measurements
Memory request scheduling
Speculative execution
Prefetching, branch prediction
Power management
Bitflips occur
Memory isolation is broken
Software
uArch
Device
Detection
Mitigation
~
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 114: Cross-Layer Communication
Attacker is often an application
Bitflips occur in the circuit level
Hardware is good at
  Detecting an attack
  Performing counter-measures
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Memory allocations
Memory access patterns
Control flow patterns
Time / power measurements
Memory request scheduling
Speculative execution
Prefetching, branch prediction
Power management
Bitflips occur
Memory isolation is broken
Detection
Mitigation
Software
uArch
Device
~
Cross-layer communication is crucial going forward
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 115: Attack Performance Overhead and Its Scaling
Mitigation mechanisms incur significantly increasing overheads
as RowHammer threshold decreases
BreakHammer significantly (40% on average) increases
system performance (even exceeding baseline with no mitigation)

## Slide 116: Attack Energy Overhead and Its Scaling
BreakHammer drastically improves (54% on average)
the DRAM energy consumption

## Slide 117: Number of Preventive Actions and Its Scaling
Mitigation mechanisms issue significantly increasing number of preventive actions as RowHammer threshold decreases
BreakHammer significantly (67% on average) reduces
the number of preventive actions performed across all mitigations

## Slide 118: Benign Performance and Its Scaling
BreakHammer does not degrade
the average system performance of benign only workloads

## Slide 119: Benign Memory Latency at NRH = 64
BreakHammer does not degrade
the memory latency of benign only workloads

## Slide 120: Comparison to BlockHammer
BreakHammer outperforms BlockHammer, the state-of-the-art throttling-based RowHammer mitigation mechanism

## Slide 121: Observing Actions and Detecting Anomalies
Preventive
Action Counters
BreakHammer tracks the number of preventive actions caused by each thread and detects anomalies in thread activity
ACT
PREF
Memory
Controller
BreakHammer
99
23
10
7
ACT
PREF
Memory
Controller
BreakHammer
100
23
10
7

## Slide 122: Filtering and Throttling Memory Usage
MSHR Limit
BreakHammer slows down suspicious threads by reducing the number of miss status holding registers (MSHR) they can allocate in the last level of the cache hierarchy
Last
Level Cache
BreakHammer

## Slide 123: Future Research

## Slide 124: Ongoing and Future Research on DRAM Read Disturbance
Cross-Layer
Communication
Flexible and Intelligent Memory Chips, Interfaces, and Controllers
Deeper Understanding of
Physics and Vulnerabilities
Aging
Online Profiling
In-field patchability
DRAM-initiated pause
Subarray-level parallelism
Identify threads that cause the problem
Hardware-level detection
System-level mitigation
Ongoing works
Notes: We can address these challenges by investing on [CLICK]
A deeper understanding of DRAM read disturbance, especially the effects of aging and efficient online profiling [CLICK]
More flexible and intelligent memory chips, interfaces, and controllers, which support in-field patchability, [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 125: Broader Research Interests

## Slide 126: Broader Research Interests
2017
2023
2021
2019
2018
2020
2022
2024
Understanding
Read Disturbance
Bostanci+
HPCA’22
Reducing DRAM Energy
Chang+
SIGMETRICS’17
Ghose+
SIGMETRICS’18
Haj-Yahya+
HPCA’22
Hassan+
ISCA’19
Luo+
ISCA’20
Haj-Yahya+
ISCA’20
Olgun+, ISCA’21
Oliveira+, HPCA’24
Luo+, CAL’23
Olgun+, TACO’23
Revisiting RowHammer ISCA’20
BlockHammer HPCA’21
Deeper Look MICRO’21
IChannels ISCA’21
Voltage Scaling DSN’22
HiRA MICRO’22
HBM RowHammer DSN Disrupt’23
RowPress ISCA’23
RowHammer Survey ASP-DAC’23
Svärd HPCA’24
CoMeT HPCA’2
HBM RowHammer DSN’24
ABACuS USENIX Sec’24
Reducing DRAM Latency
System Energy Saving Methods
Covert Channels and Security Primitives
Experimental
Infrastructure
Processing Using
Memory
Mitigating
Read Disturbance
Read Disturbance Survey
Olgun+
Disrupt’23
Olgun+, DSN’24
Olgun+, USENIX Sec’24
Bostanci+, HPCA’24
Kim+
ISCA’20
Mutlu+
ASP-DAC’23
Luo+
ISCA’23
Haj-Yahya+, ISCA’21
Koppula+
MICRO’19
Yuksel+ , DSN’24
Yuksel+, HPCA’24
Yaglikci+
HPCA’21
Orosa+
MICRO’21
Yaglikci+
MICRO’22
Yaglikci+
DSN’22
Yaglikci+
HPCA’24
Thesis Publications
Bostanci+
arXiv’24
Notes: During my Ph.D., I had the pleasure to work with many people in the SAFARI group.
We tackled a variety of different problems in computer architecture and hardware security.

## Slide 127: The Problem
Computing
is Bottlenecked by Data

## Slide 128: Data is Key for AI, ML, Genomics, …
Important workloads are all data intensive
They require rapid and efficient processing of large amounts of data
Data is increasing
  We can generate more than we can process
  We need to perform more sophisticated analyses on more data

## Slide 129: Huge Demand for Performance & Efficiency
https://www.youtube.com/watch?v=x2-qB0J7KHw
~4 orders of magnitude increase in memory requirement in just two years!

## Slide 130: Data is Key for Future Workloads
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 131: Data Overwhelms Modern Machines
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Data → performance & energy bottleneck

## Slide 132
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data is Key for Future Workloads
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 133
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data Overwhelms Modern Machines
Data → performance & energy bottleneck
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 134: Data is Key for Future Workloads
development of high-throughput sequencing (HTS) technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Notes: However, since the development of high throughput sequencing (HTS) technologies, the cost of genome sequencing has fallen off a cliff (<< 1,000$) making it viable for almost everyone's use.

## Slide 135: Data is Key for Future Workloads
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Data → performance & energy bottleneck
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 136: A Solution: Deeper and Larger Memory Hierarchies
https://wccftech.com/amd-ryzen-5000-zen-3-vermeer-undressed-high-res-die-shots-close-ups-pictured-detailed/
AMD Ryzen 5000, 2020
Core Count:
8 cores/16 threads
L1 Caches:
32 KB per core
L2 Caches:
512 KB per core
L3 Cache:
32 MB shared

## Slide 137: AMD’s 3D Last Level Cache (2021)
https://youtu.be/gqAYMx34euU
https://www.tech-critter.com/amd-keynote-computex-2021/
https://community.microcenter.com/discussion/5134/comparing-zen-3-to-zen-2
Additional 64 MB L3 cache die stacked on top of the processor die
- Connected using Through Silicon Vias (TSVs)
- Total of 96 MB L3 cache
AMD increases the L3 size of their 8-core Zen 3 processors from 32 MB to 96 MB
Notes: CCD = Core Chiplet Die
Structural silicon is used to equalize the height and facilitate heat dissipation from the cores.

## Slide 138: Deeper and Larger Memory Hierarchies
https://www.it-techblog.de/ibm-power10-prozessor-mehr-speicher-mehr-tempo-mehr-sicherheit/09/2020/
IBM POWER10,
2020
Cores:
15-16 cores,
8 threads/core
L2 Caches:
2 MB per core
L3 Cache:
120 MB shared

## Slide 139: Deeper and Larger Memory Hierarchies
https://www.gsmarena.com/apple_announces_m1_ultra_with_20core_cpu_and_64core_gpu-news-53481.php
Apple M1 Ultra System (2022)
DRAM
DRAM
A lot of
SRAM
Storage
Storage
139

## Slide 140: The Energy Perspective
Dally, HiPEAC 2015

## Slide 141: Data Movement vs Computation Energy
Dally, HiPEAC 2015
A memory access consumes ~100-1000X
the energy of a complex addition

## Slide 142: We Do Not Want to Move Data!
Dally, HiPEAC 2015
A memory access consumes ~100-1000X
the energy of a complex addition

## Slide 143: Data Movement vs. Computation Energy
Chart: Energy for a 32-bit Operation (log scale)
| ADD (int) | ADD (float) | Register File | MULT (int) | MULT (float) | SRAM Cache | DRAM
Energy (pJ) | 0.1 | 0.9 | 1 | 3.1 | 3.7 | 5 | 640
ADD (int) Relative Cost | 1 | 9 | 10 | 31 | 37 | 50 | 6400
Han+, “EIE: Efficient Inference Engine on Compressed Deep Neural Network,” ISCA 2016.

## Slide 144: Data Movement vs. Computation Energy
Chart: Energy for a 32-bit Operation (log scale)
| ADD (int) | ADD (float) | Register File | MULT (int) | MULT (float) | SRAM Cache | DRAM
Energy (pJ) | 0.1 | 0.9 | 1 | 3.1 | 3.7 | 5 | 640
ADD (int) Relative Cost | 1 | 9 | 10 | 31 | 37 | 50 | 6400
Han+, “EIE: Efficient Inference Engine on Compressed Deep Neural Network,” ISCA 2016.
6400X
A memory access consumes 6400X
the energy of a simple integer addition

## Slide 145
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement
Data Movement Overwhelms Modern Machines

## Slide 146: Data Movement Overwhelms Accelerators
Amirali Boroumand, Saugata Ghose, Berkin Akin, Ravi Narayanaswami, Geraldo F. Oliveira, Xiaoyu Ma, Eric Shiu, and Onur Mutlu, "Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks" Proceedings of the 30th International Conference on Parallel Architectures and Compilation Techniques (PACT), Virtual, September 2021. [Slides (pptx) (pdf)] [Talk Video (14 minutes)]
> 90% of the total system energy
is spent on memory in large ML models

## Slide 147: Yet …
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 148: Performance Perspective (Today)
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 149: Performance Perspective (Today)
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 150: Problem
Data access is the major performance and energy bottleneck
Our current
design principles cause
great energy waste
and
performance loss

## Slide 151: Problem
Processing of data
is performed
far away from the data

## Slide 152: Promising Solutions: Processing Near Memory (PnM)
UPMEM, founded in January 2015, announces the first real-world PIM architecture in 2016
UPMEM’s PIM-enabled DIMMs start getting commercialized in 2019
In early 2021, Samsung announces FIMDRAM at ISSCC conference
Samsung’s LP-DDR5 and DIMM-based PIM announced a few months later
In early 2022, SK Hynix announces AiM and Alibaba announces HB-PNM at ISSCC conference
https://www.eenewsautomotive.com/news/startup-plans-embed-processors-dram-0#

## Slide 153: Promising Solutions: Processing Near Memory (PnM)
Chart: Speedup over CPU (log scale)
| VA | SEL | UNI | BS | HST-S | HST-L | RED | SCAN-SSA | SCAN-RSS | TRNS | GEMV | SpMV | TS | BFS | MLP | NW | GMEAN (1) | GMEAN (2) | GMEAN | More PIM-suitable workloads (1) | Less PIM-suitable workloads (2) |
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 93.4 | 410.1 | 439.4 | 0.4 | 71.1 | 71.1 | 26.1 | 57.6 | 57.6 | 51.3 | 447.2 | 30.7 | 1552.7 | 1.6 | 305 | 68.8 | 52.2336 | 94.5778 | 65.6382
640 DPUs | 38.6 | 167 | 234.4 | 4.4 | 134.4 | 33.6 | 9.1 | 13.5 | 16 | 36.6 | 25.2 | 0.4 | 20.1 | 0.0368 | 5.6 | 0.1 | 34.1541 | 1.269 | 10.1005
2556 DPUs | 149.1 | 498.2 | 629.5 | 23 | 496.6 | 167.1 | 45.3 | 61.3 | 70.2 | 96.3 | 46.3 | 0.9 | 86.6 | 0.0019 | 5.8 | 0.1 | 132.5595 | 1.2587 | 23.2267
KEY OBSERVATION
The UPMEM-based PIM system can outperform a state-of-the-art GPU on workloads with three key characteristics:
Streaming memory accesses
No or little inter-DPU synchronization
No or little use of integer multiplication, integer division, or floating point operations
These three key characteristics make a workload potentially suitable to the UPMEM PIM architecture.

## Slide 154: Promising Solutions: Processing Using Memory (PuM) Implementing Data Movement
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
Negligible HW cost
Idea: Two consecutive ACTivates
Notes: copy

## Slide 155: Promising Solutions: Processing Using Memory (PuM) Implementing Data Movement
VDD/2
VDD/2
0
VDD/2 + δ
0
VDD
VDD
VDD/2 + δ
Sense Amplifier
(Row Buffer)
Amplify the difference
0
Data gets copied
src
dst

## Slide 156: Promising Solutions: Processing Using Memory (PuM) Implementing Data Movement
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 157: Promising Solutions: Processing Using Memory (PuM) Implementing Logic Operations
½VDD
½VDD
dis
A
B
C
Final State
AB + BC + AC
½VDD+δ
C(A + B) + ~C(AB)
en
0
VDD
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.

## Slide 158: Promising Solutions: Processing Using Memory (PuM) Implementing Logic Operations

## Slide 159: Promising Solutions: Processing Using Memory (PuM) Implementing Logic Operations
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
>4-12X Performance Improvement

## Slide 160: Motivation
Processing near/using memory
is a promising computation paradigm
Distributing execution across
CPU, GPU, PnM, and PuM
should NOT hurt security and privacy

## Slide 161: Research Scope (Going Forward)
Scope: Confidentiality, integrity, and availability in large-scale & vastly-shared processing in memory and storage
Confidentiality:
  Physical isolation
  Architecture support for encryption in memory/storage
Integrity:
  In-field patchable and dynamically tunable maintenance mechanisms
  Integrity check and efficient roll-back mechanisms
Availability:
  Intelligent scheduling and fairness mechanisms
  Adaptive maintenance supported with online profiling

## Slide 162: Enabling Efficient and Scalable DRAM Read Disturbance Mitigation via New Experimental Insights into Modern DRAM Chips
Abdullah Giray Yağlıkçı
Research Summary and Future Directions
July 9, 2024
Notes: Hello everyone, welcome to my doctoral examination. Today, I will give a high-level overview of the work that I have done throughout my Ph.D.

## Slide 163: Flexible and Intelligent Chips, Interfaces, Controllers
In-field patching is necessary
Interfaces should be more flexible
Memory controller decides what should be done when
DRAM chip has read disturbance solution inside (tracking+prevention)
The memory controller should provide the DRAM chip with necessary time window to perform preventive actions (e.g., refreshing rows)
The memory controller does not have the tracking information
Communicating is not straightforward due to strict communication protocol
A more flexible interface is necessary

## Slide 164: Flexible and Intelligent Chips, Interfaces, Controllers
In-field patching is necessary
Interfaces should be more flexible
Memory controller decides what should be done when
DRAM chip has read disturbance solution inside (tracking+prevention)
Two Key Issues:
A naïve implementation can lead to very high command bus occupancy
  Very high bandwidth consumption
  Poor parallelism
DRAM self-manages preventive refreshes. Why not other maintenance routines?
A new DDR5 extension
(JESD79-5C, 2024)
ACT
alert_n
ACT
ACT
alert_n
alert_n

## Slide 165: Flexible and Intelligent Chips, Interfaces, Controllers
In-field patching is necessary
Interfaces should be more flexible
Memory controllers should be more intelligent in detecting malicious activity
DRAM chips become more and more vulnerable to RowHammer and RowPress
Key Insight: Activation counts of benign applications get close to unsafe levels
Problem: DRAM read disturbance solutions are getting prohibitively expensive
Research Question: How to identify malicious threads/processes/users?
More intelligent detection mechanisms are needed
The memory controller observes all memory accesses
More intelligent memory controllers can help

## Slide 166: Deeper Understanding of Physics and Vulnerabilities
The effect of aging Preliminary data on aging via 68-day of continuous hammering
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
Aging can lead to read disturbance bitflips at smaller hammer counts
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
166

## Slide 167: Deeper Understanding of Physics and Vulnerabilities
The effect of aging Preliminary data on aging via 68-day of continuous hammering
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
Aging can lead to read disturbance bitflips at smaller hammer counts
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
167
Future work:
rigorous aging characterization
and online profiling of read disturbance vulnerability

## Slide 168: Deeper Understanding of Physics and Vulnerabilities
The effect of aging
Interactions across different error mechanisms
RowHammer
RowPress
Data retention time errors
Variable retention time
…

## Slide 169: Deeper Understanding of Physics and Vulnerabilities
The effect of aging
Interactions across different error mechanisms
What is the worst-case?
  Temperature
  Data pattern
  Memory access pattern
  Spatial variation
  Voltage
What is the worst-case considering all these sensitivities?
What is the minimum hammer count to induce a read disturbance bitflip?

## Slide 170: Deeper Understanding of Physics and Vulnerabilities
The effect of aging
Interactions across different error mechanisms
What is the worst-case?
How reliable are our DRAM chips?
How reliable will our DRAM chips be tomorrow?
We do not know! This is an open research problem

## Slide 171: Future Research for Better Memory Systems



Cross-Layer
Communication
Flexible and Intelligent Memory Chips, Interfaces, Controllers
Deeper Understanding of
Physics and Vulnerabilities
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 172: Flexible and Intelligent Chips, Interfaces, Controllers
In-field patching is necessary
DRAM read disturbance solution is here
DRAM chip is here
Configuration
Aging might change the chip’s characteristics
DRAM module can be replaced
Reconfiguration is needed
+ add more hardware counters
+ increase metadata cache capacity
Deployed solutions should be patchable in field

## Slide 173: Flexible and Intelligent Chips, Interfaces, Controllers
In-field patching is necessary
Interfaces should be more flexible
Memory controller decides what should be done when
DRAM chip has read disturbance solution inside (tracking+prevention)
The memory controller should provide the DRAM chip with necessary time window to perform preventive actions (e.g., refreshing rows)
The memory controller does not have the tracking information
Communicating is not straightforward due to strict communication protocol
A more flexible interface is necessary

## Slide 174: Flexible and Intelligent Chips, Interfaces, Controllers
In-field patching is necessary
Interfaces should be more flexible
Memory controller decides what should be done when
DRAM chip has read disturbance solution inside (tracking+prevention)
Two Key Issues:
A naïve implementation can lead to very high command bus occupancy
  Very high bandwidth consumption
  Poor parallelism
DRAM self-manages preventive refreshes. Why not other maintenance routines?
A new DDR5 extension
(JESD79-5C, 2024)
ACT
alert_n
ACT
ACT
alert_n
alert_n

## Slide 175: Self-Managing DRAM
Implementing new maintenance mechanisms often requires difficult-to-realize changes
The three major DRAM maintenance operations:
  Refresh
  RowHammer Protection
  Memory Scrubbing
Self-Managing DRAM (SMD)
Enables implementing
new in-DRAM maintenance mechanisms
with no further changes in the DRAM interface and the memory controller
SMD-based maintenance operations provide significant performance and energy benefits
across many system configurations and workloads
Hasan Hassan, Ataberk Olgun, A. Giray Yaglikci, Haocong Luo, and Onur Mutlu, ``Self-Managing DRAM: A Low-Cost Framework for Enabling Autonomous and Efficient in-DRAM Operations,’’ cs.AR:2207.13358, 2022 (last update in 2024)
Notes: In summary,
[CLICK] The three major DRAM maintenance operations are refresh, RowHammer protection, and memory scrubbing.
[CLICK] We observe that implementing new and efficient maintenance mechanisms often requires difficult-to-realize changes in various system components, including the DRAM interface and the memory controller.
[CLICK] In this work, our goal is to first, ease the process of enabling new DRAM maintenance operations in DRAM and
[CLICK] enable more efficient in-DRAM maintenance operations
[CLICK] To this end, we propose Self-Managing DRAM (or SMD for short), which enables implementing new in-DRAM maintenance mechanisms with no further changes in the DRAM interface and the memory controller
[CLICK] According to our evaluations, SMD-based maintenance mechanisms achieve significant performance and energy efficiency benefits across many system configurations and workloads.
[CLICK] We release the source code of SMD on github.

## Slide 176: Flexible and Intelligent Chips, Interfaces, Controllers
In-field patching is necessary
Interfaces should be more flexible
Memory controllers should be more intelligent in detecting malicious activity
DRAM chips become more and more vulnerable to RowHammer and RowPress
Key Insight: Activation counts of benign applications get close to unsafe levels
Problem: DRAM read disturbance solutions are getting prohibitively expensive
Research Question: How to identify malicious threads/processes/users?
More intelligent detection mechanisms are needed
The memory controller observes all memory accesses
More intelligent memory controllers can help

## Slide 177: BreakHammer
Key Observation: Mitigating DRAM read disturbance causes delays in memory accesses
Our Exploit: Denial of memory service is possible via triggering mitigation mechanisms
Key Idea: Throttling memory accesses of threads that trigger mitigation mechanisms repeatedly
BreakHammer:
  Detects the threads that repeatedly trigger the mitigation mechanisms
  Limits their on-the-fly memory request counts and MSHRs
  Near-zero area overhead and no additional memory access latency
Evaluation:
  Improves system performance by 48.7% on average (105.5% max)
  Reduces the maximum slowdown by 14.6% on average
Oğuzhan Canpolat, A. Giray Yağlıkçı, Ataberk Olgun, İsmail Emir Yüksel, Yahya Can Tuğrul, Konstantinos Kanellopoulos, Oğuz Ergin, Onur Mutlu, "Leveraging Adversarial Detection to Enable Scalable and Low Overhead RowHammer Mitigations,” [cs.CR] 2404.13477, 2024.
Notes: In summary,
[CLICK] The three major DRAM maintenance operations are refresh, RowHammer protection, and memory scrubbing.
[CLICK] We observe that implementing new and efficient maintenance mechanisms often requires difficult-to-realize changes in various system components, including the DRAM interface and the memory controller.
[CLICK] In this work, our goal is to first, ease the process of enabling new DRAM maintenance operations in DRAM and
[CLICK] enable more efficient in-DRAM maintenance operations
[CLICK] To this end, we propose Self-Managing DRAM (or SMD for short), which enables implementing new in-DRAM maintenance mechanisms with no further changes in the DRAM interface and the memory controller
[CLICK] According to our evaluations, SMD-based maintenance mechanisms achieve significant performance and energy efficiency benefits across many system configurations and workloads.
[CLICK] We release the source code of SMD on github.

## Slide 178: Future Research for Better Memory Systems



Cross-Layer
Communication
Flexible and Intelligent Memory Chips, Interfaces, Controllers
Deeper Understanding of
Physics and Vulnerabilities
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 179: Cross-Layer Communication
Attacker is often an application
Bitflips occur in the circuit level
Hardware is good at
  Detecting an attack
  Performing counter-measures
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Memory allocations
Memory access patterns
Control flow patterns
Time / power measurements
Memory request scheduling
Speculative execution
Prefetching, branch prediction
Power management
Bitflips occur
Memory isolation is broken
Software
uArch
Device
Detection
Mitigation
~
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 180: How Large is 1000 Activations?
Bitflips occur at ~1000 activations
Mitigation mechanisms trigger preventive actions (e.g., preventive refresh) at ~500 activations
Is 500 a distinctive activation count?
Benign workloads activate hundreds of rows more than 500 times in a refresh window
Memory intensive workloads from SPEC’06, SPEC’17, TPC, YCSB, and MediaBench
Benign workloads might not be so benign

## Slide 181: Cross-Layer Communication
Attacker is often an application
Bitflips occur in the circuit level
Hardware is good at
  Detecting an attack
  Performing counter-measures
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Memory allocations
Memory access patterns
Control flow patterns
Time / power measurements
Memory request scheduling
Speculative execution
Prefetching, branch prediction
Power management
Bitflips occur
Memory isolation is broken
Detection
Mitigation
Software
uArch
Device
~
Cross-layer communication is crucial going forward
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 182: Enabling Efficient and Scalable DRAM Read Disturbance Mitigation via New Experimental Insights into Modern DRAM Chips
Abdullah Giray Yağlıkçı
Research Summary and Future Directions
July 9, 2024
Backup Slides
Notes: Hello everyone, welcome to my doctoral examination. Today, I will give a high-level overview of the work that I have done throughout my Ph.D.

## Slide 183: Awards and Honorable Mentions
BlockHammer: One of four finalists Intel Hardware Security Academic Awards in 2022
Svärd: First place ACM SRC (PACT) in 2023 (grand final is ongoing)
Thesis: One of five finalists (ongoing) HOST Ph.D. Dissertation Competition in 2024
Notes: Lastly, I’d like to mention that some of these works already got recognition and we are competing for the Dissertation award in HOST.

## Slide 184: IChannels Exploiting Current Management Mechanisms to Create Covert Channels in Modern Processors
Jawad Haj-Yahya Jeremie S. Kim A. Giray Yağlıkçı Ivan Puddu Lois Orosa
Juan Gómez Luna Mohammed Alser Onur Mutlu
Notes: My name is Jawad Haj-Yahya and I will present our work IChannels [END]

## Slide 185: Executive Summary
Problem: Current management mechanisms throttle instruction execution and adjust voltage/frequency to accommodate power-hungry instructions (PHIs).
These mechanisms may compromise a system’s confidentiality guarantees
Goal:
Understand the throttling side-effects of current management mechanisms
Build high-capacity covert channels between otherwise isolated execution contexts
Practically and effectively mitigate each covert channel
Characterization: Variable execution times and frequency changes due to running PHIs
We observe five different levels of throttling in real Intel systems
IChannels: New covert channels that exploit side-effects of current management mechanisms
  On the same hardware thread
  Across co-located Simultaneous Multi-Threading (SMT) threads
  Across different physical cores
Evaluation: On three generations of Intel processors, IChannels provides a channel capacity
  2× that of PHIs’ variable latency-based covert channels
  24× that of power management-based covert channels
Notes: First, I will give a high-level overview of the talk [CLICK]
Current management mechanisms throttle instruction execution and adjust voltage/frequency to accommodate power-hungry instructions (PHIs).
These mechanisms may compromise a system’s confidentiality guarantees [CLICK]
Our Goal is [CLICK]
First to Understand the throttling side-effects of current management mechanisms [CLICK]
Secondly to Build high-capacity covert channels between otherwise isolated execution contexts [CLICK]
Finally to Practically and effectively mitigate each covert channel [CLICK]
We Characterize the Variable execution times and frequency changes due to running PHIs
We observe five different levels of throttling in real Intel systems [CLICK]
We propose Ichannels, a New covert channels that exploit side-effects of current management mechanisms [CLICK]
  On the same hardware thread [CLICK]
  Across co-located Simultaneous Multi-Threading (SMT) threads [CLICK]
  Across different physical cores [CLICK]
On three generations of Intel processors, IChannels provides a channel capacity [CLICK]
  2× that of PHIs’ variable latency-based covert channels [CLICK]
  24× that of power management-based covert channels [CLICK]
[END]

## Slide 186: ABACuS: All-Bank Activation Counters
Ataberk Olgun, Yahya Can Tugrul, Nisa Bostanci, Ismail Emir Yuksel, Haocong Luo, Steve Rhyner, Abdullah Giray Yaglikci, Geraldo F. Oliveira, and Onur Mutlu, "ABACuS: All-Bank Activation Counters for Scalable and Low Overhead RowHammer Mitigation" To appear in Proceedings of the 33rd USENIX Security Symposium (USENIX Security), Philadelphia, PA, USA, August 2024. [arXiv version] [ABACuS Source Code]

## Slide 187: ABACuS: All-Bank Activation Counters
Goal: Prevent RowHammer bitflips at low performance, energy, and area cost
Key Observation: Workloads tend to access the same row in all DRAM banks at around the same time
Key Idea: Use one hardware counter to keep track of activation counts of the same row across all banks
Make high-performance, area-hungry counter-based mechanisms practical
Key Results:
Faster than the lowest-area-cost counter-based defense mechanism Smaller than the lowest-performance-overhead counter-based defense mechanism
0.59% avg. performance overhead (single-core) at a RowHammer threshold (1K)
Only 9.79 KiB on-chip storage per DRAM rank (0.02% of a Xeon processor)
1.52% avg. performance overhead (single-core) at an ultra-low threshold (125)
75.70 KiB on-chip storage per DRAM rank (0.11% of the Xeon processor)
https://github.com/CMU-SAFARI/ABACuS

## Slide 188: CoMeT: Count-Min-Sketch-based Row Tracking
Nisa Bostanci, Ismail Emir Yuksel, Ataberk Olgun, Konstantinos Kanellopoulos, Yahya Can Tugrul, A. Giray Yaglikci, Mohammad Sadrosadati, Onur Mutlu "CoMeT: Count-Min-Sketch-based Row Tracking to Mitigate RowHammer at Low Cost,” in Proceedings the 30th International Symposium on High-Performance Computer Architecture (HPCA), Edinburgh, March 2024. [arXiv version] [CoMeT Source Code]

## Slide 189: Executive Summary
Evaluation: CoMeT achieves a good trade-off between area, performance and energy costs
incurs significantly less area overhead (74.2×) compared to the state-of-the-art technique
outperforms the state-of-the-art technique (by up to 39.1%)
CoMeT:
tracks most DRAM rows with scalable hash-based counters by employing the Count-Min-Sketch technique to achieve a low area cost
tracks only a small set of DRAM rows that are activated many times with highly accurate per-DRAM-row activation counters to reduce performance penalties
Key Idea: Use low-cost and scalable hash-based counters to accurately track DRAM rows
Goal: Prevent RowHammer bitflips with low area, performance, and energy overheads in highly RowHammer-vulnerable DRAM-based systems
https://github.com/CMU-SAFARI/CoMeT