## Slide 1
Future work: More research is needed to improve PRAC by tackling
increased DRAM access latencies
increasing performance loss as RowHammer worsens
memory performance attacks exploiting PRAC
Understanding the Security Benefits and Overheads of Emerging Industry Solutions to DRAM Read Disturbance
5. Key Observations
1. DRAM Background
Modern DRAM chips are more vulnerable
Defenses are becoming prohibitively expensive
To gain insights into DRAM read disturbance and its fundamental properties
To prevent RowHammer efficiently, scalably and with no proprietary information
[Kim+, ISCA’20]
[Kim+, ISCA’14]
DRAM Module
Preventive refresh is a blocking operation
ACT
2. Cutting Edge Industry Solutions
Memory controller sends an RFM command
to allow time for preventive refreshes
Preventive Refresh in DDR5 Specifications
Oğuzhan Canpolat A. Giray Yağlıkçı Geraldo Oliveira Ataberk Olgun Oğuz Ergin Onur Mutlu
Full Paper
Contact Info
DRAM Chip
Bank
Chip I/O
bitline
wordline
…
…
DRAM Cell
Row Buffer
…
…
…
…
DRAM Bank
SA0
SA1
SAN-1
…
Sense Amplifiers (SAs)
DRAM Cell
DRAM Organization
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
Row 1
Row 3
Row 0
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
DRAM Subarray
Repeatedly opening and closing
OR keeping open
a DRAM row causes
bitflips in nearby cells
DRAM Read Disturbance
Sense
Amplifier
RowHammer
[Kim+ ISCA’14]
RowPress [Luo+ ISCA’23]
Chart: 
| The Min. ACT Count to Observe Bit Flips
2023 | 1
2020 | 9.6
2014 | 139.2
[Luo+, ISCA’23]
ACT
PREF
Memory
Controller
BreakHammer
100
23
10
7
3. Per Row Activation Counting (PRAC) [JEDEC, JESD79-5C, April 2024]
Counts the number of times a hardware thread triggers a RowHammer-preventive actions (e.g., preventive refreshes)
Last
Level Cache
Slows down suspect threads by reducing the number of miss status holding registers (MSHR) they can allocate in the last level cache (LLC)
Memory
Controller
BreakHammer
MSHR
Limit
Key Results:
Fewer preventive actions performed across all mitigations
Significantly higher system performance
Significantly lower DRAM energy consumption
No performance/energy overhead for benign applications
Near zero hardware complexity
The first rigorous security and performance analyses of PRAC
RowHammer-safe for thresholds > 20
Non-negligible overheads for modern chips
Poorly scales with worsening RowHammer vulnerability
Memory performance attacks can exploit PRAC
Cycle-level simulations using
Ramulator 2.0 [Luo+, CAL 2023] DRAMPower [Chandrasekar+, DATE 2013]
System Configuration: Processor 4 cores, 4.2GHz clock frequency, 4-wide issue, 128-entry instruction window DRAM DDR5, 1 channel, 2 rank/channel, 8 bank groups x 4 banks x 64K rows Memory Ctrl. 64-entry read and write requests queues, FR-FCFS scheduling with a column cap of 4 Last-Level Cache 8 MiB (4-core)
Workloads: 60 mixes from SPEC CPU2006,
SPEC CPU2017, TPC, MediaBench, and YCSB
Significantly lower (54%)
DRAM energy consumption
Significantly fewer (34%)
preventive refreshes performed
Periodic Refresh Management (PRFM)
Memory controller periodically issues RFM commands
Per Row Activation Counting (PRAC)
DRAM chip tracks row activations for each row and requests RFMs by sending back-off signals
RFM
0
101010101010101010101010
0
0
101010101010101010101010
0
0
1
2
3
4
N
101010101010101010101010
Counters
DRAM Rows
PRAC allows accurate tracking of aggressor row activations
Row counter updates are not completely parallelized
with DRAM access
tRP
tRAS
tRTP
tWR
: +21ns
: -16ns
: -2.5ns
: -20ns
tRC
: +5ns
(+140%)
(-50%)
(-33%)
(-66%)
(+10%)
Timing parameter changes for DDR5-3200AN speed bin [JEDEC JESD79-5C, April 2024]
Back-Off
ACT
ACT
RFM
ACT
ACT
RFM
normal traffic
(180 ns)
recovery
(N RFMs)
RFM
PRAC-N
Highest activation count an attacker can achieve
RFM Threshold (# of ACTs per bank)
Highest activation count an attacker can achieve
Back-Off Threshold (# of ACTs per row)
Periodic RFM (PRFM) Security Analysis
PRAC Security Analysis
4. Performance Evaluation
PRFM
Memory controller periodically issues RFM
PRAC-N
Memory controller issues N RFMs each with back-off
PRAC+PRFM
Memory controller issues RFM periodically and with back-offs
PRAC-Optimistic
PRAC-4 with no change in DRAM timing parameters
1
2
3
4
Lower is worse
Higher is better
Graphene and Hydra outperform PRAC at relatively high RowHammer thresholds
20
PRAC has non-negligible performance overhead (10%)
due to increased access latency
10%
PRAC-Optimistic outperforms all evaluated mitigation mechanisms (RowHammer threshold of 64 and more)
PRAC incurs significant performance and energy overheads if the RowHammer threhold is smaller than 64
7. A New Attack Vector
0
Many
Back-Offs
Row Counters
Mathematical worst-case analysis at the RowHammer threshold of 20:
Hogs up to 79% of DRAM throughput
Cycle-level simulation results:
Degrades system performance by up to 98% (94% on average)
Access pattern to trigger most back-offs with fewest activations possible by targeting a single row
Adversarial Access Pattern
https://github.com/ CMU-SAFARI/ramulator2
8. Conclusion and Future Work
Simulator is available online
PRFM’s system performance overheads
significantly increase (by 25x) as NRH decreases
PRFM’s DRAM energy overhead
significantly increase (to 5x) as NRH decreases
6. Open-Source