## Slide 1: Scaling Systems Robustly and Sustainably Outstanding Challenges and Research Perspective
Abdullah Giray Yağlıkçı
Helmholtz Center for Information Security
March 25, 2025
Notes: Hi, my name is Giray and today I will give a high-level overview of my PhD research and future research plans

## Slide 2: System Scaling in Two Aspects
Scaling down manufacturing technology
Higher performance
Lower energy consumption
Circuit-level failure mechanisms
Mitigations incur
  high hardware complexity
  high energy consumption
  reduced availability
Scaling out systems in a distributed manner
Lower cost of ownership
Dynamic scaling on demand
Security and privacy concerns can prevent achieving the full potential
  Encryption worsens latency and energy
  Isolation leads to subpar utilization
Manufacturing
Technology Node Scaling
Pros
Cons
Pros
Cons

## Slide 3
Systems should scale
robustly and sustainably
as chips get denser
and many users share systems

## Slide 4: Towards Robust and Sustainable Scaling
Pre-PhD Research
  Understanding and reducing memory access latency
  Understanding and reducing memory energy consumption
PhD Research
  Understanding read disturbance failures in main memory
  Mitigating read disturbance failures in main memory
Post-PhD Research
  Improving the availability of data and resources while mitigating read disturbance failures in main memory
Future Research
  Hardware-software co-design
  Data-centric robustness
  Better understanding of hardware failures
  for technology node scaling AND scale-out systems

## Slide 5: Memory Isolation
Memory
access
1  0
Rule of thumb: An access to one memory address should not have unintended side effects on data stored in other addresses
Leak Private Information
Take Over a Computer
Data Loss or Corruption
Compromise Application Correctness
Memory isolation is difficult in modern memory chips
Data integrity and confidentiality issues may emerge

## Slide 6: Read Disturbance in Modern Memory Chips
Prevalent memory technology: Dynamic Random Access Memory (DRAM)
DRAM stores data in the form of electrical charge on a capacitor
DRAM leaks charge over time and needs periodic refresh
DRAM Read Disturbance: Accessing a DRAM cell disturbs other physically nearby cells and exacerbates their charge leakage
Wordline
Bitline
Charge
leakage
paths
Notes: Dynamic random access memory (DRAM) is the prevalent memory technology today. [CLICK]
DRAM stores a bit of data in the form of electrical charge on a capacitor [CLICK]
To access we assert a wire called wordline [CLICK]
Which enables a transistor, conducting the capacitor to another wire called bitline [CLICK]
DRAM is a volatile memory technology as it leaks charge over time and needs to be periodically refreshed [CLICK]
Accessing a DRAM cell disturbs other physically nearby cells and exacerbates their charge leakage. This is called DRAM read disturbance [CLICK]

## Slide 7: RowHammer: An Example of DRAM Read Disturbance
Row 0
Row 1
Row 2
Row 3
Row 4
Repeatedly opening (activating) and closing (precharging)
a DRAM row causes read disturbance bitflips in nearby cells
and breaks memory isolation
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 2
closed
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
closed
Aggressor Row
DRAM Subarray
Notes: A prime example of DRAM read disturbance is RowHammer, which I will show in this slide.
DRAM cells are organized in 2 dimensional arrays as rows and columns and internally accessed in a DRAM row granularity. For example, to access a data stored in Row 2, [CLICK]
We first need to open Row 2, and then perform accesses. Once we need to access another row, we need to close Row 2 and open the other row [CLICK]
[BACK& FORTH] If we keep opening and closing this row many times, called hammering a row, [CLICK]
We observe bitflips in physically nearby DRAM rows [CLICK]
This phenomenon is called RowHammer. We refer to the hammered row as the aggressor row and the rows that are affected as victim rows. [CLICK]

## Slide 8: Mitigating RowHammer: Preventive Refresh
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 0
Row 1
Row 3
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
DRAM Subarray
Refreshing potential victim rows mitigates read disturbance bitflips
Aggressor Row

## Slide 9: DRAM Read Disturbance: A Critical Challenge
DRAM cells become increasingly more vulnerable to read disturbance
Technology node scaling
Chart: 
| The Min. ACT Count to Observe Bit Flips
2023 | 1
2020 | 9.6
2014 | 139.2
[Luo+, ISCA’23]
[Kim+, ISCA’20]
[Kim+, ISCA’14]
Notes: With technology node scaling, DRAM cells get smaller in size and closer to each other[CLICK]
Such that we observe significant reductions in the minimum hammer count to induce the first bitflip in the last decade [CLICK]
Thus DRAM cells become increasingly more vulnerable to read disturbance [CLICK]

## Slide 10: Challenge: Scalability with Worsening Vulnerability
Existing solutions become prohibitively expensive or ineffective going forward [Kim+, ISCA’20] [Frigo+, IEEE S&P’20] [Hassan+, MICRO’21]
More efficient, scalable, and comprehensive solutions to DRAM read disturbance
DRAM cells become
increasingly more vulnerable
to read disturbance at device level
[Kim+, ISCA’14] [Kim+, ISCA’20] [Luo+, ISCA’23]
Notes: My thesis identifies two problems about solving DRAM read disturbance [CLICK]
First, As DRAM cells become more vulnerable, [CLICK]
Existing solutions become prohibitively expensive or ineffective going forward [CLICK]
Thus, we need more efficient and scalable solutions [CLICK]
And we believe that a more detailed understanding of DRAM read disturbance can help us to achieve it[CLICK]

## Slide 11: Major Contributions
To efficiently and scalably mitigate DRAM read disturbance, we
build a detailed understanding of DRAM read disturbance
devise novel solutions leveraging insights into DRAM chip internals and memory controllers
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
Svärd: Leveraging heterogeneity
HiRA: Parallelizing preventive actions
BlockHammer: Selectively throttling unsafe accesses
1
2
Notes: To address these two problems, we conducted several studies encompassed in this thesis statement [CLICK]
We can mitigate DRAM read disturbance efficiently and scalably from three aspects [CLICK]
First, by building a detailed understanding of DRAM read disturbance [CLICK],
Which we explore for temperature [CLICK],
Memory access patterns [CLICK],
Victim cell’s physical location [CLICK],
And voltage [CLICK]
Second, by leveraging insights into modern DRAM chips and memory controllers [CLICK],
Where we leverage the heterogeneity in DRAM cells’ vulnerability levels [CLICK]
and parallelize preventive actions [CLICK]
Third, by devising novel solutions that do not require proprietary knowledge of DRAM chip internals[CLICK],
Which we achieve by selectively throttling unsafe accesses [CLICK]

## Slide 12: Major Contributions
To efficiently and scalably mitigate DRAM read disturbance, we
build a detailed understanding of DRAM read disturbance
devise novel solutions leveraging insights into DRAM chip internals and memory controllers
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
Svärd: Leveraging heterogeneity
HiRA: Parallelizing preventive actions
BlockHammer: Selectively throttling unsafe accesses
1
2
Representative Experimental Findings
Notes: To address these two problems, we conducted several studies encompassed in this thesis statement [CLICK]
We can mitigate DRAM read disturbance efficiently and scalably from three aspects [CLICK]
First, by building a detailed understanding of DRAM read disturbance [CLICK],
Which we explore for temperature [CLICK],
Memory access patterns [CLICK],
Victim cell’s physical location [CLICK],
And voltage [CLICK]
Second, by leveraging insights into modern DRAM chips and memory controllers [CLICK],
Where we leverage the heterogeneity in DRAM cells’ vulnerability levels [CLICK]
and parallelize preventive actions [CLICK]
Third, by devising novel solutions that do not require proprietary knowledge of DRAM chip internals[CLICK],
Which we achieve by selectively throttling unsafe accesses [CLICK]

## Slide 13: DRAM Testing Infrastructure
  DRAM Bender on a Xilinx Virtex UltraScale+ XCU200
Fine-grained control over DRAM commands,
timing parameters (±1.5ns), temperature (±0.5°C ),
and voltage (±1mV)
*Olgun et al., “DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips,” in TCAD, 2023. [GitHub: https://github.com/CMU-SAFARI/DRAM-Bender]
*
Notes: We use an FPGA-based experimental setup programmed with DRAM Bender, which is an open-sourced design available on github [CLICK]
We plug in a DRAM module to test on the FPGA board [CLICK]
The board communicates with the host machine to run the test routines [CLICK]
We control the chip temperature using a pair of heaters [CLICK] connected to a temperature controller [CLICK]
We also have an external power supply that we use to sweep voltage on a power rail [CLICK]
This infrastructure provides fine-grained control over DRAM commands, timing parameters, temperature, and wordline voltage [CLICK]
=======

## Slide 14: Tested DRAM Chips
Mfr. | DDR4 DIMMs | DDR3 SODIMMs | # Chips | Density | Die | Org.
A (Micron) | 9 | 1 | 144 (8) | 8Gb (4Gb) | B (P) | x4 (x8)
B (Samsung) | 4 | 1 | 32 (8) | 4Gb (4Gb) | F (Q) | x8 (x8)
C (SK Hynix) | 5 | 1 | 40 (8) | 4Gb (4Gb) | B (B) | x8 (x8)
D (Nanya) | 4 | - | 32 (-) | 8Gb (-) | C (-) | x8 (-)
272 DRAM Chips (24 DDR3 and 248 DDR4 DRAM Chips)
4 major manufacturers: Micron, Samsung, SK Hynix, and Nanya
272 DRAM chips
2 DRAM standards
4 major manufacturers
Yağlıkçı, Orosa, et al., "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" in MICRO, 2021.
Notes: In our characterization, [CLICK]
we test 272 real DRAM chips [CLICK]
from four major manufacturers, [CLICK]
that implement DDR3 and DDR4 DRAM standards [CLICK]
and with different densities, die revisions, and chip organizations[CLICK]

## Slide 15: DRAM Testing Methodology
To characterize our DRAM chips at worst-case conditions:
Prevent sources of interference during core test loop
  No DRAM refresh: to avoid refreshing victim row
  No DRAM calibration events: to minimize variation in test timing
  No RowHammer mitigation mechanisms: to observe circuit-level effects
  Test for less than a refresh window (32ms) to avoid retention failures
Worst-case access sequence
We use worst-case access sequence based on prior works’ observations
For each row, repeatedly access the two physically-adjacent rows as fast as possible
Yağlıkçı, Orosa, et al., "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" in MICRO, 2021.
Notes: To characterize our DRAM chips at worst-case conditions we take two measures:
[CLICK] First, we prevent external sources of interference such that our tests can run consistently as desired and without interruptions. To achieve this we disable:
[CLICK] DRAM refresh to avoid refreshing victim rows during a RowHammer test,
[CLICK] DRAM calibration events to minimize variation in test timings
[CLICK] and RowHammer mitigation mechanisms to ensure that we can directly observe circuit-level bit flips
[CLICK] we also ensure that our tests complete in less than a refresh window to prevent retention failures from interfering with our results
[CLICK] Second, we issue the worst-case access sequence for inducing RowHammer bit flips based on observations from prior work
[CLICK] Using these observations, we test each row’s worst-case vulnerability to RowHammer by repeatedly activating the two physically-adjacent rows as fast as possible
=========

## Slide 16: Impact of Temperature on DRAM Cells
The fraction of vulnerable DRAM cells, experiencing bit flips at all temperature levels within their vulnerable temperature range
Temperature
bit flips
Vulnerable Temperature Range
no bit flips
no bit flips
Mfr. A | Mfr. B | Mfr. C | Mfr. D
99.1% | 98.9% | 98.0% | 99.2%
Most DRAM cells are vulnerable to RowHammer throughout a bounded continuous temperature range
Lower
Bound
Upper
Bound
50oC
90oC
Yağlıkçı, Orosa, et al., "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" in MICRO, 2021.
Notes: We analyze the temperature levels a DRAM cell is vulnerable to RowHammer [CLICK]
We observe that there exists [CLICK] a lower and [CLICK] an upper bound of temperature [CLICK]
A DRAM cell experiences bit flips only within this bounded range[CLICK]
but we do not observe any bit flips out of this range [CLICK]
We call this range: vulnerable temperature range [CLICK]
This table demonstrates the fraction of DRAM cells that experience bit flips at all temperature levels within their vulnerable temperature range
We observe that more than 98% of vulnerable cells across all four manufacturers exhibit this behavior [CLICK]
Therefore, we conclude that most DRAM cells are vulnerable to RowHammer throughout a continuous temperature range [CLICK]

## Slide 17: Temperature’s Impact at DRAM Cell Granularity
Lower Bound (°C)
Upper Bound (°C)
Fraction of Vulnerable DRAM Cells
Different DRAM cells are vulnerable to RowHammer within specific temperature ranges
Vulnerable from 70°C to 85°C
Vulnerable between
50°C and 60°C not above 60°C
A population density distribution
Hammer count: 150000 activations to each of the two aggressor rows
Yağlıkçı, Orosa, et al., "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" in MICRO, 2021.
A DRAM cell should be tested
at each possible operating temperature
Implication on testing
Notes: This figure shows the population density of cells, clustered based on their vulnerable temperature range. The x-axis and y-axis show the lower bound [CLICK] and the upper bound [CLICK] of a DRAM cell’s vulnerable temperature range [CLICK]
The color-scale and the percentage values show the fraction of cells for a given temperature range [CLICK]
For example, 0.4% of the cells are vulnerable to RowHammer only between 55 and 60 degrees Celsius [CLICK],
while 0.5% of the cells experience bit flips only between 70 and 85 degrees Celsius [CLICK]
We conclude that different DRAM cells are vulnerable to RowHammer within specific temperature ranges [CLICK]

## Slide 18: Temperature’s Impact at DRAM Row Granularity
Temperature (°C)
Variation in
Bit Flip Counts
per DRAM Row
More cells experience bit flips as temperature increases
Yağlıkçı, Orosa, et al., "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" in MICRO, 2021.
Notes: Next, we study the impact of temperature on DRAM rows. The figure shows how the number of bit flips in the victim row changes as temperature increases.[CLICK]
The x-axis shows the increasing temperature [CLICK] and y-axis reports the variation in bit flip counts normalized to the mean value at 50°C. [CLICK]
We observe that more cells experience a bit flip with increasing temperature, [CLICK]

## Slide 19: Temperature’s Impact at DRAM Row Granularity
Temperature (°C)
Variation in Bit Flip Counts per DRAM Row
A DRAM row’s bit error rate can either increase or decrease with temperature depending on the DRAM manufacturer
Yağlıkçı, Orosa, et al., "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" in MICRO, 2021.
Notes: We repeat this analysis for all four manufacturers [CLICK]
We observe that the bit error rate increases with temperature in modules from three manufacturers, [CLICK]
While it exhibits an opposite trend in modules from manufacturer B. We hypothesize that this happens due to different characteristics of charge trap error mechanisms in different manufacturers. Please refer to our full paper for more details [CLICK]
Our main observation from this figure is that A DRAM row’s BER can either increase or decrease with temperature depending on the DRAM manufacturer [CLICK]

## Slide 20: Temperature’s Impact on RowHammer
Chart: 
| 250 | 275 | 300 | 325 | 350
Trap 1 | 120 | 75 | 53 | 52 | 65
Trap 2 | 75 | 45 | 28 | 25 | 35
Trap 3 | 50 | 35 | 22 | 24 | 33
Trap 4 | 145 | 90 | 88 | 110 | 200
Ours are empirical observations
Similar to the behavior of Trap Assisted Charge Leakage
Increasing temperature
  helps electrons move easier  higher leakage  smaller RowHammer threshold
  makes traps lose charge  lower trap-assisted leakage  larger RowHammer threshold
Device characteristics determine the dominant effect
Varies across
  Cells
  Chips
  Manufacturers
3D TCAD model [Yang+, EDL'19]
Temperature (K)
RowHammer Threshold (x1000)
Lower is more vulnerable
Yağlıkçı, Orosa, et al., "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" in MICRO, 2021.

## Slide 21: Temperature Study’s Impact: Spying on a Machine’s Temperature via RowHammer
Observe RowHammer BER to measure change in temperature
Find canary cells that exhibit erroneous behavior at particular temperature points
Reverse-engineer the DRAM module’s model
Characterize an identical model in lab
Build a regression model of BER vs temperature
Identify canary cells
Monitor canary cells to identify temperature

## Slide 22: Major Contributions
To efficiently and scalably mitigate DRAM read disturbance, we
build a detailed understanding of DRAM read disturbance
devise novel solutions leveraging insights into DRAM chip internals and memory controllers
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
Svärd: Leveraging heterogeneity
HiRA: Parallelizing preventive actions
BlockHammer: Selectively throttling unsafe accesses
1
2
Representative Experimental Findings
Notes: To address these two problems, we conducted several studies encompassed in this thesis statement [CLICK]
We can mitigate DRAM read disturbance efficiently and scalably from three aspects [CLICK]
First, by building a detailed understanding of DRAM read disturbance [CLICK],
Which we explore for temperature [CLICK],
Memory access patterns [CLICK],
Victim cell’s physical location [CLICK],
And voltage [CLICK]
Second, by leveraging insights into modern DRAM chips and memory controllers [CLICK],
Where we leverage the heterogeneity in DRAM cells’ vulnerability levels [CLICK]
and parallelize preventive actions [CLICK]
Third, by devising novel solutions that do not require proprietary knowledge of DRAM chip internals[CLICK],
Which we achieve by selectively throttling unsafe accesses [CLICK]

## Slide 23: Impact of Memory Access Pattern
Chart: 
| The Min. ACT Count to Observe Bit Flips
2014 | 6.4
2020 | 10
State-of-the-Art
Our Finding w/ 15 column accesses
Minimum hammer count to induce the first bitflip
36% reduction
A smaller hammer count is sufficient to induce bitflips
with increased aggressor row on time
Open
Close
Open
Close
Existing mitigations are ineffective without this insight
This finding paved the way to the discovery of RowPress [Luo+, ISCA’23]
Follow-up
Implication on defenses
on time
Yağlıkçı, Orosa, et al., "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" in MICRO, 2021.
Notes: The second example is about the memory access patterns. [CLICK]
Previously known worst-case access pattern opens and closes an aggressor row as fast as possible [CLICK]
In contrast, in this study, we wait for some time after opening the aggressor row [CLICK]
We observe that doing this significantly reduces the necessary hammer count to induce the first bitflip [CLICK]
An implication is that an existing mitigation can be ineffective if it is not designed accounting for this effect [CLICK]
A follow-up of our work investigates this effect more rigorously and shows that this effect is an artifact of a new read disturbance phenomenon called RowPress [CLICK]

## Slide 24: Our Work Led to the Discovery of RowPress
Reduces the minimum number of row activations needed to induce a bitflip (ACmin) by 1-2 orders of magnitude
In extreme cases, activating a row only once induces bitflips
RowPress on HBM2-20nm for row on time of 3.9 us Read Disturbance Threshold: 335 activations [Olgun+, DSN’24]
[Luo+, ISCA’23]
Benign becomes attacker: Even SPEC workloads reach to this activation count
Mentored paper
Lower is more vulnerable
Notes: RowPress amplifies read disturbance because
First, it reduces the minimum number of row activations needed to induce a bitflip by 1-2 orders of magnitude
Second, in extreme cases, activating a row only once induces bitflips

## Slide 25: More Background: Row Buffer Locality
DRAM Subarray
Bitline
…
…
Wordline
…
…
…
…
DRAM Cell
Row Buffer
Row Hit: Row buffer has the desired content
  Service RD/WR from the row buffer (~10ns)
Row Miss: Row buffer has no content
  Open the row (~13ns)
  Service RD/WR from the row buffer (~10ns)
Row Conflict: Row buffer has different content
  Close the active row (~13ns)
  Open the desired row (~13ns)
  Serve RD/WR from the row buffer (~10ns)
I/O Circuitry
Row buffer hit is significantly faster than miss and conflict
Key Insight: Memory controller keeps a row open if the row is likely to be accessed again
Key Idea: Keep accessing the aggressor row to incentivize the memory controller to keep the row open
Notes: This is a simplified diagram of a DRAM cell, where the data is stored as capacitor voltage and accessed through the access transistor [CLICK]
A DRAM cell inherently exhibits several charge leakage paths [CLICK]
And requires to perform refresh operations to restore the capacitor voltage with a time period called refresh window.
[PAUSE]
To access a DRAM cell, [CLICK]
the memory controller must first open or activate the row to fetch the row’s data into the row buffer [CLICK]
The READ and WRITE requests targeting the row are serviced from the row buffer [CLICK]
After all requests are serviced from the row, the memory controller must close or precharge the row in order to begin accessing data from another row. [CLICK]

## Slide 26: RowPress Demonstration on a Real-System
Intel Core i5-10400 (Comet Lake)
Samsung DDR4 Module M378A2K43CB1-CTD
(Date Code: 20-10)
w/ TRR RowHammer Mitigation
// Sync with Refresh and Loop Below
for (k = 0; k < NUM_AGGR_ACTS; k++)
for (j = 0; j < NUM_READS; j++) ∗AGGRESSOR1[j];
for (j = 0; j < NUM_READS; j++) ∗AGGRESSOR2[j];
for (j = 0; j < NUM_READS; j++)
clflushopt(AGGRESSOR1[j]);
clflushopt(AGGRESSOR2[j]);
mfence();
activate_dummy_rows();
Number of Cache Blocks Accessed
Per Aggressor Row ACT
(NUM_READS=1 is Rowhammer)
Read Disturbance
Bitflip Count
Erroneous Row Count
Notes: We demonstrate RowPress on a real system with a recent Intel processor and a Samsung DDR4 module with TRR rowhammer mitigation. The key idea of our RowPress program is to keep a DRAM row open for a longer period by keeping accessing different cache blocks in the row.
Here is the key part of our program, where we can change the number of cache blocks read per aggressor row activation. If we only read 1 cache block, then the program does the same as RowHammer

## Slide 27: Major Contributions
To efficiently and scalably mitigate DRAM read disturbance, we
build a detailed understanding of DRAM read disturbance
devise novel solutions leveraging insights into DRAM chip internals and memory controllers
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
Svärd: Leveraging heterogeneity
HiRA: Parallelizing preventive actions
BlockHammer: Selectively throttling unsafe accesses
1
2
Representative Experimental Findings
Notes: To address these two problems, we conducted several studies encompassed in this thesis statement [CLICK]
We can mitigate DRAM read disturbance efficiently and scalably from three aspects [CLICK]
First, by building a detailed understanding of DRAM read disturbance [CLICK],
Which we explore for temperature [CLICK],
Memory access patterns [CLICK],
Victim cell’s physical location [CLICK],
And voltage [CLICK]
Second, by leveraging insights into modern DRAM chips and memory controllers [CLICK],
Where we leverage the heterogeneity in DRAM cells’ vulnerability levels [CLICK]
and parallelize preventive actions [CLICK]
Third, by devising novel solutions that do not require proprietary knowledge of DRAM chip internals[CLICK],
Which we achieve by selectively throttling unsafe accesses [CLICK]

## Slide 28: Another Key Finding: Variation across Rows
All DRAM Rows in a DRAM Bank
RowHammer vulnerability
significantly varies across DRAM rows
90% of rows
Weakest
10% of rows
Say, bitflips occur at
N hammers in these rows
We need at least 2N hammers
to induce bitflips in these rows
Configuring a solution for the worst-case overprotects many rows and makes it expensive
Implication on defenses
This finding paved the way to the design of Svärd [Yaglikci+, HPCA’24] (will be covered)
Follow-up
Yağlıkçı, Orosa, et al., "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" in MICRO, 2021.
Notes: The third key finding is about the variation of read disturbance across DRAM rows. Assume that this box represents all rows in a bank [CLICK]
If the weakest 10% of the rows experience bitflips after being hammered for N times, [CLICK]
We need at least 2N hammers to induce a bitflip in the remaining 90% [CLICK]
This shows that RowHammer vulnerability significantly varies across DRAM rows [CLICK]
And mitigation mechanisms that are configured for the worst row, overprotect many rows, leading to performance / energy / area overheads [CLICK]

## Slide 29: Major Contributions
To efficiently and scalably mitigate DRAM read disturbance, we
build a detailed understanding of DRAM read disturbance
devise novel solutions leveraging insights into DRAM chip internals and memory controllers
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
Svärd: Leveraging heterogeneity
HiRA: Parallelizing preventive actions
BlockHammer: Selectively throttling unsafe accesses
1
2
Representative Novel Solutions
Notes: To address these two problems, we conducted several studies encompassed in this thesis statement [CLICK]
We can mitigate DRAM read disturbance efficiently and scalably from three aspects [CLICK]
First, by building a detailed understanding of DRAM read disturbance [CLICK],
Which we explore for temperature [CLICK],
Memory access patterns [CLICK],
Victim cell’s physical location [CLICK],
And voltage [CLICK]
Second, by leveraging insights into modern DRAM chips and memory controllers [CLICK],
Where we leverage the heterogeneity in DRAM cells’ vulnerability levels [CLICK]
and parallelize preventive actions [CLICK]
Third, by devising novel solutions that do not require proprietary knowledge of DRAM chip internals[CLICK],
Which we achieve by selectively throttling unsafe accesses [CLICK]

## Slide 30: Spatial Variation-Aware RowHammer Defenses
Random
Number
>
Threshold
Preventively
refresh the victim row
Yes
victim row
Svärd
>
Threshold
PARA: Probabilistic Row Activation [Kim+, ISCA’14]
Row
Activation
Svärd works with many other read disturbance solutions, including:
BlockHammer [Yaglikci+, HPCA’21]
Hydra [Qureshi+, ISCA’22]
RRS [Saileshwar+, ASPLOS’22]
AQUA [Saxena+, MICRO’22]
Less vulnerable
Higher threshold
More vulnerable
Lower threshold
 Fewer refresh
 More aggressive refresh
Yağlıkçı et al., "Spatial Variation-Aware Read Disturbance Defenses:
Experimental Analysis of Real DRAM Chips and Implications on Future Solutions,” in HPCA, 2024.
Key insight: Significant variation across DRAM rows
Key Idea: Dynamically tune the aggressiveness of existing solutions to the victim row’s read disturbance vulnerability
Svärd: Spatial Variation-Aware Read Disturbance Defenses Fewer preventive actions (e.g., refresh) for stronger rows

## Slide 31: Performance Evaluation
Cycle-level simulations using Ramulator 2.0 [Luo+, CAL 2023]
System Configuration:
Workloads: 120 different 8-core multiprogrammed workloads from SPEC CPU2006, SPEC CPU2017, TPC, MediaBench, and YCSB benchmark suites
Integrated with AQUA, BlockHammer, PARA, Hydra, and RRS
HCfirst: {4K, 2K, 1K, 512, 256, 128, 64} hammers The minimum hammer count needed to induce the first bitflip
Processor | 3.2 GHz, 8 core, 4-wide issue, 128-entry instr. window
Last-Level Cache | 64-byte cache line, 8-way set-associative, 8 MB
Memory Scheduler | FR-FCFS
Address Mapping | Minimalistic Open Pages
Main Memory | DDR4, 4 bank group, 4 banks per bank group (16 banks per rank)
Yağlıkçı et al., "Spatial Variation-Aware Read Disturbance Defenses:
Experimental Analysis of Real DRAM Chips and Implications on Future Solutions,” in HPCA, 2024.
Notes: We use Ramulator for cycle-level simulations in our performance evaluation [CLICK]
We simulate a realistic system with the shown parameters that I will not explain in detail [CLICK]
We simulate 125 different 8-core multiprogrammed workloads [CLICK]
We sweep DRAM chip capacity from 2Gb to 128Gb [CLICK]
And RowHammer threshold: the minimum number of activations needed to induce the first RowHammer bit flip from 1K to 64 [CLICK]

## Slide 32: Key Results
Svärd reduces the performance overhead of existing solutions and significantly improves system throughput
Svärd’s hardware complexity:
Yağlıkçı et al., "Spatial Variation-Aware Read Disturbance Defenses:
Experimental Analysis of Real DRAM Chips and Implications on Future Solutions,” in HPCA, 2024.
BlockHammer [Yaglikci+, HPCA’21]
4.9x
Hydra [Qureshi+, ISCA’22]
1.1x
RRS [Saileshwar+, ASPLOS’22]
4.8x
AQUA [Saxena+, MICRO’22]
1.6x
PARA [Kim+, ISCA’14]
2.0x
In-DRAM
Implementation
0.006%
In-Processor
Implementation
0.027%
No
Additional
Latency
Svärd improves system’s availability at low cost without compromising data integrity

## Slide 33: Major Contributions
To efficiently and scalably mitigate DRAM read disturbance, we
build a detailed understanding of DRAM read disturbance
devise novel solutions leveraging insights into DRAM chip internals and memory controllers
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
Svärd: Leveraging heterogeneity
HiRA: Parallelizing preventive actions
BlockHammer: Selectively throttling unsafe accesses
1
2
Representative Novel Solutions
Notes: To address these two problems, we conducted several studies encompassed in this thesis statement [CLICK]
We can mitigate DRAM read disturbance efficiently and scalably from three aspects [CLICK]
First, by building a detailed understanding of DRAM read disturbance [CLICK],
Which we explore for temperature [CLICK],
Memory access patterns [CLICK],
Victim cell’s physical location [CLICK],
And voltage [CLICK]
Second, by leveraging insights into modern DRAM chips and memory controllers [CLICK],
Where we leverage the heterogeneity in DRAM cells’ vulnerability levels [CLICK]
and parallelize preventive actions [CLICK]
Third, by devising novel solutions that do not require proprietary knowledge of DRAM chip internals[CLICK],
Which we achieve by selectively throttling unsafe accesses [CLICK]

## Slide 34: Challenge (2/2): Compatibility
Application
Level
Virtual Memory Address
System
Level
Physical Memory Address
Memory
Controller
DRAM Bus Addresses
(Channel, Rank, Bank, Row…)
Visible within the processor
In-DRAM Mapping
Physical Row Addresses
DRAM chip
Processor-visible
Row Addresses
Proprietary
A RowHammer attack hammers Row A
Processor-based defenses can detect the attack
Refresh rows A+1 and A-1
Bitflips still may occur due to unknown DRAM-internal row mapping
Physical Row Layout
Row A+1
Row A-1
Victim
Rows
Row A
Many existing solutions rely on this proprietary information
Notes: The second problem is about compatibility with DRAM communication protocols [CLICK]
Let’s recap how we manage memory addresses. We use virtual addresses in the application level [CLICK]
The system software translates them to physical addresses [CLICK]
Which then parsed in the memory controller to identify DRAM bus addresses, such as banks and rows [CLICK]
All these translations are visible within the processor [CLICK]
However, yet another translation is performed within the DRAM chips from processor-visible addresses to physical row addresses [CLICK]
This translation is proprietary information of the DRAM vendors and obfuscated from the processor [CLICK]
When a RowHammer attack hammers a Row A [CLICK]
A defense implemented in the processor can detect this attack [CLICK]
And preventively refresh row addresses A+1 and A-1, which may not correspond to actual victim rows [CLICK]
As a result, bitflips still may occur [CLICK]
Unfortunately, many existing solutions rely on this proprietary information [CLICK]

## Slide 35: BlockHammer
Application
Level
Virtual Memory Address
System
Level
Physical Memory Address
Memory
Controller
DRAM Bus Addresses
(Channel, Rank, Bank, Row…)
Visible within the processor
In-DRAM Mapping
Physical Row Addresses
DRAM chip
Processor-visible
Row Addresses
Proprietary
A RowHammer attack hammers Row A
BlockHammer detects hammered rows using area-efficient Bloom filters
Selectively throttles accesses targeting hammered rows
Row A
Physical Row Layout
Row A+1
Row A-1
Victim
Rows
???
BlockHammer prevents read disturbance bitflips without the knowledge of or modifications to DRAM chip internals
Yağlıkçı, et al., ”BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows" in HPCA, 2021.
Notes: The second problem is about compatibility with DRAM communication protocols [CLICK]
Let’s recap how we manage memory addresses. We use virtual addresses in the application level [CLICK]
The system software translates them to physical addresses [CLICK]
Which then parsed in the memory controller to identify DRAM bus addresses, such as banks and rows [CLICK]
All these translations are visible within the processor [CLICK]
However, yet another translation is performed within the DRAM chips from processor-visible addresses to physical row addresses [CLICK]
This translation is proprietary information of the DRAM vendors and obfuscated from the processor [CLICK]
When a RowHammer attack hammers a Row A [CLICK]
A defense implemented in the processor can detect this attack [CLICK]
And preventively refresh row addresses A+1 and A-1, which may not correspond to actual victim rows [CLICK]
As a result, bitflips still may occur [CLICK]
Unfortunately, many existing solutions rely on this proprietary information [CLICK]

## Slide 36: BlockHammer: Evaluation
Cycle-level simulations using Ramulator and DRAMPower
System Configuration:
Single-Core Benign Workloads:
  22 SPEC CPU 2006
  4 YCSB Disk I/O
  2 Network Accelerator Traces
  2 Bulk Data Copy with Non-Temporal Hint (movnti)
Randomly Chosen Multiprogrammed Workloads:
  125 workloads containing 8 benign applications
  125 workloads containing 7 benign applications and 1 RowHammer attack
Processor | 3.2 GHz, {1,8} core, 4-wide issue, 128-entry instr. window
LLC | 64-byte cache line, 8-way set-associative, {2,16} MB
Memory scheduler | FR-FCFS
Address mapping | Minimalistic Open Pages
DRAM | DDR4 1 channel, 1 rank, 4 bank group, 4 banks per bank group
RowHammer Threshold | 32K  1K
Yağlıkçı, et al., ”BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows" in HPCA, 2021.
Notes: We conduct cycle-level simulations using RAMULATOR and DRAMPOWER to evaluate the performance and DRAM energy consumption.
[CLICK] We simulate a realistic system with a DDR4 DRAM module.
[CLICK] We use single-core workloads from four benchmarks in our simulations.
22 SPEC benchmarks, 4 disk I/O memory access traces from YCSB benchmark suite, 2 memory access traces collected from a network accelerator chip, and 2 synthetic traces that mimic bulk data copy with non-temporal hint.
[CLICK] We randomly combine these workloads to create two types of eight-core multiprogrammed workloads:
[CLICK] workloads that contain eight benign applications
[CLICK] and workloads that contain seven benign applications along with one thread performing RowHammer attack.

## Slide 37: BlockHammer: Evaluation
Cycle-level simulations using Ramulator and DRAMPower
System Configuration:
Single-Core Benign Workloads:
  22 SPEC CPU 2006
  4 YCSB Disk I/O
  2 Network Accelerator Traces
  2 Bulk Data Copy with Non-Temporal Hint (movnti)
Randomly Chosen Multiprogrammed Workloads:
  125 workloads containing 8 benign applications
  125 workloads containing 7 benign applications and 1 RowHammer attack
Processor | 3.2 GHz, {1,8} core, 4-wide issue, 128-entry instr. window
LLC | 64-byte cacheline, 8-way set-associative, {2,16} MB
Memory scheduler | FR-FCFS
Address mapping | Minimalistic Open Pages
DRAM | DDR4 1 channel, 1 rank, 4 bank group, 4 banks per bank group
RowHammer Threshold | 32K
No RowHammer attack: Negligible (<0.6%) performance and energy overheads
RowHammer attack present: Significant improvement on system performance (71%) and energy consumption (32%)
Yağlıkçı, et al., ”BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows" in HPCA, 2021.
Notes: We conduct cycle-level simulations using RAMULATOR and DRAMPOWER to evaluate the performance and DRAM energy consumption.
[CLICK] We simulate a realistic system with a DDR4 DRAM module.
[CLICK] We use single-core workloads from four benchmarks in our simulations.
22 SPEC benchmarks, 4 disk I/O memory access traces from YCSB benchmark suite, 2 memory access traces collected from a network accelerator chip, and 2 synthetic traces that mimic bulk data copy with non-temporal hint.
[CLICK] We randomly combine these workloads to create two types of eight-core multiprogrammed workloads:
[CLICK] workloads that contain eight benign applications
[CLICK] and workloads that contain seven benign applications along with one thread performing RowHammer attack.

## Slide 38: Other Works (Not Covered due to Time Limitation)
MICRO 2022
Leverages inherently-available but not exposed subarray-level parallelism in DRAM
Reduces time spent for refresh by half and improves system performance
DSN 2022
First work to investigate wordline voltage’s effect on RowHammer vulnerability
Reducing wordline voltage reduces RowHammer vulnerability
Worsens data retention time and row activation latency

## Slide 39: More Details and Discussion on YouTube
https://www.youtube.com/live/CRtm1es4n3o?si=8N5zB6e_RUc5Ejl8
https://www.youtube.com/live/YQwRYWpCsk0?si=jXPueMHb5wgs69-q

## Slide 40: Towards Robust and Sustainable Scaling
Pre-PhD Research
  Understanding and reducing memory access latency
  Understanding and reducing memory energy consumption
PhD Research
  Understanding read disturbance failures in main memory
  Mitigating read disturbance failures in main memory
Post-PhD Research
  Improving the availability of data and resources while mitigating read disturbance failures in main memory
Future Research
  Hardware-software co-design
  Data-centric robustness
  Better understanding of hardware failures
  technology node scaling AND scale-out systems

## Slide 41: Meanwhile: RowHammer in Industry Research
JEDEC* formed a RowHammer task force
Manufacturers’ attitude changed: Denial  Solution
An early secure solution emerged from UPMEM
Then Microsoft, SK Hynix, Samsung, NVIDIA
Google hacked Samsung’s solution
*JEDEC: Joint Electron Device Engineering Council
2021
2023
2023
2021
2024
2024

## Slide 42: Meanwhile: RowHammer in Industry Research
https://www.jedec.org/standards-documents/docs/jep300-1
https://www.jedec.org/standards-documents/docs/jep301-1

## Slide 43: Meanwhile: RowHammer in Industry Research
The first promising update
a decade after the discovery of RowHammer
PRAC: Per Row Activation Counting in DRAM

## Slide 44: Understanding Industry’s Solution
PRAC is secure against RowHammer
PRAC increases the latency of closing a DRAM row, causing ~10% performance degradation for benign workloads
PRAC can be exploited by memory performance attacks (up to 94% reduction in DRAM chip’s availability)
presented in DRAMSec 2024 (co-located with ISCA)
https://github.com/CMU-SAFARI/ramulator2
Co-supervised paper

## Slide 45: PRAC: Industry’s Best Solution to RowHammer
Per Row Activation Counting (PRAC) [JEDEC, 2024]
Tracking RowHammer: DRAM chip
  Maintains an activation counter for each DRAM row
  Updates the counter of a row while the row is closed
Mitigating RowHammer: DRAM chip
  Internally performs preventive refreshes
  Needs time to perform preventive refreshes
  Sends a back-off signal to the memory controller to ask for time
  Memory controller provides DRAM chip with time for RowHammer-preventive refreshes
Counter 0
Counter 1
...
Counter 3
Per Row
Activation Counters
back-off
RFM
High Activation
Count Detected
The devil is in this detail
Notes: With PRAC
[CLICK] DRAM maintains an activation counter for each DRAM row
[CLICK] Whenever one of these counters reaches a critical value
For example close to RowHammer threshold
[CLICK] The DRAM module triggers whats called a back-off
[CLICK] After a back-off is received by the memory controller
It stops performing accesses to DRAM
And starts sending special commands that allow time for preventive refreshes
=====
Make the arrow shorter for high activation count
Refreshes should be refresh with subscript ps

## Slide 46: Chronus: Making Industry’s Best Solution Better
Problem: PRAC incurs 10% slowdown (common case)
Key Insight: Closing a row has the added latency of updating the row’s counter because the counter is stored within the row
Key Idea: Update row activation counters in parallel to column accesses by leveraging subarray-level parallelism
Key Result: Chronus significantly reduces PRAC’s performance overhead to 0.04%
101010101010101010101010
0
0
101010101010101010101010
Counters
DRAM Rows
…
…
PRAC increases the latency of closing a DRAM row by 140%
Co-supervised paper

## Slide 47: Chronus’s Key Idea: Concurrent Counter Update
Chronus concurrently updates counters while serving accesses
Counter 0
Counter 2N-1
Counter N+1
Counter N-1
Counter
Subarray
Row Decoder
Regular
Subarray
Row 2N-1
Row N
Row Decoder
Regular
Subarray
Row N-1
Row 0
Row Decoder
Row Buffer
Row Buffer
Row Buffer
Increment
DRAM Bank
Regular
Accesses
Counter
Updates
Subarray
Level
Parallelism
We leverage inherently-available subarray-level parallelism to alleviate PRAC’s performance overhead
Co-supervised paper
Notes: Chronus concurrently updates counters with a small change to the bank
Alongside the regular DRAM subarrays that store data, Chronus adds an additional Counter subarray to store counters
DRAM -> access, Counter -> updates
SALP

## Slide 48: Making Industry’s Best Solution Better
published in HPCA 2025
Oğuzhan Canpolat1,2 A. Giray Yağlıkçı1 Geraldo F. Oliveira1 Ataberk Olgun1
Nisa Bostancı1 İsmail Emir Yüksel1 Haocong Luo1
Oğuz Ergin2,3 Onur Mutlu1
1ETH Zürich 2TOBB University of Economics and Technology 3University of Sharjah
https://github.com/CMU-SAFARI/Chronus
Co-supervised paper

## Slide 49: BreakHammer: Throttling Suspect Threads in Hardware
Memory
Controller
Core
Core
Attacker
User
Detect and slow down the memory accesses of threads
that trigger many RowHammer-preventive actions
Suspect Thread
https://github.com/CMU-SAFARI/BreakHammer
RowHammer-preventive actions
Trace back who triggered
Key Results:
Under attack:
  Significantly improves system performance (by 90% on average)
  Significantly reduces energy consumption (by 55% on average)
No attack:
  Slightly (<1%) improves performance and energy consumption
Co-supervised paper
Notes: BreakHammer’s key idea is to detect and slow down the memory accesses of threads that trigger many RowHammer-preventive actions
[CLICK] We refer to these threads as suspect threads

## Slide 50
https://github.com/CMU-SAFARI/BreakHammer
Co-supervised paper
published in MICRO 2024

## Slide 51: Towards Robust and Sustainable Scaling
Pre-PhD Research
  Understanding and reducing memory access latency
  Understanding and reducing memory energy consumption
PhD Research
  Understanding read disturbance failures in main memory
  Mitigating read disturbance failures in main memory
Post-PhD Research
  Improving the availability of data and resources while mitigating read disturbance failures in main memory
Future Research
  Hardware-software co-design
  Data-centric robustness
  Better understanding of hardware failures
  technology node scaling AND scale-out systems

## Slide 52: Hardware-Software Co-Design for Sustainable Robustness
CPU scheduling
Address space
Data sparsity
Error resilience
Data confidentiality requirements
User behaviors
Parent processes
Memory virtualization
Accelerators
Sensors
Counters
Prompt response
Prefetchers
Hyperthreading
Thermal management
Voltage scaling
Accurate measurements
Prompt responses
Co-design can make security low cost
Software
Hardware
Insights into data structures
Software semantics
User / Process / Thread / Address Space
Many opportunities for ensuring security at low cost

## Slide 53: Hardware-Assisted Malware Detection An Example HW-SW Co-Design Direction
Hardware-level sensors and counters can quickly and accurately collect data on application behavior and react in nanoseconds
RowHammer attacks (e.g., BlockHammer [Yaglikci+, HPCA’21])
Performance attacks (e.g., BreakHammer [Canpolat+, MICRO’24])
Timing side channel attacks (e.g., Cyclone [Harris, MICRO’19])
…
Software-level malware detection has a better big picture
Program(s) that spawn those malicious threads
User(s) that run those programs
More constructive reactions (e.g., flag functions and inform programmers)
Key Insight: System-level attacks often try the attack many times
Key Idea: Provide software-level malware detection with hardware-level observations and statistics

## Slide 54: Towards Robust and Sustainable Scaling
Pre-PhD Research
  Understanding and reducing memory access latency
  Understanding and reducing memory energy consumption
PhD Research
  Understanding read disturbance failures in main memory
  Mitigating read disturbance failures in main memory
Post-PhD Research
  Improving the availability of data and resources while mitigating read disturbance failures in main memory
Future Research
  Hardware-software co-design
  Data-centric robustness
  Better understanding of hardware failures
  technology node scaling AND scale-out systems

## Slide 55: Data-Centric Security and Privacy (1/5) Motivation for Sustainable Scaling
A memory access (off-chip data movement) consumes ~100x-1000x the energy of an arithmetic operation
William Dally,
HiPEAC 2015

## Slide 56: Data-Centric Security and Privacy (2/5) High-Level Motivation for Data-Centric S&P
Memory-centric computation
for better performance (-per-Joule and –per-area)
Processing in Memory and Storage
are two promising computation paradigms
More to do for Security in Memory and Storage

## Slide 57: Data-Centric Security and Privacy Problem Definition
Common security practices are processor-centric e.g., Intel SGX and ARM TrustZone
  Moving encrypted data across chips consumes time and energy, increases bus usage, and reduces processor’s and memory’s availability
  Supporting accelerators near memory and storage becomes complicated
Processing in memory and storage can perform
  Encryption
  Isolation
  Access control
  Error correction
  Timing obfuscation
  …
Processing in memory and storage have a lot to offer

## Slide 58: Data-Centric Security and Privacy
Specialized circuitry near data
  Hardware complexity
  Added latency
Computation using homomorphic encryption
  High capacity overhead  Against density scaling
  Increased execution time
MICRO’21
ASPLOS’25
HPCA’25
State-of-the-art is far from a definitive solution

## Slide 59: Security of Data-Centric Computation
Timing side- and covert-channel attacks are easier near/in memory
Less noise
No (or simpler) caches
Finer-grained control
Preprint available on arxiv: https://arxiv.org/pdf/2404.11284
to appear in DSN 2025
Larger channel bandwidth
No low-cost and effective solution yet

## Slide 60: Data-Centric Security and Privacy Workloads of Special Interest
Critical health applications
Agent-based simulations
Genomics
Common characteristics
Excessively large amount of data
Computation in distributed and shared environments
Data integrity is important for correctness
Confidentiality and privacy are first-order concerns
Performance challenges are barely solved so far
Bad news: We are far from ideal
Good news: Lots of research to conduct

## Slide 61: Towards Robust and Sustainable Scaling
Pre-PhD Research
  Understanding and reducing memory access latency
  Understanding and reducing memory energy consumption
PhD Research
  Understanding read disturbance failures in main memory
  Mitigating read disturbance failures in main memory
Post-PhD Research
  Improving the availability of data and resources while mitigating read disturbance failures in main memory
Future Research
  Hardware-software co-design
  Data-centric robustness
  Better understanding of hardware failures
  technology node scaling AND scale-out systems

## Slide 62: Better Understanding of Failure Mechanisms
A generic question: what is the worst-case for a given system?
Failure mechanisms depend on many conditions and can be observed somewhat probabilistically
Post-manufacturing testing cannot cover all conditions practically
Better methodologies and infrastructures are needed
Testing is costly
  the chip cannot be used while testing
  you need to buy chips to test
We need to revolutionize testing and data collection with
  Online testing methodologies: test a chip in runtime when it is idle
  Automated reverse-engineering tools
  Crowdsource data collection for scaling up sample sets

## Slide 63: Some Good Examples of Testing Infrastructures
DRAM Bender
Revizor
We need plug-and-play runtime testing tools
Examples of offline testing tools

## Slide 64
Systems should scale
robustly and sustainably
as chips get denser
and many users share systems

## Slide 65: Scaling Systems Robustly and Sustainably Outstanding Challenges and Research Perspective
Abdullah Giray Yağlıkçı
Helmholtz Center for Information Security
March 25, 2025
Notes: Hi, my name is Giray and today I will give a high-level overview of my PhD research and future research plans

## Slide 66: Scaling Systems Robustly and Sustainably Outstanding Challenges and Research Perspective
Abdullah Giray Yağlıkçı
Helmholz Center for Information Security
March 25, 2025
Backup Slides
Notes: Hi, my name is Giray and today I will give a high-level overview of my PhD research and future research plans

## Slide 67: Brief Self Introduction
Researcher
  SAFARI Research Group
    ETH Zurich (Feb 2018 – ongoing)
    Intel Labs (Aug 2017 – Feb 2018)
    Carnegie Mellon University (Aug 2016 – Aug 2017)
  Earlier:
    Univ. of Notre Dame, IN, USA (Aug 2014-Aug 2016)
    TOBB Univ., Ankara, Turkey (Aug 2011-Aug 2014)
Research interests:
  Computer architecture
  Memory and storage systems
  Hardware security, safety, reliability, performance, availability, fairness, energy efficiency
  Hardware/software cooperation
  Memory-centric security
  Testing and verification
  …
https://agyaglikci.github.io
agirayyaglikci@gmail.com
Abdullah Giray Yaglikci Postdoc. Researcher and Lecturer
ETH Zurich
PhD: ETH Zurich, 2024

## Slide 68: Memory Organization
DRAM Chip
Bank
Chip I/O
DRAM Bank
Subarray
. . .
DRAM Subarray
Row Buffer
Bitline
…
…
Wordline
…
…
…
…
DRAM Cell
DRAM Row
Prevalent memory technology: Dynamic Random Access Memory (DRAM)
DRAM
Module
Notes: This is a DRAM module, used as the main memory on many systems. [CLICK]
A DRAM module consists of multiple chips each of which contains multiple banks [CLICK]
Each bank is composed of multiple subarrays [CLICK]
And within each subarray, there is a two dimensional array of DRAM cells. [CLICK]
These cells are organized into rows that are selected using wordlines [CLICK]
And the cells are connected to a row buffer via bitlines [CLICK]

## Slide 69: DRAM Operation
DRAM Subarray
Bitline
…
…
Wordline
…
…
…
…
DRAM Cell
DRAM Cell
Row Buffer
Row Activation: Fetch the row’s content into the row buffer
Column Access: Read/Write a column in the row buffer
Precharge: Disconnect the row from the row buffer
Wordline
Capacitor
Access transistor
Bitline
charge
leakage
paths
Refresh: Restores the capacitor voltage with a time period called refresh window
I/O Circuitry
Prevalent memory technology: Dynamic Random Access Memory (DRAM)
Notes: This is a simplified diagram of a DRAM cell, where the data is stored as capacitor voltage and accessed through the access transistor [CLICK]
A DRAM cell inherently exhibits several charge leakage paths [CLICK]
And requires to perform refresh operations to restore the capacitor voltage with a time period called refresh window.
[PAUSE]
To access a DRAM cell, [CLICK]
the memory controller must first open or activate the row to fetch the row’s data into the row buffer [CLICK]
The READ and WRITE requests targeting the row are serviced from the row buffer [CLICK]
After all requests are serviced from the row, the memory controller must close or precharge the row in order to begin accessing data from another row. [CLICK]

## Slide 70: Major Contributions
To efficiently and scalably mitigate DRAM read disturbance, we
build a detailed understanding of DRAM read disturbance
leverage insights into modern DRAM chips and memory controllers
devise a novel solution that do not require proprietary knowledge of DRAM chip internals
MICRO’21
DSN’22
HPCA’24
HPCA’21
MICRO’22
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
Svärd: Leveraging heterogeneity
HiRA: Parallelizing preventive actions
BlockHammer: Selectively throttling unsafe accesses
1
2
3
Notes: To address these two problems, we conducted several studies encompassed in this thesis statement [CLICK]
We can mitigate DRAM read disturbance efficiently and scalably from three aspects [CLICK]
First, by building a detailed understanding of DRAM read disturbance [CLICK],
Which we explore for temperature [CLICK],
Memory access patterns [CLICK],
Victim cell’s physical location [CLICK],
And voltage [CLICK]
Second, by leveraging insights into modern DRAM chips and memory controllers [CLICK],
Where we leverage the heterogeneity in DRAM cells’ vulnerability levels [CLICK]
and parallelize preventive actions [CLICK]
Third, by devising novel solutions that do not require proprietary knowledge of DRAM chip internals[CLICK],
Which we achieve by selectively throttling unsafe accesses [CLICK]

## Slide 71: RowHammer under Reduced Refresh Latency
published in HPCA 2025
https://github.com/CMU-SAFARI/PaCRAM
PaCRAM: Partial Charge Restoration for Aggressive Mitigation
Reduces the latency of RowHammer-preventive refreshes
Performs preventive refreshes slightly more frequently
Improves system performance and energy efficiency
Near-zero hardware complexity
Experimental data out of 388 DDR4 DRAM chips from 3 major vendors
RowHammer-preventive refresh latency can be significantly reduced without jeopardizing the DRAM chip’s data integrity
Co-supervised paper
Notes: In summary,
[CLICK] The three major DRAM maintenance operations are refresh, RowHammer protection, and memory scrubbing.
[CLICK] We observe that implementing new and efficient maintenance mechanisms often requires difficult-to-realize changes in various system components, including the DRAM interface and the memory controller.
[CLICK] In this work, our goal is to first, ease the process of enabling new DRAM maintenance operations in DRAM and
[CLICK] enable more efficient in-DRAM maintenance operations
[CLICK] To this end, we propose Self-Managing DRAM (or SMD for short), which enables implementing new in-DRAM maintenance mechanisms with no further changes in the DRAM interface and the memory controller
[CLICK] According to our evaluations, SMD-based maintenance mechanisms achieve significant performance and energy efficiency benefits across many system configurations and workloads.
[CLICK] We release the source code of SMD on github.

## Slide 72: A Deeper Look into RowHammer’s Sensitivities Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses
Lois Orosa Abdullah Giray Yağlıkçı
Haocong Luo Ataberk Olgun Jisung Park
Hasan Hassan Minesh Patel Jeremie S. Kim Onur Mutlu
Notes: Hello, I am Giray,
and I will be presenting our work
A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses

## Slide 73: Impact of Temperature on DRAM Cells
Lower Bound (°C)
Upper Bound (°C)
Fraction of Vulnerable DRAM Cells
Different DRAM cells are vulnerable to RowHammer within specific temperature ranges
Vulnerable from 70°C to 85 ° C
Vulnerable
from 55°C to 60°C
Notes: This figure shows the population density of cells, clustered based on their vulnerable temperature range. The x-axis and y-axis show the lower bound [CLICK] and the upper bound [CLICK] of a DRAM cell’s vulnerable temperature range [CLICK]
The color-scale and the percentage values show the fraction of cells for a given temperature range [CLICK]
For example, 0.4% of the cells are vulnerable to RowHammer only between 55 and 60 degrees Celsius [CLICK],
while 0.5% of the cells experience bit flips only between 70 and 85 degrees Celsius [CLICK]
We conclude that different DRAM cells are vulnerable to RowHammer within specific temperature ranges [CLICK]

## Slide 74: Impact of Temperature on DRAM Cells
Lower Bound (°C)
Upper Bound (°C)
29.8% of the cells experience bit flips at all tested temperatures
OBSERVATION 2
A significant fraction of vulnerable DRAM cells exhibit bit flips at all tested temperatures
Notes: Here are the results for all four manufacturers.
We make two observations from this figure. [CLICK]
First, we observe that a significant fraction of vulnerable DRAM cells exhibit bit flips at all tested temperatures For example, almost 30% of cells from manufacturer D experience bit flips at all temperatures we tested, [CLICK]

## Slide 75: Impact of Temperature on DRAM Cells
0.2% of the cells experience bit flips only at 70°C
Lower Bound (°C)
Upper Bound (°C)
OBSERVATION 3
A small fraction of all vulnerable DRAM cells are vulnerable to RowHammer only in a very narrow temperature range
Notes: Second, we observe that [CLICK]
a small fraction of the cells from all four manufacturers are vulnerable to RowHammer only in a very narrow temperature range. [CLICK]
For example, 0.2% of the cells from manufacturer D experience bit flips only at 70C. [CLICK]

## Slide 76: Impact of Temperature on DRAM Rows
Temperature (°C)
Variation in
Bit Flip Counts
per DRAM Row
More cells experience bit flips as temperature increases
Notes: Next, we study the impact of temperature on DRAM rows. The figure shows how the number of bit flips in the victim row changes as temperature increases.[CLICK]
The x-axis shows the increasing temperature [CLICK] and y-axis reports the variation in bit flip counts normalized to the mean value at 50°C. [CLICK]
We observe that more cells experience a bit flip with increasing temperature, [CLICK]

## Slide 77: Impact of Temperature on DRAM Rows
Temperature (°C)
Variation in Bit Flip Counts per DRAM Row
OBSERVATION 4
A DRAM row’s bit error rate can either increase or decrease with temperature depending on the DRAM manufacturer
Notes: We repeat this analysis for all four manufacturers [CLICK]
We observe that the bit error rate increases with temperature in modules from three manufacturers, [CLICK]
While it exhibits an opposite trend in modules from manufacturer B. We hypothesize that this happens due to different characteristics of charge trap error mechanisms in different manufacturers. Please refer to our full paper for more details [CLICK]
Our main observation from this figure is that A DRAM row’s BER can either increase or decrease with temperature depending on the DRAM manufacturer [CLICK]

## Slide 78: Memory Access Patterns in Aggressor Row Active Time Analysis
Baseline access pattern:
Increasing aggressor row active time:
Increasing bank precharged time:
Time
Row A is active
Row B is active
Row A is active
Row B is active
Time
Row A is active
Time
Row A is active
Row B is active
Row A is active
Row B is active
Row A is active
Aggressor row active time
Bank precharged time
Aggressor row active time
Aggressor row active time
Bank precharged time
Bank precharged time
Notes: To perform this analysis, we conduct two sets of experiments [CLICK]
In the baseline, we hammer rows A and B as frequently as possible [CLICK]
In the first set of tests, we increase the time that an aggressor row is active [CLICK],
And in the second set of experiments we increase the time that the bank is precharged [CLICK]

## Slide 79: Increasing Aggressor Row Active Time
Aggressor Row Active Time (ns)
Number of Bit Flips
per DRAM Row
As the aggressor row stays active longer, more DRAM cells experience RowHammer bit flips
Notes: This plot demonstrates how [CLICK]
bit error rate varies [CLICK]
when aggressor row active time increases [CLICK]
We observe that: As the aggressor row stays active longer, more DRAM cells experience RowHammer bit flips [CLICK]

## Slide 80: Increasing Aggressor Row Active Time
Aggressor Row Active Time (ns)
Number of Bit Flips
per DRAM Row
As the aggressor row stays active longer, more DRAM cells experience RowHammer bit flips
Notes: We observe the same trend on modules from all four manufacturers [CLICK]

## Slide 81: Increasing Aggressor Row Active Time
Aggressor Row Active Time (ns)
Minimum Activation Count
to Observe a Bit Flip (HCfirst)
Fewer activations are required to cause RowHammer bit flips when aggressor rows stay active for longer time
Notes: In this plot, we investigate the variation in Hcfirst, [CLICK]
the minimum activation count to observe a bit flip [CLICK]
With increasing aggressor row active time [CLICK]
We observe that DRAM cells experience bit flips at smaller activation counts when aggressor rows stay active longer [CLICK]

## Slide 82: Increasing Aggressor Row Active Time
Aggressor Row Active Time (ns)
Minimum Activation Count
to Observe a Bit Flip (HCfirst)
OBSERVATION 8
As the aggressor row stays active longer, more DRAM cells experience RowHammer bit flips and they experience RowHammer bit flips at lower activation counts
Notes: We observe the same trend on modules from all four manufacturers [CLICK]
Based on our observations on the bit error rate and Hcfirst, we conclude that: as the aggressor row stays active longer, more DRAM cells experience RowHammer bit flips AND they experience RowHammer bit flips at lower activation counts [CLICK]

## Slide 83: RowPress vs. RowHammer
Instead of using a high activation count,
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
We observe bitflips even with ONLY ONE activation in extreme cases where the row stays open for 30ms
36ns, 47K activations to induce bitflips
7.8µs, only 5K activations to induce bitflips
☞ increase the time that the aggressor row stays open
Notes: Instead of a high activation count, RowPress increases the time the that aggressor stays open.
Doing disturbs adjacent rows enough to cause bitflips without a very high activation count.
We observe bitflips even with only one activation in extreme cases.

## Slide 84: Spatial Variation across Rows
DRAM Rows (sorted by reducing HCfirst)
The minimum activation count to observe bit flips (HCfirst) across DRAM rows:
Minimum Activation Count
to Observe a Bit Flip (HCfirst)
The RowHammer vulnerability
significantly varies across DRAM rows
Notes: To do this analysis, we first investigate how Hcfirst, [CLICK]
the minimum activation count to observe bit flips, varies [CLICK]
across different DRAM rows sorted by reducing Hcfirst value on the x-axis.
Each curve in this plot represents a different DRAM module [CLICK]
We observe that Hcfirst values and thus the RowHammer vulnerability significantly varies across DRAM rows, as we highlight [CLICK]

## Slide 85: Spatial Variation across Rows
Min. Activation Count
to Observe a Bit Flip (HCfirst)
DRAM Rows (sorted by reducing HCfirst)
The RowHammer vulnerability
significantly varies across DRAM rows
Notes: This significant variation can be observed on modules from all four manufacturers

## Slide 86: Spatial Variation across Rows
Minimum Activation Count
to Observe a Bit Flip (HCfirst)
DRAM Rows (sorted by reducing HCfirst)
OBSERVATION 12
A small fraction of DRAM rows are significantly more vulnerable to RowHammer than the vast majority of the rows
Notes: Zooming into the most vulnerable DRAM rows, [CLICK]
We observe that the most vulnerable 10% of the rows experience bit flips at activation counts about half the Hcfirst of the other rows [CLICK]
Therefore, we conclude that a small fraction of DRAM rows are significantly more vulnerable to RowHammer than the vast majority of the rows [CLICK]

## Slide 87: Spatial Variation across Columns
Column Index
Chip ID
Number of Bit Flips in a Column
OBSERVATION 13
Certain columns are significantly more vulnerable
to RowHammer than other columns
Notes: To investigate how the RowHammer vulnerability varies across columns, we generate a heatmap plot of [CLICK]
bit error rates [CLICK]
across columns [CLICK]
and chips [CLICK]
We observe that bit errors concentrate on certain DRAM columns more than others, implying that certain columns are significantly more vulnerable to RowHammer than other columns [CLICK]

## Slide 88: Spatial Variation across Columns
Worse RowHammer Vulnerability
Larger Variation across DRAM Chips
16.7%
30.6%
High RowHammer vulnerability across all chips
High variation in vulnerability across chips
 manufacturing-process-induced variation
design-induced variation
0.0 0.2 0.4 0.6 0.8 1.0
1.0
0.5
0.0
Notes: To further investigate the variation across columns and chips, we cluster each DRAM column based on [CLICK]
its RowHammer vulnerability on average across DRAM chips [CLICK]
and the variation in its vulnerability across DRAM chips
This plot shows the population density of DRAM columns exhibiting a level of RowHammer vulnerability and variation across chips
For example, [CLICK] 16.7% of DRAM columns exhibit a high RowHammer vulnerability across all chips, indicating design-induced variation across columns [CLICK]
In contrast, 30.6% of DRAM columns exhibit a high variation in their RowHammer vulnerability across chips, indicating manufacturing-process-induced variation [CLICK]

## Slide 89: Spatial Variation across Columns
16.7%
50.8%
59.8%
30.6%
29.1%
OBSERVATION 14
Both manufacturing process and design
affect a DRAM column’s RowHammer vulnerability
Worse RowHammer Vulnerability
Larger Variation across DRAM Chips
Notes: Here we see the same analysis for four manufacturers [CLICK]
We observe that there exist columns with very low or very high variation across chips from all four manufacturers [CLICK]
Based on this analysis, we conclude that both manufacturing process and design affect a DRAM column’s RowHammer vulnerability [CLICK]

## Slide 90: Attack Improvement 1: Making DRAM Cells More Vulnerable
An attacker can manipulate temperature to make the cells that store sensitive data more vulnerable
Vulnerable Temperature Range
Temperature
no bit flips
no bit flips
45°C
55°C
65°C
75°C
50°C
70°C
DRAM cells are vulnerable in a bounded temperature range
Heating up chip temperature
Cooling down chip temperature
Notes: In the first example for an attack improvement, the attacker manipulates the DRAM module’s temperature to increase the RowHammer vulnerability of the cells that store sensitive data [CLICK]
We observe that DRAM cells are vulnerable to RowHammer in a bounded temperature range [CLICK]
that we call vulnerable temperature range [CLICK]
For example, let this range be from 50 to 70 degrees celsius for the victim cells
To attack the cells within their vulnerable temperature range, an attacker can [CLICK]
heat up the chip if its current temperature is below 50 [CLICK]
Or cool down the chip if its current temperature is above 70 degrees celsius [CLICK]

## Slide 91
  Identify abnormal increase in temperature to attack a data center during its peak hours
  Precisely measure the temperature to trigger an attack exactly at the desired temperature
Temperature
70 °C
76.6%
of the cells*
*Example fraction values from Mfr. C
0.4%
of the cells*
Temperature
70 °C
Temperature
70 °C
0.4%
of the cells*
1.
2.
Attack Improvement 2: Temperature-Dependent Trigger
Notes: In the second attack example, the attacker uses RowHammer to understand the DRAM chip’s current temperature [CLICK]
As an example, more than 76% of the vulnerable cells experience bit flips above 70 degrees Celsius for Mfr C. Focusing on these cells, an attacker can identify abnormal operating conditions that might occur in a data center during its peak hours. This information can be used to trigger an attack when the data center is under pressure[CLICK]
If it is important to measure temperature precisely, the attacker can focus on a smaller set of vulnerable cells that experience bit flips only in a narrow temperature range. For example, 0.4% of vulnerable cells experience bit flips only at 70 degrees Celsius in Mfr C. Using these cells, the attacker can precisely detect the temperature and trigger an attack accordingly [CLICK]

## Slide 92
Reduces the minimum activation count to induce a bit flip by 36%
Bypasses defenses that do not account for this reduction
Time
Row A is active
Row B is active
Row A is active
Activating aggressor rows as frequently as possible:
Time
Row A is active
Row B is active
Keeping the aggressor rows active for a longer time:
36% reduction in HCfirst
Attack Improvement 3: Bypassing Defenses with Aggressor Row Active Time
Notes: In the third example, an attacker can leverage the effect of aggressor row active time [CLICK]
In this scenario, instead of activating aggressor rows as frequently as possible, [CLICK]
the attacker can keep the aggressor rows active for longer time [CLICK]
Based on our analyses, HCfirst reduces by 36% on average with the proposed access pattern
With this reduction, an attacker can bypass RowHammer defenses that do not account for this reduction [CLICK]

## Slide 93: Defense Improvements
Example 1: Leveraging the variation across DRAM rows
Example 2: Leveraging the variation with temperature
  A DRAM cell experiences bit flips within a bounded temperature range
  A row can be disabled within the row’s vulnerable temperature range
Vulnerable Temperature Range
Temperature
no bit flips
no bit flips
Disable RowA
Temperature
Disable RowB
80% area reduction for Graphene [Park+, MICRO'20]
33% area reduction for BlockHammer [Yağlıkçı+, HPCA'21]
90%
10%
Breakdown of DRAM Rows
HCfirst
HCfirst
Aggressiveness can be reduced:
Notes: I will also explain two improvements for defense mechanisms in this slide, but you can find more in the paper [CLICK]
The first improvement leverages the variation across rows [CLICK]
We observe that 90% of the rows do not experience bit flips until the activation count reaches the double Hcfirst of the 10% of the rows.[CLICK]
Therefore, we can reduce the aggressiveness of defense mechanisms for 90% of the rows, which can reduce the area overheads of state-of-the-art defense mechanisms: [CLICK] BlockHammer and [CLICK] Graphene, by 33 and 80%, respectively [CLICK]
The second example leverages the variation in RowHammer vulnerability with temperature [CLICK]
We show that DRAM cells experience bit flips in bounded temperature ranges [CLICK]
To avoid bit flips, A DRAM row can be disabled when its cells are vulnerable to RowHammer at the current operating temperature [CLICK]

## Slide 94: More Defense Implications in the Paper
Leveraging the similarity across subarrays in a DRAM module can reduce the module’s profiling time for RowHammer errors
Monitoring and limiting the aggressor row active time from the memory controller can reduce the RowHammer vulnerability and make defenses more efficient
ECC schemes can target the non-uniform bit error distribution caused by design-induced variation across DRAM columns
Cooling DRAM chips can reduce overall bit error rate
Notes: We propose more defense improvements in the paper that I will briefly mention in this slide [CLICK]
First, Leveraging the similarity across subarrays in a DRAM module can reduce the module’s profiling time for RowHammer errors
Second, Monitoring and limiting the aggressor row active time from the memory controller can reduce the RowHammer vulnerability and make defenses more efficient
Third, ECC schemes can target the non-uniform bit error distribution caused by design-induced variation across DRAM columns
Fourth, Cooling DRAM chips can reduce overall bit error rate

## Slide 95: Distribution of the Change in HCfirst
Percentage Change in
Minimum Activation Count
to Observe a Bit Flip (HCfirst)
Rows Ordered by HCFirst change
More Vulnerable
Less Vulnerable
Notes: This figure shows the distribution of the change in HCfirst, which is the minimum activation count to observe a bit flip. The purple line indicates how HCfirst changes when changing the temperature from 50 to 55 celsius degrees, and the orange line indicates how HCfirst changes when the temperature increases from 50 to 90 Celsius degrees [CLICK]
The y-axis shows the percentage change in in HCfirst. Positive percentage changes indicate that the cell is less vulnerable to RowHammer when the temperature increases, and a negative percentage change indicates that the cell is more vulnerable when the temperature increases [CLICK]
The x-axis shows the vulnerable cells ordered from most positive to most negative temperature change [CLICK]
For each curve, we mark the x- axis point at which the curve crosses the y = 0% line. This represents the percentile of rows whose vulnerability decreases [CLICK]

## Slide 96: Distribution of the Change in HCfirst
OBSERVATION 5
DRAM rows can show either higher or lower HCfirst
when temperature increases
Notes: Here are the results for all four manufacturers.
We make three observations from this figure. [CLICK]
First, we observe that a DRAM rows can show either higher or lower HCfirst when temperature increases [CLICK]
For example, in manufacturer C, some DRAM cells show higher HCfirst, and other show lower HCfirst [CLICK]

## Slide 97: Distribution of the Change in HCfirst
OBSERVATION 6
HCfirst tends to generally decrease
as temperature change (ΔT) increases
Notes: Second, [CLICK]
We observe that HCfirst tends to generally decrease as temperature change (ΔT) increases [CLICK]
The figure shows that, for all manufacturer, the percentage of cells that are more vulnerable to RowHammer increases, when comparing the temperature change from 50 to 55C to the temperature change from 50 to 90C [CLICK]

## Slide 98: Distribution of the Change in HCfirst
OBSERVATION 7
The HCfirst change (ΔHCfirst) tends to be larger
as temperature change (ΔT) increases
Notes: And third, [CLICK]
We observe thatThe HCfirst change tends to be larger as temperature change increases [CLICK]
The figure shows that, for all manufacturer, when increase the temperature change from 50-55C to 50-90C, the absolute changes values increase [CLICK]

## Slide 99: Circuit-Level Justification Temperature Analysis
We hypothesize that our observations are caused by the non-monotonic behavior of charge trapping characteristics of DRAM cells
3D TCAD model [Yang+, EDL'19]
HCfirst decreases as temperature increases, until a temperature inflection point where HCfirst starts to increase as temperature increases
A cell is more vulnerable to RowHammer at temperatures close to its temperature inflection point
Notes: And third, [CLICK]
We observe thatThe HCfirst change tends to be larger as temperature change increases [CLICK]
The figure shows that, for all manufacturer, when increase the temperature change from 50-55C to 50-90C, the absolute changes values increase [CLICK]

## Slide 100: Increasing Aggressor Row Active Time (tAggOn)
Bit Error Rate
HCfirst
** Please refer to the full paper for coefficient of variation-based (CV) analysis
*
We analyze how the coefficient of variation* values for BER and HCfirst change across rows when the aggressor row stays active longer
OBSERVATION 8
As the aggressor row stays active longer,
more DRAM cells experience RowHammer bit flips and
they experience RowHammer bit flips at lower hammer counts
OBSERVATION 9
RowHammer vulnerability consistently worsens
as tAggOn increases across all tested DRAM rows**
Notes: These plots demonstrate how bit error rate [CLICK]
And Hcfirst changes with increasing aggressor row active time for all four manufacturers [CLICK]
We observe a significant increase in bit error rates [CLICK]
And a significant decrease in Hcfirst with the increasing aggressor row active time [CLICK]
Therefore, we conclude that: As the aggressor row stays active longer, more DRAM cells experience RowHammer bit flips AND they experience RowHammer bit flips at lower hammer counts [CLICK]
We also analyze the relative standard deviation (or coefficient of variation) of both metrics with increasing active time in the paper [CLICK] and conclude that RowHammer vulnerability consistently worsens as the aggressor row active time increases across all DRAM rows we tested [CLICK]
Jeremie's method of explaining on one figure and showing all in the next slide
one observation per slide
write hcfirst openly
just flash hcfirst

## Slide 101
Bit Error Rate
HCfirst
** Please refer to the full paper for coefficient of variation-based (CV) analysis
*
Increasing Bank Precharged Time (tAggOff)
We repeat the coefficient of variation* analysis for BER and HCfirst change across rows when the bank stays precharged longer
OBSERVATION 10
As the bank stays precharged longer, fewer DRAM cells
experience RowHammer bit flips and they experience RowHammer
bit flips at higher hammer counts
OBSERVATION 11
RowHammer vulnerability consistently reduces
as tAggOff increases across all tested DRAM rows**
Notes: Similarly, these plots demonstrate how bit error rate [CLICK]
And Hcfirst changes with increasing the bank’s precharged time [CLICK]
We observe that bit error rates significantly decrease [CLICK]
And Hcfirst values increase as the bank’s precharged time increases [CLICK]
Therefore, as the bank stays precharged longer, fewer DRAM cells experience RowHammer bit flips and they experience RowHammer bit flips at higher hammer counts [CLICK]
We also analyze the relative standard deviation (or coefficient of variation) of both metrics with increasing the bank's precharged time in the paper [CLICK] and conclude that RowHammer vulnerability consistently reduces as the bank’s precharged time increases [CLICK]
can be more inthe paper slide

## Slide 102: Circuit-Level Justification Aggressor Row Active Time Analysis
Two possible circuit level justifications for RowHammer bit flips:
Electron injection in the victim cell [Walker+, TED'21][Yang+, TDMR'16]
Wordline-to-wordline cross-talk noise between aggressor and victim rows that occurs when the aggressor row is being activated [Ryu+, IEDM'17][Walker+, TED'21]
We hypothesize that increasing the aggressor row’s active time (𝑡𝐴𝑔𝑔𝑂𝑛) has a larger impact on exacerbating electron injection to the victim cell, compared to the reduction in cross-talk noise due to lower activation frequency. Thus, RowHammer vulnerability worsens when 𝑡𝐴𝑔𝑔𝑂𝑛 increases
Increasing a bank’s precharged time (𝑡𝐴𝑔𝑔𝑂ff) decreases RowHammer vulnerability because longer 𝑡𝐴𝑔𝑔𝑂ff reduces the effect of cross-talk noise without affecting electron injection (since 𝑡𝐴𝑔𝑔𝑂n is unchanged).
Notes: And third, [CLICK]
We observe thatThe HCfirst change tends to be larger as temperature change increases [CLICK]
The figure shows that, for all manufacturer, when increase the temperature change from 50-55C to 50-90C, the absolute changes values increase [CLICK]

## Slide 103: Spatial Variation across Rows
Minimum Activation Count
to Observe a Bit Flip (HCfirst)
DRAM Rows (sorted by reducing HCfirst)
HCfirst worst-to-best ratio in this range: P100/P90
OBSERVATION 12
A small fraction of DRAM rows
are significantly more vulnerable to RowHammer
than the vast majority of the rows
Hcfirst Worst-to-Best Ratio
Manufacturers
Notes: Zooming into the most vulnerable DRAM rows, We compare the HCfirst of the most vulnerable row [CLICK]
to the minimum HCfirst in 90th percentile of rows [CLICK]
This boxplot shows [CLICK] the distribution of this ratio [CLICK] across DRAM modules for each manufacturer
We observe that the most vulnerable 10% of the rows experience bit flips at activation counts about half the Hcfirst of the other rows [CLICK]
Therefore, we conclude that a small fraction of DRAM rows are significantly more vulnerable to RowHammer than the vast majority of rows [CLICK]

## Slide 104: Spatial Variation across Columns
We analyze BER variation across DRAM columns
OBSERVATION 13
Certain columns are significantly more vulnerable
to RowHammer than other columns
Notes: To investigate how the RowHammer vulnerability varies across columns, we generate a heatmap plot of bit error rates across columns [CLICK] and chips [CLICK]
We observe that bit errors concentrate on certain DRAM columns more than others, implying that certain columns are significantly more vulnerable to RowHammer than other columns [CLICK]
define color scale
remove the first sentence

## Slide 105: Spatial Variation across Subarrays
OBSERVATION 15
The most vulnerable DRAM row in a subarray
is significantly more vulnerable
than the other rows in the subarray
Notes: Next we investigate how the RowHammer vulnerability varies across DRAM subarrays in a DRAM module
Subarrays are marked in terms of the average [CLICK] and the minimum [CLICK] HCfirst values they exhibit across DRAM rows that they contain [CLICK]
We observe that the minimum Hcfirst in a subarray is about the half of the average Hcfirst in a subarray [CLICK]
Therefore, we conclude that The most vulnerable DRAM row in a subarray is significantly more vulnerable than the other rows in the subarray [CLICK]
avoid highlighting the linear regression
slope of the curve is approx .5

## Slide 106: Spatial Variation across Subarrays
* We analyze the similarity between Hcfirst distributions of different subarrays based on Bhattacharyya distance in the paper
OBSERVATION 16
HCfirst distributions of subarrays within a DRAM module
are significantly more similar to each other
than those of subarrays from different modules
Notes: In this plot, each marker style represents subarrays in a different DRAM module [CLICK]
We observe that subarrays within a DRAM module exhibit more similar Hcfirst values to each other, compared to subarrays in different DRAM modules [CLICK]
and we verify this observation based on Bhattacharyya distance analysis in the paper [CLICK]

## Slide 107: Spatial Variation across Subarrays Bhattacharyya Distance Analysis
HCfirst distributions of subarrays within a DRAM module exhibit significantly more similarity to each other
than HCfirst distributions of subarrays from different modules
Identical
Different
Different
Notes: To investigate these similarities more, we compare the similarity of HCfirst distributions between subarrays from the same module [CLICK]
And from different modules [CLICK]
This plot shows the cumulative distribution of this similarity in terms of normalized Bhattacharyya distance (BD)
A normalized BD of 1.0 [CLICK]
indicates that two distributions are identical, while [CLICK]
two distributions exhibit more difference as the normalized BD takes larger or smaller values than 1.0 [CLICK]
Especially in manufacturers B and C, we observe a significant difference between normaized BD values of subarray within the same module and subarrays in different modules [CLICK]
Therefore, we conclude that HCfirst distributions of subarrays within a DRAM module exhibit significantly more similarity to each other than HCfirst distributions of subarrays from different modules

## Slide 108: Circuit-Level Justification Spatial Variation Analysis
Variation across rows, columns, and chips:
Manufacturing process variation causes differences in cell size and bitline/wordline impedance values, which introduces variation in cell reliability characteristics within and across DRAM chips
Design-induced variation causes cell access latency characteristics to vary deterministically based on a cell’s physical location in the memory chip (e.g., its proximity to I/O circuitry)
Similarity across subarrays:
Cell’s access latency is dominated by its physical distance from the peripheral structures (e.g., local senseamplifiers and wordline drivers) within the subarray, causing corresponding cells in different subarrays to exhibit similar access latency characteristics
Notes: And third, [CLICK]
We observe thatThe HCfirst change tends to be larger as temperature change increases [CLICK]
The figure shows that, for all manufacturer, when increase the temperature change from 50-55C to 50-90C, the absolute changes values increase [CLICK]

## Slide 109: Example Attack Improvements
The attacker can reduce HCfirst (by 36%) by performing (10-15) additional READ commands targeting the aggressor row to bypass RowHammer defenses that do not account for this reduction
Aggressor Row Active Time
These observations can be leveraged
to craft more effective RowHammer attacks
Notes: As another improvement, an attacker can leverage the observation that increasing aggressor row's active time reduces HCfirst [CLICK]
The attacker can exploit this observation to reduce Hcfirst by 36% on average, by performing [CLICK]
10 to 15 additional column accesses to an aggressor row, [CLICK]
This way, an attacker can bypass RowHammer defenses that do not account for this reduction in Hcfirst [CLICK]
We believe that these observations can be leveraged to craft more effective RowHammer attacks [CLICK]
HCfirst is cut
what do arrows mean?
avoid using hcfirst
draw the attack pattern and emphasize bypassing

## Slide 110: Example Attack Improvements
Example 1: Temperature-dependent trigger
  An attacker can measure DRAM chip’s current temperature
    To identify when the DRAM chip is at a certain temperature
      To precisely measure temperature for covert channels
    To identify abnormal operating conditions (e.g., warmer than usual)
      To attack a data center during its peak hours
      To spy on an end-user’s behavioral patterns
Example 2: Manipulating temperature to make chips more vulnerable
  An attacker can heat up or cool down a DRAM chip to a temperature level where the victim cells are vulnerable
Lower Bound (°C)
Upper Bound (°C)
0.4% of DRAM cells exhibit bit flips only at 70°C
76.6% of DRAM cells exhibit bit flips above 70°C
Notes: Using our observations, [CLICK] an attacker can measure a DRAM chip’s current temperature [CLICK]
As an example, 0.4% of DRAM cells are vulnerable to RowHammer only at 70 degree Celsius. Focusing on these cells, an attacker can trigger another attack when the DRAM chip is at this temperature level [CLICK]
As another example, more than 76% of the cells are vulnerable above 70 degrees Celsius. Focusing on these cells, an attacker can identify abnormal operating conditions that might be caused by a data center’s peak hours or an end-user’s behavioral changes. [CLICK]
Alternatively, if physical access is possible, the attacker can heat up or cool down a DRAM chip to increase the success probability of the attack [CLICK]

## Slide 111: Understanding RowHammer Under Reduced Wordline Voltage An Experimental Study Using Real DRAM Devices
Abdullah Giray Yağlıkçı
Haocong Luo Geraldo F. de Oliviera Ataberk Olgun
Minesh Patel Jisung Park Hasan Hassan Jeremie S. Kim
Lois Orosa Onur Mutlu
Notes: Hello, I am Giray, and I will present our new paper Understanding RowHammer Under Reduced Wordline Voltage

## Slide 112: A Closer Look into RowHammer
Low Voltage
Victim Row
Bitline
Low Voltage
Victim Row
Aggressor Row
Disturbance
High Voltage
Aggressor Row
Low Voltage
Low Voltage
Victim Row
Victim Row
Low Voltage
time
Agressor Row
Wordline Voltage
Repeatedly toggling
wordline voltage
is the key to inducing RowHammer bit flips
Notes: This cartoon provides a closer look into RowHammer. [CLICK]
Asserting high voltage to a row’s wordline for row activation disturbs nearby rows [CLICK]
Repeating this operation [CLICK] many times [CLICK] exacerbates the leakage in victim rows and leads to bit flips [CLICK]
Therefore, repeatedly toggling wordline voltage is the key to induce RowHammer bit flips [CLICK]

## Slide 113
Our Hypothesis
Reducing wordline voltage
can reduce RowHammer vulnerability
without significantly affecting reliable DRAM operation
time
Wordline
Voltage
Reduction in Disturbance
Aggressor Row
Victim Row
Aggressor Row
Victim Row
Wordline
Bitline
Wordline
Bitline
Weaker Channel in Access Transistor
Strong Channel
Weaker Channel
time
Wordline
Voltage
Notes: In this work, we hypothesize that [CLICK]
Lowering the magnitude of wordline voltage [CLICK]
can reduce RowHammer vulnerability [CLICK]
without significantly affecting reliable DRAM operation [END]

## Slide 114: DRAM Chips Tested
Mfr. | # DIMMs | # Chips | Density | Die | Org. | Date
A (Micron) | 1 4 3 2 | 8 64 24 16 | 4Gb 8Gb 4Gb 4Gb | - B F - | x8 x4 x8 x8 | 48-16 11-19 07-21
B (Samsung) | 2 1 3 1 1 2 | 16 8 24 8 8 16 | 8Gb 8Gb 8Gb 4Gb 4Gb 8Gb | B C D E F | x8 x8 x8 x8 x8 x8 | 52-20 19-19 10-21 08-17 02-21
C (SK Hynix) | 2 3 2 3 | 16 24 16 24 | 16Gb 4Gb 4Gb 8Gb | A B C D | x8 x8 x8 x8 | 51-20 02-21 48-20
272 DDR4 DRAM Chips
3 Major Manufacturers
Notes: In our characterization, [CLICK]
we test 272 real DRAM chips [CLICK]
from three major manufacturers, [CLICK]
that implement different densities, die revisions, and chip organizations[CLICK]

## Slide 115: More Details in the Paper
Mfr. | # DIMMs | # Chips | Density | Die | Org. | Date
A (Micron) | 1 4 3 2 | 8 64 24 16 | 4Gb 8Gb 4Gb 4Gb | - B F - | x8 x4 x8 x8 | 48-16 11-19 07-21
B (Samsung) | 2 1 3 1 1 2 | 16 8 24 8 8 16 | 8Gb 8Gb 8Gb 4Gb 4Gb 8Gb | B C D E F | x8 x8 x8 x8 x8 x8 | 52-20 19-19 10-21 08-17 02-21
C (SK Hynix) | 2 3 2 3 | 16 24 16 24 | 16Gb 4Gb 4Gb 8Gb | A B C D | x8 x8 x8 x8 | 51-20 02-21 48-20
272 DDR4 DRAM Chips
3 Major Manufacturers
Full paper on arXiv: https://arxiv.org/abs/2206.09999
Notes: The full paper provides for more detailed information about both the algorithms for each of our experiments and the chips that we test

## Slide 116: Wordline Voltage’s Effect on RowHammer
Wordline Voltage: VPP (V)
1.2
1.0
0.8
0.6
0.4
0.2
1.5 1.7 1.9 2.1 2.3 2.5
OBSERVATION 1
Fewer DRAM cells experience RowHammer bit flips under reduced wordline voltage
BER reduces as VPP reduces
Bit Error Rate
(Normalized to VPP=2.5V)
Wordline Voltage: VPP (V)
1.2
1.0
0.8
0.6
0.4
0.2
1.5 1.7 1.9 2.1 2.3 2.5
Different DRAM modules
Lower is better
Variation across DRAM rows
Notes: We begin with investigating wordline voltage’s effect on RowHammer bit error rate. This figure shows how [CLICK]
reducing wordline voltage [CLICK]
affects RowHammer bit error rate. Lower bit error rate is better for robustness [CLICK]
In this plot, each curve represents a different DRAM module [CLICK]
And the shade around each curve shows the variation across different DRAM rows [CLICK]
We observe that fewer DRAM cells experience RowHammer bit flips under reduced wordline voltage [CLICK]

## Slide 117: Wordline Voltage’s Effect on RowHammer
Wordline Voltage: VPP (V)
1.5 1.7 1.9 2.1 2.3 2.5
OBSERVATION 2
Reducing wordline voltage can cause more DRAM cells to experience bit flips in a small fraction of rows (15.4%)
Bit error rate increases
Bit Error Rate
(Normalized to VPP=2.5V)
1.2
1.0
0.8
0.6
0.4
0.2
Lower is better
Notes: In contrast to the dominant trend,
we also observe that BER slightly increases for a small fraction of DRAM rows [CLICK]
Therefore, we conclude that reducing wordline voltage can cause more cells to experience bit flips in small fraction of rows [END]

## Slide 118: Wordline Voltage’s Effect on RowHammer
Wordline Voltage: VPP (V)
1.5 1.7 1.9 2.1 2.3 2.5
1.3 1.6 1.9 2.2 2.5
1.5 1.7 1.9 2.1 2.3 2.5
1.2
1.0
0.8
0.6
0.4
0.2
OBSERVATION 1
Fewer DRAM cells experience RowHammer bit flips under reduced wordline voltage
OBSERVATION 2
Reducing wordline voltage can cause more DRAM cells to experience bit flips in a small fraction of rows (15.4%)
3
Bit Error Rate
(Normalized to VPP=2.5V)
Mfr. A
Mfr. B
Mfr. C
Notes: We make these observations for all three manufacturers

## Slide 119: Wordline Voltage’s Effect on RowHammer
Wordline Voltage: VPP (V)
Minimum Activation Count to Induce the First Bit Flip
(Normalized to VPP=2.5V)
2.0
1.8
1.6
1.4
1.2
1.0
0.8
1.5 1.7 1.9 2.1 2.3 2.5
OBSERVATION 4
The first bit flip occurs at higher activation counts
as wordline voltage reduces
Min. activation count
to induce the first bit flip
increases as VPP reduces
Higher is better
Different DRAM modules
Variation across DRAM rows
Minimum Activation Count to Induce the First Bit Flip (Normalized to VPP=2.5V)
2.0
1.8
1.6
1.4
1.2
1.0
0.8
Notes: This figure shows how [CLICK]
reducing wordline voltage [CLICK]
affects the minimum activation count needed to induce a RowHammer bit flip. Higher is better for robustness in this plot [CLICK]
Again, each curve represents a different DRAM module [CLICK]
and the shade around a curve shows the variation across DRAM rows [CLICK]
We observe that a RowHammer bit flip occurs at larger activation counts under reduced wordline voltage [CLICK]

## Slide 120: Wordline Voltage’s Effect on RowHammer
OBSERVATION 5
For a small fraction of rows (14.2%), the first bit flip occurs at a smaller activation count as wordline voltage reduces
Min. activation count
to induce the first bit flip
reduces
Wordline Voltage: VPP (V)
1.5 1.7 1.9 2.1 2.3 2.5
Higher is better
Minimum Activation Count to Induce the First Bit Flip (Normalized to VPP=2.5V)
2.0
1.8
1.6
1.4
1.2
1.0
0.8
Notes: We observe that bit flips can also occur at slightly lower activation counts for a small fraction of DRAM rows [CLICK]
Therefore, we conclude that reducing wordline voltage can worsen RowHammer vulnerability of a small fraction of rows [END]

## Slide 121: Wordline Voltage’s Effect on RowHammer
Wordline Voltage: VPP (V)
1.5 1.7 1.9 2.1 2.3 2.5
1.3 1.6 1.9 2.2 2.5
1.5 1.7 1.9 2.1 2.3 2.5
2.0
1.8
1.6
1.4
1.2
1.0
0.8
OBSERVATION 4
The first bit flip occurs at higher activation counts
as wordline voltage reduces
Minimum Activation Count to Induce the First Bit Flip
(Normalized to VPP=2.5V)
OBSERVATION 5
For a small fraction of rows (14.2%), the first bit flip occurs at a smaller activation count as wordline voltage reduces
Mfr. A
Mfr. B
Mfr. C
Notes: These two observations apply to DRAM chips from all three manufacturers

## Slide 122
Our Hypothesis
Reducing wordline voltage
can reduce RowHammer vulnerability
without significantly affecting reliable DRAM operation
time
Wordline
Voltage
Reduction in Disturbance
Aggressor Row
Victim Row
Aggressor Row
Victim Row
Wordline
Bitline
Wordline
Bitline
Weaker Channel in Access Transistor
Strong Channel
Weaker Channel
time
Wordline
Voltage
Notes: Until this point our we observe that reducing wordline voltage reduces RowHammer vulnerability [CLICK]
However, it can negatively affect DRAM row activation and refresh rate by causing a weaker channel in access transistors [CLICK]

## Slide 123: Wordline Voltage’s Effect on Row Activation Latency
Wordline Voltage: VPP (V)
Row Activation
Latency (tRCD)
25
20
15
10
5
1.5 1.7 1.9 2.1 2.3 2.5
OBSERVATION 7
Row activation latency increases with reduced wordline voltage
208 out of 272 DRAM chips complete row activation before the nominal activation latency
Row activation latency increases as VPP reduces
Nominal activation latency has a significant guardband
Different DRAM modules
Variation across DRAM rows
Notes: We begin with investigating wordline voltage's effect on row activation latency [CLICK]
This figure shows how [CLICK]
reducing wordline voltage [CLICK]
affects the row activation latency[CLICK]
We observe that the row activation latency increases with reduced wordline voltage [CLICK]
However, the nominal activation latency already has a significant guardband, [CLICK]
allowing most DRAM chips to complete row activation before the nominal activation latency [END]

## Slide 124: Wordline Voltage’s Effect on Row Activation Latency
Wordline Voltage: VPP (V)
25
20
15
10
5
OBSERVATION 7
Row activation latency increases with reduced wordline voltage
208 out of 272 DRAM chips complete row activation before the nominal activation latency
1.5 1.7 1.9 2.1 2.3 2.5
1.3 1.6 1.9 2.2 2.5
1.5 1.7 1.9 2.1 2.3 2.5
Row Activation
Latency (tRCD)
Nom. tRCD
Nom. tRCD
Nom. tRCD
Mfr. A
Mfr. B
Mfr. C
Notes: We observe across all three manufacturers that 208 out of 272 DRAM chips work reliably using the nominal activation latency

## Slide 125: Wordline Voltage’s Effect on Row Activation Latency
Wordline Voltage: VPP (V)
25
20
15
10
5
48 DRAM chips from Mfr A. reliably work with a row activation latency of 24 ns
16 DRAM chips from Mfr. B reliably work with a row activation latency of 15 ns
All DRAM chips from Mfr. C reliably work using the nominal latency of 13.5ns
1.5 1.7 1.9 2.1 2.3 2.5
1.3 1.6 1.9 2.2 2.5
1.5 1.7 1.9 2.1 2.3 2.5
Row Activation
Latency (tRCD)
Nom. tRCD
Nom. tRCD
Nom. tRCD
Mfr. A
Mfr. B
Mfr. C
Notes: We have 64 DRAM chips that exhibit erroneous behavior. Among those, 48 from manufacturer A reliably work with a row activation latency of 24ns [CLICK]
the remaining 16 from Mfr B reliably works with a row activation latency of 15ns [CLICK]
All DRAM chips from Mfr C reliably works using the nominal row activation latency [CLICK]

## Slide 126: SPICE Simulation Methodology
Insights into wordline voltage’s affect on DRAM operation
22 nm transistor model
Monte-Carlo analysis with 5% variation and 10K iterations
Chang et al., "Understanding Reduced-Voltage Operation in Modern DRAM Devices: Experimental Characterization, Analysis, and Mechanisms," SIGMETRICS, 2018. [SPICE Model on GitHub]
Notes: To provide more insights into our experimental observations we also conduct SPICE simulations [CLICK]
We use a 22 nm transistor model with the component parameters shown in this table [CLICK]
and we conduct Monte Carlo analysis with 5% variation and 10K iterations to account for manufacturing process variation [CLICK]

## Slide 127: A Closer Look into Row Activation Latency
Row activation completes when the bitline voltage reaches a threshold (VTH)
Reduced wordline voltage leads to a weaker channel in the access transistor
Bitline voltage takes longer to reach VTH
Capacitor
Bitline
Wordline
Access transistor
Weaker
channel
OBSERVATION 8
Row activation latency increases
with reduced wordline voltage
Reducing
Wordline
Voltage
Notes: This is the waveform of the bitline voltage during a row activation. Different colors represent different levels of wordline voltage [CLICK]
Row activation completes when the bitline voltage reaches a threshold value [CLICK]
We observe that the row activation latency increases when wordline voltage is reduced from 2.5V (yellow) to 1.7V (purple) [CLICK]
To show why it happens, here we have a DRAM cell [CLICK]
When we reduce the wordline voltage, the voltage difference between the gate and the source of the access transistor gets lower, potentially leading to a weaker channel [CLICK]
Therefore, the row activation latency increases with reduced wordline voltage [CLICK]

## Slide 128: Variation in Row Activation Latency
When wordline voltage is reduced from 2.5V to 1.9V:
  The worst-case row activation latency is still lower than nominal value
  The guardband reduces from 4.4% to 1.5% as the worst-case latency increases from 12.9ns to 13.3ns
The SPICE simulation results are not identical with real chip observations
because the SPICE model cannot simulate a real DRAM chip’s exact behavior without proprietary design and manufacturing information
Worst case tRCDmin when VPP = 2.5V
Nominal row activation latency
Worst case tRCDmin when VPP = 1.9V
OBSERVATION 9
SPICE simulation results agree with our observations based on experiments on real chips
Notes: This is the probability density function of the row activation latency across different iterations of Monte Carlo analysis in our SPICE simulations. Different wordline voltages are color-coded. [CLICK]
We observe that the worst-case row activation latency is still lower than the nominal activation latency when the wordline voltage is larger than or equal to 1.9V [CLICK]
and voltage scaling reduces the available guardband [CLICK]
We observe that our experimental observations and SPICE simulation results agree with each other [CLICK]

## Slide 129: Wordline Voltage’s Effect on DRAM Refresh
Refresh Window (ms)
Data Retention
Bit Error Rate
0.05
0.04
0.03
0.02
0.01
0
64 256 1K 4K 16K
OBSERVATION 12
More DRAM cells tend to experience data retention bit flips
when wordline voltage is reduced
Data retention BER increases
as wordline voltage reduces
OBSERVATION 13
216 out of 272 DRAM chips reliably operate using nominal refresh rate due to the built-in safety margins (guardbands)
Different colors represent different wordline voltage levels
Notes: Next we investigate how wordline voltage affects DRAM refresh. This figure shows how [CLICK]
Retention bit errors occur for different wordline voltage levels[CLICK]
For different refresh windows [CLICK]
We observe that more DRAM cells tend to experience data retention bit flips when wordline voltage is reduced [CLICK]

## Slide 130: Wordline Voltage’s Effect on DRAM Refresh
OBSERVATION 12
More DRAM cells tend to experience data retention bit flips
when wordline voltage is reduced
OBSERVATION 13
216 out of 272 DRAM chips reliably operate using nominal refresh rate due to the built-in safety margins (guardbands)
Notes: For all three manufacturers, we observe that more DRAM cells tend to experience data retention bit flips under reduced wordline voltage [CLICK]
However, 216 out of 272 tested DRAM chips reliably operate using nominal refresh rate [CLICK]

## Slide 131: Spatial Distribution of Data Retention Bit Flips
There are no 64-bit words with more than one bit flip
A small fraction of DRAM rows contain erroneous words
OBSERVATION 14
Data retention errors can be avoided using single error correcting codes at the smallest refresh window that yields non-zero bit error rate
Fraction of DRAM Rows
Number of 64-bit data words with one bit flip
Notes: Then, we focus on the spatial distribution of data retention bit flips at the SMALLEST refresh window with non-zero bit flips [CLICK]
We first observe that there are no 64-bit data words with more than one bit flip [CLICK]
Therefore, we conclude that data retention errors can be avoided using simple single error correcting codes [CLICK]
Then, we investigate the distribution of these erroneous data words across DRAM rows [CLICK]
The x-axis shows the number of 64-bit data words with one bit flip in a DRAM row [CLICK]
And the y-axis shows the fraction of DRAM rows in log-scale that contain those data words [CLICK]
From this plot, we conclude that only a small fraction of DRAM rows contain erroneous data words [CLICK]

## Slide 132: Spatial Distribution of Data Retention Bit Flips
There are no 64-bit words with more than one bit flip
A small fraction of DRAM rows contain erroneous words
OBSERVATION 15
Only a small fraction (16.4%/5.0%) of DRAM rows have erroneous words at the smallest refresh rate (64ms/128ms) that yields non-zero bit error rate
OBSERVATION 14
Data retention errors can be avoided using single error correcting codes at the smallest refresh window that yields non-zero bit error rate
Notes: We make the same observation for DRAM chips that observe the first data retention bit flips at 64ms and 128ms refresh windows [CLICK]

## Slide 133: Distribution of Bit Flips across DRAM Rows
OBSERVATION 3
BER reduction with reduced wordline voltage varies across different DRAM rows and manufacturers
Across manufacturers
Across rows
Notes: Please refer to the full paper for more information about the distribution of RowHammer bit flips we observe

## Slide 134: Distribution of HCfirst across DRAM Rows
OBSERVATION 3
HCfirst reduction with reduced wordline voltage varies across different DRAM rows and manufacturers
Across manufacturers
Across rows
Notes: Please refer to the full paper for more information about the distribution of RowHammer bit flips we observe

## Slide 135: Wordline Voltage’s Effect on DRAM Refresh
Data Retention Bit Error Rate
Probability Density
0.32
0.24
0.16
0.08
0
0 0.5% 1.0% 1.5%
OBSERVATION 12
More DRAM cells tend to experience data retention bit flips
when wordline voltage is reduced
Notes: This figure shows how [CLICK]
reducing wordline voltage [CLICK]
affects the minimum hammer count needed to induce a RowHammer bit flip [CLICK]
We observe that fewer DRAM cells experience RowHammer bit flips under reduced wordline voltage [CLICK]

## Slide 136: Wordline Voltage’s Effect on DRAM Refresh
OBSERVATION 12
More DRAM cells tend to experience data retention bit flips
when wordline voltage is reduced
Notes: This figure shows how [CLICK]
reducing wordline voltage [CLICK]
affects the minimum hammer count needed to induce a RowHammer bit flip [CLICK]
We observe that fewer DRAM cells experience RowHammer bit flips under reduced wordline voltage [CLICK]

## Slide 137: Charge Restoration Process
OBSERVATION 10
A DRAM cell’s capacitor voltage can saturate at a lower voltage level when wordline voltage is reduced
Notes: You can find these analyses in the full paper

## Slide 138: Also in the Paper
OBSERVATION 11
A DRAM cell’s charge restoration latency (tRASmin) can increase with reduced wordline voltage
Notes: You can find these analyses in the full paper

## Slide 139: DRAM Chips Tested
Notes: Please refer to our full paper for more detailed information about our tested chips

## Slide 140: RowHammer Test

## Slide 141: Row Activation and Refresh Rate Tests

## Slide 142: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray a Ph.D. candidate in SAFARI Resarch Group.
Today, I will present our work Spatial Variation-Aware Read Disturbance Defenses

## Slide 143: Tested DRAM Chips
144 DRAM chips from SK Hynix, Micron, and Samsung
Notes: We test 144 DRAM chips [CLICK]
That implement various densities-die revisions [CLICK]
And chip organizations [CLICK]

## Slide 144: Spatial Variation in the Minimum Hammer Count to Induce the First Bitflip across DRAM Rows
The minimum hammer count to induce the first bitflip
significantly varies across rows in a DRAM bank
Minimum hammer count to induce the first bitflip (HCfirst)
Fraction of DRAM Rows
Variation across banks
Different DRAM modules from Mfr. S
S0
S1
S2
S3
S4
Worst
HCfirst
Notes: And show that there is a large variation in read disturbance across rows

## Slide 145: Spatial Variation in the Minimum Hammer Count to Induce the First Bitflip across DRAM Rows
Minimum hammer count to induce the first bitflip (HCfirst)
Fraction of DRAM Rows
Fraction of DRAM Rows
Fraction of DRAM Rows

## Slide 146: Spatial Variation in the Minimum Hammer Count to Induce the First Bitflip across DRAM Rows
Minimum Hammer Count to Induce the First Bitflip (HCfirst)
The minimum hammer count to induce the first bitflip
significantly varies across rows in a DRAM bank

## Slide 147: More Detailed Information in the Extended Version
https://arxiv.org/pdf/2402.18652.pdf

## Slide 148: Regularity in Spatial Variation of Read Disturbance across DRAM Rows
The minimum hammer count to induce the first bitflip
irregularly varies with respect to row’s location in DRAM bank
The minimum hammer count
to induce the first bitflip (HCfirst)
DRAM Row Address
No visible regularity in HCfirst based on the row’s location
Notes: There are different bins but do not correlate well with the row address

## Slide 149: Regularity in Spatial Variation of Read Disturbance across DRAM Rows
DRAM Row Address
The minimum hammer count
to induce the first bitflip (HCfirst)
No visible regularity in HCfirst based on the row’s location
The minimum hammer count to induce the first bitflip
irregularly varies with respect to row’s location in DRAM bank
Notes: There are different bins but do not correlate well with the row address

## Slide 150: Regularity in Spatial Variation of Read Disturbance across DRAM Rows
DRAM Row Address
The minimum hammer count
to induce the first bitflip (HCfirst)
No visible regularity in HCfirst based on the row’s location
The minimum hammer count to induce the first bitflip
irregularly varies with respect to row’s location in DRAM bank
Notes: There are different bins but do not correlate well with the row address

## Slide 151: Svärd: Spatial Variation-Aware Read Disturbance Defenses
Key Experimental Takeaway: Read disturbance vulnerability varies significantly and irregularly across DRAM rows
Key Idea: Leverage the variation in read disturbance vulnerability across DRAM rows
Svärd: Spatial Variation-Aware DRAM Read Disturbance Defenses Dynamically tunes the aggressiveness of existing solutions to the victim row’s read disturbance vulnerability
Svärd performs fewer preventive actions (e.g., refresh) for rows that are less vulnerable to read disturbance
Svärd is Swedish for sword, a weapon with a long blade for cutting or thrusting [Merriam-Webster]
Svärd significantly reduces the performance overhead of existing solutions
Notes: We leverage this observation [CLICK]
By protecting weak rows more aggressively than strong rows [CLICK]
We do this by dynamically tuning the aggressiveness of defense mechanisms [CLICK]
and we show significant improvement in system performance. [CLICK]

## Slide 152: Svärd: Integration with Existing Read Disturbance Solutions
PARA: Probabilistic Row Activation [Kim+, ISCA’14]
Row
Activation
Random
Number
>
Threshold
Preventively
refresh the victim row
Yes
victim row
Svärd
>
Threshold
Svärd dynamically tunes PARA’s threshold to the victim row’s vulnerability
Svärd works with many read disturbance solutions, including:
BlockHammer [Yaglikci+, HPCA’21]
Hydra [Qureshi+, ISCA’22]
RRS [Saileshwar+, ASPLOS’22]
AQUA [Saxena+, MICRO’22]
Less vulnerable
Higher threshold
More vulnerable
Lower threshold
 Fewer refresh
 More aggressive refresh

## Slide 153: Svärd: Metadata Management
Classifies DRAM rows into several vulnerability bins
Maintains a few (e.g., four) bits per DRAM row
Implemented where the read disturbance solution is
Memory controller-based implementation:
Metadata can be maintained in
  SRAM table in the memory controller
  Data integrity bits in the DRAM chip
  …
In-DRAM implementation:
Metadata can be maintained in
  DRAM rows
  Separate DRAM array
  …

## Slide 154: Performance Evaluation
Cycle-level simulations using Ramulator 2.0 [Luo+, CAL 2023] https://github.com/CMU-SAFARI/ramulator2
System Configuration:
Workloads: 120 different 8-core multiprogrammed workloads from SPEC CPU2006, SPEC CPU2017, TPC, MediaBench, and YCSB benchmark suites
Integrated with AQUA, BlockHammer, PARA, Hydra, and RRS
HCfirst: {4K, 2K, 1K, 512, 256, 128, 64} hammers The minimum hammer count needed to induce the first bitflip
Processor | 3.2 GHz, 8 core, 4-wide issue, 128-entry instr. window
Last-Level Cache | 64-byte cache line, 8-way set-associative, 8 MB
Memory Scheduler | FR-FCFS
Address Mapping | Minimalistic Open Pages
Main Memory | DDR4, 4 bank group, 4 banks per bank group (16 banks per rank)
Notes: We use Ramulator for cycle-level simulations in our performance evaluation [CLICK]
We simulate a realistic system with the shown parameters that I will not explain in detail [CLICK]
We simulate 125 different 8-core multiprogrammed workloads [CLICK]
We sweep DRAM chip capacity from 2Gb to 128Gb [CLICK]
And RowHammer threshold: the minimum number of activations needed to induce the first RowHammer bit flip from 1K to 64 [CLICK]

## Slide 155: Implications on Future Solutions
Reduction in Performance Overhead
Minimum Hammer Count to Induce the First Bitflip
Weighted Speedup
(Norm. to No Mitigation Baseline)
1.95x
Speedup
Chart: 
| 4K | 2K | 1K | 512 | 256 | 128 | 64
No-Svärd | 0.96807 | 0.93819 | 0.88595 | 0.80096 | 0.67494 | 0.51565 | 0.35924
Svärd-H1 | 0.99152 | 0.98255 | 0.96742 | 0.93687 | 0.88376 | 0.79729 | 0.66985
Svärd-M0 | 0.98584 | 0.97286 | 0.94624 | 0.90116 | 0.82393 | 0.70759 | 0.55516
Svärd-S0 | 0.99782 | 0.99574 | 0.99085 | 0.98196 | 0.96583 | 0.93471 | 0.87954
PARA
Evaluated for three different vulnerability profiles gathered from real DRAM modules

## Slide 156: Implications on Future Solutions
Weighted Speedup
(Norm. to No Mitigation Baseline)
Minimum Hammer Count to Induce the First Bitflip

## Slide 157: Implications on Future Solutions
Weighted Speedup
(Norm. to No Mitigation Baseline)
Minimum Hammer Count to Induce the First Bitflip
1.63x Speedup
4.88x Speedup
1.07x Speedup
4.80x Speedup
Svärd significantly reduces the performance overhead of existing solutions

## Slide 158: More in the Paper
Spatial variation in read disturbance bit error rate across rows
Spatial variation of RowPress [Luo+ ISCA23] across DRAM rows
Algorithms and details of our experiments
Reverse-engineering of subarray boundaries
Svärd’s memory controller-based and on-DRAM-die implementations
Hardware complexity analysis
  Chip area cost
    MC-based: 0.027% of a processor die per DRAM bank
    DRAM-based: 0.006% increase the DRAM array (4 bits per row per chip)
  No additional latency overhead
A preliminary analysis of the effect of aging on DRAM read disturbance vulnerability

## Slide 159: Conclusion
The first rigorous experimental study on the spatial variation of DRAM read disturbance across DRAM rows
  144 DDR4 DRAM chips from three major manufacturers
  Characterize all rows in a bank and four banks in a DRAM chip
Svärd: Spatial Variation-Aware Read Disturbance Defenses
  Dynamically tunes a solution’s aggressiveness (e.g., perform more/less refresh) to the victim row’s vulnerability to DRAM read disturbance
  Implemented either in the memory controller or in the DRAM chip
Read disturbance vulnerability varies significantly and irregularly across DRAM rows
Svärd significantly reduces the performance overhead of existing solutions
..

## Slide 160: More in the Paper (2/2): Aging Study
Preliminary data on aging via 68-day of continuous hammering
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
Aging can lead to read disturbance bitflips at smaller hammer counts
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)

## Slide 161: More in the Paper (2/2): Aging Study
Preliminary data on aging via 68-day of continuous hammering
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
Aging can lead to read disturbance bitflips at smaller hammer counts
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
Future work:
rigorous aging characterization
and online profiling of read disturbance vulnerability

## Slide 162: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Hydra’s Performance
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 163: An Outlier Solution: Hydra
Minimum Hammer Count to Induce the First Bitflip
Weighted Speedup
(Norm. to No Mitigation Baseline)
Only 7% Speedup

## Slide 164: Hydra Mitigation Mechanism
Hydra maintains a row activation counter for each DRAM row
Stores these activation counters in the DRAM array
Caches the counters of hot rows in the memory controller
At low HCfirst configurations, many rows are hot
Fetching / evicting counters dominate the performance overhead
Svärd needs further customizations for Hydra
Qureshi et al. "Hydra: Enabling Low-Overhead Mitigation of Row-Hammer at Ultra-Low Thresholds via Hybrid Tracking," in ISCA, 2022.

## Slide 165: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
HCfirst across Rows
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 166: The Minimum Hammer Count to Induce the First Bitflip across DRAM Rows
Relative location of a DRAM row
(0 and 1 are the two edges of a DRAM bank)
No visible regularity in HCfirst based on the row’s location
The minimum hammer count to induce the first bitflip
irregularly varies with respect to row’s location in DRAM bank
The minimum hammer count
to induce the first bitflip (HCfirst) Norm. to the Lowest Hcfirst in the module

## Slide 167: The Minimum Hammer Count to Induce the First Bitflip across DRAM Rows
Relative location of a DRAM row
(0 and 1 are the two edges of a DRAM bank)
No visible regularity in HCfirst based on the row’s location
The minimum hammer count to induce the first bitflip
irregularly varies with respect to row’s location in DRAM bank
The minimum hammer count
to induce the first bitflip (HCfirst) Norm. to the Lowest Hcfirst in the module

## Slide 168: The Minimum Hammer Count to Induce the First Bitflip across DRAM Rows
Relative location of a DRAM row
(0 and 1 are the two edges of a DRAM bank)
No visible regularity in HCfirst based on the row’s location
The minimum hammer count to induce the first bitflip
irregularly varies with respect to row’s location in DRAM bank
The minimum hammer count
to induce the first bitflip (HCfirst) Norm. to the Lowest Hcfirst in the module

## Slide 169: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
BER across Rows
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 170: The Read Disturbance Bit Error Rate across DRAM Rows
Relative location of a DRAM row
(0 and 1 are the two edges of a DRAM bank)
Bit error rate periodically increases and decreases
The variation in read disturbance bit error rate
exhibits a stronger regularity compared to the variation in varies with respect to row’s location in DRAM bank

## Slide 171: The Read Disturbance Bit Error Rate across DRAM Rows
Relative location of a DRAM row
(0 and 1 are the two edges of a DRAM bank)
Bit error rate periodically increases and decreases
The variation in read disturbance bit error rate
exhibits a stronger regularity compared to the variation in varies with respect to row’s location in DRAM bank

## Slide 172: The Read Disturbance Bit Error Rate across DRAM Rows
Relative location of a DRAM row
(0 and 1 are the two edges of a DRAM bank)
Bit error rate periodically increases and decreases
The variation in read disturbance bit error rate
exhibits a stronger regularity compared to the variation in varies with respect to row’s location in DRAM bank

## Slide 173: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Background
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 174: Two Main Types of DRAM Refresh
2
Periodic Refresh: Periodically restores the charge DRAM cells leak over time
1
DRAM Row
Preventive Refresh
Preventive Refresh
RowHammer: Repeatedly accessing a DRAM row can cause bit flips in other physically nearby rows
Preventive Refresh: Mitigates RowHammer by refreshing physically nearby rows of a repeatedly accessed row
Notes: DRAM Refresh is mainly used for two purposes [CLICK]
The first one is called: Periodic Refresh to periodically restore the charge that DRAM cells leak over time [CLICK]
The second one is relevant to a read-disturb error mechanism called RowHammer, where repeatedly accessing a DRAM row can cause bit flips in other physically near by rows [CLICK]
A common method of mitigating RowHammer is refreshing potentially affected rows, called preventive refresh [CLICK]

## Slide 175: Periodic Refresh with Increasing DRAM Chip Density
A larger capacity chip has more rows to be refreshed
A smaller cell stores less charge
Significant performance and energy overhead
Chart: DRAM Chip Capacity
| 2 | 4 | 8 | 16 | 32 | 64 | 128
Baseline | 0.97444 | 0.96375 | 0.94679 | 0.92168 | 0.88302 | 0.82497 | 0.73698
26% Slowdown
More periodic refresh operations incur larger performance overhead as DRAM chip density increases
Notes: With increasing DRAM chip density, [CLICK]
More rows need to be refreshed [CLICK]
And cells can store smaller charge leading to more periodic refresh operations[CLICK]
In this plot, we sweep DRAM chip capacity on the x-axis and investigate how the performance overhead of DRAM refresh operations change[CLICK]
We observe 26% slowdown in system performance caused by periodic refreshes [CLICK]

## Slide 176: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
RowPress
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 177: DRAM Organization
DRAM Chip
Bank
Chip I/O
DRAM Bank
Subarray
. . .
DRAM Subarray
Row Buffer
Bitline
…
…
Wordline
…
…
…
…
DRAM Cell
DRAM Row
Notes: This is a DRAM module, used as the main memory on many systems. [CLICK]
A DRAM module consists of multiple chips each of which contains multiple banks [CLICK]
Each bank is composed of multiple subarrays [CLICK]
And within each subarray, there is a two dimensional array of DRAM cells. [CLICK]
These cells are organized into rows that are selected using wordlines [CLICK]
And the cells are connected to a row buffer via bitlines [CLICK]

## Slide 178: DRAM Operation
DRAM Subarray
Bitline
…
…
Wordline
…
…
…
…
DRAM Cell
DRAM Cell
Row Buffer
Row Activation: Fetch the row’s content into the row buffer
Column Access: Read/Write a column in the row buffer
Precharge: Disconnect the row from the row buffer
Wordline
Capacitor
Access transistor
Bitline
charge
leakage
paths
Refresh: Restores the capacitor voltage with a time period called refresh window
I/O Circuitry
Notes: This is a simplified diagram of a DRAM cell, where the data is stored as capacitor voltage and accessed through the access transistor [CLICK]
A DRAM cell inherently exhibits several charge leakage paths [CLICK]
And requires to perform refresh operations to restore the capacitor voltage with a time period called refresh window.
[PAUSE]
To access a DRAM cell, [CLICK]
the memory controller must first open or activate the row to fetch the row’s data into the row buffer [CLICK]
The READ and WRITE requests targeting the row are serviced from the row buffer [CLICK]
After all requests are serviced from the row, the memory controller must close or precharge the row in order to begin accessing data from another row. [CLICK]

## Slide 179: RowHammer Mitigation Approaches
Increased refresh rate
Physical isolation
Reactive refresh
Proactive throttling
DRAM Bank
Aggressor Row
Victim Rows
Isolation Rows
Large-enough distance
DRAM Bank
Aggressor Row
Victim rows
Refresh
Victim Rows
Refresh
Rapidly activated (hammered)
REF-to-REF time reduces
Fewer activations can fit
Fewer activations can be performed
Notes: There are four high-level RowHammer mitigation approaches.
[CLICK] The first approach is to increase refresh rate
[CLICK] which reduces the refresh window,
[CLICK] and thus the activation count that an attacker can reach in a refresh window.
[CLICK] The second approach is to physically isolate
[CLICK] potential victim rows with sensitive data
[CLICK] from aggressor rows that a potential attacker can hammer
[CLICK] by allocating isolation rows in between
such that the attacker cannot disturb sensitive data by performing RowHammer attack.
[CLICK] The third approach is reactive refresh.
[CLICK] In this approach, when an aggressor row is hammered
[CLICK] potential victim rows are refreshed to avoid bit-flips.
[CLICK] Finally the fourth approach suggests
[CLICK] throttling or slowing down memory accesses proactively such that no row’s activation rate can reach RowHammer threshold.

## Slide 180: RowHammer Mitigation across Generations
105
104
103
102
105
104
103
102
DDR3-old
DDR3-new
DDR4-old
LPDDR4-1x
DDR4-new
LPDDR4-1y
PARA
TWiCe-ideal
Ideal
HCfirst (number of hammers required to induce first RowHammer bit flip)
14%
J. S. Kim, M. Patel, A. G. Yaglikci, H. Hassan, R. Azizi, L. Orosa, and O. Mutlu, "Revisiting RowHammer: An Experimental Analysis of Modern Devices and Mitigation Techniques,” in ISCA, 2020.

## Slide 181: RowPress [ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023.

## Slide 182: RowPress A New DRAM Read Disturbance Phenomenon
Row 0
Row 1
Row 2
Row 3
Row 4
Keeping a DRAM row open (activated)
causes RowPress bitflips in nearby cells
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 2
closed
Victim Row
Victim Row
Aggressor Row
Row 2
open
Aggressor Row
DRAM Subarray
Notes: Due to an increase in cell-to-cell interference, as a result of aggressive technology node scaling, rapidly activating [CLICK] and precharging
[FORTH & BACK] a DRAM row can result in bit flips in physically adjacent rows [CLICK]
[FORTH & BACK] Continuing to access the same row results in even more failures in nearby rows. This phenomenon is known as RowHammer. [CLICK]
We refer to the rapidly accessed row as an aggressor row and the rows containing bit flips as victim rows.

## Slide 183: Two Prime Examples of DRAM Read Disturbance: RowHammer and RowPress
Instead of using a high activation count,
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
☞ increase the time that the aggressor row stays open
Notes: Instead of a high activation count, RowPress increases the time the that aggressor stays open.
Doing disturbs adjacent rows enough to cause bitflips without a very high activation count.
We observe bitflips even with only one activation in extreme cases.

## Slide 184: RowPress [ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023.

## Slide 185: Effect of RowPress on Spatial Variation of Read Disturbance Vulnerability across Rows
RowPress reduces the mean of the distribution with increased tAggOn
There is still significant variation in the HCfirst across rows
Effect of RowPress on the HCfirst Distribution
Minimum Hammer Count
To Induce the First Bitflip
(HCfirst)
Aggressor Row’s On Time (tAggOn) (ns)

## Slide 186: Effect of RowPress on the HCfirst Distribution
Bitflips occur at lower hammer counts with RowPress and these hammer counts still significantly vary across DRAM rows
Aggressor Row’s On Time (tAggOn) (ns)
Minimum Hammer Count
To Induce the First Bitflip
(HCfirst)
Aggressor Row’s On Time (tAggOn) (ns)
Notes: Assume that an attacker hammers a row to induce bit flips in its nearby rows [CLICK]
Existing RowHammer defenses detect the attack [CLICK]
And try refreshing the nearby rows [CLICK]
However, the DRAM chip can internally map these row addresses to different physical rows [CLICK]
And thus bit flips may still occur[CLICK]
To avoid this, existing mechanisms need to know proprietary DRAM-internal row address mapping [CLICK]

## Slide 187: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Predictability
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 188: Cumulative Distribution of Spatial Features based on F1 Score
F1 score
Cumulative Distribution
of Spatial Features
Different DRAM modules
Weak prediction observed between a row’s spatial features & read disturbance vulnerability
More than 50% of the features have F1 scores larger than 0.1
Notes: Make the x-axis more intuitive

## Slide 189: Cumulative Distribution of Spatial Features based on F1 Score
F1 score
F1 score
F1 score
Cumulative Distribution of Spatial Features
A few spatial features from Mfr. S can exhibit F1 score >0.7
Different DRAM modules
Weak prediction observed between a row’s spatial features & read disturbance vulnerability
Notes: Make the x-axis more intuitive

## Slide 190: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Implementation Details
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 191: Svärd: Spatial Variation-Aware Read Disturbance Defenses Integration Examples with Existing Defenses
Svärd tunes the threshold based on the victim row’s vulnerability
Integrate Svärd with five solutions
1) PARA [Kim+, ISCA’14]
  Generates a random number
  Compares the random number with a threshold
  Refreshes the victim row if the random number exceeds the threshold
2) BlockHammer [Yaglikci+, HPCA’21]
  Counts the number of activations of DRAM rows
  Compares the activation count with a threshold
  Throttles accesses to the aggressor row if the activation count reaches the threshold
3) Hydra [Qureshi+, ISCA’22]
  Counts the number of activations of DRAM rows
  Compares the activation count with a threshold
  Refreshes the victim row when the activation count reaches the threshold
4) AQUA [Saxena+, MICRO’22] and 5) RRS [Saileshwar+, ASPLOS’22]
  Counts the number of activations of DRAM rows
  Compares the activation count with a threshold
  Relocates the aggressor row when the activation count reaches the threshold
Notes: We leverage this observation [CLICK]
By protecting weak rows more aggressively than strong rows [CLICK]
We do this by dynamically tuning the aggressiveness of defense mechanisms [CLICK]
and we show significant improvement in system performance. [CLICK]
Too high level
Put ataberk’s explanation here

## Slide 192: Svärd: Spatial Variation-Aware Read Disturbance Defenses Example Implementation 1
Classifies DRAM rows into several vulnerability-level bins
  Maintains a few (e.g., four) bits per DRAM row
Implemented in either the memory controller or the DRAM chip
Two example memory controller-based implementations:
Data
Memory
Request
DRAM Commands, Address, Data
Memory Controller
Memory
Request
Scheduler
DRAM
Chip
Existing Read
Disturbance
Solution
Preventive Action
HCfirst
HCfirst Table
Row
Addr
Metadata
Bits
Two potential ways of handling metadata
Notes: Too busy
Make either or more obvious
Table in the dram chip
Why memory controllers?
s/w based metadata?

## Slide 193: Svärd: Spatial Variation-Aware Read Disturbance Defenses Example Implementation 2
Classifies DRAM rows into several vulnerability-level bins
  Maintains a few (e.g., four) bits per DRAM row
Implemented in either the memory controller or the DRAM chip
An example DRAM chip-based implementation:
  Additional few (e.g., four) bits per DRAM row (e.g., 8Kb)
Data
DRAM
command
address
data
DRAM Chip
I/O Periphery
Existing Read
Disturbance
Solution
Preventive Action
HCfirst Bin
Refresh
Controller
DRAM Subarray
DRAM Row
DRAM Row
Row Buffer
DRAM Row

## Slide 194: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Backup Slides
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 195: More in the Paper
Security Proof
  Mathematically represent all possible access patterns
  We show that no row can be activated high-enough times to induce bit-flips when BlockHammer is configured correctly
Addressing Many-Sided Attacks
Evaluation of 14 mechanisms representing four mitigation approaches
  Comprehensive Protection
  Compatibility with Commodity DRAM Chips
  Scalability with RowHammer Vulnerability
  Deterministic Protection
Notes: We provide more analyses and implementation details available in the full paper.
[CLICK] First, the paper shares a security proof where we mathematically represent ALL POSSIBLE access patterns and show that NO ROW can be activated at a high-enough rate to induce bit-flips when BlockHammer is configured correctly.
[CLICK] Second, the paper explains how BlockHammer addresses many-sided attacks by tuning its thresholds.
[CLICK] Third, we evaluate all four high-level RowHammer mitigation approaches through analyzing 14 mechanisms from four aspects
[CLICK] comprehensive protection
[CLICK] compatibiltiy with commodity DRAM chips
[CLICK] scalability with worsening RowHammer vulnerability
[CLICK] and deterministic protection.
[CLICK] We show that BlockHammer is the only mechanism that satisfies all of them.
[END]

## Slide 196: Two Main Types of DRAM Refresh
2
Periodic Refresh: Periodically restores the charge DRAM cells leak over time
1
DRAM Row
Preventive Refresh
Preventive Refresh
RowHammer: Repeatedly accessing a DRAM row can cause bit flips in other physically nearby rows
Preventive Refresh: Mitigates RowHammer by refreshing physically nearby rows of a repeatedly accessed row
Notes: DRAM Refresh is mainly used for two purposes [CLICK]
The first one is called: Periodic Refresh to periodically restore the charge that DRAM cells leak over time [CLICK]
The second one is relevant to a read-disturb error mechanism called RowHammer, where repeatedly accessing a DRAM row can cause bit flips in other physically near by rows [CLICK]
A common method of mitigating RowHammer is refreshing potentially affected rows, called preventive refresh [CLICK]

## Slide 197: Periodic Refresh with Increasing DRAM Chip Density
A larger capacity chip has more rows to be refreshed
A smaller cell stores less charge
Significant performance and energy overhead
Chart: DRAM Chip Capacity
| 2 | 4 | 8 | 16 | 32 | 64 | 128
Baseline | 0.97444 | 0.96375 | 0.94679 | 0.92168 | 0.88302 | 0.82497 | 0.73698
26% Slowdown
More periodic refresh operations incur larger performance overhead as DRAM chip density increases
Notes: With increasing DRAM chip density, [CLICK]
More rows need to be refreshed [CLICK]
And cells can store smaller charge leading to more periodic refresh operations[CLICK]
In this plot, we sweep DRAM chip capacity on the x-axis and investigate how the performance overhead of DRAM refresh operations change[CLICK]
We observe 26% slowdown in system performance caused by periodic refreshes [CLICK]

## Slide 198: Future Research
The effect of aging
Preliminary data on aging via 68-day of hammering
Min. Hammer Count to Induce Read Disturbance Bitflips HCfirst (before aging)
Min. Hammer Count to Induce Read Disturbance Bitflips HCfirst (after aging)
Aging can lead to read disturbance bitflips at fewer hammers

## Slide 199: Two Prime Examples of DRAM Read Disturbance: RowHammer and RowPress
Instead of using a high activation count,
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
☞ increase the time that the aggressor row stays open
Notes: Instead of a high activation count, RowPress increases the time the that aggressor stays open.
Doing disturbs adjacent rows enough to cause bitflips without a very high activation count.
We observe bitflips even with only one activation in extreme cases.

## Slide 200: RowPress [ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023.

## Slide 201: Effect of RowPress on Spatial Variation of Read Disturbance Vulnerability across Rows
RowPress reduces the mean of the distribution with increased tAggOn
There is still significant variation in the HCfirst across rows
Effect of RowPress on the HCfirst Distribution
Minimum Hammer Count
To Induce the First Bitflip
(HCfirst)
Aggressor Row’s On Time (tAggOn) (ns)

## Slide 202: Effect of RowPress on the HCfirst Distribution
Bitflips occur at lower hammer counts with RowPress and these hammer counts still significantly vary across DRAM rows
Aggressor Row’s On Time (tAggOn) (ns)
Minimum Hammer Count
To Induce the First Bitflip
(HCfirst)
Aggressor Row’s On Time (tAggOn) (ns)
Notes: Assume that an attacker hammers a row to induce bit flips in its nearby rows [CLICK]
Existing RowHammer defenses detect the attack [CLICK]
And try refreshing the nearby rows [CLICK]
However, the DRAM chip can internally map these row addresses to different physical rows [CLICK]
And thus bit flips may still occur[CLICK]
To avoid this, existing mechanisms need to know proprietary DRAM-internal row address mapping [CLICK]

## Slide 203: Cumulative Distribution of Spatial Features based on F1 Score
F1 score
Cumulative Distribution
of Spatial Features
Different DRAM modules
No good prediction observed between a row’s spatial features & read disturbance vulnerability
More than 50% of the features have F1 scores larger than 0.1
Notes: Make the x-axis more intuitive

## Slide 204: Cumulative Distribution of Spatial Features based on F1 Score
F1 score
F1 score
F1 score
Cumulative Distribution of Spatial Features
A few spatial features from Mfr. S can exhibit F1 score >0.7
Different DRAM modules
No good prediction observed between a row’s spatial features & read disturbance vulnerability
Notes: Make the x-axis more intuitive

## Slide 205: An Outlier Solution: Hydra
Minimum Hammer Count to Induce the First Bitflip
Weighted Speedup
(Norm. to No Mitigation Baseline)
Only 3% Speedup

## Slide 206: Hydra Mitigation Mechanism
Hydra maintains a row activation counter for each DRAM row
Stores these activation counters in the DRAM array
Caches the counters of hot rows in the memory controller
At low HCfirst configurations, many rows are hot
Fetching / evicting counters dominate the performance overhead
Svärd needs further customizations for Hydra
Qureshi et al. "Hydra: Enabling Low-Overhead Mitigation of Row-Hammer at Ultra-Low Thresholds via Hybrid Tracking," in ISCA, 2022.

## Slide 207: Conclusion
Experimental study: 136 DDR4 DRAM chips from 3 major vendors
A large variation in the necessary activation count to induce the first bitflip
No strong correlation between a row’s spatial features and its vulnerability to read disturbance
SVÄRD: Dynamically adapts the aggressiveness of mitigations
Implemented in either the DRAM chip or the memory controller
Reduces the performance overheads by 2.4x, 2.7%, 1.6x, and 3.0x for BlockHammer, Hydra, PARA, and RRS
Future Work:
A deeper understanding is needed to account for irregularities in row and column addresses across chips
Finding correlations is essential to reduce the hardware cost
Reducing also the hardware cost of defenses
Notes: RowHammer is a worsening DRAM reliability and security problem [CLICK]
However, state-of-the-art RowHammer mitigation mechanisms face limitations supporting current and future commodity DRAM chips because of two challenges [CLICK]
First, they cannot scale efficiently with worsening RowHammer vulnerability[CLICK]
Second, they are not compatible with commodity DRAM chips as they rely on proprietary information [CLICK]
To overcome these two challenges, our key idea is to SELECTIVELY throttle memory accesses that may cause RowHammer bit flips

## Slide 208: RowHammer Mitigation across Generations
105
104
103
102
105
104
103
102
DDR3-old
DDR3-new
DDR4-old
LPDDR4-1x
DDR4-new
LPDDR4-1y
PARA
TWiCe-ideal
Ideal
HCfirst (number of hammers required to induce first RowHammer bit flip)
14%
J. S. Kim, M. Patel, A. G. Yaglikci, H. Hassan, R. Azizi, L. Orosa, and O. Mutlu, "Revisiting RowHammer: An Experimental Analysis of Modern Devices and Mitigation Techniques,” in ISCA, 2020.

## Slide 209: BlockHammer Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows
Abdullah Giray Yağlıkçı
Minesh Patel Jeremie S. Kim Roknoddin Azizi
Ataberk Olgun Lois Orosa Hasan Hassan Jisung Park
Konstantinos Kanellopoulos Taha Shahroodi
Saugata Ghose* Onur Mutlu
*
Notes: Hello, my name is Abdullah Giray Yağlıkçı
and I will be presenting our work
BlockHammer: Preventing RowHammer at Low Cost
by Blacklisting Rapidly-Accessed DRAM Rows

## Slide 210: Compatibility with Commodity DRAM Chips
Vendors apply in-DRAM mapping for two reasons:
Design Optimizations: By simplifying DRAM circuitry to provide better density, performance, and power
Yield Improvement: By mapping faulty rows and columns to redundant ones
In-DRAM mapping scheme includes insights into chip design and manufacturing quality
In-DRAM mapping is proprietary information
Notes: DRAM vendors apply in-DRAM mapping for two reasons.
[CLICK] to enable circuit design optimizations to meet density, performance, and power constraints
[CLICK] and for improving yield by mapping faulty rows and columns to redundant ones
[CLICK] Therefore, in-DRAM mapping includes insights into CHIP DESIGN and MANUFACTURING QUALITY.
[CLICK] and that’s why, it is PROPRIETARY information.

## Slide 211: RowHammer Mitigation Approaches
Increased refresh rate
Physical isolation
Reactive refresh
Proactive throttling
REF-to-REF time reduces
Fewer activations can fit
Fewer activations can be performed
DRAM Bank
Aggressor Row
Victim Rows
Isolation Rows
DRAM Bank
Aggressor Row
Victim rows
Victim Rows
Identifying victim and isolation rows requires
proprietary knowledge of in-DRAM mapping
Notes: Unfortunately, physical isolation and reactive refresh need this proprietary information to identify which rows to isolate or refresh.

## Slide 212: Our Goal
To prevent RowHammer efficiently and scalably
without knowledge of or modifications to DRAM internals
Notes: To address these two challenges,
OUR GOAL in this paper is to prevent RowHammer efficiently and scalably without knowledge of or modification to DRAM internals.

## Slide 213: BlockHammer Key Idea
Selectively throttle memory accesses
that may cause RowHammer bit-flips
Notes: BlockHammer's key idea is to selectively throttle memory accesses
that may cause RowHammer bit-flips.

## Slide 214: A Major Issue of Past Read Disturbance Mitigations
A RowHammer attack hammers Row A
Existing mechanisms detect the attack
Refresh rows A+1 and A-1
Bit flips still may occur due to unknown DRAM-internal row mapping
Physical
Row Layout
Row A+1
Row A-1
Victim
Rows
Row A
Existing read disturbance mitigation mechanisms need to know proprietary DRAM-internal row address mapping
Notes: Assume that an attacker hammers a row to induce bit flips in its nearby rows [CLICK]
Existing mitigation mechanisms detect the attack [CLICK]
And try refreshing the nearby rows [CLICK]
However, the DRAM chip can internally map these row addresses to different physical rows [CLICK]
And thus bit flips may still occur[CLICK]
To avoid this, existing mechanisms need to know proprietary DRAM-internal row address mapping [CLICK]

## Slide 215: BlockHammer: Throttling Unsafe Accesses
A RowHammer attack hammers Row A
BlockHammer detects and selectively throttles accesses from within the memory controller
Bit flips do not occur
BlockHammer can optionally inform the system software about the attack
Physical
Row Layout
Row A
BlockHammer is compatible with commodity DRAM chips
No need for proprietary info of or modifications to DRAM chips
Notes: In contrast, BlockHammer detects and selectively throttles the attack’s memory accesses [CLICK]
Therefore, the row’s activation count cannot reach critical levels, and no bit flip occurs [CLICK]
BlockHammer can optionally inform the system software about the attack for higher-level countermeasures [CLICK]
BlockHammer achieves all of these without needing proprietary information of or modifications to commodity DRAM chips [CLICK]

## Slide 216: Intel Hardware Security Academic Award
Abdullah Giray Yağlıkçı, Minesh Patel, Jeremie S. Kim, Roknoddin Azizi, Ataberk Olgun, Lois Orosa, Hasan Hassan, Jisung Park, Konstantinos Kanellopoulos, Taha Shahroodi, Saugata Ghose, and Onur Mutlu, "BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows,” in HPCA, 2021.
Notes: BlockHammer was chosen as a finalist

## Slide 217: Intel Hardware Security Academic Award
Abdullah Giray Yağlıkçı, Minesh Patel, Jeremie S. Kim, Roknoddin Azizi, Ataberk Olgun, Lois Orosa, Hasan Hassan, Jisung Park, Konstantinos Kanellopoulos, Taha Shahroodi, Saugata Ghose, and Onur Mutlu, "BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows,” in HPCA, 2021.
Notes: in Intel Hardware Security Academic Awards

## Slide 218: BlockHammer Overview of Approach
RowBlocker
Tracks row activation rates using area-efficient Bloom filters
Blacklists rows that are activated at a high rate
Throttles activations targeting a blacklisted row
AttackThrottler
Identifies threads that perform a RowHammer attack
Reduces memory bandwidth usage of identified threads
No row can be activated at a high enough rate to induce bit-flips
Greatly reduces the performance degradation
and energy wastage a RowHammer attack inflicts on a system
Notes: BlockHammer consists of two mechanisms [CLICK] RowBlocker [CLICK] and AttackThrottler.
RowBlocker [CLICK] tracks ROW ACTIVATION RATES using area-efficient Bloom filters
[CLICK] BLACKLISTS rows that are activated at a high rate
[CLICK] THROTTLES (or enforces a certain delay between) activations targeting a blacklisted row.
[CLICK] By doing so, RowBlocker ensures that NO ROW can be activated at a high enough rate to induce RowHammer bit-flips.
[CLICK] AttackThrottler IDENTIFIES threads that try activating blacklisted rows.
[CLICK] and reduces their memory bandwidth consumption by throttling their memory requests.
[CLICK] By doing so, AttackThrottler greatly reduces the performance degradation and energy wastage a RowHammer attack inflicts on a system.

## Slide 219: RowBlocker
Modifies the memory request scheduler to throttle row activations
Blacklists rows with a high activation rate and delays subsequent activations targeting blacklisted rows
Blacklisting
Logic
Delaying
Logic
Notes: RowBlocker modifies the memory request scheduler TO THROTTLE row activations that could lead to bit-flips.
[CLICK] to do so, it BLACKLISTS rows with high activation rates and DELAYS subsequent activations targeting them.
[CLICK] we call the blacklisting logic RowBlocker-BL
[CLICK] and thedelaying logic RowBlocker-HB.
[END]

## Slide 220: RowBlocker
Blocks a row activation if the row is both blacklisted and recently activated
Notes: To throttle row activations with a high activation rate, RowBlocker blocks a row activation if the row is BOTH blacklisted AND recently activated.
This slide explains how RowBlocker operates in high level.
[CLICK] Memory request scheduler pings RowBlocker with a "is the row activation RowHammer-safe" query before performing the row activation.
[CLICK] RowBlocker simultaneously checks both components
[CLICK] if a row is blacklisted [CLICK] and recently activated,
activating the row can be unsafe.
Therefore, the row activation is blocked.
Meanwhile, other requests in the request queue can be serviced.
[END]

## Slide 221: RowBlocker
When a row activation is performed, both RowBlocker-BL and RowBlocker-HB are updated with the row activation information
Notes: When the memory request scheduler issues a row activation,
BOTH components are updated with the row activation information.

## Slide 222: RowBlocker-BL Blacklisting Logic
Blacklists a row when the row’s activation count in a time window exceeds a threshold
Employs two counting Bloom filters for area-efficient activation rate tracking
Notes: RowBlocker-BL or the blacklisting logic
[CLICK] Tracks row activation rates
and Blacklists a row when its activation count in a time window exceeds a threshold.
[CLICK] To do this in an area-efficient way, it employs two counting Bloom filters

## Slide 223: Counting Bloom Filters
Blacklisting logic counts activations using counting Bloom filters
A row’s activation count
  can be observed more than it is (false positive)
  cannot be observed less than it is (no false negative)
To avoid saturating counters, we use a time-interleaving approach
0
0
0
0
0
0
0
0
0
0
Hash functions
ACT Row A
1
1
1
1
1
1
1
1
ACT Row B
1
1
2
1
1
1
2
1
Minimum
1
Test Row A
1
1
2
1
Notes: A counting Bloom filter is essentially an array of counters
[CLICK] addressed by hashed identifiers
[CLICK] When a row A is activated,
its row id is provided to a set of hash functions
that evaluate a set of indices to the counter array
each of which is incremented.
[CLICK] Activating another row,
[CLICK] say row B,
increments another subset of counters.
[CLICK] As shown here, counter can be used for more than one row ids.
[CLICK] Therefore, a row's activation count can be observed
more than its actual value leading false positives.
[CLICK] We estimate a row's activation count as
[CLICK] the minimum value across its corresponding counters.
[CLICK] These counters are never decremented. Therefore, a row’s activation count cannot be observed less than its actual value, hence no false negatives.
[CLICK] The counters can saturate though as they are never decremented. To avoid this, we periodically reset them without losing data by adopting a time-interleaving approach.

## Slide 224: RowBlocker-BL Blacklisting Logic
Blacklisting logic employs two counting Bloom filters
A new row activation is inserted in both filters
Only one filter (active filter) responds to test queries
The active filter changes at every epoch
CBFA is active
CBFB is active
CBFA is passive
CBFB is passive
Notes: I will explain this time interleaving next
[CLICK] Blacklisting logic employs TWO counting bloom filters
[CLICK] A new row activation is inserted in BOTH filters at ALL times.
[CLICK] Only one filter responds to test queries at a given time that we call the ACTIVE FILTER.
[CLICK] The active filter alternates at every epoch between two filters.
[CLICK] Let's look at the operation of two filters CBFA and CBFB across the timeline shown here.
[CLICK] A green bar indicates that the filter is active at a given time.
[CLICK] We call the other filter PASSIVE and indicate its state with a gray bar.
[END]

## Slide 225: RowBlocker-BL Blacklisting Logic
Blacklisting logic employs two counting Bloom filters
A new row activation is inserted in both filters
Only one filter (active filter) responds to test queries
The active filter changes at every epoch
Blacklists a row if its activation count reaches the blacklisting threshold (NBL)
Assume that the row is
activated at a high rate
Assume that the row is
not activated at a high rate
Notes: At timestamp 1, CBFA is active.
[CLICK] Assume that a row is activated at a high rate
in epochs one and two
[CLICK] and at a low rate later on.
[CLICK] RowBlocker blacklists a row if the row's activation count reaches the blacklisting threshold called NBL
A blue bar shows that the row's activation count is below the blacklisting threshold.
[CLICK] at timestamp 2, the row's activation count reaches blacklisting threshold (NBL)
and the row is blacklisted
[CLICK] as indicated by the red bar.
[CLICK] at timestamp 3, the active filter (CBFA) is cleared
[CLICK] and CBFB becomes the active filter for epoch 2.
[CLICK] since CBFB knows the high activation rate during epoch 1, it keeps the row blacklisted until the end of epoch 2.
[CLICK] meanwhile, at timestamp 4, row's activation counters in CBFA exceeds blacklisting threshold again
[CLICK] At the end of epoch 2 (at timestamp 5), CBFB is cleared
[CLICK] and CBFA becomes the active filter again.
CBFA immediately blacklists the row because its counters reached NBL at timestamp 4.
[CLICK] Assuming that the row is no longer rapidly activated during epoch 3, its counters in CBFB remain below the blacklisting threshold
[CLICK] and it is no longer blacklisted starting from timestamp 6.
[END]

## Slide 226: Limiting the Row Activation Rate
The activation rate is RowHammer-safe if it is smaller than or equal to RowHammer threshold (NRH) activations in a refresh window (tREFW)
RowBlocker limits the activation count (NCBF) in a CBF’s lifetime (tCBF)
tCBF
tCBF
Clear CBFB
Clear CBFB
Clear CBFA
Clear CBFA
Notes: To ensure RowHammer-safe operation, RowBlocker limits the activation rate of blacklisted rows at a RowHammer-safe level.
[CLICK] An activation rate is RowHammer-safe if it is smaller than the ratio of RowHammer threshold (NRH) to the refresh window tREFW.
[CLICK] RowBlocker ensures this activation rate within the lifetime of each counting Bloom filter (tCBF) which is bounded by CLEAR operations.
[CLICK] Therefore, we write the RowHammer-safe condition as activation rate in a tCBF to be smaller than or equal to NRH row activations per tREFW refresh window.
[END]

## Slide 227: Limiting the Row Activation Rate
The activation rate is RowHammer-safe if it is smaller than or equal to RowHammer threshold (NRH) activations in a refresh window (tREFW)
RowBlocker limits the activation count (NCBF) in a CBF’s lifetime (tCBF)
tCBF
tCBF
Clear CBFB
Clear CBFB
Clear CBFA
Clear CBFA
RowHammer Safety Constraint
Notes: Denoting the number of activations in a tCBF as nCBF, we derive the shown constraint.

## Slide 228: RowBlocker-HB Limiting the Row Activation Rate
Ensures that all rows experience a RowHammer-safe activation rate
We limit NCBF by configuring tDelay :
Row
activation
tDelay
tDelay
NCBF row activations
tDelay
tCBF
time
tDelay
tRC x NBL
tCBF – (tRC ✖️NBL)
tRC
NBL row activations
Blacklisted row activation
Notes: RowBlocker-HB is the component which ensures that all rows experience a RowHammer-safe activation rate.
[CLICK] I will explain how this mechanism works on a timeline.
[CLICK] Within a tCBF time window,
[CLICK] RowBlocker limits a row’s activation count to NCBF.
[CLICK] Now assume that an attacker tries hammering a row as rapidly as possible.
Each spike in this illustration represents a row activation.
Due to the DDR specs, there has to be a minimum time window between subsequent activations called tRC.
[CLICK] Therefore, A row’s activation count can reach the blacklisting threshold (NBL) at a minimum time window of tRC times NBL.
[CLICK] At this point the row is blacklisted and subsequent activations targeting the row are throttled until the end of tCBF time window.
[CLICK] A red spike represents an activation targeting the row when the row is blacklisted.
[CLICK] To throttle subsequent row activations, RowBlocker ensures a time delay (tDelay) between them.
Therefore, a row can be activated at most this [CLICK] many times when it is blacklisted.
[CLICK] and by configuring tDelay, RowBlocker limits NCBF.
Please refer to the full paper for more details about this calculation.
[END]

## Slide 229: Example Adversarial of BlockHammer
Blacklisting threshold: 512
RowHammer threshold: 1024
512 activations can be performed in 2.56us
We need to spread the next 512 activations across 64ms-2.56us
tDelay: 125us instead of 50ns
An adversarial can blacklist 25K rows in a refresh window and practically block the whole bank

## Slide 230: RowBlocker-HB Delaying Row Activations
RowBlocker-HB ensures no subsequent blacklisted row activation is performed sooner than tDelay
RowBlocker-HB implements a history buffer for row activations that can fit in a tDelay time window
A blacklisted row activation is blocked as long as a valid activation record of the row exists in the history buffer
No row can be activated at a high enough rate to induce bit-flips
Notes: RowBlocker-HB ensures that no subsequent blacklisted row activation is performed sooner than tDelay.
[CLICK] To do so, it implements a history buffer that contains the information of all row activations that can fit in a tDelay time window.
[CLICK] A blacklisted row activation is blocked as long as a valid activation record of the row exists in the history buffer.
[CLICK] this way, no row can be activated at a high enough rate to induce bit-flips.

## Slide 231: AttackThrottler
Tackles a RowHammer attack’s performance degradation and energy wastage on a system
A RowHammer attack intrinsically keeps activating blacklisted rows
RowHammer Likelihood Index (RHLI): Number of activations that target blacklisted rows (normalized to maximum possible activation count)
RHLI is larger when the thread’s access pattern
is more similar to a RowHammer attack
0.0
1.0
RHLI
Benign application
No blacklisted row activations
RowHammer attack Blacklisted row activation count approaches RowHammer threshold
Notes: AttackThorttler tackles the performance degradation and energy wastage that a RowHammer attack causes.
[CLICK] To identify and reduce the negative impact of a RowHammer attack, AttackThrottler leverages the observation that a RowHammer attack intrinsically keeps activating blacklisted rows.
[CLICK] To this end, AttackThrottler introduces a new metric called RowHammer Likelihood Index (RHLI), which is calculated as the number of blacklisted row activations normalized to the maximum number of blacklisted row activations that BlockHammer allows.
[CLICK] RHLI is zero for benign threads that do not try activating any blacklisted row.
[CLICK] RHLI is one when the thread's row activation count reaches RowHammer threshold, meaning that the thread performs RowHammer attack.
[CLICK] RHLI of a thread increases when the thread behaves more similar to a RowHammer attack.

## Slide 232: AttackThrottler
Applies a smaller quota to a thread’s in-flight request count as RHLI increases
Reduces a RowHammer attack’s memory bandwidth consumption, enabling a larger memory bandwidth for concurrent benign applications
RHLI can also be used as a RowHammer attack indicator by the system software
Greatly reduces the perfomance degradation and energy wastage
a RowHammer attack inflicts on a system
RHLI
Benign application
No blacklisted row activations
No quota applied
RowHammer attack Blacklisted row activation count approaches RowHammer threshold
No request is allowed
0.0
1.0
Notes: [CLICK] AttackThrottler applies a smaller quota to a thread’s in-flight request count as RHLI increases.
[CLICK] If RHLI is 0: No quota is applied as the thread is benign. [CLICK] When RHLI reaches 1, no request is allowed as the thread performs a RowHammer attack.
[CLICK] Through this throttling, AttackThrottler reduces a thread\s memory bandwidth consumption proportional to its similarity to a RowHammer attack, freeing up memory bandwidth for concurrent benign applications.
[CLICK] By doing so, AttackThrottler greatly reduces the perfomance degradation and energy wastage a RowHammer attack inflicts on the system.
[CLICK] Alternatively, RHLI can also be used as a RowHammer attack indicator
by the system software for software-level countermeasures.

## Slide 233: Evaluation BlockHammer’s Hardware Complexity
We analyze six state-of-the-art mechanisms and BlockHammer
We calculate area, access energy, and static power consumption*
Mitigation |  | SRAM | CAM | Area |  | Access Energy | Static Power
Mechanism |  | KB | KB | mm2 | %CPU | pJ | mW
BlockHammer |  |  |  |  |  |  | 
PARA [73] |  |  |  |  |  |  | 
ProHIT [137] |  |  |  |  |  |  | 
MRLoc [161] |  |  |  |  |  |  | 
CBT [132] |  |  |  |  |  |  | 
TWiCe [84] |  |  |  |  |  |  | 
Graphene [113] |  |  |  |  |  |  | 
Mitigation |  | SRAM | CAM | Area |  | Access Energy | Static Power
Mechanism |  | KB | KB | mm2 | %CPU | pJ | mW
BlockHammer |  | 51.48 | 1.73 | 0.14 | 0.06 | 20.30 | 22.27
PARA [73] |  | - | - | <0.01 | - | - | -
ProHIT [137] |  | - | 0.22 | <0.01 | <0.01 | 3.67 | 0.14
MRLoc [161] |  | - | 0.47 | <0.01 | <0.01 | 4.44 | 0.21
CBT [132] |  | 16.00 | 8.50 | 0.20 | 0.08 | 9.13 | 35.55
TWiCe [84] |  | 23.10 | 14.02 | 0.15 | 0.06 | 7.99 | 21.28
Graphene [113] |  | - | 5.22 | 0.04 | 0.02 | 40.67 | 3.11
NRH=32K
  BlockHammer is low cost and competitive
  with state-of-the-art mechanisms
*Assuming a high-end 28-core Intel Xeon processor system with 4-channel single-rank DDR4 DIMMs with a RowHammer threshold (NRH) of 32K
Notes: We analyze and compare BlockHammer's hardware complexity
with six state-of-the-art RowHammer mitigation mechanisms, namely
PARA, ProHIT, MRLoc, CBT, TWiCe, and Graphene.
[CLICK] we calculate hardware complexity in terms of AREA, ACCESS ENERGY, and STATIC POWER consumption for a RowHammer threshold of 32K,
which is a realistic assumption for current DRAM chips
[CLICK] We observe that BlockHammer is LOW COST and competitive with state-of-the-art RowHammer mitigation mechanisms

## Slide 234: Evaluation BlockHammer’s Hardware Complexity
Mitigation |  | SRAM | CAM | Area |  | Access Energy | Static Power
Mechanism |  | KB | KB | mm2 | %CPU | pJ | mW
BlockHammer |  | 51.48 | 1.73 | 0.14 | 0.06 | 20.30 | 22.27
PARA [73] |  | - | - | <0.01 | - | - | -
ProHIT [137] |  | - | 0.22 | <0.01 | <0.01 | 3.67 | 0.14
MRLoc [161] |  | - | 0.47 | <0.01 | <0.01 | 4.44 | 0.21
CBT [132] |  | 16.00 | 8.50 | 0.20 | 0.08 | 9.13 | 35.55
TWiCe [84] |  | 23.10 | 14.02 | 0.15 | 0.06 | 7.99 | 21.28
Graphene [113] |  | - | 5.22 | 0.04 | 0.02 | 40.67 | 3.11
Mitigation |  | SRAM | CAM | Area |  | Access Energy | Static Power
Mechanism |  | KB | KB | mm2 | %CPU | pJ | mW
BlockHammer |  | 51.48 | 1.73 | 0.14 | 0.06 | 20.30 | 22.27
PARA [73] |  | - | - | <0.01 | - | - | -
ProHIT [137] |  | - | 0.22 | <0.01 | <0.01 | 3.67 | 0.14
MRLoc [161] |  | - | 0.47 | <0.01 | <0.01 | 4.44 | 0.21
CBT [132] |  | 16.00 | 8.50 | 0.20 | 0.08 | 9.13 | 35.55
TWiCe [84] |  | 23.10 | 14.02 | 0.15 | 0.06 | 7.99 | 21.28
Graphene [113] |  | - | 5.22 | 0.04 | 0.02 | 40.67 | 3.11
BlockHammer |  | 441.33 | 55.58 | 1.57 | 0.64 | 99.64 | 220.99
PARA [73] |  | - | - | <0.01 | - | - | -
ProHIT [137] |  | x | x | x | x | x | x
MRLoc [161] |  | x | x | x | x | x | x
CBT [132] |  | 512.00 | 272.00 | 3.95 | 1.60 | 127.93 | 535.50
TWiCe [84] |  | 738.32 | 448.27 | 5.17 | 2.10 | 124.79 | 631.98
Graphene [113] |  | - | 166.03 | 1.14 | 0.46 | 917.55 | 93.96
Mitigation |  | SRAM | CAM | Area |  | Access Energy | Static Power
Mechanism |  | KB | KB | mm2 | %CPU | pJ | mW
BlockHammer |  |  |  |  | 0.06 | 20.30 | 22.27
PARA [73] |  |  |  |  |  |  | 
ProHIT [137] |  |  |  |  |  |  | 
MRLoc [161] |  |  |  |  |  |  | 
CBT [132] |  |  |  |  | 0.08 |  | 35.55
TWiCe [84] |  |  |  |  | 0.06 |  | 21.28
Graphene [113] |  |  |  |  | 0.02 | 40.67 | 3.11
BlockHammer |  |  |  |  | 0.64 | 99.64 | 220.99
PARA [73] |  |  |  |  |  |  | 
ProHIT [137] |  |  |  |  |  |  | 
MRLoc [161] |  |  |  |  |  |  | 
CBT [132] |  |  |  |  | 1.60 |  | 535.50
TWiCe [84] |  |  |  |  | 2.10 |  | 631.98
Graphene [113] |  |  |  |  | 0.46 | 917.55 | 93.96
20x
35x
23x
10x
15x
30x
30x
10x
23x
5x
NRH=32K
NRH=1K
  BlockHammer’s hardware complexity scales more efficiently than state-of-the-art mechanisms
Notes: To understand how hardware complexity scales with worsening RowHammer vulnerability,
[CLICK] we repeat the analysis for a RowHammer threshold of 1K, which is projected for future DRAM chips.
[CLICK] We compare how the complexity of each mechanism changes in terms of
[CLICK] chip area,
[CLICK] access energy,
[CLICK] and static power consumption.
[CLICK] We observe that BlockHammer’s hardware complexity scales more efficiently than state-of-the-art RowHammer mitigaiton mechanisms.

## Slide 235: Evaluation Performance and DRAM Energy
Cycle-level simulations using Ramulator and DRAMPower
System Configuration:
Single-Core Benign Workloads:
  22 SPEC CPU 2006
  4 YCSB Disk I/O
  2 Network Accelerator Traces
  2 Bulk Data Copy with Non-Temporal Hint (movnti)
Randomly Chosen Multiprogrammed Workloads:
  125 workloads containing 8 benign applications
  125 workloads containing 7 benign applications and 1 RowHammer attack thread
Processor | 3.2 GHz, {1,8} core, 4-wide issue, 128-entry instr. window
LLC | 64-byte cacheline, 8-way set-associative, {2,16} MB
Memory scheduler | FR-FCFS
Address mapping | Minimalistic Open Pages
DRAM | DDR4 1 channel, 1 rank, 4 bank group, 4 banks per bank group
RowHammer Threshold | 32K
Notes: We conduct cycle-level simulations using RAMULATOR and DRAMPOWER to evaluate the performance and DRAM energy consumption.
[CLICK] We simulate a realistic system with a DDR4 DRAM module.
[CLICK] We use single-core workloads from four benchmarks in our simulations.
22 SPEC benchmarks, 4 disk I/O memory access traces from YCSB benchmark suite, 2 memory access traces collected from a network accelerator chip, and 2 synthetic traces that mimic bulk data copy with non-temporal hint.
[CLICK] We randomly combine these workloads to create two types of eight-core multiprogrammed workloads:
[CLICK] workloads that contain eight benign applications
[CLICK] and workloads that contain seven benign applications along with one thread performing RowHammer attack.

## Slide 236: Evaluation Performance and DRAM Energy
We classify single-core workloads into three categories based on row buffer conflicts per thousand instructions
No application’s row activation count exceeds BlockHammer’s blacklisting threshold (NBL)
0.0
1.0
5.0
RBCPKI
Low (L)
Medium (M)
High (H)
BlockHammer does not incur performance or DRAM energy overheads for single-core benign applications
Notes: We start with evaluating for single-core benign workloads.
[CLICK] We classify single-core workloads into three categories based on their Row Buffer Conflicts per Kilo Instruction
[CLICK] We evaluate the performance and DRAM energy consumption for BlockHammer and six state-of-the-art RowHammer mitigation mechanisms.
[CLICK] We observe that no application’s row activation count exceeds BlockHammer’s blacklisting threshold.
[CLICK] Therefore, BlockHammer does not change the performance or DRAM energy consumption for single-core benign applications.

## Slide 237: Evaluation Performance and DRAM Energy
System throughput (weighted speedup)
Job turnaround time (harmonic speedup)
Unfairness (maximum slowdown)
DRAM energy consumption
RowHammer
Attack
Present
No
RowHammer
Attack
BlockHammer introduces very low performance (<0.5%) and DRAM energy (<0.4%) overheads
BlockHammer significantly increases benign application performance (by 45% on average)
and reduces DRAM energy consumption (by 29% on average)
Notes: We evaluate these RowHammer mitigation mechanisms and BlockHammer for eight-core multiprogrammed workloads
[CLICK] when there is no RowHammer attack.
[CLICK] and when there is a RowHammer attack present.
[CLICK] We use four metrics in this evaluation to demonstrate
[CLICK] the system throughput,
[CLICK] job turnaround time,
[CLICK] unfairness,
[CLICK] and DRAM energy consumption.
[CLICK] When there is no attack in the system, BlockHammer introduces very low performance and DRAM energy overheads.
[CLICK] When there is an attack present in the system,
BlockHammer significantly increases benign application performance
and reduces DRAM energy consumption.

## Slide 238: Evaluation Scaling with RowHammer Vulnerability
RowHammer
Attack Present
No RowHammer
Attack
BlockHammer’s performance and energy overheads remain negligible (<0.6%)
BlockHammer scalably provides much higher performance (71% on average)
and lower energy consumption (32% on average) than state-of-the-art mechanisms
System throughput (weighted speedup)
Job turnaround time (harmonic speedup)
Unfairness (maximum slowdown)
DRAM energy consumption
Notes: We conduct a scalability study with worsening RowHammer vulnerability.
[CLICK] again for the cases where there is no RowHammer attack
[CLICK] and when there is a RowHammer attack present.
We scale the RowHammer threshold from 32K down to 1K.
[CLICK] Here are the results for system throughput
[CLICK] job turnaround time
[CLICK] unfairness
[CLICK] and DRAM energy consumption
[CLICK] We observe that BlockHammer's performance and energy overheads remain negligible even when RowHammer threshold is scaled downto 1K
[CLICK] and BlockHammer scalably provides much higher performance and lower energy consumption than state-of-the-art mechanisms when there is a RowHammer attack present.

## Slide 239: More in the Paper
Security Proof
  Mathematically represent all possible access patterns
  We show that no row can be activated high-enough times to induce bit-flips when BlockHammer is configured correctly
Addressing Many-Sided Attacks
Evaluation of 14 mechanisms representing four mitigation approaches
  Comprehensive Protection
  Compatibility with Commodity DRAM Chips
  Scalability with RowHammer Vulnerability
  Deterministic Protection
Notes: We provide more analyses and implementation details available in the full paper.
[CLICK] First, the paper shares a security proof where we mathematically represent ALL POSSIBLE access patterns and show that NO ROW can be activated at a high-enough rate to induce bit-flips when BlockHammer is configured correctly.
[CLICK] Second, the paper explains how BlockHammer addresses many-sided attacks by tuning its thresholds.
[CLICK] Third, we evaluate all four high-level RowHammer mitigation approaches through analyzing 14 mechanisms from four aspects
[CLICK] comprehensive protection
[CLICK] compatibiltiy with commodity DRAM chips
[CLICK] scalability with worsening RowHammer vulnerability
[CLICK] and deterministic protection.
[CLICK] We show that BlockHammer is the only mechanism that satisfies all of them.
[END]

## Slide 240: BlockHammer Hardware Complexity
RowBlocker
  RowBlocker-BL: Implemented per-bank
    1K counters in a CBF
    4 H3 hash functions
  RowBlocker-HB: Implemented per-rank
    887 entries
AttackThrottler
  Two counters per <Bank, Thread> pair.

## Slide 241: RowHammer Characteristics
RowHammer Threshold (NRH): The minimum row activation count in a refresh window to induce a RowHammer bit-flip.
Blast Radius (rBlast): The maximum physical distance from the aggressor row at which RowHammer bit-flips can be observed.
Blast Impact Factor (ci): Set of coefficients that scale a RowHammer attacks impact on victim rows based on their physical distance to the aggressor row.
Notes: Two properties indicate how vulnerable a DRAM chip is to RowHammer.
[CLICK] RowHammer threshold is the minimum number of row activations in a refresh window to induce a RowHammer bit-flip.
[CLICK] Blast radius is the maximum physical distance from the aggressor row at which RowHammer bit-flips can be observed.

## Slide 242: Many-Sided Attacks
NRH : RowHammer threshold for single-sided attack.
NRH* : Maximum activation count that BlockHammer allows in a refresh window.
rBlast : Blast radius
ci : Blast impact factor
We configure NRH* such that hammering all rows NRH* times does not cause bit-flips.
=

## Slide 243: Security Analysis
No permutation of epochs can satisfy the necessary constraints of a successful attack

## Slide 244: HiRA: Hidden Row Activation for Reducing Refresh Latency of Off-the-Shelf DRAM Chips
Abdullah Giray Yağlıkçı
Ataberk Olgun Minesh Patel Haocong Luo Hasan Hassan
Lois Orosa Oğuz Ergin Onur Mutlu
Notes: Hello, I am Giray, and I will present our new paper HiRA: Hidden Row Activation

## Slide 245: Two Main Types of DRAM Refresh
2
Periodic Refresh: Periodically restores the charge DRAM cells leak over time
1
DRAM Row
Preventive Refresh
Preventive Refresh
RowHammer: Repeatedly accessing a DRAM row can cause bit flips in other physically nearby rows
Preventive Refresh: Mitigates RowHammer by refreshing physically nearby rows of a repeatedly accessed row
Notes: DRAM Refresh is mainly used for two purposes [CLICK]
The first one is called: Periodic Refresh to periodically restore the charge that DRAM cells leak over time [CLICK]
The second one is relevant to a read-disturb error mechanism called RowHammer, where repeatedly accessing a DRAM row can cause bit flips in other physically near by rows [CLICK]
A common method of mitigating RowHammer is refreshing potentially affected rows, called preventive refresh [CLICK]

## Slide 246: Periodic Refresh with Increasing DRAM Chip Density
A larger capacity chip has more rows to be refreshed
A smaller cell stores less charge
Significant performance and energy overhead
Chart: DRAM Chip Capacity
| 2 | 4 | 8 | 16 | 32 | 64 | 128
Baseline | 0.97444 | 0.96375 | 0.94679 | 0.92168 | 0.88302 | 0.82497 | 0.73698
26% Slowdown
More periodic refresh operations incur larger performance overhead as DRAM chip density increases
Notes: With increasing DRAM chip density, [CLICK]
More rows need to be refreshed [CLICK]
And cells can store smaller charge leading to more periodic refresh operations[CLICK]
In this plot, we sweep DRAM chip capacity on the x-axis and investigate how the performance overhead of DRAM refresh operations change[CLICK]
We observe 26% slowdown in system performance caused by periodic refreshes [CLICK]

## Slide 247: RowHammer and Preventive Refresh with Increasing DRAM Chip Density
Significant performance and energy overhead
Chart: 
| The Min. ACT Count to Observe Bit Flips
2014 | 139.2
2020 | 9.6
Preventive refresh operations need to be performed more aggressively as DRAM chip density increases
Chart: RowHammer Threshold The Minimum Activation Count needed to induce the first RowHammer bit flip
| 1024 | 512 | 256 | 128 | 64
PARA | 0.71 | 0.55 | 0.36 | 0.13 | 0.04
96% Slowdown
RowHammer vulnerability worsens as DRAM chip density increases
Notes: Again with increasing DRAM chip density, [CLICK]
RowHammer vulnerability worsens such that [CLICK] RowHammer threshold, which is the minimum activation count needed to induce RowHammer bit flips, is reduced by more than an order of magnitude in less than a decade, requiring more aggressive preventive refresh operations [CLICK]
We observe as large as 96% slowdown in system performance with reducing RowHammer threshold [CLICK]

## Slide 248: HiRA: Hidden Row Activation – Key Insight
Subarray X
Subarray Y
Activating two rows in quick succession that are in different subarrays in the same bank can refresh one row concurrently with activating the other row
Row A
Row B
Refreshes RowA
concurrently with
Activating RowB
ACT
ACT
DRAM Bank
Notes: HiRA is based on the key insight that [CLICK]
activating two rows in quick succession [CLICK]
That are in different subarrays in the same bank[CLICK]
Can refresh one row [CLICK]
Concurrently with activating the other row [CLICK]

## Slide 249: HiRA: Hidden Row Activation
Refresh RowA concurrently with Activating RowB
HiRA
Saved time using HiRA
ACT
RowA
PRE
ACT
RowB
PRE
time
time
RowA’s
refresh
RowB’s activation
ACT
RowA
PRE
ACT
RowB
PRE
RowA’s
refresh
RowB’s activation
Reduction in the time spent for two refreshes
RD
RD
RD
RD
Without HiRA
With HiRA
Precharge
Notes: Here is an example of how HiRA refreshes a RowA concurrently with activating a RowB [CLICK]
Without HiRA, only one row can be activated in a bank at a given time [CLICK]
Therefore, we activate RowA, wait until the row is refreshed [CLICK]
Precharge the bank [CLICK]
And activate RowB to read data from RowB [CLICK]
With HiRA, [CLICK]
We issue ACT-PRE-ACT command sequence [CLICK]
Which starts RowA’s refresh with the first ACT [CLICK]
And RowB’s activation with the second ACT [CLICK]
With this parallelization, we can perform the column access earlier [CLICK]

## Slide 250: HiRA in Off-the-Shelf DRAM Chips: Key Result 1
HiRA works in 56 off-the-shelf DRAM chips from SK Hynix
HiRA performs a given row’s refresh concurrently with activating any of the 32% of the rows in the same bank
Refresh RowA
32%
ACT RowB
DRAM Bank
HiRA(RowA, RowB)
Notes: We observe that HiRA works in 56 off-the-shelf dRAM chips from SK-Hynix, which we specify in the full paper [CLICK]
To leverage HiRA [CLICK]
for a given DRAM row's refresh, [CLICK]
we can choose any of the 32% of the rows in the same bank to activate concurently with the refresh [CLICK]

## Slide 251: HiRA in Off-the-Shelf DRAM Chips: Key Result 2
HiRA works in 56 off-the-shelf DRAM chips from SK Hynix
51.4% reduction in the time spent for refresh operations
HiRA effectively reduces the time spent for refresh operations in off-the-shelf DRAM chips
Notes: And we observe that HiRA reduces time spent for refresh operations by 51.4% [CLICK]
Therefore, we conclude that HiRA effectively reduces the time spent for refresh operation in off-the-shelf DRAM chips [CLICK]

## Slide 252: HiRA in Off-the-Shelf DRAM Chips: Key Results
HiRA works in 56 off-the-shelf DRAM chips from SK Hynix
51.4% reduction in the time spent for refresh operations
HiRA performs a given row’s refresh concurrently with activating any of the 32% of the rows in the same bank
Refresh RowA
32%
ACT RowB
DRAM Bank
HiRA(RowA, RowB)
HiRA effectively reduces the time spent for refresh operations in off-the-shelf DRAM chips
https://arxiv.org/pdf/2209.10198.pdf
Notes: The full paper contains more experimental results [CLICK]

## Slide 253: HiRA-MC: HiRA Memory Controller
Goal: Leverage HiRA’s parallelism as much as possible
Key Insight: A time slack is needed to find a row activation and a refresh to perform HiRA
  RowA and RowZ are in two electrically disconnected subarrays
Ref(RowA) is generated
Ref(RowA)
deadline
time slack
ACT
RowX
ACT
RowY
ACT
RowZ
ACT
RowT
time
Ref(RowA) is generated
Ref(RowA) deadline
time slack
ACT
RowX
ACT
RowY
HiRA
RowA,RowZ
ACT
RowT
time
Notes: HiRA-MC’s goal is to leverage HiRA’s parallelism as much as possible [CLICK]
It is based on the key insight that a time slack is needed to find a row activation and a refresh that we can perform HiRA on [CLICK]
Here is an example on a timeline [CLICK]
HiRA-MC generates a refresh request [CLICK]
With a time slack before it needs to be performed [CLICK]
During this time slack, the memory controller can perform row activations [CLICK]
Assuming that RowZ and RowA are in two electrically disconnected subarrays, [CLICK]
HiRA-MC replaces rowZ’s activation with a hiRA operation targeting both RowA and RowZ. [CLICK]

## Slide 254: HiRA-MC: HiRA Memory Controller
Generates each periodic refresh and RowHammer-preventive refresh with a deadline
Buffers each refresh request and performs the refresh request until the deadline
Finds if it can refresh a DRAM row concurrently with a DRAM access or another refresh
1
2
3
Notes: HiRA-MC contains the necessary components to timely generate each periodic and RowHammer-preventive refresh request with a deadline [CLICK]
To buffer each refresh request until its deadline [CLICK]
And to find if it can refresh a row concurrently with a DRAM access or another refresh request [CLICK]

## Slide 255: Performance Evaluation
Cycle-level simulations using Ramulator [Kim+, CAL 2015]
System Configuration:
Workloads: 125 different 8-core multiprogrammed workloads from the SPEC2006 benchmark suite
DRAM Chip Capacity: {2, 4, 8, 16, 32, 64, 128} Gb
RowHammer Threshold: {1024, 512, 256, 128, 64} activations The minimum number of row activations needed to induce the first RowHammer bit flip
Processor | 3.2 GHz, 8 core, 4-wide issue, 128-entry instr. window
Last-Level Cache | 64-byte cache line, 8-way set-associative, 8 MB
Memory Scheduler | FR-FCFS
Address Mapping | Minimalistic Open Pages
Main Memory | DDR4, 4 bank group, 4 banks per bank group (16 banks per rank)
Timing Parameters | t1=t2=3ns, tRC= 46.25ns, tFAW=16ns
Notes: We use Ramulator for cycle-level simulations in our performance evaluation [CLICK]
We simulate a realistic system with the shown parameters that I will not explain in detail [CLICK]
We simulate 125 different 8-core multiprogrammed workloads [CLICK]
We sweep DRAM chip capacity from 2Gb to 128Gb [CLICK]
And RowHammer threshold: the minimum number of activations needed to induce the first RowHammer bit flip from 1K to 64 [CLICK]

## Slide 256: HiRA for Periodic Refreshes
No-Refresh: No periodic refresh is performed (Ideal case)
Baseline: Auto-Refresh (using conventional REF commands)
Chart: DRAM Chip Capacity (Gb)
No Refresh | 1 | 1 | 1 | 1 | 1 | 1 | 1
Baseline | 0.97444 | 0.96375 | 0.94679 | 0.92168 | 0.88302 | 0.82497 | 0.73698
HiRA | 0.99767 | 0.99559 | 0.99078 | 0.98242 | 0.96378 | 0.91933 | 0.82891
26%
slowdown
12.6% speedup
Periodic refreshes cause significant (26%) performance overhead
HiRA improves system performance by 12.6% over the baseline
Notes: This plot shows DRAM chip capacity on the x-axis and system performance on the y-axis [CLICK]
System performance is normalized to an ideal system with no periodic refresh [CLICK]
Baseline system uses conventional REF commands [CLICK]
We observe that periodic refreshes cause significant slow down as DRAM chip capacity increases [CLICK]
And HiRA improves system performance by 12.6% compared to the baseline [CLICK]

## Slide 257: HiRA for Preventive Refreshes
Chart: RowHammer Threshold (Number of Activations)
| 1024 | 512 | 256 | 128 | 64
No-Defense | 1 | 1 | 1 | 1 | 1
PARA | 0.71 | 0.55 | 0.36 | 0.13 | 0.04
HiRA | 0.75281 | 0.74292 | 0.58374 | 0.37517 | 0.14937
No Defense: No RowHammer mitigation employed (i.e., no preventive refresh)
PARA [Kim+, ISCA’14]: the RowHammer defense with the lowest hardware overhead
96%
slowdown
3.7x speedup
PARA significantly reduces (by 96%) system performance
HiRA improves system performance by 3.7x over PARA
Notes: This plot shows RowHammer threshold on the x-axis and system performance on the y-axis [CLICK]
System performance is normalized to a system with no RowHammer defense and thus no preventive refreshes [CLICK]
As the baseline, we choose PARA the RowHammer defense with the lowest hardware overhead for this analysis [CLICK]
We observe that preventive refreshes cause significant slow down as RowHammer threshold reduces[CLICK]
And HiRA improves system performance by 3.7x compared to PARA [CLICK]
Proof of concept

## Slide 258: More in the Full Paper
Real DRAM Chip Experiments
  Verification of HiRA’s functionality
  Variation in HiRA’s characteristics across banks
Sensitivity to
  length of time slack for refreshes
  number of channels
  number of ranks
Hardware Complexity Analysis
  Chip area cost of 0.0023% of a processor die per DRAM rank
  No additional latency overhead
Experimental Methodology
  Detailed algorithms for each set of real chip experiments
  Extensive security analysis for RowHammer-preventive refreshes
Detailed Algorithm of Finding Concurrent Refreshes
Notes: Please refer to the full paper for more
Real DRAM chip experiments on verification of HiRA and HiRA’s variation across banks [CLICK]
Sensitivity to the time slack and the number of channels and ranks [CLICK]
The hardware complexity analysis where we show that HiRA-MC is a low cost mechanism [CLICK]
Details about the experimental methodology, including detailed algorithms of real chip experiments and an extensive security analysis for preventive refreshes [clICK]
And detailed algorithm of finding concurrent refreshes [CLICK]

## Slide 259: HiRA: Hidden Row Activation
HiRA concurrently activates two rows in a DRAM bank
  Challenge 1 : Only one row can be activated in a DRAM bank at a given time
  Solution 1 : HiRA violates timing constraints for concurrent row activations
HiRA activates two DRAM rows in the same bank
  Challenge 3: The two rows can override each other’s data via shared bitlines
  Solution 3 : HiRA uses rows from two electrically disconnected subarrays
HiRA issues two row activation (ACT) commands in quick succession
  Challenge 2 : DRAM chips ignore the second activation before precharge
  Solution 2 : HiRA issues a precharge (PRE) command between two ACTs
HiRA violates DRAM timing constraints by issuing a sequence of ACT-PRE-ACT commands that target two rows in two electrically disconnected subarrays
Notes: To make HiRA work, we overcome three challenges: [CLICK]
First, HiRA concurrently activates two rows in the same bank [CLICK]
But row activations in a bank are not performed concurrently [CLICK]
HiRA overcomes this challenge by violating certain timing constraints that leads to concurrent row activations in a bank [CLICK]
Second, HiRA needs to issue two row activation commands in quick succession [CLICK]
But DRAM chips ignore a. second row activation before a DRAM bank is precharged [CLICK]
HiRA overcomes this challenge by issuing a precharge command in between two row activations [CLICK]
Third, HiRA activates two DRAM rows in the same bank [CLICK]
But concurrently activating two rows in the same bank can lead the two rows to override each other’s data over shared bitlines [CLICK]
HiRa overcomes this challenge by choosing two rows from electrically disconnected subarrays [CLICK]
Therefore, hiRA violates DRAM timing constraints in issuing a sequence of Act-PRE-ACT commands that target two rows in two electrically disconnected subarrays []CLICK

## Slide 260: HiRA: Hidden Row Activation
Refreshing RowA concurrently with Activating RowB
The time saved using HiRA
ACT
RowA
PRE
ACT
RowB
PRE
time
time
RowA’s refresh
RowB’s activation
ACT
RowA
PRE
ACT
RowB
PRE
RowA’s refresh
RowB’s activation
Reduction in the time spent for two refreshes
RD
RD
RD
RD
HiRA
Without HiRA
With HiRA
Precharge
RowB’s refresh
RowB’s refresh

## Slide 261: HiRA Operation
Overlapped
ACT
PRE
RD
RD
RD
ACT RowB
PRE
ACT RowA
HiRA
t1
t2
tRCD
RowA
RowB
tRestoreA
tRestoreB
tRP
time
Local Row
Buffer X
Local Row
Buffer Y
HiRA refreshes RowA concurrently with activating RowB by issuing ACT-PRE-ACT commands in quick succession
Bank I/O
Notes: ACT RowA : Connencts RowA to its Local Row Buffer, starting the refresh of RowA
PRE: Interrupts row activation before the local row buffer X is connnected to the bank i/o
ACT RowB: Interrupts the PRE operation before it closes the rowB

## Slide 262: HiRA in Off-the-Shelf DRAM Chips: Key Results
HiRA works in 56 off-the-shelf DRAM chips from SK Hynix
51.4% reduction in the time spent for refresh operations
HiRA performs a given row’s refresh concurrently with activating any of the 32% of the rows in the same bank
Refresh RowA
32%
ACT RowB
DRAM Bank
HiRA(RowA, RowB)
HiRA effectively reduces the time spent for refresh operations in off-the-shelf DRAM chips
Notes: To leverage HiRA [CLICK]
for a given DRAM row's refresh, [CLICK]
we can choose any of the 32% of the rows in the same bank to concurrently activate [CLICK]
Therefore, HiRA effectively reduces the time spent for refresh operations in off-the-shelf DRAM chips [CLICK]
KEEP THE TABLE HERE

## Slide 263: HiRA Support in Off-the-Shelf DRAM Chips
56 off-the-shelf DDR4 DRAM chips support HiRA (from SK Hynix)
HiRA Coverage of a given DRAM row:
  Refresh a given DRAM row while activating other rows in the same bank
  We sweep two timing parameters: t1 and t2
ACT RowB
PRE
ACT RowA
HiRA
t1
t2
HiRA can refresh a DRAM row concurrently with 32% of any of the other DRAM rows in the same bank
t1 and t2 can be as small as 3ns

## Slide 264: HiRA’s Second Row Activation
Does performing HiRA in between refresh the victim row?
  If HiRA’s second row activation is performed, more activations are needed to induce RowHammer bit flips
  If HiRA’s second row activation is ignored, RowHammer threshold should not change
Hammer N/2 times
Hammer N/2 times
NOP
Hammer N/2 times
Hammer N/2 times
HiRA

## Slide 265: Variation across DRAM Banks
Coverage: Identical across banks
The effect of second row activation

## Slide 266: HiRA-MC: HiRA Memory Controller
Goal: Leverage HiRA’s parallelism as much as possible
Periodic and preventive refresh controllers generate each refresh request with a deadline
Refresh Table buffers a refresh request until its deadline
Concurrent Refresh Finder finds if HiRA can refresh a row
  Concurrently with a memory request
  Concurrently with another refresh request
Refresh Generator
RefPtr Table
RefPtr SA1
RefPtr SAn
RefPtr SA0
Periodic Refresh Controller
PR FIFO
RowHammer
Defense Mechanism
Preventive Refresh Controller
Concurrent Refresh Finder
Refresh Table
Memory Request Scheduler

## Slide 267: The Concurrent Refresh Finder
Case 1: Executes when a precharge is issued (completes before the precharge completes)
Case 2: Periodically executes after every tRC (completes before tRC)

## Slide 268: HiRA-MC Example
Case 1: Refresh – Access Parallelism
Case 2: Refresh – Refresh Parallelism
RD SA:A Row:0
RD SA:B Row:0
Head
Memory Request Queue
REF SA:B Row:6
REF SA:B Row:1
REF SA:C Row:2
Refresh Table
HiRA(Row SA:B Row:6, SA:A Row:0)
time
ACT SA:B Row:6
ACT SA:A Row:0
PRE
6ns
RD SA:B Row:0
Head
Memory Request Queue
REF SA:B Row:1
REF SA:C Row:2
Refresh Table
HiRA(Row SA:B Row:1, SA:C Row:2)
time
ACT SA:B Row:1
ACT SA:C Row:2
PRE
6ns
HiRA-MC provides refresh-access and refresh-refresh parallelism

## Slide 269: HiRA-MC Hardware Complexity
We use CACTI with 22nm technology node
HiRA-MC Component | Area (mm2) | Area (% of Chip Area) | Access Latency
Refresh Table | 0.00031 | <0.0001% | 0.07ns
RefPtr Table | 0.00683 | 0.0017% | 0.12ns
PR-FIFO | 0.00029 | <0.0001% | 0.07ns
Subarray Pairs Table | 0.00180 | 0.0005% | 0.09ns
Overall | 0.00923 | 0.0023% | 6.31ns
HiRA-MC does not increase memory access latency
HiRA-MC consumes only 0.0023% of CPU chip area per DRAM rank
HiRA-MC Overall Latency: 6.31ns
PRE
ACT
Precharge latency: ~14.5ns
time

## Slide 270: Estimating Periodic Refresh Overhead
Latency of a REF command
DRAM Chip
Capacity

## Slide 271: Reducing Overall Latency of Two Refreshes
Refreshing two rows using nominal timing parameters:
Using HiRA:
ACT RowA
PRE
ACT RowB
PRE
tRAS: 32ns
tRP: 14.25ns
tRAS: 32ns
time
ACT RowA
PRE
ACT RowB
PRE
t1: 3ns
tRAS: 32ns
time
t2: 3ns
51.4% reduction
Overall latency of refreshing two rows reduces by 51.4%
from 78.25ns down to 38ns

## Slide 272: Tested DRAM Chips
https://arxiv.org/pdf/2209.10198.pdf

## Slide 273: HiRA-MC: HiRA Memory Controller
Periodic and preventive refresh controllers generate each refresh request with a deadline
Refresh Table buffers a refresh request until its deadline
Concurrent Refresh Finder finds if HiRA can refresh a row
  Concurrently with a DRAM access
  Concurrently with another refresh request
Periodic Refresh Controller
RowHammer
Defense Mechanism
Preventive Refresh Controller
Concurrent Refresh Finder
Refresh Table
Memory Request Scheduler

## Slide 274: HiRA for Periodic Refreshes

## Slide 275: RowHammer Thresholds

## Slide 276: HiRA for Preventive Refreshes

## Slide 277: HiRA for Periodic Refresh Sensitivity to Number of Channels and Ranks

## Slide 278: HiRA for Preventive Refresh Sensitivity to Number of Channels and Ranks

## Slide 279: Workload Memory Access Characteristics
125 different 8-core multiprogrammed workloads
Three histograms showing MPKI, RBCPKI, and RBHPKI respectively
Notes: ADD THIS TO ARXIV VERSION

## Slide 280: RowHammer Mitigation across Generations
105
104
103
102
105
104
103
102
DDR3-old
DDR3-new
DDR4-old
LPDDR4-1x
DDR4-new
LPDDR4-1y
PARA
TWiCe-ideal
Ideal
HCfirst (number of hammers required to induce first RowHammer bit flip)
14%
J. S. Kim, M. Patel, A. G. Yaglikci, H. Hassan, R. Azizi, L. Orosa, and O. Mutlu, "Revisiting RowHammer: An Experimental Analysis of Modern Devices and Mitigation Techniques,” in ISCA, 2020.

## Slide 281: Refresh Delay
DDRx protocols allow a REF command to be postponed for ~70us
HiRA-MC’s current design does not leverage this flexibility
A longer time slack allows
  the baseline to better utilize DRAM idle time to perform refresh operations
  HiRA to find more opportunities to perform a refresh operation concurrently with a DRAM access
Future sensitivity study: the effect of long refresh delays
REF
REF
REF
REF
REF
7.8us
7.8us
7.8us
7.8us
REF
REF
REF
REF
REF
~70us
REF
REF
REF
REF
REF
7.8us
7.8us
7.8us
7.8us
REF
REF
REF
REF
REF
7.8us
7.8us
7.8us
7.8us
time slack
longer time slack

## Slide 282: Energy
HiRA does not change the number of refresh operations at a given time window
  Overall energy consumed for refresh operations is the same
HiRA improves system performance
  Reduces the background energy consumption
Evaluation requires an accurate power model based on real system measurements, similar to VAMPIRE [Ghose+ SIGMETRICS’17], but for HiRA operations

## Slide 283: HiRA: Hidden Row Activation for Reducing Refresh Latency of Off-the-Shelf DRAM Chips
Abdullah Giray Yağlıkçı
Ataberk Olgun Minesh Patel Haocong Luo Hasan Hassan
Lois Orosa Oğuz Ergin Onur Mutlu
Notes: This concludes my talk. Thanks for listening. I’m happy to receive your questions.

## Slide 284: Identifying Suspect Threads: High Level Algorithm
BreakHammer detects threads that trigger too many RowHammer-preventive actions
Thread 1
Thread 2
Thread 3
Thread 4
>
Minimum score to consider a thread as suspect
Maximum deviation
from the average score
>
>
Benign
Benign
Benign
Suspect
Notes: BreakHammer identifies threads that cause too much overhead due to triggering RowHammer-preventive actions, we call such threads suspect threads.
BreakHammer performs two checks to determine a thread as suspect:
[CLICK] First, BreakHammer checks if a thread’s score exceeds a minimum threshold
[CLICK] Second, BreakHammer checks if a thread’s score largely deviates from the average score of all threads
[CLICK] A thread that satisfies both checks is identified as a suspect thread