## Slide 1: Enabling Efficient and Scalable Read Disturbance Mitigation via New Experimental Insights into Modern Memory Chips
agyaglikci.github.io
safari.ethz.ch
Abdullah Giray Yaglikci
agyaglikci@gmail.com
https://agyaglikci.github.io
13 March 2024
ARM Cambridge
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 2: Lack of Memory Isolation
Memory
access
1  0
An access to one memory address
should not have unintended side effects
on data stored in other addresses
Leak Private Information
Take Over a Computer
Data Loss or Corruption
Compromise Application Correctness
Memory isolation is difficult in modern memory chips
Notes: I will start with a brief background on memory isolation, a fundamental primitive for system security and privacy [CLICK]
Imagine that you access a memory location, and a bitflip occurs in some other location [CLICK]
Prior works show that if this happens

## Slide 3: DRAM Read Disturbance
Reading from a memory location disturbs data in physically nearby locations
Used Lane
Swimming in a lane disturbs
nearby lanes
Read
Bitflips
Bitflips
Notes: Unfortunately, [CLICK]
an access to a DRAM region, [CLICK]
disturbs the data in other physically nearby regions and this phenomenon is called DRAM read disturbance [CLICK]

## Slide 4: DRAM Read Disturbance – Swimming Pool Analogy
Swimming in a lane disturbs nearby lanes
Notes: Let me explain read disturbance with an analogy of a swimming pool[CLICK]
With multiple lanes [CLICK]
A swimmer uses only the middle lane [CLICK]
but by creating waves, causes disturbance in nearby lanes [CLICK]

## Slide 5: The RowHammer Vulnerability [Kim+, ISCA’14]
Row 0
Row 1
Row 2
Row 3
Row 4
Repeatedly opening (activating) and closing (precharging)
a DRAM row causes RowHammer bitflips in nearby cells
and breaks memory isolation
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 2
closed
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
closed
Aggressor Row
DRAM Subarray
Notes: Due to an increase in cell-to-cell interference, as a result of aggressive technology node scaling, rapidly activating [CLICK] and precharging
[FORTH & BACK] a DRAM row can result in bit flips in physically adjacent rows [CLICK]
[FORTH & BACK] Continuing to access the same row results in even more failures in nearby rows. This phenomenon is known as RowHammer. [CLICK]
We refer to the rapidly accessed row as an aggressor row and the rows containing bit flips as victim rows.

## Slide 6: An Example RowHammer Mitigation: Preventive Refresh
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 0
Row 1
Row 3
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
DRAM Subarray
Refreshing potential victim rows mitigates read disturbance bitflips
Aggressor Row

## Slide 7: Motivation
DRAM chips are increasingly more vulnerable to read disturbance with technology scaling
Technology Scaling
Chart: 
| The Min. ACT Count to Observe Bit Flips
2023 | 1
2020 | 9.6
2014 | 139.2
[Luo+, ISCA’23]
[Kim+, ISCA’20]
[Kim+, ISCA’14]
Notes: With technology node scaling, DRAM chips are getting more vulnerable to read disturbance [CLICK]
and defenses become prohibitively expensive [CLICK]
Therefore, we need a deeper understanding of DRAM read disturbance [CLICK]
to provide effective and efficient solutions [CLICK]

## Slide 8: Two Main Types of DRAM Refresh
2
Periodic Refresh:
Periodically restores the charge which DRAM cells leak over time once in every 32ms or 64ms
1
Preventive Refresh:
Mitigates read disturbance by refreshing potential victim rows
Putting into Perspective:
Bitflips occur at ~1000 row activations scattered across 64ms
64ms is as large as to accommodate 1,280,000 activations
An attack needs only 0.08% of the activation budget
1280 rows can be concurrently hammered
1280 additional refreshes are needed
Notes: DRAM Refresh is mainly used for two purposes [CLICK]
The first one is called: Periodic Refresh to periodically restore the charge that DRAM cells leak over time [CLICK]
The second one is relevant to a read-disturb error mechanism called RowHammer, where repeatedly accessing a DRAM row can cause bit flips in other physically near by rows [CLICK]
A common method of mitigating RowHammer is refreshing potentially affected rows, called preventive refresh [CLICK]

## Slide 9: Two Main Types of DRAM Refresh
2
Periodic Refresh:
Periodically restores the charge which DRAM cells leak over time once in every 32ms or 64ms
1
Preventive Refresh:
Mitigates read disturbance by refreshing potential victim rows
Putting into Perspective:
Bitflips occur at ~1000 row activations scattered across 32ms
64ms is as large as to accommodate 1,280,000 activations
An attack needs only 0.08% of the activation budget
1280 rows can be concurrently hammered
1280 additional refreshes are needed
An attacker can keep low profile (e.g., uses 0.08% of activation budget)
and induce bitflips
Preventing bitflips requires
tracking many rows and performing many refreshes
Notes: DRAM Refresh is mainly used for two purposes [CLICK]
The first one is called: Periodic Refresh to periodically restore the charge that DRAM cells leak over time [CLICK]
The second one is relevant to a read-disturb error mechanism called RowHammer, where repeatedly accessing a DRAM row can cause bit flips in other physically near by rows [CLICK]
A common method of mitigating RowHammer is refreshing potentially affected rows, called preventive refresh [CLICK]

## Slide 10: How Large is 1000 Activations?
Bitflips occur at ~1000 activations
Mitigation mechanisms trigger preventive actions (e.g., preventive refresh) at ~500 activations
Is 500 a distinctive activation count?
Benign workloads activate hundreds of rows more than 512 times in a refresh window
Benchmark | MPKI | # of Rows w/ ACT count >512
429.mcf | 68.27 | 2564
470.lbm | 28.09 | 664
519.lbm | 24.37 | 2482
434.zeusmp | 22.24 | 292
510.parest | 17.79 | 94
437.leslie3d | 15.82 | 7
483.xalancbmk | 13.67 | 113
482.sphinx3 | 12.59 | 304
505.mcf | 11.35 | 732
471.omnetpp | 10.72 | 122
tpch2 | 9.09 | 88
520.omnetpp | 9.00 | 32
tpch17 | 7.43 | 26
Memory intensive workloads from SPEC’06/17, TPC, YCSB, and MediaBench
Sorted

## Slide 11: How Large is 1000 Activations?
Bitflips occur at ~1000 activations
Mitigation mechanisms trigger preventive actions (e.g., preventive refresh) at ~500 activations
Is 500 a distinctive activation count?
Benign workloads activate hundreds of rows more than 500 times in a refresh window
Benchmark | MPKI | # of Rows w/ ACT count >512
429.mcf | 68.27 | 2564
470.lbm | 28.09 | 664
519.lbm | 24.37 | 2482
434.zeusmp | 22.24 | 292
510.parest | 17.79 | 94
437.leslie3d | 15.82 | 7
483.xalancbmk | 13.67 | 113
482.sphinx3 | 12.59 | 304
505.mcf | 11.35 | 732
471.omnetpp | 10.72 | 122
tpch2 | 9.09 | 88
520.omnetpp | 9.00 | 32
tpch17 | 7.43 | 26
Memory intensive workloads from SPEC’06/17, TPC, YCSB, and MediaBench
Sorted
Benign workloads might not be so benign
even if they are not very memory intensive

## Slide 12: Read Disturbance is an Outstanding Problem
Increasing DRAM chip density
exacerbates DRAM read disturbance
Attackers can keep low profile
(using <0.16% of the row activation budget)
Benign applications become not-so-benign
Efficient and scalable solutions are needed

## Slide 13: Thesis
A deeper understanding of
DRAM read disturbance
is the key to enable
efficient and scalable solutions

## Slide 14: My Dissertation Works
A deeper look into DRAM read disturbance
Solutions to DRAM read disturbance
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
Throttling Unsafe Accesses
Parallelizing Preventive Actions
Leveraging
Heterogeneity
Notes: I also developed solutions that [CLICK]
throttle unsafe accesses [CLICK
parallelize maintenance operations [CLICK]
and leverage heterogeneity [CLICK]
Let me quickly explain one of these works [CLICK]

## Slide 15: Our Recent Works
Temperature
Memory access patterns
Victim cell’s physical location
Leveraging
Heterogeneity
Notes: I also developed solutions that [CLICK]
throttle unsafe accesses [CLICK
parallelize maintenance operations [CLICK]
and leverage heterogeneity [CLICK]
Let me quickly explain one of these works [CLICK]

## Slide 16: DRAM Testing Infrastructure
  DRAM Bender on a Xilinx Virtex UltraScale+ XCU200
Fine-grained control over DRAM commands,
timing parameters (±1.5ns), temperature (±0.5°C ),
and wordline voltage (±1mV)
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips,” in TCAD, 2023. [GitHub: https://github.com/CMU-SAFARI/DRAM-Bender]
*
Notes: We use an FPGA-based experimental setup programmed with a modified version of SoftMC [CLICK]
We control the chip temperature using a pair of heaters [CLICK] connected to a temperature controller [CLICK]
We supply the wordline voltage using the VPP power rail from an external power supply [CLICK]
This infrastructure provides fine-grained control over DRAM commands, timing parameters, temperature, and wordline voltage [CLICK]
=======

## Slide 17: DRAM Chips Tested
Mfr. | DDR4 DIMMs | DDR3 SODIMMs | # Chips | Density | Die | Org.
A (Micron) | 9 | 1 | 144 (8) | 8Gb (4Gb) | B (P) | x4 (x8)
B (Samsung) | 4 | 1 | 32 (8) | 4Gb (4Gb) | F (Q) | x8 (x8)
C (SK Hynix) | 5 | 1 | 40 (8) | 4Gb (4Gb) | B (B) | x8 (x8)
D (Nanya) | 4 | - | 32 (-) | 8Gb (-) | C (-) | x8 (-)
272 DRAM Chips in total
Two DRAM standards
4 Major Manufacturers
Notes: In our characterization, [CLICK]
we test 272 real DRAM chips [CLICK]
from four major manufacturers, [CLICK]
that implement DDR3 and DDR4 DRAM standards [CLICK]
and with different densities, die revisions, and chip organizations[CLICK]

## Slide 18: Key Findings: Temperature
Temperature
Vulnerability to Read Disturbance
DRAM read disturbance is more effective within a bounded temperature range
Vulnerable temperature range varies across cells
A DRAM cell should be tested at each possible operating temperature
Different
DRAM Cells
Trap-Assisted Charge Leakage Model
Hammering a wordline pulls and pushes electrons
Electrons get trapped and exacerbate charge leakage, leading to cause bitflips
With increasing temperature, it becomes less likely for an electron to get trapped
Notes: I will share two examples of many novel observations in these works. The first one is temperature. [CLICK]
We observe that DRAM read disturbance is more effective within a temperature range [CLICK]
Vulnerable temperature range varies across memory regions [CLICK]

## Slide 19: Contributions to Understanding RowHammer
Lois Orosa*, Abdullah Giray Yağlıkçı*, Haocong Luo, Ataberk Olgun, Jisung Park, Hasan Hassan, Minesh Patel, Jeremie S. Kim, and Onur Mutlu, "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Talk Video (21 minutes)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (1.5 minutes)] [arXiv version]
Notes: Our goal in this work is to Provide insights into three fundamental properties of RowHammer:
Temperature [CLICK]
Aggressor row active time [CLICK]
Victim DRAM cell's physical location [CLICK]
By doing so we aim enabling research to find effective and efficient attacks and defenses [CLICK]

## Slide 20: A Follow-Up Work: SpyHammer [Orosa+, arXiv’22]
https://arxiv.org/pdf/2210.04084.pdf

## Slide 21: Our Recent Works
Temperature
Memory access patterns
Victim cell’s physical location
Leveraging
Heterogeneity
Notes: I also developed solutions that [CLICK]
throttle unsafe accesses [CLICK
parallelize maintenance operations [CLICK]
and leverage heterogeneity [CLICK]
Let me quickly explain one of these works [CLICK]

## Slide 22: Key Findings: Memory Access Patterns
Read disturbance is more effective
if the activated aggressor row stays active longer
Chart: 
| The Min. ACT Count to Observe Bit Flips
2014 | 6.4
2020 | 10
State-of-the-Art
Our Finding
Minimum activation count to induce the first bitflip
36% reduction
Fewer reads cause a more significant read disturbance
when the activated aggressor row stays active longer
Open
Close
Open
Close
Existing mitigations are ineffective without this insight
Notes: The second example is about the memory access patterns. [CLICK]
We observe that read disturbance is more effective if the read memory region stays active longer [CLICK]
And thus fewer reads cause bitflips[CLICK]

## Slide 23: Contributions to Understanding RowHammer
Lois Orosa*, Abdullah Giray Yağlıkçı*, Haocong Luo, Ataberk Olgun, Jisung Park, Hasan Hassan, Minesh Patel, Jeremie S. Kim, and Onur Mutlu, "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Talk Video (21 minutes)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (1.5 minutes)] [arXiv version]
Notes: Our goal in this work is to Provide insights into three fundamental properties of RowHammer:
Temperature [CLICK]
Aggressor row active time [CLICK]
Victim DRAM cell's physical location [CLICK]
By doing so we aim enabling research to find effective and efficient attacks and defenses [CLICK]

## Slide 24: RowPress [Luo+, ISCA 2023] (Follow up of our analysis)
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 min)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Best artifact award at ISCA 2023.
Keep rows active for 36ns: 47K activations are enough to induce bitflips
Keep rows active for 7.8us: 5K activations are enough to induce bitflips
Keep rows active for 30ms: 1 activation is enough to induce bitflips

## Slide 25: Our Recent Works
Temperature
Memory access patterns
Victim cell’s physical location
Leveraging
Heterogeneity
Notes: I also developed solutions that [CLICK]
throttle unsafe accesses [CLICK
parallelize maintenance operations [CLICK]
and leverage heterogeneity [CLICK]
Let me quickly explain one of these works [CLICK]

## Slide 26: Variation in Read Disturbance Vulnerability Across DRAM Rows
DRAM Rows
To induce a read disturbance bitflip, one should access a row
Read disturbance solutions are configured for the worst row
Not all rows need the same level of protection
Read disturbance solutions incur large performance overheads due to overprotecting many rows
>100K times
10K-100K times
1-10K times
Spatial variation in read disturbance vulnerability
across DRAM rows

## Slide 27: Tested DRAM Chips
144 DRAM chips from SK Hynix, Micron, and Samsung
Notes: We test 144 DRAM chips [CLICK]
That implement various densities-die revisions [CLICK]
And chip organizations [CLICK]

## Slide 28: Key Takeaway from Real Chip Experiments
Read disturbance vulnerability varies
significantly and irregularly across DRAM rows
Notes: And show that there is a large variation in read disturbance across rows

## Slide 29: Spatial Variation in the Minimum Hammer Count to Induce the First Bitflip across DRAM Rows
The minimum hammer count to induce the first bitflip
significantly varies across rows in a DRAM bank
Minimum hammer count to induce the first bitflip (HCfirst)
Fraction of DRAM Rows
Variation across banks
Different DRAM modules from Mfr. S
S0
S1
S2
S3
S4
Worst
HCfirst
Notes: And show that there is a large variation in read disturbance across rows

## Slide 30: Spatial Variation in the Minimum Hammer Count to Induce the First Bitflip across DRAM Rows
Minimum hammer count to induce the first bitflip (HCfirst)
Fraction of DRAM Rows
Fraction of DRAM Rows
Fraction of DRAM Rows

## Slide 31: Spatial Variation in the Minimum Hammer Count to Induce the First Bitflip across DRAM Rows
Minimum Hammer Count to Induce the First Bitflip (HCfirst)
The minimum hammer count to induce the first bitflip
significantly varies across rows in a DRAM bank

## Slide 32: More Detailed Information in the Extended Version
https://arxiv.org/pdf/2402.18652.pdf

## Slide 33: Our Recent Works
Temperature
Memory access patterns
Victim cell’s physical location
Leveraging
Heterogeneity
Notes: I also developed solutions that [CLICK]
throttle unsafe accesses [CLICK
parallelize maintenance operations [CLICK]
and leverage heterogeneity [CLICK]
Let me quickly explain one of these works [CLICK]

## Slide 34: Motivation
Significant performance and energy overhead
DRAM read disturbance worsens as DRAM chip density increases
Existing solutions become more aggressive
Overprotecting many rows significantly increases their performance overhead
Notes: Quantify

## Slide 35: Motivation
Can we leverage the variation in read disturbance vulnerability across DRAM rows
to reduce the performance overheads
of existing read disturbance solutions?

## Slide 36: Svärd: Spatial Variation-Aware Read Disturbance Defenses
Dynamically tunes the aggressiveness of existing solutions to the victim row’s read disturbance vulnerability
Svärd performs fewer preventive actions (e.g., refresh) for rows that are less vulnerable to read disturbance
Svärd performs more preventive actions (e.g., refresh) for rows that are more vulnerable to read disturbance
Svärd is Swedish for sword, a weapon with a long blade for cutting or thrusting [Merriam-Webster]
Svärd significantly reduces the performance overhead of existing solutions
Notes: We leverage this observation [CLICK]
By protecting weak rows more aggressively than strong rows [CLICK]
We do this by dynamically tuning the aggressiveness of defense mechanisms [CLICK]
and we show significant improvement in system performance. [CLICK]

## Slide 37: Svärd: Integration with Existing Read Disturbance Solutions
PARA: Probabilistic Row Activation [Kim+, ISCA’14]
Row
Activation
Random
Number
>
Threshold
Preventively
refresh the victim row
Yes
victim row
Svärd
>
Threshold
Svärd dynamically tunes PARA’s threshold to the victim row’s vulnerability
Svärd works with many read disturbance solutions, including:
BlockHammer [Yaglikci+, HPCA’21]
Hydra [Qureshi+, ISCA’22]
RRS [Saileshwar+, ASPLOS’22]
AQUA [Saxena+, MICRO’22]
Less vulnerable
Higher threshold
More vulnerable
Lower threshold
 Fewer refresh
 More aggressive refresh

## Slide 38: Svärd: Metadata Management
Classifies DRAM rows into several vulnerability bins
Maintains a few (e.g., four) bits per DRAM row
Implemented where the read disturbance solution is
Memory controller-based implementation:
Metadata can be maintained in
  SRAM table in the memory controller
  Data integrity bits in the DRAM chip
  …
In-DRAM implementation:
Metadata can be maintained in
  DRAM rows
  Separate DRAM array
  …

## Slide 39: Performance Evaluation
Cycle-level simulations using Ramulator 2.0 [Luo+, CAL 2023] https://github.com/CMU-SAFARI/ramulator2
System Configuration:
Workloads: 120 different 8-core multiprogrammed workloads from SPEC CPU2006, SPEC CPU2017, TPC, MediaBench, and YCSB benchmark suites
Integrated with AQUA, BlockHammer, PARA, Hydra, and RRS
HCfirst: {4K, 2K, 1K, 512, 256, 128, 64} hammers Minimum hammer count needed to induce the first bitflip
Processor | 3.2 GHz, 8 core, 4-wide issue, 128-entry instr. window
Last-Level Cache | 64-byte cache line, 8-way set-associative, 8 MB
Memory Scheduler | FR-FCFS
Address Mapping | Minimalistic Open Pages
Main Memory | DDR4, 4 bank group, 4 banks per bank group (16 banks per rank)
Notes: We use Ramulator for cycle-level simulations in our performance evaluation [CLICK]
We simulate a realistic system with the shown parameters that I will not explain in detail [CLICK]
We simulate 125 different 8-core multiprogrammed workloads [CLICK]
We sweep DRAM chip capacity from 2Gb to 128Gb [CLICK]
And RowHammer threshold: the minimum number of activations needed to induce the first RowHammer bit flip from 1K to 64 [CLICK]

## Slide 40: Implications on Future Solutions
Reduction in Performance Overhead
Minimum Hammer Count to Induce the First Bitflip
Weighted Speedup
(Norm. to No Mitigation Baseline)
1.95x
Speedup
Chart: 
| 4K | 2K | 1K | 512 | 256 | 128 | 64
No-Svärd | 0.96807 | 0.93819 | 0.88595 | 0.80096 | 0.67494 | 0.51565 | 0.35924
Svärd-H1 | 0.99152 | 0.98255 | 0.96742 | 0.93687 | 0.88376 | 0.79729 | 0.66985
Svärd-M0 | 0.98584 | 0.97286 | 0.94624 | 0.90116 | 0.82393 | 0.70759 | 0.55516
Svärd-S0 | 0.99782 | 0.99574 | 0.99085 | 0.98196 | 0.96583 | 0.93471 | 0.87954
PARA
Evaluated for three different vulnerability profiles gathered from real DRAM modules

## Slide 41: Implications on Future Solutions
Weighted Speedup
(Norm. to No Mitigation Baseline)
Minimum Hammer Count to Induce the First Bitflip

## Slide 42: Implications on Future Solutions
Weighted Speedup
(Norm. to No Mitigation Baseline)
Minimum Hammer Count to Induce the First Bitflip
1.63x Speedup
4.88x Speedup
1.07x Speedup
4.80x Speedup
Svärd significantly reduces the performance overhead of existing solutions

## Slide 43: Spatial Variation-Aware Read Disturbance Defenses
The first rigorous experimental study on the spatial variation of DRAM read disturbance across DRAM rows
  144 DDR4 DRAM chips from three major manufacturers
  Characterize all rows in a bank and four banks in a DRAM chip
Svärd: Spatial Variation-Aware Read Disturbance Defenses
  Dynamically tunes a solution’s aggressiveness (e.g., perform more/less refresh) to the victim row’s vulnerability to DRAM read disturbance
  Implemented either in the memory controller or in the DRAM chip
Read disturbance vulnerability varies significantly and irregularly across DRAM rows
Svärd significantly reduces the performance overhead of existing solutions
..

## Slide 44: Enabling Efficient and Scalable Solutions
Spatial variation in read disturbance bit error rate across rows
Spatial variation of RowPress across DRAM rows
Algorithms and details of our experiments
Reverse-engineering of subarray boundaries
Hardware Complexity Analysis
  Chip area cost
    Either 0.43% of a processor die per DRAM rank with 16 banks in the memory contr.
    0.006% increase in the DRAM array (4 bits / 8KB)
  No additional latency overhead
A preliminary analysis of the effect of aging on DRAM read disturbance vulnerability
https://arxiv.org/pdf/2402.18652.pdf

## Slide 45: Our Recent Works
Temperature
Memory access patterns
Victim cell’s physical location
Leveraging
Heterogeneity
Notes: I also developed solutions that [CLICK]
throttle unsafe accesses [CLICK
parallelize maintenance operations [CLICK]
and leverage heterogeneity [CLICK]
Let me quickly explain one of these works [CLICK]

## Slide 46: My Dissertation Works
A deeper look into DRAM read disturbance
Solutions to DRAM read disturbance
Temperature
Memory access patterns
Victim cell’s physical location
Voltage
Throttling Unsafe Accesses
Parallelizing Preventive Actions
Leveraging
Heterogeneity
Notes: I also developed solutions that [CLICK]
throttle unsafe accesses [CLICK
parallelize maintenance operations [CLICK]
and leverage heterogeneity [CLICK]
Let me quickly explain one of these works [CLICK]

## Slide 47: More Details and Discussion on YouTube
https://www.youtube.com/live/CRtm1es4n3o?si=8N5zB6e_RUc5Ejl8
https://www.youtube.com/live/YQwRYWpCsk0?si=jXPueMHb5wgs69-q

## Slide 48: Enabling Efficient and Scalable Read Disturbance Mitigation via New Experimental Insights into Modern Memory Chips
agyaglikci.github.io
safari.ethz.ch
Abdullah Giray Yaglikci
agyaglikci@gmail.com
https://agyaglikci.github.io
13 March 2024
ARM Cambridge
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 49: Enabling Efficient and Scalable Read Disturbance Mitigation via New Experimental Insights into Modern Memory Chips
agyaglikci.github.io
safari.ethz.ch
Abdullah Giray Yaglikci
agyaglikci@gmail.com
https://agyaglikci.github.io
11 March 2024
Huawei Cambridge
Current and Future Work Discussion
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 50: Current and Future Challenges
  While the memory systems
  scale-up and are shared across many users (e.g., disaggregated memory systems)
  scale-down in manufacturing technology node size
  support processing near/using memory

Energy
Efficiency

Fairness

Reliability

Performance
Notes: Going forward, we need to address [CLICK]
reliability [CLICK]
Performance [CLICK
Fairness [CLIKC]
And energy efficiency challenges [CLICK]
While memory systems
[CLICK] scale up and shared
[CLICK] scale down in technology node size
[CLICK and support processing near/using memory

## Slide 51: Future Research for Better Memory Systems



Cross-Layer
Communication
Flexible and Intelligent Memory Chips, Interfaces, Controllers
Deeper Understanding of
Physics and Vulnerabilities
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 52: Deeper Understanding of Physics and Vulnerabilities
The effect of aging Preliminary data on aging via 68-day of continuous hammering
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
Aging can lead to read disturbance bitflips at smaller hammer counts
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
52

## Slide 53: Deeper Understanding of Physics and Vulnerabilities
The effect of aging Preliminary data on aging via 68-day of continuous hammering
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
Aging can lead to read disturbance bitflips at smaller hammer counts
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
53
Future work:
rigorous aging characterization
and online profiling of read disturbance vulnerability

## Slide 54: Deeper Understanding of Physics and Vulnerabilities
The effect of aging
Interactions across different error mechanisms
RowHammer
RowPress
Data retention time errors
Variable retention time
…

## Slide 55: Deeper Understanding of Physics and Vulnerabilities
The effect of aging
Interactions across different error mechanisms
What is the worst-case?
  Temperature
  Data pattern
  Memory access pattern
  Spatial variation
  Voltage
What is the worst-case considering all these sensitivities?
What is the minimum hammer count to induce a read disturbance bitflip?

## Slide 56: Deeper Understanding of Physics and Vulnerabilities
The effect of aging
Interactions across different error mechanisms
What is the worst-case?
How reliable are our DRAM chips?
How reliable will our DRAM chips be tomorrow?
We do not know! This is an open research problem

## Slide 57: Future Research for Better Memory Systems



Cross-Layer
Communication
Flexible and Intelligent Memory Chips, Interfaces, Controllers
Deeper Understanding of
Physics and Vulnerabilities
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 58: Flexible and Intelligent Chips, Interfaces, Controllers
In-field patching is necessary
DRAM read disturbance solution is here
DRAM chip is here
Configuration
Aging might change the chip’s characteristics
DRAM module can be replaced
Reconfiguration is needed
+ add more hardware counters
+ increase metadata cache capacity
Deployed solutions should be patchable in field

## Slide 59: Flexible and Intelligent Chips, Interfaces, Controllers
In-field patching is necessary
Interfaces should be more flexible
Memory controller decides what should be done when
DRAM chip has read disturbance solution inside (tracking+prevention)
The memory controller should provide the DRAM chip with necessary time window to perform preventive actions (e.g., refreshing rows)
The memory controller does not have the tracking information
Communicating is not straightforward due to strict communication protocol
A more flexible interface is necessary

## Slide 60: How Large is 1000 Activations?
Bitflips occur at ~1000 activations
Mitigation mechanisms trigger preventive actions (e.g., preventive refresh) at ~500 activations
Is 500 a distinctive activation count?
Benign workloads activate hundreds of rows more than 500 times in a refresh window
Memory intensive workloads from SPEC’06, SPEC’17, TPC, YCSB, and MediaBench
Benign workloads might not be so benign

## Slide 61: Flexible and Intelligent Chips, Interfaces, Controllers
In-field patching is necessary
Interfaces should be more flexible
Memory controllers should be more intelligent in detecting malicious activity
DRAM chips become more and more vulnerable to RowHammer and RowPress
Key Insight:
  A thousand activations are enough to induce bitflips
  Benign applications perform as many activations
Problem: DRAM read disturbance solutions are getting prohibitively expensive
Research Question: How to identify malicious threads/processes/users?
More intelligent detection mechanisms are needed  AI can play an important role
The memory controller observes all memory accesses  has the ground truth data
More intelligent memory controllers can help

## Slide 62: Future Research for Better Memory Systems



Cross-Layer
Communication
Flexible and Intelligent Memory Chips, Interfaces, Controllers
Deeper Understanding of
Physics and Vulnerabilities
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 63: Cross-Layer Communication
Attacker is often an application
Bitflips occur in the circuit level
Hardware is good at
  Detecting an attack
  Performing counter-measures
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Memory allocations
Memory access patterns
Control flow patterns
Time / power measurements
Memory request scheduling
Speculative execution
Prefetching, branch prediction
Power management
Bitflips occur
Memory isolation is broken
Software
uArch
Device
Detection
Mitigation
~
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 64: Cross-Layer Communication
Attacker is often an application
Bitflips occur in the circuit level
Hardware is good at
  Detecting an attack
  Performing counter-measures
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Memory allocations
Memory access patterns
Control flow patterns
Time / power measurements
Memory request scheduling
Speculative execution
Prefetching, branch prediction
Power management
Bitflips occur
Memory isolation is broken
Detection
Mitigation
Software
uArch
Device
~
Cross-layer communication is crucial going forward
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 65: Future Research for Better Memory Systems



Cross-Layer
Communication
Flexible and Intelligent Memory Chips, Interfaces, Controllers
Deeper Understanding of
Physics and Vulnerabilities
Notes: We can address these challenges by investing on [CLICK]
Better cross-layer communication[CLICK]
More intelligent memory chips, interfaces, and controllers [CLICK]
And deeper understanding of physics and vulnerabilities [CLICK]

## Slide 66: Enabling Efficient and Scalable Read Disturbance Mitigation via New Experimental Insights into Modern Memory Chips
agyaglikci.github.io
safari.ethz.ch
Abdullah Giray Yaglikci
agyaglikci@gmail.com
https://agyaglikci.github.io
Backup Slides
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 67: Circuit-Level Justification
3D TCAD Evaluation [Yang+, EDL'19]
Until a temperature inflection point: As temperature increases, fewer activations can cause bitflips
After the temperature inflection point:
As temperature increases, more activations are needed to cause bitflips
Trap-Assisted Charge Leakage Model
Hammering a wordline pulls and pushes electrons
Electrons get trapped and exacerbate charge leakage, leading to cause bitflips
With increasing temperature, it becomes less likely for an electron to get trapped
Notes: And third, [CLICK]
We observe thatThe HCfirst change tends to be larger as temperature change increases [CLICK]
The figure shows that, for all manufacturer, when increase the temperature change from 50-55C to 50-90C, the absolute changes values increase [CLICK]

## Slide 68: Example Attack Improvement: Bypassing Defenses with Aggressor Row Active Time
Reduces the minimum activation count to induce a bitflip by 36%
Bypasses defenses that do not account for this reduction
Time
Row A is active
Row B is active
Row A is active
Activating aggressor rows as frequently as possible:
Time
Row A is active
Row B is active
Keeping the aggressor rows active for a longer time:
36% reduction in HCfirst
Notes: In the third example, an attacker can leverage the effect of aggressor row active time [CLICK]
In this scenario, instead of activating aggressor rows as frequently as possible, [CLICK]
the attacker can keep the aggressor rows active for longer time [CLICK]
Based on our analyses, HCfirst reduces by 36% on average with the proposed access pattern
With this reduction, an attacker can bypass RowHammer defenses that do not account for this reduction [CLICK]

## Slide 69: RowPress vs. RowHammer
Instead of using a high activation count,
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
We observe bitflips even with ONLY ONE activation in extreme cases where the row stays open for 30ms
36ns, 47K activations to induce bitflips
7.8µs, only 5K activations to induce bitflips
☞ increase the time that the aggressor row stays open
Notes: Instead of a high activation count, RowPress increases the time the that aggressor stays open.
Doing disturbs adjacent rows enough to cause bitflips without a very high activation count.
We observe bitflips even with only one activation in extreme cases.

## Slide 70: RowPress [Luo+, ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023.

## Slide 71: Circuit-Level Justification
We hypothesize that our observations are caused by the non-monotonic behavior of charge trapping characteristics of DRAM cells
3D TCAD model [Yang+, EDL'19]
HCfirst decreases as temperature increases, until a temperature inflection point where HCfirst starts to increase as temperature increases
A cell is more vulnerable to RowHammer at temperatures close to its temperature inflection point
Notes: And third, [CLICK]
We observe thatThe HCfirst change tends to be larger as temperature change increases [CLICK]
The figure shows that, for all manufacturer, when increase the temperature change from 50-55C to 50-90C, the absolute changes values increase [CLICK]

## Slide 72: Example Attack Improvement: Temperature-Dependent Trigger
  Identify abnormal increase in temperature to attack a data center during its peak hours
  Precisely measure the temperature to trigger an attack exactly at the desired temperature
Temperature
70 °C
76.6%
of the cells*
*Example fraction values from SK Hynix modules
0.4%
of the cells*
Temperature
70 °C
Temperature
70 °C
0.4%
of the cells*
1.
2.
Notes: In the second attack example, the attacker uses RowHammer to understand the DRAM chip’s current temperature [CLICK]
As an example, more than 76% of the vulnerable cells experience bit flips above 70 degrees Celsius for Mfr C. Focusing on these cells, an attacker can identify abnormal operating conditions that might occur in a data center during its peak hours. This information can be used to trigger an attack when the data center is under pressure[CLICK]
If it is important to measure temperature precisely, the attacker can focus on a smaller set of vulnerable cells that experience bit flips only in a narrow temperature range. For example, 0.4% of vulnerable cells experience bit flips only at 70 degrees Celsius in Mfr C. Using these cells, the attacker can precisely detect the temperature and trigger an attack accordingly [CLICK]

## Slide 73: Enabling Efficient and Scalable Read Disturbance Mitigation via New Experimental Insights into Modern Memory Chips
agyaglikci.github.io
safari.ethz.ch
Abdullah Giray Yaglikci
agyaglikci@gmail.com
https://agyaglikci.github.io
11 March 2024
Huawei Cambridge
Backup Slides
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 74: Memory Access Patterns in Aggressor Row Active Time Analysis
Baseline access pattern:
Increasing aggressor row active time:
Increasing bank precharged time:
Time
Row A is active
Row B is active
Row A is active
Row B is active
Time
Row A is active
Time
Row A is active
Row B is active
Row A is active
Row B is active
Row A is active
Aggressor row active time
Bank precharged time
Aggressor row active time
Aggressor row active time
Bank precharged time
Bank precharged time
Notes: To perform this analysis, we conduct two sets of experiments [CLICK]
In the baseline, we hammer rows A and B as frequently as possible [CLICK]
In the first set of tests, we increase the time that an aggressor row is active [CLICK],
And in the second set of experiments we increase the time that the bank is precharged [CLICK]

## Slide 75: Thesis Statement
Developing
a deeper understanding of DRAM read disturbance and revisiting memory controller designs enable scientists and engineers to build reliable, secure, and safe DRAM-based systems
Notes: My thesis is that Developing a deeper understanding of DRAM read disturbance and revisiting memory controller designs accordingly enable building reliable, safe, and secure systems. [CLICK]

## Slide 76: DRAM Organization
DRAM Chip
Bank
Chip I/O
DRAM Bank
Subarray
. . .
DRAM Subarray
Row Buffer
Bitline
…
…
Wordline
…
…
…
…
DRAM Cell
DRAM Row
Notes: This is a DRAM module, used as the main memory on many systems. [CLICK]
A DRAM module consists of multiple chips each of which contains multiple banks [CLICK]
Each bank is composed of multiple subarrays [CLICK]
And within each subarray, there is a two dimensional array of DRAM cells. [CLICK]
These cells are organized into rows that are selected using wordlines [CLICK]
And the cells are connected to a row buffer via bitlines [CLICK]

## Slide 77: DRAM Chips Tested
Mfr. | DDR4 DIMMs | DDR3 SODIMMs | # Chips | Density | Die | Org.
A (Micron) | 9 | 1 | 144 (8) | 8Gb (4Gb) | B (P) | x4 (x8)
B (Samsung) | 4 | 1 | 32 (8) | 4Gb (4Gb) | F (Q) | x8 (x8)
C (SK Hynix) | 5 | 1 | 40 (8) | 4Gb (4Gb) | B (B) | x8 (x8)
D (Nanya) | 4 | - | 32 (-) | 8Gb (-) | C (-) | x8 (-)
272 total DRAM chips tested
Four major DRAM manufacturers
DDR3 and DDR4 DRAM standards
Different densities, die revisions and chip organizations
Notes: We provide more details about the chips we test in extended arxiv version of the paper [CLICK]

## Slide 78: DRAM Testing Methodology
To characterize our DRAM chips at worst-case conditions:
Prevent sources of interference during core test loop
  No DRAM refresh: to avoid refreshing victim row
  No DRAM calibration events: to minimize variation in test timing
  No RowHammer mitigation mechanisms: to observe circuit-level effects
  Test for less than a refresh window (32ms) to avoid retention failures
  Repeat tests for ten times
Worst-case access sequence
We use worst-case access sequence based on prior works’ observations
For each row, repeatedly access the two physically-adjacent rows as fast as possible
Notes: To characterize our DRAM chips at worst-case conditions we take two measures:
[CLICK] First, we prevent external sources of interference such that our tests can run consistently as desired and without interruptions. To achieve this we disable:
[CLICK] DRAM refresh to avoid refreshing victim rows during a test,
[CLICK] DRAM calibration events to minimize variation in test timings
[CLICK] and RowHammer mitigation mechanisms to ensure that we can directly observe circuit-level bit flips
[CLICK] we also ensure that our RowHammer tests complete in less than a refresh window to prevent retention failures from interfering with our results
[CLICK] and we repeat our tests ten times to filter out the noise in measurements
[CLICK] Second, we issue the worst-case access sequence for inducing RowHammer bit flips based on observations from prior work
[CLICK] which suggest to repeatedly activate the two physically-adjacent rows as fast as possible
=========

## Slide 79: Attack Improvement 1: Making DRAM Cells More Vulnerable
An attacker can manipulate temperature to make the cells that store sensitive data more vulnerable
Vulnerable Temperature Range
Temperature
no bit flips
no bit flips
45°C
55°C
65°C
75°C
50°C
70°C
DRAM cells are vulnerable in a bounded temperature range
Heating up chip temperature
Cooling down chip temperature
Notes: In the first example for an attack improvement, the attacker manipulates the DRAM module’s temperature to increase the RowHammer vulnerability of the cells that store sensitive data [CLICK]
We observe that DRAM cells are vulnerable to RowHammer in a bounded temperature range [CLICK]
that we call vulnerable temperature range [CLICK]
For example, let this range be from 50 to 70 degrees celsius for the victim cells
To attack the cells within their vulnerable temperature range, an attacker can [CLICK]
heat up the chip if its current temperature is below 50 [CLICK]
Or cool down the chip if its current temperature is above 70 degrees celsius [CLICK]

## Slide 80: Key Takeaways from Spatial Variation Analysis
RowHammer vulnerability significantly varies
across DRAM rows and columns due to design and manufacturing-process
Key Takeaway 1
Minimum hammer count to induce the first bitflip (HCfirst) significantly varies across rows in a subarray
but not as much across subarrays
Key Takeaway 2

In-Chip
Variations
Notes: In this analysis, we investigate how the RowHammer vulnerability varies based on a victim DRAM cell's physical location
We have two key takeaways from this analysis. [CLICK]
First, The RowHammer vulnerability significantly varies across DRAM rows and columns due to both design induced and manufacturing process induced variation [CLICK]
Second, the distribution of HCfirst exhibits
- a diverse set of values within a subarray
- But similar values across subarrays within a DRAM module [CLICK]

## Slide 81: Regularity in Spatial Variation of Read Disturbance across DRAM Rows
The minimum hammer count to induce the first bitflip
irregularly varies with respect to row’s location in DRAM bank
The minimum hammer count
to induce the first bitflip (HCfirst)
DRAM Row Address
No visible regularity in HCfirst based on the row’s location
Notes: There are different bins but do not correlate well with the row address

## Slide 82: Regularity in Spatial Variation of Read Disturbance across DRAM Rows
DRAM Row Address
The minimum hammer count
to induce the first bitflip (HCfirst)
No visible regularity in HCfirst based on the row’s location
The minimum hammer count to induce the first bitflip
irregularly varies with respect to row’s location in DRAM bank
Notes: There are different bins but do not correlate well with the row address

## Slide 83: Regularity in Spatial Variation of Read Disturbance across DRAM Rows
DRAM Row Address
The minimum hammer count
to induce the first bitflip (HCfirst)
No visible regularity in HCfirst based on the row’s location
The minimum hammer count to induce the first bitflip
irregularly varies with respect to row’s location in DRAM bank
Notes: There are different bins but do not correlate well with the row address

## Slide 84: Predictability of Read Disturbance Vulnerability
Predictability of a DRAM row’s read disturbance vulnerability based on the row’s spatial features
bank address bits
subarray address bits
row address bits
row’s distance to local row buffer
Methodology
Cluster DRAM rows into 15 bins based on each row’s minimum hammer count to induce the first bitflip (HCfirst)
Predict whether a row is in a cluster, based on each spatial feature
Measure the F1 score for these predictions
Key Result: Only a few spatial features have F1 scores > 0.7 only for Mfr. S
A row’s spatial features are weak predictors for the row’s read disturbance vulnerability

## Slide 85: My Dissertation Works
A deeper look into DRAM read disturbance
Solutions to DRAM read disturbance

Temperature

Memory Access Patterns

In-Chip
Variations
Voltage
Throttling Unsafe Accesses
Parallelizing Preventive Measures

Leveraging
Heterogeneity
Notes: I also developed solutions that [CLICK]
throttle unsafe accesses [CLICK
parallelize maintenance operations [CLICK]
and leverage heterogeneity [CLICK]
Let me quickly explain one of these works [CLICK]

## Slide 86: A Closer Look into RowHammer
Low Voltage
Victim Row
Bitline
Low Voltage
Victim Row
Aggressor Row
Disturbance
High Voltage
Aggressor Row
Low Voltage
Low Voltage
Victim Row
Victim Row
Low Voltage
time
Agressor Row
Wordline Voltage
Repeatedly toggling
wordline voltage
is the key to inducing RowHammer bitflips
Notes: This cartoon provides a closer look into RowHammer. [CLICK]
Asserting high voltage to a row’s wordline for row activation disturbs nearby rows [CLICK]
Repeating this operation [CLICK] many times [CLICK] exacerbates the leakage in victim rows and leads to bit flips [CLICK]
Therefore, repeatedly toggling wordline voltage is the key to induce RowHammer bit flips [CLICK]

## Slide 87: Our Key Finding
Reducing wordline voltage
reduces RowHammer vulnerability
without significantly affecting reliable DRAM operation
time
Wordline
Voltage
Reduction in Disturbance
Aggressor Row
Victim Row
Aggressor Row
Victim Row
Wordline
Bitline
Wordline
Bitline
Weaker Channel in Access Transistor
Strong Channel
Weaker Channel
time
Wordline
Voltage
Notes: In this work, we hypothesize that [CLICK]
Lowering the magnitude of wordline voltage [CLICK]
can reduce RowHammer vulnerability [CLICK]
without significantly affecting reliable DRAM operation [END]

## Slide 88: My Dissertation Works
A deeper look into DRAM read disturbance
Solutions to DRAM read disturbance

Temperature

Memory Access Patterns

In-Chip
Variations
Voltage
Throttling Unsafe Accesses
Parallelizing Preventive Measures

Leveraging
Heterogeneity
Notes: I also developed solutions that [CLICK]
throttle unsafe accesses [CLICK
parallelize maintenance operations [CLICK]
and leverage heterogeneity [CLICK]
Let me quickly explain one of these works [CLICK]

## Slide 89: Compatibility with Commodity DRAM Chips
A RowHammer attack hammers Row A
Existing mechanisms detect the attack
Refresh rows A+1 and A-1
Bit flips still may occur due to unknown DRAM-internal row mapping
Physical
Row Layout
Row A+1
Row A-1
Victim
Rows
Row A
Existing read disturbance mitigation mechanisms need to know proprietary DRAM-internal row address mapping
Notes: Assume that an attacker hammers a row to induce bit flips in its nearby rows [CLICK]
Existing mitigation mechanisms detect the attack [CLICK]
And try refreshing the nearby rows [CLICK]
However, the DRAM chip can internally map these row addresses to different physical rows [CLICK]
And thus bit flips may still occur[CLICK]
To avoid this, existing mechanisms need to know proprietary DRAM-internal row address mapping [CLICK]

## Slide 90: BlockHammer – HPCA 2021
A. Giray Yaglikci, Minesh Patel, Jeremie S. Kim, Roknoddin Azizi, Ataberk Olgun, Lois Orosa, Hasan Hassan, Jisung Park, Konstantinos Kanellopoulos, Taha Shahroodi, Saugata Ghose, and Onur Mutlu, "BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows" Proceedings of the 27th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, February-March 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Intel Hardware Security Academic Awards Short Talk Slides (pptx) (pdf)] [Talk Video (22 minutes)] [Short Talk Video (7 minutes)] [Intel Hardware Security Academic Awards Short Talk Video (2 minutes)] [BlockHammer Source Code] Intel Hardware Security Academic Award Finalist (one of 4 finalists out of 34 nominations)
Notes: We provide more analyses and implementation details available in the full paper.
[CLICK] First, the paper shares a security proof where we mathematically represent ALL POSSIBLE access patterns and show that NO ROW can be activated at a high-enough rate to induce bit-flips when BlockHammer is configured correctly.
[CLICK] Second, the paper explains how BlockHammer addresses many-sided attacks by tuning its thresholds.
[CLICK] Third, we evaluate all four high-level RowHammer mitigation approaches through analyzing 14 mechanisms from four aspects
[CLICK] comprehensive protection
[CLICK] compatibiltiy with commodity DRAM chips
[CLICK] scalability with worsening RowHammer vulnerability
[CLICK] and deterministic protection.
[CLICK] We show that BlockHammer is the only mechanism that satisfies all of them.
[END]

## Slide 91: BlockHammer: Throttling Unsafe Accesses
A RowHammer attack hammers Row A
BlockHammer detects and selectively throttles accesses from within the memory controller
Bit flips do not occur
BlockHammer can optionally inform the system software about the attack
Physical
Row Layout
Row A
BlockHammer is compatible with commodity DRAM chips
No need for proprietary info of or modifications to DRAM chips
Notes: In contrast, BlockHammer detects and selectively throttles the attack’s memory accesses [CLICK]
Therefore, the row’s activation count cannot reach critical levels, and no bit flip occurs [CLICK]
BlockHammer can optionally inform the system software about the attack for higher-level countermeasures [CLICK]
BlockHammer achieves all of these without needing proprietary information of or modifications to commodity DRAM chips [CLICK]

## Slide 92: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Aging Slides
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 93: More in the Paper (2/2): Aging Study
Preliminary data on aging via 68-day of continuous hammering
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
Aging can lead to read disturbance bitflips at smaller hammer counts
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)

## Slide 94: More in the Paper (2/2): Aging Study
Preliminary data on aging via 68-day of continuous hammering
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
Aging can lead to read disturbance bitflips at smaller hammer counts
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
Future work:
rigorous aging characterization
and online profiling of read disturbance vulnerability

## Slide 95: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Hydra’s Performance
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 96: An Outlier Solution: Hydra
Minimum Hammer Count to Induce the First Bitflip
Weighted Speedup
(Norm. to No Mitigation Baseline)
Only 7% Speedup

## Slide 97: Hydra Mitigation Mechanism
Hydra maintains a row activation counter for each DRAM row
Stores these activation counters in the DRAM array
Caches the counters of hot rows in the memory controller
At low HCfirst configurations, many rows are hot
Fetching / evicting counters dominate the performance overhead
Svärd needs further customizations for Hydra
Qureshi, et al. "Hydra: Enabling Low-Overhead Mitigation of Row-Hammer at Ultra-Low Thresholds via Hybrid Tracking," in ISCA, 2022.

## Slide 98: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
HCfirst across Rows
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 99: The Minimum Hammer Count to Induce the First Bitflip across DRAM Rows
Relative location of a DRAM row
(0 and 1 are the two edges of a DRAM bank)
No visible regularity in HCfirst based on the row’s location
The minimum hammer count to induce the first bitflip
irregularly varies with respect to row’s location in DRAM bank
The minimum hammer count
to induce the first bitflip (HCfirst) Norm. to the Lowest Hcfirst in the module

## Slide 100: The Minimum Hammer Count to Induce the First Bitflip across DRAM Rows
Relative location of a DRAM row
(0 and 1 are the two edges of a DRAM bank)
No visible regularity in HCfirst based on the row’s location
The minimum hammer count to induce the first bitflip
irregularly varies with respect to row’s location in DRAM bank
The minimum hammer count
to induce the first bitflip (HCfirst) Norm. to the Lowest Hcfirst in the module

## Slide 101: The Minimum Hammer Count to Induce the First Bitflip across DRAM Rows
Relative location of a DRAM row
(0 and 1 are the two edges of a DRAM bank)
No visible regularity in HCfirst based on the row’s location
The minimum hammer count to induce the first bitflip
irregularly varies with respect to row’s location in DRAM bank
The minimum hammer count
to induce the first bitflip (HCfirst) Norm. to the Lowest Hcfirst in the module

## Slide 102: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
BER across Rows
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 103: The Read Disturbance Bit Error Rate across DRAM Rows
Relative location of a DRAM row
(0 and 1 are the two edges of a DRAM bank)
Bit error rate periodically increases and decreases
The variation in read disturbance bit error rate
exhibits a stronger regularity compared to the variation in varies with respect to row’s location in DRAM bank

## Slide 104: The Read Disturbance Bit Error Rate across DRAM Rows
Relative location of a DRAM row
(0 and 1 are the two edges of a DRAM bank)
Bit error rate periodically increases and decreases
The variation in read disturbance bit error rate
exhibits a stronger regularity compared to the variation in varies with respect to row’s location in DRAM bank

## Slide 105: The Read Disturbance Bit Error Rate across DRAM Rows
Relative location of a DRAM row
(0 and 1 are the two edges of a DRAM bank)
Bit error rate periodically increases and decreases
The variation in read disturbance bit error rate
exhibits a stronger regularity compared to the variation in varies with respect to row’s location in DRAM bank

## Slide 106: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Background
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 107: Two Main Types of DRAM Refresh
2
Periodic Refresh: Periodically restores the charge DRAM cells leak over time
1
DRAM Row
Preventive Refresh
Preventive Refresh
RowHammer: Repeatedly accessing a DRAM row can cause bit flips in other physically nearby rows
Preventive Refresh: Mitigates RowHammer by refreshing physically nearby rows of a repeatedly accessed row
Notes: DRAM Refresh is mainly used for two purposes [CLICK]
The first one is called: Periodic Refresh to periodically restore the charge that DRAM cells leak over time [CLICK]
The second one is relevant to a read-disturb error mechanism called RowHammer, where repeatedly accessing a DRAM row can cause bit flips in other physically near by rows [CLICK]
A common method of mitigating RowHammer is refreshing potentially affected rows, called preventive refresh [CLICK]

## Slide 108: Periodic Refresh with Increasing DRAM Chip Density
A larger capacity chip has more rows to be refreshed
A smaller cell stores less charge
Significant performance and energy overhead
Chart: DRAM Chip Capacity
| 2 | 4 | 8 | 16 | 32 | 64 | 128
Baseline | 0.97444 | 0.96375 | 0.94679 | 0.92168 | 0.88302 | 0.82497 | 0.73698
26% Slowdown
More periodic refresh operations incur larger performance overhead as DRAM chip density increases
Notes: With increasing DRAM chip density, [CLICK]
More rows need to be refreshed [CLICK]
And cells can store smaller charge leading to more periodic refresh operations[CLICK]
In this plot, we sweep DRAM chip capacity on the x-axis and investigate how the performance overhead of DRAM refresh operations change[CLICK]
We observe 26% slowdown in system performance caused by periodic refreshes [CLICK]

## Slide 109: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
RowPress
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 110: DRAM Organization
DRAM Chip
Bank
Chip I/O
DRAM Bank
Subarray
. . .
DRAM Subarray
Row Buffer
Bitline
…
…
Wordline
…
…
…
…
DRAM Cell
DRAM Row
Notes: This is a DRAM module, used as the main memory on many systems. [CLICK]
A DRAM module consists of multiple chips each of which contains multiple banks [CLICK]
Each bank is composed of multiple subarrays [CLICK]
And within each subarray, there is a two dimensional array of DRAM cells. [CLICK]
These cells are organized into rows that are selected using wordlines [CLICK]
And the cells are connected to a row buffer via bitlines [CLICK]

## Slide 111: DRAM Operation
DRAM Subarray
Bitline
…
…
Wordline
…
…
…
…
DRAM Cell
DRAM Cell
Row Buffer
Row Activation: Fetch the row’s content into the row buffer
Column Access: Read/Write a column in the row buffer
Precharge: Disconnect the row from the row buffer
Wordline
Capacitor
Access transistor
Bitline
charge
leakage
paths
Refresh: Restores the capacitor voltage with a time period called refresh window
I/O Circuitry
Notes: This is a simplified diagram of a DRAM cell, where the data is stored as capacitor voltage and accessed through the access transistor [CLICK]
A DRAM cell inherently exhibits several charge leakage paths [CLICK]
And requires to perform refresh operations to restore the capacitor voltage with a time period called refresh window.
[PAUSE]
To access a DRAM cell, [CLICK]
the memory controller must first open or activate the row to fetch the row’s data into the row buffer [CLICK]
The READ and WRITE requests targeting the row are serviced from the row buffer [CLICK]
After all requests are serviced from the row, the memory controller must close or precharge the row in order to begin accessing data from another row. [CLICK]

## Slide 112: RowHammer Mitigation Approaches
Increased refresh rate
Physical isolation
Reactive refresh
Proactive throttling
DRAM Bank
Aggressor Row
Victim Rows
Isolation Rows
Large-enough distance
DRAM Bank
Aggressor Row
Victim rows
Refresh
Victim Rows
Refresh
Rapidly activated (hammered)
REF-to-REF time reduces
Fewer activations can fit
Fewer activations can be performed
Notes: There are four high-level RowHammer mitigation approaches.
[CLICK] The first approach is to increase refresh rate
[CLICK] which reduces the refresh window,
[CLICK] and thus the activation count that an attacker can reach in a refresh window.
[CLICK] The second approach is to physically isolate
[CLICK] potential victim rows with sensitive data
[CLICK] from aggressor rows that a potential attacker can hammer
[CLICK] by allocating isolation rows in between
such that the attacker cannot disturb sensitive data by performing RowHammer attack.
[CLICK] The third approach is reactive refresh.
[CLICK] In this approach, when an aggressor row is hammered
[CLICK] potential victim rows are refreshed to avoid bit-flips.
[CLICK] Finally the fourth approach suggests
[CLICK] throttling or slowing down memory accesses proactively such that no row’s activation rate can reach RowHammer threshold.

## Slide 113: RowHammer Mitigation across Generations
105
104
103
102
105
104
103
102
DDR3-old
DDR3-new
DDR4-old
LPDDR4-1x
DDR4-new
LPDDR4-1y
PARA
TWiCe-ideal
Ideal
HCfirst (number of hammers required to induce first RowHammer bit flip)
14%
J. S. Kim, M. Patel, A. G. Yaglikci, H. Hassan, R. Azizi, L. Orosa, and O. Mutlu, "Revisiting RowHammer: An Experimental Analysis of Modern Devices and Mitigation Techniques,” in ISCA, 2020.

## Slide 114: RowPress [ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023.

## Slide 115: RowPress A New DRAM Read Disturbance Phenomenon
Row 0
Row 1
Row 2
Row 3
Row 4
Keeping a DRAM row open (activated)
causes RowPress bitflips in nearby cells
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 2
closed
Victim Row
Victim Row
Aggressor Row
Row 2
open
Aggressor Row
DRAM Subarray
Notes: Due to an increase in cell-to-cell interference, as a result of aggressive technology node scaling, rapidly activating [CLICK] and precharging
[FORTH & BACK] a DRAM row can result in bit flips in physically adjacent rows [CLICK]
[FORTH & BACK] Continuing to access the same row results in even more failures in nearby rows. This phenomenon is known as RowHammer. [CLICK]
We refer to the rapidly accessed row as an aggressor row and the rows containing bit flips as victim rows.

## Slide 116: Two Prime Examples of DRAM Read Disturbance: RowHammer and RowPress
Instead of using a high activation count,
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
☞ increase the time that the aggressor row stays open
Notes: Instead of a high activation count, RowPress increases the time the that aggressor stays open.
Doing disturbs adjacent rows enough to cause bitflips without a very high activation count.
We observe bitflips even with only one activation in extreme cases.

## Slide 117: RowPress [ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023.

## Slide 118: Effect of RowPress on Spatial Variation of Read Disturbance Vulnerability across Rows
RowPress reduces the mean of the distribution with increased tAggOn
There is still significant variation in the HCfirst across rows
Effect of RowPress on the HCfirst Distribution
Minimum Hammer Count
To Induce the First Bitflip
(HCfirst)
Aggressor Row’s On Time (tAggOn) (ns)

## Slide 119: Effect of RowPress on the HCfirst Distribution
Bitflips occur at lower hammer counts with RowPress and these hammer counts still significantly vary across DRAM rows
Aggressor Row’s On Time (tAggOn) (ns)
Minimum Hammer Count
To Induce the First Bitflip
(HCfirst)
Aggressor Row’s On Time (tAggOn) (ns)
Notes: Assume that an attacker hammers a row to induce bit flips in its nearby rows [CLICK]
Existing RowHammer defenses detect the attack [CLICK]
And try refreshing the nearby rows [CLICK]
However, the DRAM chip can internally map these row addresses to different physical rows [CLICK]
And thus bit flips may still occur[CLICK]
To avoid this, existing mechanisms need to know proprietary DRAM-internal row address mapping [CLICK]

## Slide 120: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Predictability
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 121: Cumulative Distribution of Spatial Features based on F1 Score
F1 score
Cumulative Distribution
of Spatial Features
Different DRAM modules
Weak prediction observed between a row’s spatial features & read disturbance vulnerability
More than 50% of the features have F1 scores larger than 0.1
Notes: Make the x-axis more intuitive

## Slide 122: Cumulative Distribution of Spatial Features based on F1 Score
F1 score
F1 score
F1 score
Cumulative Distribution of Spatial Features
A few spatial features from Mfr. S can exhibit F1 score >0.7
Different DRAM modules
Weak prediction observed between a row’s spatial features & read disturbance vulnerability
Notes: Make the x-axis more intuitive

## Slide 123: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Implementation Details
Full Paper
arXiv [cs.CR] 2402.18652
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Notes: Hi my name is Giray and I am happy to share my research with you

## Slide 124: Svärd: Spatial Variation-Aware Read Disturbance Defenses Integration Examples with Existing Defenses
Svärd tunes the threshold based on the victim row’s vulnerability
Integrate Svärd with five solutions
1) PARA [Kim+, ISCA’14]
  Generates a random number
  Compares the random number with a threshold
  Refreshes the victim row if the random number exceeds the threshold
2) BlockHammer [Yaglikci+, HPCA’21]
  Counts the number of activations of DRAM rows
  Compares the activation count with a threshold
  Throttles accesses to the aggressor row if the activation count reaches the threshold
3) Hydra [Qureshi+, ISCA’22]
  Counts the number of activations of DRAM rows
  Compares the activation count with a threshold
  Refreshes the victim row when the activation count reaches the threshold
4) AQUA [Saxena+, MICRO’22] and 5) RRS [Saileshwar+, ASPLOS’22]
  Counts the number of activations of DRAM rows
  Compares the activation count with a threshold
  Relocates the aggressor row when the activation count reaches the threshold
Notes: We leverage this observation [CLICK]
By protecting weak rows more aggressively than strong rows [CLICK]
We do this by dynamically tuning the aggressiveness of defense mechanisms [CLICK]
and we show significant improvement in system performance. [CLICK]
Too high level
Put ataberk’s explanation here

## Slide 125: Svärd: Spatial Variation-Aware Read Disturbance Defenses Example Implementation 1
Classifies DRAM rows into several vulnerability-level bins
  Maintains a few (e.g., four) bits per DRAM row
Implemented in either the memory controller or the DRAM chip
Two example memory controller-based implementations:
Data
Memory
Request
DRAM Commands, Address, Data
Memory Controller
Memory
Request
Scheduler
DRAM
Chip
Existing Read
Disturbance
Solution
Preventive Action
HCfirst
HCfirst Table
Row
Addr
Metadata
Bits
Two potential ways of handling metadata
Notes: Too busy
Make either or more obvious
Table in the dram chip
Why memory controllers?
s/w based metadata?

## Slide 126: Svärd: Spatial Variation-Aware Read Disturbance Defenses Example Implementation 2
Classifies DRAM rows into several vulnerability-level bins
  Maintains a few (e.g., four) bits per DRAM row
Implemented in either the memory controller or the DRAM chip
An example DRAM chip-based implementation:
  Additional few (e.g., four) bits per DRAM row (e.g., 8Kb)
Data
DRAM
command
address
data
DRAM Chip
I/O Periphery
Existing Read
Disturbance
Solution
Preventive Action
HCfirst Bin
Refresh
Controller
DRAM Subarray
DRAM Row
DRAM Row
Row Buffer
DRAM Row

## Slide 127: Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Abdullah Giray Yağlıkçı
Yahya Can Tuğrul Geraldo F. Oliveira İsmail Emir Yüksel
Ataberk Olgun Haocong Luo Onur Mutlu
Backup Slides
Notes: Hi my name is Giray and I am happy to share my research with you